## Slide 1
Instrumentation and Control
(ACDB5011)
Lecture - 1

## Slide 2: Content
What is Control system?
Transducers
Sensors
Actuators

## Slide 3: Control System
System:
A combination of components or subsystems that act together and perform a certain objective.
Control System :
An interconnection of components forming a system that will provide a desired response for a given input.
Control System
Inputs
Desired Output

## Slide 4: Transducers
Transducer
noun
  a device that converts variations in a physical quantity, such as pressure or brightness, into an electrical signal, or vice versa.
For the purposes of this module, we shall consider transducers as devices which produce electrical signals - sensors.

## Slide 5: Transducers
There are two types of transducers
  Electrical (Responds to non-electrical quantities but generate output signal which is electrical in nature)
  Mechanical (Primary sensing elements that responds to changes in the physical condition of a system and gives output in non-electrical signal form)

## Slide 6: Transducers
Electrical transducer has two parts,
  Sensing or detecting part
  Transduction element
The sensing or detecting element is commonly called as sensor.
The transduction element transfers the output of the sensor to an electrical output.

## Slide 7: Transducers
Sensors can be classified as
Active
Passive

## Slide 8: Active Sensors
Active sensors typically require an external power source to produce the output signal.
Active sensors will usually produce a voltage (1 to 10V) or current (4 to 20mA) proportional to the measured property.
Active sensors can also produce signal amplification.

## Slide 9: Active Sensors
Examples
Thermistor
Strain gauge

## Slide 10: Active Sensors
Thermistor:
  Thermistor —short for thermally sensitive resistor
  It is a resistor that changes value with the temperature.
  Thermistors increase or decrease resistance with changing temperatures.

## Slide 11: Active Sensors
Strain gauge:
  A Strain gauge is a sensor whose resistance varies with applied force.
  It converts force, pressure, tension, weight, etc., into a change in electrical resistance which can be measured.
  When external forces are applied to a stationary object, stress and strain are the result.

## Slide 12: Passive Sensors
Passive sensors do not need any additional power source to operate
The output signal is generated in response to some external stimulus.

## Slide 13: Passive Sensors
Examples
  Thermocouple
  Photodiode
  Piezoelectric sensors

## Slide 14: Passive Sensors
  Thermocouple
      A thermocouple is a device for measuring temperature.
      It comprises two dissimilar metallic wires joined together to form a junction.
      When the junction is heated or cooled, a small voltage is generated in the electrical circuit of the thermocouple which can be measured, and this corresponds to temperature.

## Slide 15: Passive Sensors
  Photodiode
      A photodiode is a semiconductor device with a P-N junction that converts photons (or light) into electrical current.

## Slide 16: Passive Sensors
  Piezoelectric sensors
      A piezoelectric sensor is a device that uses the piezoelectric effect to measure changes in pressure, acceleration, temperature, strain, or force by converting them to an electrical charge.

## Slide 17: Sensor or Transducer?
There are two main types of sensor:
  Switches
  Transducers, e.g. Light sensors

## Slide 18: Switches
A Switch can be used as a sensor that is either ON or OFF
A limit switch is the most common switch sensor. It is used to restrict the movement of a machine
The machine moves until it reaches a position and activates the limit switch
A switch is then triggered, and the control stops the machine movement
On
Off
1
0
Digital Signal of a Switch Sensor

## Slide 19: Inductive proximity switch
Is used to detect metallic objects
An AC current is passed through a coil in the sensor creating a magnetic field.
Metallic object interferes with the magnetic field changing the electrical properties of the coil.
Change in electrical properties detected by internal circuitry and outputted as a high or low voltage level

## Slide 20: Inductive proximity switch
Often used in industrial machines to detect metallic objects like tin cans or used as limit switches to control movement.
Larger version is used to detect cars at traffic lights and car park barriers

## Slide 21: Capacitive proximity switch
Similar to inductive proximity switch
Can be used to detect conductive objects
Senses objects with dielectric constant different to air.
Changes in dielectric constant are detected as a change in oscillator frequency.
Detect metallic and non-metallic object.

## Slide 22: Optical switches
Detect the presence or absence of light.
Can be used in reflective or transmission mode.
Can be used to detect size, or other physical property of moving components
  Height, Width, or presence of some feature e.g. if there is a cap on a bottle
Can be used to detect difference between light and dark

## Slide 23: Optical switches
Can be used to measure rotational speed
Opaque disc with a single slot used to allow light to pass only once per revolution
Switch will activate once per revolution producing a pulse
Frequency of pulses measured to give rotational speed

## Slide 24: Optical switches
Rotational speed could relate to a few different physical properties we might want to measure
  Wind speed
  Record playback speed
  Vehicle road or engine speed

## Slide 25: Optical encoders
Adding a second detector allows us to detect direction of rotation through quadrature phase detection
Adding more slots increases resolution and allows us to measure angular displacement.
Angular displacement can be related to physical movement of an object and used to measure distance.

## Slide 26: Hall effect sensors
Hall effect sensors are used to detect and measure magnetic field intensity
Hall sensor has four terminals –
  2 power supply and 2 measurement terminals
Current flows between power terminals
Electrons are deflected by magnetic field towards measurement terminals

## Slide 27: Hall effect sensor
Output from hall sensor can be thresholded to give digital on/off output
Output from hall sensor can be linear to allow measurement of magnetic field
Can be used to measure current in a wire
Can be used to detect presence of a magnet

## Slide 28: Actuators
An actuator is a part of a device or machine that helps it to achieve physical movements by converting energy, often electrical, air, or hydraulic, into mechanical force.
Simply put, it is the component in any machine that enables movement.
for example, opening a valve.

## Slide 29: Actuator
Examples of actuator include
  Motors – converts electrical to mechanical energy (rotational)
  Solenoids - converts electrical to mechanical energy (linear motion)
  Piezoelectric devices – Due to inverse piezoelectric effect - electrical to mechanical energy

## Slide 30: Actuator
Actuators may be used to control the position of a valve in a control system
  Your central heating at home may have motorised valves to control the flow of hot water to radiators or a hot water tank
Actuator
(Motor)
Valve

## Slide 31: Thank You
Notes: Health and Safety module – coming soon on Moodle