## Slide 1
Level : Foundation
Lecturer :Tim Tudor
Email : timothy.tudor@smu.ac.uk
Year : 2011
Engineering Science Electronics

## Slide 2: Topic 1 – DC Theory
Some Questions
Calculate the current flowing in the circuit below and the voltage drop over the middle resistor.
(3.056 A and 12.22 V)

## Slide 3: Topic 1 – DC Theory
Some Questions
Calculate the total resistance of the circuit shown.
Determine the current, total power dissipated and the voltage drop over each resistor.
(0.333 A, 16.7W , 33.3 V and 16.67 V)

## Slide 4: Topic 1 – DC Theory
Resistors in parallel
Consider 3 resistors in parallel as shown.
The voltage across each is the supply voltage V.
The current flowing in each is given by Ohms' Law
I1= V/R1 I2= V/R2 I3= V/R3

## Slide 5: Topic 1 – DC Theory
Resistors in parallel
The current is divided according to the resistance.
If the resistors were all the same, the same current would flow in each.
The total current drawn from the supply is
I = I1 + I2 + I3
I = V/R1 + V/R2 + V/R3
I = V(1/R1 + 1/R2 + 1/R3)

## Slide 6: Topic 1 – DC Theory
Resistors in parallel
If the same current was drawn from the supply by a single resistor RT the current would be
I = V/RT
Comparing the two equations
V/RT = I = V(1/R1 + 1/R2 + 1/R3)

## Slide 7: Topic 1 – DC Theory
Resistors in parallel
In general for resistors in parallel

## Slide 8: Topic 1 – DC Theory
Resistors in parallel
Calculate the total resistance and all the currents in the circuit below

## Slide 9: Topic 1 – DC Theory
Resistors in parallel
IT = 48 / 5.077 x 103 = 9.455 x 10-3 A
I1 = 48/10 x 103 = 4.800 x 10-3 A
I2 = 48/15 x 103 = 3.200 x 10-3 A
I3 = 48/33 x 103 = 1.455 x 10-3 A
Check total = 4.8 + 3.2 +1.455 = 9.455 mA

## Slide 10: Topic 1 – DC Theory
Some Questions
Calculate the total resistance for the circuit shown. Determine the total current drawn from the
supply.

## Slide 11: Topic 1 – DC Theory
Some Questions
Calculate the total resistance for the circuit shown. Determine the current in each resistor and
the total current drawn from the supply.
(1.66Ω, 40 A, 120 A)