## Slide 1
Module Name : Electronics 1
Module Code : ACDB5002
Topic : 7 – Segment Display
Lecture : 14
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk

## Slide 2: 7 – Segment Display in Counters
At the end of this session, the students will be able to
Acquire the skill to design microcontroller-based circuits for specific counter objectives.
Develop proficiency in writing Embedded C codes to implement an up/down counter function using switch to control a 7-segment display.
UWTSD Lectures / ACDB5002 – Electronics 1
Learning Objectives

## Slide 3: 7 – Segment Display in Counters
The seven-segment display is a widely used electronic display device that displays numbers/ characters using a combination of seven illuminated segments.
They are used in applications such as Digital Displays, Counters and Timers, Temperature Display.
UWTSD Lectures / ACDB5002 – Electronics 1
7- Segment Display

## Slide 4: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
7- Segment Display
Types
Common Anode: All the anodes of the seven LEDs are internally connected to a common pin and then connected to a positive voltage supply.
Common Cathode: All the Cathode of the seven LEDs are internally connected to a common pin and then connected to a positive voltage supply.

## Slide 5: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
7- Segment Display- Anode Connection
1
2
3
4
5
6
7
8
1
2
3
4
5
6
7
8
 | B7 | B6 | B5 | B4 | B3 | B2 | B1 | B0 | Hex
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0C
1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | F9
2 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | A4
3 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | B0
4 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 99
5 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 92
6 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 82
7 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | F8
8 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 80
9 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 90

## Slide 6: 7 – Segment Display in Counters
Demonstrate an up counter using 7- Segment Display by considering the following conditions.
When a push button connected to port pin RC1 is pressed once, the 7 segment should count up from 1 to 9 within a delay of 100ms.
The counter should stop counting when the button is released.
UWTSD Lectures / ACDB5002 – Electronics 1
Up Counter
Example

## Slide 7: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up Counter
Declaring 7- segment Patterns
int i: Declares an integer variable named ‘i’.
unsigned seg_display[] : Declares an unsigned array named seg_display and initializes it with 10 hexadecimal values.

## Slide 8: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up Counter
Initialization of Ports and Pins
Declaring the Output Port : TRISB
Declaring the Input Port : TRISC
Initialize PORTB and PORTC to be ‘0’

## Slide 9: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up Counter
Conditions in do- while Loop

## Slide 10: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up Counter
Conditions in do- while Loop
if(input(PIN_C1))
When the push button is pressed, the value of the bit at position C1 in the PORTC register is equal to 1.
    It makes to execute the code inside the curly braces.
‘for (i = 0; i < 10; i++)’
This loop iterates over the block of code inside it 10 times, incrementing the variable i from 0 to 9.

## Slide 11: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up Counter
Conditions in do- while Loop
output_b(0xFF);
This line will be executed until the value of i <10 and when it fails it sets the value of 7 segment display to be PORTB = 0Xff which makes the display OFF.

## Slide 12: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up Counter
Simulation for Up counter

## Slide 13: 7 – Segment Display in Counters
Demonstrate a down counter using 7- Segment Display by considering the following conditions.
When a push button connected to port pin RC0 is pressed once, the 7 segment should count down from 9 to 1 within a delay of 100ms.
The counter should stop counting when the button is released.
UWTSD Lectures / ACDB5002 – Electronics 1
Down Counter
Exercise : Hint - Replace the for loop in the previous code by ‘for(i=9;i>=1;i--)’

## Slide 14: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Down Counter
Simulation for Down counter

## Slide 15: 7 – Segment Display in Counters
Demonstrate an up-down counter using 7- Segment Display by considering the following conditions.
When a push button is connected to port pin RC0 is pressed once, the 7 segment should count up from 1 to 9 within a delay of 100ms.
When a push button is connected to port pin RC7 is pressed once, the 7 segment should count down from 9 to 1 within a delay of 100ms.
The counter should stop counting when the button is released.
The counter should stop counting when the button is released.
UWTSD Lectures / ACDB5002 – Electronics 1
Up-Down Counter
Exercise : Hint – use both up and down counter ‘for loops’

## Slide 16: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up-Down
Counter

## Slide 17: 7 – Segment Display in Counters
UWTSD Lectures / ACDB5002 – Electronics 1
Up-Down
Counter

## Slide 18
Thank You