## Slide 1
Electrical Engineering
(ACDA5001)
Lecture 17

## Slide 2: Content
Introduction
Electrical Machines
DC generator
Construction
Types

## Slide 3: Learning Outcome
The student upon completion of the lecture will be able to:
Describe the components of DC generators
Describe the types of DC generators

## Slide 4: Types of DC machines
DC machines are classified as follows.
DC generator (Converts mechanical energy into electrical energy)
DC Motor (Converts electrical energy into mechanical energy)
(These machines operates in DC current)

## Slide 5: Types of DC machines
DC machine operates in DC current.
They work on the principle of Faraday’s law of electromagnetic induction (Whenever a flux linking with a conductor or a coil changes, an emf is induced which will cause a current to flow through the circuit).
The basic requirement for the DC machines are magnetic field, conductor and relative motion between them.

## Slide 6: DC generator - working principle
Working principle
DC generator works on the principle of Faraday’s law of electromagnetic induction (i.e) Whenever a flux linking with a conductor or a coil changes, an emf is induced which will cause a current to flow through the circuit.
The direction of induced emf is given by Fleming’s right hand rule.

## Slide 7: DC generator - working principle
Working principle - Fleming’s right hand rule.
If thumb, forefinger and middle finger are outstretched, so that the three fingers are at right angle to each other. If the fore finger points the direction of the line of flux, thumb points the direction of relative motion of the conductor with respect to the flux, then the middle finger gives the direction of the induced emf in the conductor

## Slide 8: DC generator - Construction
Construction –Cross section of DC machine

## Slide 9: DC generator - Construction

## Slide 10: DC generator - Construction
DC generator and DC motor has the same general construction, any DC generator can be used as a DC motor and Vice versa.
The Major parts of DC machine are
  Yoke
  Field system
  Armature core
  Amature windings
  Commutators
  Brushes

## Slide 11: DC generator - Construction
Yoke
It is also called as magnetic frame, it serves for two purposes
  Protecting cover for DC machine and provide mechanical support
  It carries the magnetic poles.
Field system
  Function - To provide uniform magnetic field.
  Consists of number of poles bolted inside the circular frame.
  Field windings are mounted on the poles and carry the DC exciting current.
  Field coils are connected in such a way the adjacent poles have opposite polarity.
  The mmf (magnetomotive force) produced by the field windings provides a magnetic flux that passes through the pole pieces, the air gap, the armature and the frame.

## Slide 12: DC generator - Construction
Armature core
  The armature core is keyed to the machine shaft and rotate between the field poles.
  The armature core consists of slotted soft –iron laminated that are stacked to form a cylindrical core.
  The laminations are individually coated with a thin insulating fills so that they do not come in electrical contact with each other.
  The purpose of laminating the core is to reduce he eddy current loss.
  The laminations are slotted to accommodate and provide security to the armature winding and give shorter air gap for the flux.

## Slide 13: DC generator - Construction

## Slide 14: DC generator - Construction
Armature winding
  The slots of the armature core holds the insulated conductors that are called as armature windings.
  The emf is induced in armature windings
  The armature conductors are connected in series-parallel connection.
    The conductor being connected in series so as to increase the voltage.
    Conductors connected in parallel to increase the current.
  The armature winding of a DC machine is a closed- circuit winding.
  Armature winding (two types)
    Lap winding
    Wave winding

## Slide 15: DC generator - Construction
  Lap winding:
    Connection starts from conductor in first slot, the connections overlap each other as windings proceeds sill starting point is reached again.
    Number of Parallel paths = Number of poles

## Slide 16: DC generator - Construction
  Wave winding
    This type of windings travels as wave and avoid overlapping.
    Number of parallel paths =2

## Slide 17: DC generator - Construction
Commutator
  Commutator acts as a mechanical rectifier which converts the AC induced emf in the armature winding into DC across the brushes.
  It is made of copper segment insulated from each other by mica sheet.
  It is mounted on the shaft of the machine.
  The characteristics of the DC commutator is that it should not produce spark during the working condition. If not the sparks may burn the brushes and overheat and carbonise the commutator.

## Slide 18: DC generator - Construction
Brushes
  The purpose of the brushes is to collect the current from commutator to external load circuit.

## Slide 19: DC generator - working

## Slide 20: DC generator - Working
The field winding is supplied with power supply. So, the poles get magnetised and the magnetic flux across the pole increases.
The armature is provide with a mechanical force (rotational force), which cuts the magnetic flux lines.
The Emf will be induced in the conductor, as per the Faraday’s law of electromagnetic induction.
The direction of the induced Emf is given by the Flemming’s right hand rule.

## Slide 21: DC generator - Emf equation
The EMF equation of the DC generator is
  Where
    flux /Pole in weber
    Z –Total number of armature conductors
    P- Number of poles
    A –Number of Parallel paths
    N- Speed of the armature in r.p.m

## Slide 22: DC generator – Symbol

## Slide 23: Types of DC generator
DC Generator
Compound Generator
Shunt Generator
Series Generator
Cumulative Compound Generator
Differential Compound Generator
Long Shunt Compound Generator
Short shunt Compound Generator
Separately Excited DC generator
Self Excited DC generator

## Slide 24: DC generator - Types
i) Separately Excited DC generator
The field winding is supplied with an external DC source is called a separately excited generator.
- Armature Current
Load Current
Field Current

## Slide 25: DC generator - Types
The field winding of this type of generator has large number of turns of thin wire. So length of such winding is more with less cross sectional area. Hence, the resistance is high in order to limit the field winding.
The armature current,
The terminal voltage,
Developed Electric power =
Power delivered to load =

## Slide 26: DC generator - Types
ii) Self excited DC generator
It does not require any external supply to excite the winding. Based on the manner the field winding is connected to the armature, the self excited generators are classified into three types.
They are as follow.
  a) Shunt generator
  b) Series generator
  c) Compound generator

## Slide 27: DC generator - Types
a) Shunt generator
In shunt generator, the field winding is connected in parallel with the armature winding.
Shunt winding has many turns of fine wire, provide high resistance.
Only a portion of current will flow through winding and remaining flows through load

## Slide 28: DC generator - Types
Rsh = Shunt winding resistance
Ish = Current flowing through the shunt field
Ra = Armature resistance
Ia = Armature current
IL = Load current
V = Terminal voltage
Eg = Generated EMF

## Slide 29: DC generator - Types
The armature current,
The effective power across the load will be maximum when IL is maximum. So, it is required to keep shunt field current as small as possible.
Shunt field current is equal to,
Voltage across the load is equal to,
Power generated is equal to,
Power Delivered to the load is equal to,

## Slide 30: DC generator - Types
b) Series generator
In a series wound generator, the field winding is connected in series with the armature winding.
As fields and armature windings are in series, the whole current flows through fields as well as load.

## Slide 31: DC generator - Types
Rsc = Series winding resistance
Isc = Current flowing through the series field
Ra = Armature resistance
Ia = Armature current
IL = Load current
V = Terminal voltage
Eg = Generated EMF

## Slide 32: DC generator - Types
Armature current,
Voltage across the load is equal to,
Power generated is equal to,
Power delivered to the load is equal to,

## Slide 33: DC generator - Types
C) Compound generator
The compound generator has both the series and shunt winding. This type of generators are classified as
  Long shunt
  Short shunt
  Differential
  Cumulative

## Slide 34: DC generator - Types
i) Long shunt compound generator
The compound generator have more than one winding.
In long shunt the field winding is in parallel with both series fields and armature winding.
The armature current,
Shunt field current is equal to,

## Slide 35: DC generator - Types
ii) Short shunt compound generator
The shunt field winding is in parallel with the armature winding.

## Slide 36: DC generator - Types
iii) Differential compound generator
Shunt and series windings are wounded on the same pole.
Depending on the direction of winding, flux produced by shunt and series field may oppose each other.
If the two fluxes oppose each other, then it is called differential compound generator

## Slide 37: DC generator - Types
iv) Cumulative compound generator
Shunt and series windings are wounded on the same pole.
Depending on the direction of winding, flux produced by shunt and series field will not oppose each other.
If the two fluxes aid each other, then it is called cumulative compound generator

## Slide 38: DC Generator - Applications
Applications of DC generator
Shunt generator
  Battery charging
  Exciter for synchronous motor
Series generator
  Boosters in transmission line
  Traction applications
Compound generator
  Voltage regulator
  Compensator for control system applications
  Used in arc welding

## Slide 39: Thank You
Notes: Health and Safety module – coming soon on Moodle