## Slide 1: Advanced Instrumentation Systems M6X00942

## Slide 2: Module Outcomes
Upon the successful completion of this module, the student should be able to:
  Demonstrate a sound understanding of the principles and methods used in tracking and surveillance of airborne targets.
  Select and critically evaluate appropriate methods and technologies used in the acquisition of telemetry data in Test Range trials.

## Slide 3: Module Content
Tracking Radar and Surveillance Radar;
  Doppler tracking and mono pulse;
  Radar Cross Section - factors affecting RCS, Measurement and Calculation, RCS reduction
  Flight Termination Systems;
Telemetry;
Global Positioning System, Inertial Navigation Systems; GPS and Automatic Dependent Surveillance;
Spatial Coordinate Systems, Geodetics and Geocoding systems;

## Slide 4: Assessment
1 Assignment (50%)
  2500 Word equivalent
1 Exam (50%)
  2 Hour exam
  Around the last week in June

## Slide 5: Units
There are 7 SI Base units – All other units are derived from these
Symbol | Name | Quantity
m | metre | Length
kg | kilogram | Mass
s | second | Time
A | ampere | Electric current
K | kelvin | Temperature
mol | mole | Amount of substance
cd | candela | Luminous Intensity

## Slide 6: Decibels
Decibels (dB) are a logarithmic unit to express ratios.
Radio Frequency (RF) power is commonly expressed in dB using 1mW as a reference, or dBm.

## Slide 7: Decibels
So if a transmitter had an output power of 1W, the output power in dBm would be:

## Slide 8: RADAR
RAdio Detection And Ranging
Radio/microwaves are reflected and scattered in many directions by objects they hit
If a reflected wave is received it can tell us
  Range (derived from the time difference between transmitted and reflected wave)
  Direction (if the transmitter and receiver antennae are directional
  Speed (an approaching or retreating object introduces frequency shifting on the signal by the Doppler effect)

## Slide 9: Radar Types
Primary Surveillance Radar (PSR)
  Limited
    Range Finding
    Angle
    Velocity (Doppler)
Secondary Surveillance Radar (SSR)
  More advanced but requires transponder on aircraft

## Slide 10: Radar types
Identification of Friend or Foe (IFF)
  Extension of SSR
Multilateration – ADS-B
Semi-Active Radar Homing

## Slide 11: The RADAR Equation
The scattering cross-section σ of a target is the imaginary area which intercepts a power Sσ from the plane wave incident upon it and scatters the power isotropically such that the power flux incident on the receiver is that observed
T
R
O – the scattering object
r1
r2
Sσ
S (in W/m2)

## Slide 12: The Radar Equation
for the “bistatic” configuration
In a “monostatic” configuration (transmitter and receiver at the same place) = r, and

## Slide 13: Radar Equation
As , we can also state this as:
Notes
  Dependence on r-4
  σ is a function of angle of incidence, observation and polarisation

## Slide 14: OK, But What About Radar Systems?
Objects scatter and reflect radio waves
Some of that energy reaches the receiver
  How much depends on the object’s radar cross-section, σ
If the signal is greater than the noise background, we can detect it
  Same problem as with communications systems in DSP & Comms last semester
  Signal-to-noise ratio (SNR) is usually stated in dBs
  Noise figures are usually given as noise temperatures (again, see DSP & Comms)

## Slide 15: Radar Cross Section
Courtesy of Prof. David Jenn, Navy Postgraduate School, available from:
http://faculty.nps.edu/jenn/Seminars/RadarFundamentals.pdf,
accessed 11.00, 04/03/16

## Slide 16: Radar Detection Range
Change the equation around to solve for r:

## Slide 17: Radar Detection Range
And the maximum range will depend on the minimum received power for detection:
We need also to consider a variety of losses that occur in the real situation (the equations have assumed perfect wave conditions)

## Slide 18: Detection Range with Losses
Sources of losses (taken together as )
  Internal attenuation in the radar set,
  Fluctuation losses during reflection,
  Atmospheric losses during propagation,

## Slide 19: So?
Calculate for a monostatic L-band radar with:
SNR for detection = 10dB
Noise Power = -120 dBW

## Slide 20: Detection Range Calculation
Noise power = -120dB; SNR = 10dB
Threshold signal level = -110dB
Frequency = L-band
Wavelength = 3x108/2x109 = 0.15m
10dB gain = signal x 10

## Slide 21: Detection Range Calculation
= 5010m

## Slide 22: Range Calculation
Change the power up to 2 MW. What is the new detection range?
Reduce the noise power to -140dBW. What is the new detection range?
Change the radar cross section to 200m2. What is the new detection range?
Change the frequency down to 1GHz. What is the new detection range?

## Slide 23: Answers
7085m
15842m
10594m
7085m

## Slide 24: The Answers Tell Us?
Up the power, get a increase in range
  Q1 multiplied the power by 4
Up the radar cross section, get a increase
  Q2 reduced the noise figure, and hence the detection power, by 100 (-20dB)
Reduce the system noise, get a increase
  Q3 increased the cross section by 20
Increase the wavelength, get a increase
  Q4 increased the wavelength by 2

## Slide 25: Noise Power?
Watts for an ideal receiver
  k = Boltzmann’s constant
  = system temperature (usually 209K)
  = receiver noise bandwidth
This is only thermal noise!
Receivers aren’t usually ideal, so we add a noise factor, NF, to the equation:
Watts

## Slide 26: Try One
The new Qinetiq stealth drone has a maximum radar equivalent reflecting area of 1m2. What is the equivalent reflection gain if illuminated with an X-band (10GHz) radar? With an L-band (1GHz) radar?

## Slide 27: Answer
λ=3x108/10x109 = 0.03m
L-band λ=3x108/1x109 = 0.3m

## Slide 28: Using Radar

## Slide 29: What Can We Measure?
Distance (via return signal delay estimation)
Speed (via the Doppler frequency shift in the returned signal)
Direction (because our antennae are generally directional, or by using multiple receivers)

## Slide 30: Signature Analysis and Inverse Scattering
Target size (from magnitude of return)
Target shape and components (return as a function of direction)
Moving parts (modulation of the return)
Material composition
More functions, more complex radar
  Cost and size increases

## Slide 31: Time Delay Range Estimation
Bistatic: round trip time =
Monostatic:
  Where c = 3x108
T
R
rT
rR
Object (target)

## Slide 32: Only One (Small?) Problem
Multipath reflections or multiple targets?
Scenario
  Multiple pulses transmitted
  Which one generated the return?
TR1
TR2
Pulse 1
Pulse 2

## Slide 33: Unambiguous Range?
Only if
    = time between pulses
    R = range to target
Maximum unambiguous range

## Slide 34: Range Gates
Use our knowledge of pulse propagation to create a set of sub-sets of time (gates)
Each gate is opened and closed
The time each gate is open is a range increment
Gates must include the ranges of interest, or cover interval between pulses
For tracking a target, we acquire it in one particular gate period
We can then follow it
We know which gate period it is going into next so can continue to track
Dwell time = N/fp

## Slide 35: Range Gates and Bins
The returned signal “gates” are imaginary, a way to describe dividing time into slots according to range
This is all handled by the signal processing at the receiver
  As DSP&Comms – timing of gate open, delay intervals based on time of transmission

## Slide 36: Multipath Returns
Airborne radar
Target
Grazing angle, ψ
Ground
Aircraft
HA
HT

## Slide 37: Doppler Frequency Shift
Velocity has radial and tangential components, vr and vt
Vr is in the direction of our radar detector
v
vt
vr
Radar Set

## Slide 38: Doppler Issues
Our transmitted signal isn’t spectrally “pure”
  Can we tell side bands from Doppler return?
  Only if sufficiently high pulse repetition frequency
  But high fP = small TP , which give us problems with range ambiguity (see earlier)

## Slide 39: Radar Cross Section
Radar cross section is the measure of a target's ability to reflect radar signals in the direction of the radar receiver, i.e. It is a measure of the ratio of backscatter power per steradian (unit solid angle) in the direction of the radar (from the target) to the power density that is intercepted by the target.

## Slide 40: Radar Cross Section
The RCS of a target can be viewed as a comparison of the strength of the reflected signal from a target to the reflected signal from a perfectly smooth sphere of cross sectional area of 1 m2

## Slide 41: Radar Cross Section
The conceptual definition of RCS includes the fact that not all of the radiated energy falls on the target.
A target’s RCS (F) is most easily visualized as the product of three factors:
F = Projected cross section x Reflectivity x Directivity .

## Slide 42: Radar Cross Section
Reflectivity: The percent of intercepted power reradiated (scattered) by the target.
Directivity: The ratio of the power scattered back in the radar's direction to the power that would have been backscattered had the scattering been uniform in all directions (i.e. isotropically).

## Slide 43: Radar Cross Section

## Slide 44: Radar Cross Section
RCS is dependant on shape of reflector

## Slide 45: Radar Cross Section
RCS patterns are shown as objects are rotated about their vertical axes (the arrows indicate the direction of the radar reflections).
The sphere is essentially the same in all directions.
The flat plate has almost no RCS except when aligned directly toward the radar.
The corner reflector has an RCS almost as high as the flat plate but over a wider angle, i.e., over ±60E.
The return from a corner reflector is analogous to that of a flat plate always being perpendicular to your collocated transmitter and receiver.

## Slide 46: Radar Cross Section

## Slide 47: Radar Cross Section
Targets such as ships and aircraft often have many effective corners.
Corners are sometimes used as calibration targets or as decoys, i.e. corner reflectors.
An aircraft target is very complex. It has a great many reflecting elements and shapes.
The RCS of real aircraft must be measured.
It varies significantly depending upon the direction of the illuminating radar

## Slide 48: Radar Cross Section
Typical RCS of a jet aircraft

## Slide 49: Radar Cross Section
Courtesy of Prof. David Jenn, Navy Postgraduate School, available from:
http://faculty.nps.edu/jenn/Seminars/RadarFundamentals.pdf,
accessed 11.00, 04/03/16

## Slide 50: Huygens Principle
The wavefront of a propagating wave of light at any instant conforms to the envelope of spherical wavelets emanating from every point on the wavefront at the prior instant (with the understanding that the wavelets have the same speed as the overall wave).
http://www.mathpages.com/home/kmath242/kmath242.htm

## Slide 51: Huygens Principle
Allows a decent explanation of diffraction and reflection
Lots of debate about the scientific value of Huygens’ work
It gives the right answers to some early problems

## Slide 52: Shape of the Plane Wave in the Far Field Case
Far field? Where
Consider a plane wave. All points on the wavefront propagate at the same speed.
Take three imaginary “rays”
As the waves propagate in the x-direction, over time the front curves as shown
r
r
r

## Slide 53: Far Field (Fraunhofer Region)
The far field starts at , where D is the geometric dimension
Can also understand this as where r>>λ
In this region, the shape of the wave is independent of the antenna
How “plane” are our plane waves?
  Think about a very large sphere
  For any given point on the large sphere, locally the area seems to be flat
  So treat it as flat when it hits a far-away object

## Slide 54: Let’s Look at Phased Arrays
The phase difference between successive elements is how far additionally the wavefront has to travel to hit the next array element = δr
d
d
d
θ
θ
δr
Wavefront
This is the equation for time delay beam steering: array separation is d,
pick your direction, θ, and calculate the time delay between elements δt

## Slide 55: Phased Arrays – Phase Steering
A full cycle of wavelength λ = 2π radians of phase
δφ/2π = δr/λ
δφ = 2πδr/λ
= 2πdsinθ/λ
There’s no reason why δφ should not exceed 2π
  If so, simply subtract 2π to get the phase angle

## Slide 56: Phased Array Antennae
Huygens basically gives us the good news
Excite the elements in a transmitter array with the phase differences to steer the beam
  Steerable with no moving parts!
Array elements are set a distance apart
Choose θ, the angle we want away from broadside
Calculate δφ for each of N array elements and set phase shifters accordingly. For element n:

## Slide 57: Corporate-fed Phased Array

## Slide 58: Grating Lobes
Grating lobes occur when a phased array is steered too far
  Main beam reappears on the wrong side
Array elements must be spaced properly in order to avoid grating lobes
  Maximum spacing is a function of wavelength of operation λ and maximum look angle θ

## Slide 59: Questions
What are the maximum separations of array elements for an x-band (λ = 3cm) radar with a maximum steer angle of (a) 60 degrees; (b) 30 degrees?

## Slide 60: Phased Array Gain
Gain at broadside in a phased array is a function of the individual element gain and the number of elements
= aperture area
= aperture efficiency
λ = wavelength

## Slide 61: A Radar Block Diagram
Courtesy of Prof. David Jenn, Navy Postgraduate School, available from:
http://faculty.nps.edu/jenn/Seminars/RadarFundamentals.pdf,
accessed 11.00, 04/03/16

## Slide 62: Radios

## Slide 63: Microwave generation
Magnetron
http://www.radartutorial.eu/08.transmitters/Magnetron.en.html

## Slide 64: Automatic Dependent Surveillance

## Slide 65: Multilateration

## Slide 66: Factors effecting Radar reception
RCS
Ghosting

## Slide 67: RADAR Cross Section

## Slide 68: Telemetry

## Slide 69: Flight Termination Systems

## Slide 70: Problem
We need to measure the distance from point A to point B along an the shortest path. How can we do this?
Where is point A?
How can we describe where points A and B are?
We need some kind of frame of reference

## Slide 71
Assuming we have a frame of reference, can’t we just use Pythagoras?
Yes we can, so long as…
A
B

## Slide 72: Geodetics and Geocoding systems
Geodetics is the science of measuring and representing the Earth

## Slide 73: Coordinate Systems

## Slide 74: Global Positioning System

## Slide 75: Inertial Navigation Systems