## Slide 1: Dimensioning Floor Jig and Shadow Boards
David de Vall
Safran Seats GB

## Slide 2: Gantt Chart

## Slide 3: Feasibility Studies

## Slide 4: Final solutions

## Slide 5: PDS
Performance
The product must contain instructions, tools and materials required by the unit fitting process.
The product must not contain excess parts.
The product must contain materials for separate operations in separate locations.
The product must clearly label or otherwise demonstrate what instruction, tool or material is contained in each location.
The product should make the retrieval or return of all instructions, tools and materials as simple and time-efficient as possible.
The product should house instructions, tool and materials in such a way that it is immediately recognisable if any retrieved items have not been returned.
Economy
The product must be producible for as little cost as possible.
Target Production Cost
The product must have a production cost of no more than £100, comparable to the combined cost of similar products available that could be used to construct and equivalent.
Quantity
Only one product needs to be produced.
The product must house parts sufficient to supply two floor jigs.
Product Life Span
The product must be operational for at least ten years.
The product should have an indefinite potential operational life span, as 767 and 787 units will continue to be produced until such a time as there is no demand for seats to fit or retrofit Boeing aircraft.
Environment
The product must be suitable to operate within the environment of the QA workshop.
The product must be resistant to physical impact due to movement of other tools and materials during fitting, dimensioning and unfitting operations.
The product must be located in such a way as to not interfere with fitting, dimensioning or unfitting operations, and must not restrict access through the workshop.
The product should be located near one or both floor jigs that it provides materials for.
Size
The product must be large enough to contain the maximum number of required parts per floor jig, plus one or more copies of the instructions for each fitting and unfitting operation.
The product should be no larger than strictly necessary, to minimise the time a user spends searching for tool, materials or instructions relevant to the operation he is to perform, and also to minimise the amount of material required for its construction.
If wall mounted, the product must have as small a profile from the wall as possible, in order to minimise the risk of accidental collision.
If free standing, the product must be of sufficient height so as to fulfil the criteria described in the Ergonomics specifications.
Weight
The weight of the product must not exceed the maximum safe lifting weight for any user (25kg for an adult male, 16kg for an adult female).
The target maximum weight of the product will be 10kg.
The product will be built to have as low a weight as possible.
Maintenance
The product must be designed such that all elements of it can be easily accessed to allow them to be repaired or replaced if damaged.
All bespoke parts of the product such as shadowboard cutouts must be simply produced from as inexpensive materials as possible, to allow for replacement parts to be easily and affordably constructed.
Material
The product must be constructed from sufficiently robust materials as to withstand accidental impact from testing equipment or finished units.
The product must be constructed from non-hazardous materials so as not to present a health risk to operatives within the environment.
The product must be constructed from cost-effective materials to keep the project expenditure to a minimum.
Ergonomics
The product must stand at a comfortable height for a standing human to operate.
Industry Standards
The product must comply with BS EN 527-1:2011, which details appropriate height and dimensions for office furniture.
Testing
The product must be tested to ensure that it fulfils its purpose and performs well, notably to ensure that parts and tools are easily located and swiftly retrieved in the exact quantity required.
The product must be tested to ensure that it does not break during regular use, and is resistant to damage in the event of an accident.
Safety
The product must be designed for safe operation; no sharp edges must be present on the final product and no materials should be used in its construction that will present a hazard to the end user.
The product should be designed such that its manufacture uses no materials hazardous to the manufacturer. Any hazardous materials that are necessary should present as little hazard as possible and should be controlled so as to minimise the risk of injury or ill health.
Safe operating instructions must be mentioned clearly in all relevant literature.
All relevant legal requirements will be observed, such as the Health and Safety at Work Act and the Provision and Use of Work Equipment Regulations.

## Slide 6: Procedures

## Slide 7: Procedures

## Slide 8: Research

## Slide 9: Research

## Slide 10: Research

## Slide 11: PERT Charts and Plan of Action

## Slide 12: FMEA - Kanban

## Slide 13: FMEA – Floor Jigs

## Slide 14: Work Breakdown Structure – Floor Jigs

## Slide 15: Work Breakdown Structure – Shadow Boards

## Slide 16: Time and Costings

## Slide 17: Implementation – Floor Jig (15/02/2019)

## Slide 18: Implementation – Floor Jig (16/03/2019)

## Slide 19: Implementation – Shadow Boards

## Slide 20: Problems encountered and testing

## Slide 21: What I learned
How to assess a project’s suitability (Feasibility Studies, FMEAs)
How to manage personnel throughout a project (Work Breakdown Structure, Responsibility Tracker)
Time management for self and others (Plan of Action, Times)
Improvement in sourcing resources (Costings)

## Slide 22: Thank you for your time
Please ask any questions you may have!