## Slide 1: Sensor Networks for Environmental Monitoring
Professor Ian Wells,
BSc, MSc, PhD, CEng, FIET, SMIEEE, FBCS
Professor of Digital Signal Processing
and
Head of the School of Applied Computing
University of Wales Trinity Saint David, Swansea

## Slide 2: Objectives
Sensor Network Overview
Environmental Uses
ASTEC:
  Coastal Erosion
  Purpose of the Sensor Network
  Data Collection and Transmission
  Details of the System
  Sea Trials
Floating Sensor Networks

## Slide 3: Wireless Sensor Networks (WSNs)

## Slide 4: Wireless Sensor Networks
Some types of WSNs can be considered to be a special case of Mobile Ad-Hoc Networks (MANETs)
A MANET is an autonomous system of mobile hosts, which also serves as both a router and intermediate node connected by wireless links.

## Slide 5: Applications
Mobile Vehicular Networks
Ref: http://www.diva-portal.org/smash/get/diva2:830723/FULLTEXT01.pdf

## Slide 6: Applications
UAV Networks
Military Battlefield Networks
Ref: http://rain.aa.washington.edu/Research_Areas/Flight_Systems

## Slide 7: Applications
Disaster relief
“Self-Powered Cyborg Cockroaches Could Locate Disaster Victims”
Ref: http://inhabitat.com/self-powered-cyborg-cockroaches-could-be-sustainable-solution-to-locating-disaster-victims/

## Slide 8: Applications
Vital Sign Medical Monitoring: patient identifier, position, electrocardiogram etc.
Ref: http://ti-bg.com/?page_id=275

## Slide 9: Applications
Monitoring of farm animals: vital signs and movements
Ref: http://www.computer.org/csdl/mags/pc/2007/02/b2050-abs.html

## Slide 10: Applications
Internet of Things (IoT)
Morgan Stanley: 75 Billion Devices Will Be Connected To The Internet Of Things By 2020 Ref: http://www.businessinsider.com/75-billion-devices-will-be-connected-to-the-internet-by-2020-2013-10?IR=T

## Slide 11: Environmental Applications
Floating sensors measuring temperature, salinity, pollution levels etc. (e.g. Britton and Sacks, 2004)
Wildlife observations e.g. Storm Petrel observations on Great Duck Island (Mainwaring et al, 2002)
Glacier movement measurements (http://www.ecs.soton.ac.uk/research/projects/565)
Environmental parameter measurements

## Slide 12: Case Study 1: ASTEC
The ASTEC project was a £611 thousand research project sponsored by the Technology Strategy Board (TSB).
It began in August 2008 and concluded in March 2010.
The project deployed a novel marine wireless sensor network on the sea bed:
  to enable the gathering of data
  to quantify the effects of coastal erosion beneath the sea surface.

## Slide 13: Project Partners
Wireless Fibre Systems Ltd (WFS)
School of Applied Computing and School of Built and Natural Environment UWTSD
Valeport Ltd.

## Slide 14: Coastal Erosion
Coastal erosion is becoming a more common and destructive process and can have significant and costly effects on human populations.
(photographs courtesy of Prof. Mike Phillips, UWTSD)

## Slide 15: Coastal Erosion
Up to now, data has largely been obtained by measurements of exposed coastal areas such as beaches.
While these studies have revealed lots of important information, the details of what was happening below the sea’s surface has not been remotely measurable.
This means that we have only a partial picture of coastal erosion because of the absence of this important data.

## Slide 16: The Beach Profile
Engineers have classically modeled the submerged beach profile by describing two different zones:
  near shore zone
  offshore zone
Near Shore
Zone
Offshore
Zone
Closure
Contour
Visible
Beach

## Slide 17: Depth of Closure
The near shore zone is active while the offshore zone is inactive with respect to the movement of sediment, silt, sand etc.
The dividing contour between these zones is known as the depth of closure.
This contour and its movement is important to measure since it would give very useful data regarding the dynamics of sedimentary movement on the sea bed and enable more accurate measurements of coastal erosion.
Near Shore
Zone
Offshore
Zone
Closure
Contour
Visible
Beach

## Slide 18: Existing Technologies
Acoustic
Optical
Electromagnetic

## Slide 19: Acoustic Technology
Acoustics is a proven technology for underwater sensor applications:
  transmission range of up to 20km [1]
  yields poor performance in shallow water where the acoustic transmission can be affected by
    Turbidity
    ambient noise
    salinity gradients
    pressure gradients
  can have an adverse impact on marine life [2].
  cannot perform smooth transition through the air-and-water interface.

## Slide 20: Optical Technology
Another option that may be used for underwater transmission is optical:
  only delivers good performance in very clear water
  requires tight alignment due to the demand for line of sight and the limitation of very short transmission ranges [3].
  cannot perform smooth transition through the air-and-water interface.

## Slide 21: Problems of Shallow Sea Water
In a shallow water coastal environment where there is a high level of sediment and aeration in the water column, radio technology can provide many advantages over acoustic and optical waves.
Electromagnetic waves can cross water-to-air boundaries easily, these multiple transmission paths can extend the transmission range.
Image: http://www.123rf.com/photo_36078497_sea-water-turbulent-foam-splash.html

## Slide 22: Advantages of EM
Path 1. Completely through the salt water
Path 2. Through the sea bed
Path 3. Through salt water- through the air-and again through salt water

## Slide 23: Advantages of EM
EM is tolerant to turbulences that are caused by waves or human activities. This is not the case with acoustic and optical waves.
EM waves can work in dirty water conditions, while optical waves are susceptible to particulates and marine fouling. Image: https://www.quora.com/What-do-electromagnetic-waves-look-like

## Slide 24: Disadvantages of EM Radiation in Salt Water
Radio signals have a limited transmission range through salt water due to its high conductivity leading to severe attenuation, although long-wave radio can be used for short distances.
Critical trade-off between the transmission range and the offered data rate.
100bps was used allowing a 40m transmission radius (calculated through sea trials) set to be the distance between any two adjacent nodes
Image: http://bestsurfwax.com/category/uncategorized/

## Slide 25: Disadvantages of EM Radiation in Salt Water
The following equations describing the behaviour of EM radiation were developed

## Slide 26: Publications
Xianhui Che, Ian Wells, Gordon Dickers, Paul Kear, “TDMA Frame Design for a Prototype Underwater RF Communication Network”, Ad Hoc Networks, Elsevier, Volume 10, Issue 3, May 2012, pp 317-327 . (DOI: 10.1016/j.adhoc.2011.07.002)
Che, X.; Wells, I.; Dickers, G.; Kear, P.; Gong, X.; , "Re-evaluation of RF electromagnetic communication in underwater sensor networks," Communications Magazine, IEEE , vol.48, no.12, pp.143-151, December 2010 doi: 10.1109/MCOM.2010.5673085
Wells, I.; Davies, A.; Xianhui Che; Kear, P.; Dickers, G.; Xiaochun Gong; Rhodes, M.; , "Node pattern simulation of an undersea sensor network using RF electromagnetic communications," Ultra Modern Telecommunications & Workshops, 2009. ICUMT '09. International Conference on , vol., no., pp.1-4, 12-14 Oct. 2009 doi: 10.1109/ICUMT.2009.5345555
Xianhui Che; Wells, I.; Kear, P.; Dickers, G.; Xiaochun Gong; Rhodes, M.; , "A Static Multi-hop Underwater Wireless Sensor Network Using RF Electromagnetic Communications," Distributed Computing Systems Workshops, 2009. ICDCS Workshops '09. 29th IEEE International Conference on , vol., no., pp.460-463, 22-26 June 2009 doi: 10.1109/ICDCSW.2009.36
Xianhui Che; Wells, I.; Dickers, G.; Kear, P.; Xiaochun Gong; Rhodes, M.; , "Failure Tolerance Analysis of a Small Scale Underwater Sensor Network with RF Electromagnetic Communications," Sensor Technologies and Applications, 2009. SENSORCOMM '09. Third International Conference on , vol., no., pp.671-675, 18-23 June 2009 doi: 10.1109/SENSORCOMM.2009.108

## Slide 27: Purpose of the Sensor Network
The fundamental purpose to find the depth of closure and the movement of seabed sediment around this contour.
Only necessary to monitor sea bed movement below the low tide line
Sensors were positioned either side of the closure contour
4
6
1
5
7
2
Near Shore
Zone
Offshore
Zone
Visible
Beach
Closure
Contour
Sensors
3
Sink

## Slide 28: Overview of the Sensor Network
Flexible and reconfigurable sensor network system that could be placed on the sea bed in various patterns
Nodes were either a sensor node or a main data collection/sink node.
4
6
1
5
7
2
Near Shore
Zone
Offshore
Zone
Visible
Beach
Closure
Contour
Sensors
3
Sink

## Slide 29: Overview of the Sensor Network
Sensor nodes were fixed and capable of determining the amount of sediment settling on top of them using a differential pressure sensor.
System could be deployed for many months to build up a detailed profile of the movement of sediment at many positions on the sea bed.
4
6
1
5
7
2
Near Shore
Zone
Offshore
Zone
Visible
Beach
Closure
Contour
Sensors
3
Sink

## Slide 30: Data Collection
Sensor data was typically gathered at 2 hour intervals and stored locally.
Typically once per day all the nodes could transfer their collected data across the sensor network to the sink node.
The sink node, positioned on a buoy, then transferred data using the mobile phone (GSM) system.
This enabled the remote collection and processing of the data

## Slide 31: Data Transmission
The sensor network was a multi-hop wireless network with a fixed topology.
The architecture was based on multiple-source single destination traffic patterns.
The data communication process was carried out separately from the data-sensing procedure.
Image: http://www.speedguide.net/news/scientists-send-data-at-the-speed-of-32-gbps-using-5647

## Slide 32: Data Transmission
In each cycle, all the nodes are kept in a sleeping mode until a scheduled synchronization signal is transmitted.
Data is delivered in cycles.
Then, all the nodes will wake up and be ready for data communication.
Once data transmission is complete, the nodes will return to their sleeping mode.
Sleep
State
Communicate
State
Synchronise

## Slide 33: Time Division Multiple Access
At the top level the system used a flexible Time Division Multiple Access (TDMA) method of allocating timeslots to each node in the network as a data collision avoidance mechanism.

## Slide 34: Flexible TDMA
The flexibility comes from the ability of the system to redefine the size of the timeslots as desired; this capability enables the prototype system to experiment with different settings to obtain optimum settings.

## Slide 35: Data Frame Format
The sensor data is transported around the network by means of a Data Frame

## Slide 36: Other Frames
The other frame types are:
  Command Frame
  Acknowledgement Frame (ACK)
  Time Synchronisation Frame

## Slide 37: The Command Frame
The Command Frame was used to initialise most of the functionality of the sensor network and this is the mechanism used to keep the network as flexible as possible.
  It is able to initialise the following features:
  Data Gathering Period (DGP Field)
  Data Transmission Period (DTP Field)
  Number of data transmission retries (Ret Field)

## Slide 38: The Command Frame
  ‘RetD field’ (number of retries that a DATA frame will attempt when the frame fails to reach the destination
  ‘RET Flag’ (number of retries that a frame has so far taken to cross a link)
  ‘Fr Type’ defines if the frame is of type DATA, COMMAND, ACK etc

## Slide 39: Clock Sync Frame
The clock synchronisation algorithm needs to use a special ‘Time Sync’ Frame.
In order for the TDMA structure to accommodate multiple timestamp transmissions it is important that the Time synchronisation frame is as small as possible.

## Slide 40: Details of the System
The system consisted of several components shown in the diagram
  Aerial
  Sensor Housing
  Battery Pack Canister
  Circuit Board Canister

## Slide 41: The Sensor Housing
The sensor assembly comprised a differential pressure transducer within an oil filled capsule.

## Slide 42: The Sensor Housing
The differential transducer consisted of two separate sensing elements, and a small PCB which samples these elements and outputs data in RS485 format.
The format could be configured to give the individual readings from each element, the difference between the two readings (the differential value) or all three values.

## Slide 43: Aerial

## Slide 44: Prototype Development at UWTSD

## Slide 45: System Components

## Slide 46: Testing The Sensor Assembly

## Slide 47: Sea Trials
In March 2010 the system was deployed on Tenby South Beach.
Boats were hired to deploy the sensors

## Slide 48: Results
The figure shows the measured tidal changes from one of the undersea node tests.
This indicates water pressure measurements are being captured.

## Slide 49: Case Study 2: Floating Sensor Network
Aim: A sensor network that is able to monitor various environmental parameters in moving water, that may be moving rapidly

## Slide 50: Example
UC Berkeley’s Floating Sensor Network
  Ref: https://blog.adafruit.com/2012/05/17/uc-berkeleys-floating-sensor-network/

## Slide 51: Work to date - ANTMANET
By modelling the behaviour of ants optimization and innovations in routing protocols can be achieved,
Improved routing performance, compared to standard protocols DYMO and LAR in rapidly moving networks

## Slide 52: Questions