## Slide 1: Storage and Warehousing Techniques
Warehouse Management, 3rd edition by Gwynne Richards
Published November 2017 (Kogan Page)

## Slide 2: Warehouse Location
Section 2

## Slide 3
Exercise
30%
volume
70% volume
20 40 60 80 100 80 60 40 20
(Kilometres)
Customer area A
Customer Area B
Where would you site a distribution centre to economically supply both customer areas?
200 kms
Richards (2005)
Warehouse location

## Slide 4
Richards (2005)
Warehouse location
Richards (2005)
Exercise
30%
volume
Cost of transport = $5 per kilometre
70 loads per day into Customer area A
30 loads per day into Customer area B
200 Days per annum
20 40 60 80 100 80 60 40 20
(Kilometres)
Customer area A
Customer area B
70% volume
Where would you site a distribution centre to economically supply both customer areas?
What if it costs an additional $350,000 to operate a warehouse within 10 kms of
customer area A? Minimum distance away is 1 km.

## Slide 5
Calculations
Loads | Days | Kms | $ per km | Sub-Total | Additional cost (If applicable) | Total
70 | 200 |  | $5 |  |  | 
30 | 200 |  | $5 |  |  | 
TOTAL |  |  |  |  |  | 
70 | 200 |  | $5 |  |  | 
30 | 200 |  | $5 |  |  | 
TOTAL |  |  |  |  |  | 
70 | 200 |  | $5 |  |  | 
30 | 200 |  | $5 |  |  | 
TOTAL |  |  |  |  |  | 
70 | 200 |  | $5 |  |  | 
30 | 200 |  | $5 |  |  | 
TOTAL |  |  |  |  |  | 
70 | 200 |  | $5 |  |  | 
30 | 200 |  | $5 |  |  | 
TOTAL |  |  |  |  |  | 

## Slide 6
Answers
Richards (2005)
Loads | Days | Kms | $ per km | Total | SubTotal | Additional cost | Total
70 | 200 | 1 | $5 | $70,000 |  |  | 
30 | 200 | 199 | $5 | $5,970,000 |  |  | 
 |  |  |  |  | $6,040,000 | $350,000 | $6,390,000
70 | 200 | 10 | $5 | $700000 |  |  | 
30 | 200 | 190 | $5 | $5700000 |  |  | 
 |  |  |  |  | $6,400,000 | $350,000 | $6,750,000
70 | 200 | 11 | $5 | $770,000 |  |  | 
30 | 200 | 189 | $5 | $5,670,000 |  |  | 
 |  |  |  |  | $6,440,000 |  | $6,440,000
70 | 200 | 60 | $5 | $4,200,000 |  |  | 
30 | 200 | 140 | $5 | $4,200.000 |  |  | 
 |  |  |  |  | $8,400,000 |  | $8,400,000
70 | 200 | 100 | $5 | $7,000,000 |  |  | 
30 | 200 | 100 | $5 | $3,000,000 |  |  | 
 |  |  |  |  | $10,000,000 |  | $10,000,000

## Slide 7: Exercise (continued)
What other factors do you need to take into account when making this decision?
Notes: Where demand is equally balanced it doesn’t matter where along the route the warehouse is sited. Grants, rent, rates, labour cost and quality should dominate the decision. Other things to take into account are – where do the raw materials come from? Body Shop example!!!

## Slide 8: Factors affecting warehouse location
Of importance to Local Government Planners
Utilisation of brown field sites
Build in areas of high unemployment
Appropriate mix of industry
Companies
Access to transport networks e.g. parcel and pallet hubs
Availability of trained labour
Transport links for staff
Availability of funding, grants etc
Use of suitable existing buildings
Availability of utilities including telecoms
Availability of finance and resources
Goods traffic flows
Proximity to ports and airports
Where are our suppliers and manufacturing points?
No weather issues such as flooding

## Slide 9: Warehouse location criteria
Best location selection criteria for warehouse location
Cost
Land cost
Labour costs
Transportation cost
Tax incentives
Tax structures
Financial incentives
Handling costs
Labour characteristics
Labour availability
Skilled labour
Transport links for staff
Infrastructure
Markets
Macro environment
Government policies
Industry regulations
Enterprise Zones and construction plans
Existence of modes of transport
Telecommunication systems
Energy and water utilities
Quality and reliability of modes of transport
Proximity to ports and airports
Existing sites
Proximity to customers
Proximity to supplier/producer
Lead times and responsiveness
Environment
Geography
Weather
Location 1Location
Adapted from T. Demirel et al./Expert Systems with Applications 37 (2010) 3943–3952
Location 1
Location 2
Location 3
Location 4

## Slide 10: Port centric Logistics
“The provision of distribution and other value adding logistics services at a port.”
Advantages:
Faster unloading (emptying) of containers as long journeys from
ports to DCs eliminated.
Subsequent empty running between the DC and the port
eliminated.
Lower demurrage fees
No need to worry about landside weight restrictions on
imported containers allowing them to be filled to capacity.
Faster repositioning of ‘empties’.
Reduced carbon footprint.
Example: Asda Walmart at Teesport

## Slide 11: Location determination
Centre of Gravity
Volume Centre of Gravity
  Locates warehouse at the centre of supply & demand by minimizing distances to customers
Cost Centre of Gravity
  Locates warehouses at the centre of supply or demand by minimizing transportation costs

## Slide 12: Global land and rent costs
USD/sq m/year |  |  | 
Top 10 | Rent | Outgoings | Total costs
London (Heathrow) | 214.34 | 98.86 | 313.19
Hong Kong | 222.96 | 48.31 | 271.27
Zurich | 196.63 | 21.85 | 218.48
Singapore | 174.19 | 40.51 | 214.70
Oslo | 208.45 | 2.70 | 211.15
Moscow | 157.00 | 48.00 | 205.00
St. Petersburg | 144.00 | 41.00 | 185.00
South East England | 122.48 | 57.74 | 180.22
São Paulo | 152.13 | 26.04 | 178.17
Taipei | 149.04 | 15.00 | 164.04
Bottom 15 |  |  | 
Philadelphia | 42.73 | 32.34 | 75.07
Chicago | 44.35 | 30.01 | 74.36
Shanghai | 67.35 | 5.27 | 72.62
Budapest | 51.45 | 20.58 | 72.03
Denver | 38.10 | 33.25 | 71.35
Lyon | 56.73 | 13.46 | 70.19
Houston | 41.98 | 27.42 | 69.40
Brussels | 60.69 | 7.59 | 68.27
Antwerp | 59.37 | 8.13 | 67.50
Dallas | 40.36 | 26.45 | 66.81
Marseille | 54.09 | 12.14 | 66.23
Chengdu | 59.60 | 2.98 | 62.58
Atlanta | 42.19 | 17.00 | 59.19
Shenyang | 54.69 | 3.66 | 58.35
Wuhan | 42.44 | 4.39 | 46.83

## Slide 13: How many warehouses?
MANY WAREHOUSES
Inbound transport is expensive (to supply warehouses)
Outbound transport is cheaper (to deliver to customers)
Closer to customers so quicker to react
Cost of maintaining many warehouses is expensive
Cost of keeping many buffer stocks is expensive
Notes: Close to the customer – react quicker,

## Slide 14: How many warehouses?
FEWER WAREHOUSES
Inbound transport is cheaper
Outbound transport is more expensive
Less responsive to urgent orders
Less cost to maintain & equip warehouses
Less cost of buffer stock

## Slide 15
Number of DCs / depots
Cost
Local delivery cost
Systems cost
Storage cost
Inventory holding cost
Primary transport cost
Total logistics cost
Rushton, Croucher and Baker (2010)
Major Cost Relationships

## Slide 16: Cost versus Service
Evans & Castek in Gattorna (1998)
Cost to Serve
Service quality
Customer Satisfaction
Business Profit
Perfect service = High cost
Low cost = Lower service

## Slide 17: Maister’s Rule
Reducing the number of warehouses from y to x, reduces the total amount of safety stock in the system by:
1 - [ √x ]
[ √y ]
Multiply the result by 100 to find the percentage reduction

## Slide 18: Exercise: Maister’s rule
Use the data from the European manufacturer example to test Maister’s rule:
From 16 to 3 warehouses
Original safety stock in the system was $16M
By how much will the stock be reduced?
1 - [ √x ] =
[ √y ]

## Slide 19: Answer
Reducing from y to x
y = 16 16 = 4
x = 3  3 = 1.732
% Reduction = 1 – 1.732 = 56.7%
4
56.7% of $16M = $9M

## Slide 20: Maister’s rule - grid
Original number of warehouses |  |  |  |  |  |  |  | 
 | Percentage extra stock or reduced stock for change in no. of warehouses |  |  |  |  |  |  | 
 | New number of warehouses |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 10 | 15 | 20
1 | 0% | 41% | 73% | 100% | 124% | 216% | 287% | 347%
2 | -29% | 0% | 22% | 41% | 58% | 124% | 174% | 216%
3 | -42% | -18% | 0% | 15% | 29% | 83% | 124% | 158%
4 | -50% | -29% | -13% | 0% | 12% | 58% | 94% | 124%
5 | -55% | -37% | -23% | -11% | 0% | 41% | 73% | 100%
10 | -68% | -55% | -45% | -37% | -29% | 0% | 22% | 41%
15 | -74% | -63% | -55% | -48% | -42% | -18% | 0% | 15%
20 | -78% | -68% | -61% | -55% | -50% | -29% | -13% | 0%