## Slide 1: 1m² Brickwork Example 1
Calculate the unit rate for the brickwork from the data provided:

## Slide 2
Facing brickwork one side half brick thick in cement mortar 1:4 built in stretcher bond (unit: m²)
Brickwork gang = 2 bricklayers and 1 labourer
Brickwork rate per hour = £12.50
Labourer rate per hour = £9.50
Output per bricklayer = 45 bricks per hour
1m² of brickwork contains 60 bricks
Brick costs = £335 per 1000
Wastage = 5%
Mortar delivered to site = £52.50 per 1m³ tub
Mortar used = 0.04m³ per 1m² of brickwork.

## Slide 3: Answer:
Labour portion of Nett Rate:
Bricklayers = 2 x 12.50 = £25.00
Labourer = 9.50
Total Hourly Rate = £34.50
Output for the gang = 60 bricks per m² / (2 x 45) bricks per hour = 1.5 m² per hour.
Labour = £34.50 / 1.5 = £23.00 per m²

## Slide 4: Answer
Material portion of the Nett Rate:
Bricks = 335 x 60/100 = £20.10 per m²
Add wastage @ 5% = £1.01
Mortar = 0.04 x £52.50 = £2.10
Total Cost = £23.21 per m²
Unit Rate = £23.00 + £23.21 = £46.21 per m²