## Slide 1
Lowland Rivers & Fluvial landscapes
Dr Alissa Flatley
ACNA4007 – Physical Landscape and the Geosphere

## Slide 2
Zones of a River
Understanding the fluvial system...
Draw a hypothetical catchment.
1
Notes: - Key themes in course

## Slide 3
Zones of a River
Understanding the fluvial system...
What is a river cross section?
Draw a cross section of a river
2
Notes: - Key themes in course

## Slide 4
Zones of a River
Find a river channel...
Find a river channel
Label the source and output of the river channel
3
https://padlet.com/aflatley2/physical-landscapes-and-the-geosphere-hbprou7jn194avs5
Find an example of a modification in a river
Label any key features in your river channel
(these can be natural or anthropogenic)
Notes: - Key themes in course

## Slide 5
Depositional
zone
Source
zone
Transition
zone
Zones of a River
Understanding the fluvial system...
Alluvial rivers: Qs > Qc
sediment storage in floodplains - lowlands, high Q, low S
2
Bedrock rivers: Qc > Qs (i.e. excess power)
>50% ‘bedrock’ exposed, minimal sediment storage (frequent flushing), steep headwaters, high Ω
1
Notes: - Key themes in course

## Slide 6
Driving variables
Understanding the fluvial system...
Baselevel
(erosional base)
Tectonics
Climate
External controls
Internal controls / boundary conditions
Topography
Geology
Vegetation
Soils
Sedimentary
Perspective
Hydrological
Perspective
A river at work... (i.e. energy consumed to transport water and sediment)
Geomorphic Perspective:
Rivers only want the energy to transport their water and supplied sediment to ocean basins, and nothing more!
Approaching a “balance” (dynamic equilibrium)
Graded river concept...

## Slide 7
From small to large-scale... (from short to long timescale)
Understanding the fluvial system...
Fluvial Dunes
Fluvial Ripples
Channel bars
Scales of depositional elements in a fluvial system
Depositional elements built with sedimentary characteristics (grain size, structure, lithologies etc.): Facies
Characteristics depend on type of river (depositional style) = Channel form
Channel
& Reach
Depositional Environment = specific set of depositional elements
Channel pattern
Bedforms

## Slide 8
Gravel-dominated
1 Gravel-bed braided river
2 Gravel-bed braided river
3 Deep Gravel-bed braided river
X Wandering gravel bed river
4 Gravel bed meandering river
Sand-dominated high-sinuosity
5 Gravel-sand meandering river
6 Sand bed meandering stream
X Ephemeral sand bed meandering
7 Fine-grained meandering river
8 Anastomosed river
X Low-sinuosity river with alternate bars
9 Shallow perennial sand-bed braided river
10 Deep perennial sand-bed braided river
11 Distal sheetflood sand-bed river
12 Flashy ephemeral sheetflood sand-bed river
Sand-dominated low-sinuosity
Channel form and depositional environments
Sedimentary perspecitve

## Slide 9
Gravel-dominated
1 Gravel-bed braided river
2 Gravel-bed braided river
3 Deep Gravel-bed braided river
X Wandering gravel bed river
4 Gravel bed meandering river
Sand-dominated high-sinuosity
5 Gravel-sand meandering river
6 Sand bed meandering stream
X Ephemeral sand bed meandering
7 Fine-grained meandering river
8 Anastomosed river
X Low-sinuosity river with alternate bars
9 Shallow perennial sand-bed braided river
10 Deep perennial sand-bed braided river
11 Distal sheetflood sand-bed river
12 Flashy ephemeral sheetflood sand-bed river
Sand-dominated low-sinuosity
Channel form and depositional environments
Sedimentary perspecitve
Forms & process
Key measurements?

## Slide 10
Q = A* V
Discharge = Area X Velocity
Q = Discharge= m^3/s
Q = Discharge
local shear stress and velocity
How Streamflow is Measured | U.S. Geological Survey (usgs.gov)
In hydrology, discharge (Q) is the volume of water flowing through a given cross-sectional area of a stream or river per unit of time. It is typically measured in cubic meters per second (m³/s) or cubic feet per second (cfs).

## Slide 11
Stream power = 49 W = 0.049 kW
(73 500 W = 73.5 kW in flood)
1 kW = 1.34 horsepower...
Discharge ~ 2 m3/s (3000 m3/s in flood)
Density is 1000 kg/m3
Gravitation 9.8 m/s2
Gradient 0.0025 m/m
Stream Power
= … amount of energy the water in a river or stream is exerting on the sides and bottom of the river

## Slide 12
Width 2 m (60 m in flood)
Stream power = 49 W/m
Specific stream power = 24.5 W/m2
(1225 W/m2 in flood)
Specific stream power world wide...
> 12 000 W/m2 in riverine floods
> 300 000 W/m2 in outburst floods
Specific Stream Power
local shear stress and velocity

## Slide 13
Channel form and depositional environments
Qw
Qs
Qs
Topography
River planform = adjustment to boundary conditions (internal variables) + controlling variables Qs and Qw
Vegetation
Stream power
Mixed load
channels
Suspended load
Bed load
Geomorphic perspecitve
Sedimentary perspecitve
a continuum of channel pattern

## Slide 14
Rivers with exactly the energy required to move their bedload are straight without bedforms and are in the stationary equilibrium state
Sv – valley slope
Sfmin – min frictional slope
Planform adjustment to energy ??
Channel form and depositional environments

## Slide 15
Qw and Qs both fluctuate through time, and boundary conditions can change over long timescales - continuous adjustment takes place… how?
Dynamics – adjustment and change
Slope – Longprofile
Cross-Section
Planform (pattern)
Bed forms and roughness
Qw, Qs and boundary conditions change downstream – systematic change in form (pattern) and processes downstream…

## Slide 16
Landforms
Lateral accretion
Floodplain lake
Overbank fines
Point bar
Channel fill
Oxbow
Cut-off (soon)
... Meandering River

## Slide 17
Meanderbelt
yazoo
Landforms
Meandering dynamics – forms
Channel fill
Oxbow
Lateral accretion
Floodplain lake
Overbank fines
Point bar
Cut-off
Oxbow
yazoo

## Slide 18
Meandering over time
Meandering dynamics – processes and rates
1
2
3
4
3
4

## Slide 19
Modelling channel form

## Slide 20
Future models
Forward numerical modelling
What drives meandering rates – discharge/flow or sediment ?

## Slide 21
Lab time
Part 1 of rivers (Today)
Fieldwork week in Lampeter next week – Discharge measurements and river form.

## Slide 22
Lab time
Part 1 of rivers (Today)
Fieldwork week in Lampeter next week – Discharge measurements and river form.