## Slide 1: Bioethanol & Biomethane Fuels
By Andrew Thorn

## Slide 2: What is Bioethanol?
The principle fuel used as a petrol substitute for road transport
Bioethanol fuel is mainly produced by the sugar fermentation process, although it can be made by reacting ethylene with steam

## Slide 3: What is Bioethanol?
Ethanol or ethyl alcohol (C2H5OH) is a clear colourless liquid
It is biodegradable, low in toxicity and causes little environmental problem if spilt
Ethanol turns to produce carbon dioxide and water
Ethanol is a high octane fuel and has replaced lead as an octane enhancer in petrol

## Slide 4: Advantages of Bioethanol
Unlike petroleum, ethanol is renewable
Ethanol burns more clearly in air than petroleum, producing less carbon and carbon monoxide
The use of ethanol as opposed to petroleum could reduce CO2 emissions provided that a renewable energy resource was used to produce the crops

## Slide 5: Advantages of Bioethanol
Some of the greenhouse gases emissions will be reduced as the fuel crops absorb the CO they emit through growing
Blending Bioethanol with petrol will help extend the life of the UK’s diminishing oil supplies
Help ensure greater fuel security, avoiding reliance on oil producing nations

## Slide 6: Advantages of Bioethanol
Bioethanol is biodegradable and far less toxic than fossil fuels
By using bioethanol in older engines can help reduce the amount of carbon monoxide produced by the vehicle
Bioethanol can easily be integrated into the existing road transport fuel system

## Slide 7: Disadvantages of Bioethanol
Production of bioethanol requires a high amount of energy
Bioethanol fuel with more than 10% ethanol is not compatible with already established engine components and may cause engine corrosion
Requires a large amount of land to produce biomass

## Slide 8: Disadvantages of Bioethanol
Farmers may sacrifice food crops for biofuel production which could lead to increased food prices
Emissions of GHGs from production of bioethanol is comparable to the emissions of internal-combustion engines
Not as efficient as petroleum- its energy content is 70% of that of petrol

## Slide 9: Disadvantages of Bioethanol
Ethanol is hygroscopic and thus has high corrosion aggressiveness
Cold start difficulties as pure ethanol is difficult to vapourise
Negatively affect electric fuel pumps by increasing internal wear and undesirable spark generation

## Slide 10: Bioethanol Production
Ethanol can be produced from biomass by the hydrolysis and sugar fermentation processes
Biomass wastes contain a complex mixture of carbohydrate polymers from the plant cell walls known as cellulose, hemi cellulose and lignin
In order to produce sugars from the biomass, the biomass is pre-treated with acids or enzymes in order to reduce the size of the feedstock and to open up the plant structure

## Slide 11: Bioethanol Production
The cellulose and hemi cellulose portions are hydrolysed by enzymes or dilute acids into sucrose that is then fermented into ethanol
The lignin in the biomass is normally used as a fuel for the ethanol production plants boilers

## Slide 12: Methods of Extracting Sugars from Biomass
Concentrated acid hydrolysis
Dilute acid hydrolysis
Enzymatic hydrolysis

## Slide 13: Concentrated Acid Hydrolysis Process
Works by adding 70-77% sulphuric acid to the biomass that has been dried to a 10% moisture content
The acid is added in the ratio of 1.25 acid to 1 biomass and the temperature is controlled to 50°C

## Slide 14: Concentrated Acid Hydrolysis Process
Water is then added to dilute the acid to 20-30% and the mixture is again heated to 100°C for 1 hour
The gel produced from this mixture is then pressed to release an acid sugar mixture
A chromatographic column is used to separate the acid and sugar mixture

## Slide 15: Dilute Acid Hydrolysis
The first stage uses 0.7% sulphuric acid at 190°C to hydrolyse the hemi-cellulose present in the biomass
The second stage is optimized to yield the more resistant cellulose fraction
This is achieved by using 0.4% sulphuric acid at 215°C
The liquid hydrolates are then neutralized and recovered from the process

## Slide 16: Wet Milling
The grain is soaked or “steeped” in water and dilute sulphuric acid for 24 to 48 hours
The steeping facilitates this separation of the grain into its many component parts
After steeping the slurry is processed through a series of grinders to separate the corn germ or grain

## Slide 17: Wet Milling
The oil from the germ is either extracted on-site or sold to crushers who extract the oil
The remaining fibre, gluten and starch components are further segregated using centrifugal screen and hydroclonic separators

## Slide 18: Wet Milling
The steeping liquor is concentrated in an evaporator
This concentrated product, heavy steep water, is co dried with the fibre component and sold as corn gluten feed to livestock industry
Heavy steep water is also sold as a feed ingredient

## Slide 19: Wet Milling

## Slide 20: Wet Milling
The gluten component (protein) is filtered and dried to produce the corn gluten meal co-product
This product is highly sought after as a feed ingredient in poultry operations

## Slide 21: Wet Milling
The starch and any remaining water from the mash can be processed in one of three ways: -
Fermented into ethanol
Dried and sold as dried or modified corn starch
Processed into corn syrup

## Slide 22: Dry Milling
The starchy grain is first ground into flour, which is referred to in the industry as “meal” and processed with separating out the various component parts of the grain
The meal is slurried with water to form a “mash”
Enzymes are added to the mash to convert the starch to dextrose
Ammonia is added for pH control and as nutrient to the yeast

## Slide 23: Dry Milling
The mash is processed in a high-temperature cooker to reduce bacteria levels ahead of fermentation
The mash is cooked and transferred to fermenters where yeast is added and the conversion of sugar to ethanol and carbon dioxide begins
The fermentation process generally takes about 40 to 50 hours

## Slide 24: Dry Milling
During this part of the process, the mash is agitated and kept cool to facilitate the activity of the yeast
After fermentation, the resulting “beer” is transferred to distillation column where the ethanol is separated from the remaining “stillage.”

## Slide 25: Dry Milling
The ethanol is concentrated to 190 proof using conventional distillation and then is dehydrated to approx. 200 proof in a molecular sieve
The anhydrous ethanol is then blended with about 5% denaturant (such as gasoline) to render it non potable

## Slide 26: Dry Milling
The stillage is sent through a centrifuge that separates the coarse grain from the solubles
The solubles are then concentrated to about 30% solids by evaporation, resulting in condensed distillers solubles (CDS) or “syrup”

## Slide 27: Dry Milling
The coarse grain and the syrup are then dried together to produce dried distillers grains with solubles (DDGS), a high quality, nutritious livestock feed
The CO2 released during fermentation is captured and sold for use in carbonating soft drinks and beverages and the manufacture of dry ice

## Slide 28: Ethanol from Cellulosic Biomass
Cellulosic biomass is the structural portion of plants, including complex sugars that cannot directly be used for food ingredients of fermentation substrates

## Slide 29: Cellulosic Biomass
Cellulosic biomass can be obtained from a variety of sources, such as
Agricultural residues (sugar cane bagasse and spent sugar beet pulp)
Forestry residues (fallen branches, twigs, saw dust, etc.)
Municipal solid waste (paper and paperboard products)
Industrial wastes (paper making sludges)

## Slide 30: Cellulosic Biomass
Three main components- cellulose, hemi-cellulose and lignin- make up the cell walls that form the tissue structure of cellulose biomass
These cell walls also include a small amount of pectin, waxes, water soluble sugars and organic acids

## Slide 31: Cellulosic Biomass Process
Consists of four steps
Pretreatment
Enzyme hydrolysis
Fermentation
Distillation

## Slide 33: Pretreatment
The purpose of pretreatment is to make the cellulose more susceptible to being broken down so that it is ready for the enzyme hydrolysis step
Pretreatment does this by partially removing the lignin and hemi-cellulose which block the cellulose inside the cell wall

## Slide 34: Pretreatment
This step can be done by using acid, alkali, organic solvents, heat treatments, etc.
Some options for pretreatment are steam explosion, liquid hot water, lime-ammonia and acid treatment

## Slide 35: Pretreatment Challenges
Reducing the cost of the process (capital & operating)
Ensuring that the particle size is reduced enough in order to increase surface area-to-mass ratio for maximum exposure to contact surfaces
Minimising the accumulation of inhibitory products that could interfere with the subsequent fermentation step
Enhancing the sugar yield and allowing efficient hydrolysis at a lower concentration of enzymes

## Slide 36: Enzyme Hydrolysis
Is the process used to convert polysaccharides (cellulose and hemi-celluloses) and their oligomers (molecules with a few single sugar units) into simple sugars, which can be fermented by bacteria or yeast
The high cost of enzymes is currently the greatest challenge in this processing step

## Slide 37: Enzyme Hydrolysis
An important approach to reduce cost for enzyme hydrolysis is to develop an efficient pretreatment method to reduce the enzyme dosage and enhance the yield of simple sugars
Sugar yield is typically less than 20% without pretreatment, whereas yield after pretreatment often exceeds 90%

## Slide 38: Fermentation
Conventional fermentation is the process that converts the sugars from sugar-rich feedstocks into alcohol in the brewing and beverage alcohol industries
In a cellulosic bioethanol process, fermentation is used to convert the single sugars obtained from the enzyme hydrolysis step to fuel ethanol

## Slide 39: Fermentation
Organisms such as yeast (Saccharomyces Cerevisiae) or bacteria (E.Coli) are used to convert these simple sugars to ethanol
In order to keep distillation costs low, the appropriate micro-organisms is selected based on the need to achieve high ethanol yield while also withstanding inhibition from accumulating toxic substances and auto intoxication from increasing ethanol concentration

## Slide 40: Fermentation
The fermentation step usually follows enzymatic hydrolysis as a separate step
This procedure is known as separate hydrolysis and fermentation (SHF)
However, the most commonly used technique is called the simultaneous saccharification and fermentation (SSF) process, which carried out by combining fermentation and enzyme hydrolysis in the same step

## Slide 41: Fermentation
Normally, higher ethanol yield can be achieved with SSF, which can be attributed to the reduction of inhibitory end-products (glucose and cellulose)

## Slide 42: Distillation
Ethanol is recovered from the fermentation broth by the process called distillation
Distillation works by boiling the liquid mixture of water and ethanol
Ethanol vapours are separated from the liquid portion because ethanol has a lower boiling point (78.3°C) at atmospheric pressure compared to water (100°C)

## Slide 43: Distillation
The lignin residues, along with unreacted cellulose, hemi-cellulose, ash, enzymes, and remaining micro-organisms, end up in the bottom of the distillation column during the bioethanol process
The solid waste (still bottoms) has high energy content, which can be burned as fuel for power or may be converted to various value-added products

## Slide 44: Fuel Ethanol
The blending of ethanol makes the fuel mixture burn more completely and reduces pollution emissions
However, the energy content of ethanol is approximately 33% lower than petrol
If you use E10 petrol/ethanol mixtures instead of pure petrol, the mileage may decrease 3.3%

## Slide 45: Fuel Ethanol
Blending must be done very carefully, and is usually done locally
Ethanol easily absorbs water and water does not mix with oil and phase separation will occur
Water contamination may result in engine damage and reduction of fuel efficiency

## Slide 46: Anaerobic Digestion
By Andrew Thorn

## Slide 47: Introduction
Anaerobic digestion is the technology that can convert the agri-industrial waste chain, the municipal solid waste and/or wastewater sludge into renewable energy
An important economic consideration is the fact that the biogas can be produced at the production site and used as fuel on that site eliminating transportation costs

## Slide 48: Anaerobic Digestion Process
Anaerobic digestion is a natural biological process when bacteria breakdown organic matter in environments with little or no oxygen
A controlled version of the anaerobic breakdown of organic waste is a landfill process which releases methane as one of the end products
The AD process can be split into three main stages; hydrolysis, acidogenesis and methanogenesis

## Slide 49: Anaerobic Digestion Process
Anaerobic fermentation significantly reduces the total mass of waste, generates solid or liquid fertilizer and yields energy
It can be maintained at psychrophilic conditions (12-16°C landfills, swamps) mesophilic conditions (35-37°C) or thermophilic conditions (55-60°C anaerobic digesters)

## Slide 50: Anaerobic Digestion Issues
Thermophilic anaerobic fermentation leads to reduced process stability and dewatering properties of the fermented sludge
Requirements for large amounts of energy for heating
Thermal destruction of pathogenic bacteria at elevated temperatures

## Slide 51: Hydrolysis/Liquefaction
Fermentative bacteria convert the insoluble complex organic matter such as cellulose, into soluble molecules such as sugars, amino acids and fatty acids
The complex polymeric matter is hydrolysed to monmers, e.g. cellulose to sugars or alcohols and proteins to peptides or amino acids, by hydrolytic enzymes, secreted by microbes

## Slide 52: Hydrolysis/Liquefaction Reactions
Lipids Fatty Acids
Polysaccharides Monosaccharides
Protein Amino Acids
Nucleic Acids Purines & Pyrimidines

## Slide 53: Acidogenesis
In this stage acetogenic bacteria convert the products of the first phase to simple organic acids, carbon dioxide and hydrogen
The principal acids produced are acetic acid, propionic acid, butyric acid and ethanol

## Slide 54: Acidogenesis
The products formed during acetogenesis are due to a number of different microbes, e.g. Syntrophobacter Wolini, a propionate decomposer and Sytrophomonas Wolfei, a butyrate decomposer
Other acid formers are Clostridium Spp., Peptococcus Anerobus, Lactobacillus, and Actinomyces

## Slide 55: Acidogenesis
C6 H12 O6 2C2 H5 OH + 2CO2

## Slide 56: Methanogenesis
Methane is produced by bacteria called methane formers in two ways
By cleavage of acetic acid molecules to generate carbon dioxide and methane
Reduction of carbon dioxide with hydrogen

## Slide 57: Methanogenesis Reactions
CH3 COOH CH4 + CO2
Acetic acid Methane Carbon dioxide
2C2 H5 OH + CO2 CH4 + 2CH3 COOH
Ethanol
CO2 + 4H2 CH4 2H2 O
Hydrogen Water

## Slide 58: Biogas Product
The products from Anaerobic digestion contain methane, carbon dioxide, hydrogen, hydrogen sulphide, ammonia and other substances that may inhibit the anaerobic digestion process or cause corrosion problems in pipelines of plants or in the distribution
At the end of the purification process the biogas still contains hydrogen, carbon dioxide and trace of suphidric acid and ammonia (<100ppm) that must be removed from the stream to produce biomethane

## Slide 59: Combustible Gas Quality
The parameter typically used to determine the combustible quality of the gas is the Wobbe Index
The Wobbe Index (WI) or Wobbe Number is an indicator of the interchangeability of fuel gases such as natural gas and liquefied petroleum gas (LPG) and is frequently defined in the specifications of gas by customers and utilities

## Slide 60: Wobbe Index
If VC is the higher heating value, or calorific value, GS is the specific gravity, the Wobbe Index, IW is defined as
IW = VC / (GS)0.5

## Slide 61: Wobbe Index
Is used to compare combusting energy output of fuel gas of different quality for use in an appliance
If two fuels have identical Wobbe indices then for given pressure and valve settings the energy output will also be identical
Typically variations of up to 5% are allowed as this would not be noticeable to the consumer

## Slide 62: Wobbe Index
Is a critical factor to minimize the impact of the changeover when analyzing the use of substitute natural gas fuels such as propane- air mixture
There are three families of fuel gases that have been internationally agreed upon based on the Wobbe Index
Family 1 covers manufactured gases, family 2 covers natural gases and family 3 covers liquefied petroleum gas (LPG)

## Slide 63: Wobbe Index Specifications
Family | Type of gas | Wobbe Index range | Wobbe number range
1 | Town gas/ Syn gas | 22.5 - 30 | 24 - 29
2L | Natural | 39 - 45 | 
2H |  | 45.5 - 55 | 48 - 53
3 | LPG | 73.5 – 87.5 | 72 - 87

## Slide 64: Digester Sizing
The energy available from a biogas is given by:
E = η Hb Vb
η = is the combustion efficiency of burners,
boilers, etc.
Hb = is the heat of combustion per unit volume
biogas
Vb = is the volume of biogas

## Slide 65: Digester Sizing
Some of the heat of combustion of the methane goes to heating CO2 present in the biogas
This is therefore unavailable for other purposes, so decreasing the efficiency

## Slide 66: Digester Sizing
Alternatively
E = η Hm Fm Vb
Hm = is the heat of combustion of methane
(56 MJ/Kg, 28MJ/m3 at STP)
Fm = is the fraction of methane in the biogas

## Slide 67: Digester Sizing
For biogas directly from the digester, Fm should be between 0.5 and 0.7
However, if the gas is passed through a counter flow of water to dissolve the CO2 and increase Fm to nearly 1.0

## Slide 68: Digester Sizing
The volume of biogas is given by:
Vb = CmO
C = is the biogas yield per unit dry mass of
whole input (0.2 to 0.4 m3/kg)
mO = is the mass of dry input

## Slide 69: Digester Sizing
The volume of fluid in the digester is given by: -
Vf = mo/pm
pm = is the density of dry matter in the fluid
(~ 50 kg/m3)

## Slide 70: Digester Sizing
The volume of the digester is given by: -
Vf = is the flow rate of the diagram
tr = is the retention time in the digester
(~8 to 20 days)

## Slide 71: Typical Manure from Farm Animals
Animal | Total Wet Manure/ Animal/day/kg | Total Solids/kg | Moisture mass content/wet mass
Dairy cow (~500kg) | 35 | 4.5 | 87%
Beef steer (~300kg) | 25 | 3.2 | 87%
Fattening pig (~60kg) | 3.3 | 0.3 | 91%
Laying hen | 0.12 | 0.03 | 75%

## Slide 72: Example
Calculate (1) the volume of a biogas digester suitable for the output of 6000 pigs; and (2) the power available from the digester, assuming a retention time of 20 days and a burner efficiency of 0.6

## Slide 73: Solution (1)
Mass of solids (per day) in waste is approximately
mO = (0.3 kg d-1) (6000) = 1800 kg d-1
Fluid volume (per day) is:
V = = 36m3 d-1

## Slide 74: Solution (2)
Digester volume is:
Vd = (36m3 d-1) (20 days) = 720m3
Vb = (0.24m3 kg-1) (1800 kg d-1) = 430m3 d-1
Energy output
E = (0.6) (20 MJ m3) (430m3 d-1)
E = 5200 MJ d-1 =1400 kWh d-1
E = 60 kW