## Slide 1: Why EIA? Intro and background to EIA
ACBA 7004
Alisdair Cunningham
a.cunningham@uwtsd.ac.uk

## Slide 2: Outline
History of the EIA
What is Environmental Impact
Process of conducting an EIA
BREAK
Key EIA Stages
Reviewing EIA

## Slide 3: Activity
Comment on your progress with finding an EIA report. Consider the following and report back to the group:
What EIA did you find? Was it hard to find? Briefly summarise its scope/purpose.

## Slide 4: Introduction and History of the EIA
ACBA 7004

## Slide 5: Last Week…
Read the following:
Beatley (1989) Environmental Ethics and Planning Theory
Select an EIA for your assessment

## Slide 6
Short history of EIA
The Agricultural and Industrial revolutions resulted in the ability for humans to exceed the previous carrying capacity of the land
      Escaping ‘Malthusian checks’
Populations exploded, resulting in increased pressure on the natural environment and its resources

## Slide 7
Short history of EIA
Increased awareness of exploitation of the environment in the US (and elsewhere) and the impacts on nature and public health led to increased activism and environmentalism and development of ‘Sustainable Development’
Source: Allan E. Settle (1966) Public Opinion and Community Involvement, Journal of the Air Pollution Control Association, 16:9, 490-491

## Slide 8
Short history of EIA
US set up NEPA in 1969, first time agencies had to investigate and document potential impacts to the environment
First time legislative action at federal level was required to consider the environment when conducting certain projects
establishment of the Council on Environmental Quality (CEQ)
  Regulations and guidance
First time policy included non-government stakeholders, specifically the public.
A procedural process to guide decision-making for developers
An Environmental Assessment may need to be conducted
An Environmental Impact Statement (EIS) may need to be prepared
“the 1970s absolutely must be the years when America pays its debt to the past by reclaiming the purity of its air, its waters, and our living environment.”

## Slide 9
Short history of EIA
Despite some early scepticism, the UK eventually took on the requirement for EIAs in 1988, under the European Commission.
Slow uptake of mandatory EIA’s between 1970 and 1985:
Canada in 1973, Australia and New Zealand in 1974, West Germany in 1975, and France in 1976
While they vary in scope and format, the requirement for an EIA has now spread globally.
Source: Glasson et al., 2018

## Slide 10
EIA Definition
“a tool used to identify the environmental, social and economic impacts of a project prior to decision-making. It aims to predict environmental impacts at an early stage in project planning and design, find ways and means to reduce adverse impacts, shape projects to suit the local environment and present the predictions and options to decision-makers.”
Source: Ling, Matthew A., et al. An Introduction to Environmental Assessment. UNEP, 2015.
Source: Convention on Biological Diversity. https://www.cbd.int/impact/whatis.shtml
“a process for identifying the positive and negative environmental effects of proposed developments. It applies to projects which are likely to have significant effects on the environment because of their nature, size or location. The developer submits the EIA report along with the proposal to the decision makers (e.g. the local planning authority if planning permission is needed), and the decision makers consider the EIA along with the plan when deciding whether to grant consent.
Source: NRW (https://naturalresources.wales/guidance-and-advice/business-sectors/planning-and-development/advice-for-developers/environmental-assessment)

## Slide 11: Why EIA is important
Reducing the burden of environmental impacts is necessary if development is to become sustainable.
These impacts are more complex, larger in scale and further reaching in their potential consequences than thirty years ago when EIA was first introduced.
As a result, EIA has become of ever increasing importance as a tool for development decision-making.

## Slide 12: Why EIA is important
In practice, EIA is applied primarily to prevent or minimise the adverse effects of major development proposals, such as a power station, dams and reservoirs, industrial complexes, etc.
This process is also used as a planning tool to promote sustainable development by integrating environmental considerations into a wide range of proposed actions.

## Slide 13
Environmental crisis in the industrial economies
1952 “killer fog” kills 4,000 in London
1963 Rachel Carson’s Silent Spring documents the negative effects of DDT
1966 Cayahoga River in Ohio catches fire

## Slide 15
Cuyahoga River burns in 1966 (3rd time). Cleveland, Ohio, U.S.
“30 Years of Environmental Progress,” USEPA, 2000.

## Slide 17: Evolution of EIA
early 1970s — initial development
1970s to 1980s — increasing scope
mid to late 1980s — process strengthening and policy integration
mid 1990s — towards sustainability (SEA, Biodiversity)
ACBA 7004

## Slide 18
Regions | Major Environmental Issues
Africa | The continent has the world’s poorest and most resource dependent population. It carries the highest health burden due to severe environmental problems. These include desertification and soil degradation, declining food security, and increasing water scarcity.
Asia and Pacific | Rapid economic growth, urbanization and industrialization have helped in poverty alleviation but also increased pressure on land and water resources, widespread environmental degradation and high pollution levels. Mega- cities are a particular focus of environmental and health concerns.
Eastern Europe and Central Asia | Despite progress with economic restructuring and environmental clean up, there is a legacy of industrial pollution and contaminated land during communist era. In many areas, emissions of particulates, SO2, lead, heavy metals and toxic chemicals continue to expose the residents to health risks.
Latin America and the Caribbean | Approximately three-quarters of the population live in urban areas. Many cities are poor, overcrowded, polluted and lack basic infrastructure. The major environmental issue is the destruction of tropical forests and consequent loss of biodiversity, which is especially serious in the Amazon basin.

## Slide 19: Increasingly significant
ACBA 7004

## Slide 20: What are the aims and objectives of EIA?
The aims and objectives of EIA can be divided into two categories.
The immediate aim and ultimate (long term) aim
The immediate aim of EIA is to inform the process of decision-making by identifying the potentially significant environmental effects and risks of development proposals.
The ultimate (long term) aim of EIA is to promote sustainable development by ensuring that development proposals do not undermine critical resource and ecological functions or the wellbeing, lifestyle and livelihood of the communities and peoples who depend on them.

## Slide 21: Immediate objectives of EIA are
To
improve the environmental design of the proposal;
ensure that resources are used appropriately and efficiently;
identify appropriate measures for mitigating the potential impacts of the proposal; and
facilitate informed decision making, including setting the environmental terms and conditions for implementing the proposal.

## Slide 22: Long term objectives of EIA are
To:
protect human health and safety;
avoid irreversible changes and serious damage to the environment;
safeguard valued resources, natural areas and ecosystem components;
and
enhance the social aspects of the proposal.

## Slide 23: Fundamental Approach to Environmental Impact Assessment (EIA)
BASIC CONCEPTS OF EIA :
EIA is an activity designed to identify and predict the impact of a project on bio-geo-physico-chemical environment and on human health so as to recommend appropriate legislative measures, programs, and operational procedures to minimize the impact.

## Slide 24
EIA is an exercise to be carried out before any project or major activity is undertaken to ensure that it will not in any away harm the environment on a short-term or long-term basis.
Any developmental activity requires EIA to be done before executed to know the effect of a proposed development on the environment.

## Slide 25: EIA: Purpose
To provide information for decision-making on the environmental consequences of proposed actions;
and
To promote environmentally sound and sustainable development through the identification of appropriate enhancement and mitigation measures.

## Slide 26: Benefits of EIA include:
environmentally sound and sustainable design
better compliance with standards
savings in capital and operating costs
reduced time and costs for approvals
increased project acceptance
better protection of the environment and human health

## Slide 27: The EIA processes in sequences of application.
(UNEP, 2012)

## Slide 28
Impact?
In EIA, the term “impacts” is used instead of “effects of activities.”
What is an impact?

## Slide 29: What is an impact?
The impact of an activity is a deviation (a change) from the baseline situation that is caused by the activity.
To measure an impact, you must know what the baseline situation is.
!
The baseline situation is the existing environmental situation or condition in the absence of the activity.
The baseline situation is a key concept in EIA.

## Slide 30: Environmental impacts (key words)
type and nature
magnitude
extent
timing
duration
uncertainty
reversibility
significance

## Slide 31
Environmental impact categories - Enviroscore (azti.es)

## Slide 32: What is an impact?
The impact of an activity is the change from the baseline situation caused by the activity.
The baseline situation is the existing environmental situation or condition in the absence of the activity.
The baseline situation is a key concept in environmental impact assessment.
!
To measure an impact, you must know what the baseline situation is.

## Slide 33: The baseline situation
In characterizing the baseline situation, many environmental components MAY be of interest
Water Quantity, quality, reliability, accessibility
Soils Erosion, crop productivity, fallow periods, salinity, nutrient concentrations
Flora Composition and density of natural vegetation, productivity, key species
Fauna Populations, habitat
Special Key species ecosystems
Env Health Disease vectors, pathogens
The components of interest are those that are likely to be affected by the activity—or upon which your activity depends for its success
Notes: For example, an ecotourism activity might depend on water level in watering holes---but this environmental component is not in fact affected by your activity.

## Slide 34: The baseline situation
The baseline situation is not simply a “snapshot.”
Describing the baseline situation requires describing both the normal variability in environmental components & current trends in these components.
time
Water table
This chart of groundwater levels shows both variability and a trend over time.
Both are part of the groundwater baseline situation.

## Slide 35: Types of impacts & their attributes
Direct & indirect impacts
Short-term & long-term impacts
Adverse & beneficial impacts
Cumulative impacts
The EIA process is concerned with all types of impacts and may describe them in a number of ways
 Intensity  Direction
 Spatial extent  Duration
 Frequency  Reversibility
 Probability
But all impacts are NOT treated equally.

## Slide 36: Key terms in the EIA process
Defining “impact”
Defining “activity”
Characterizing the baseline situation
Time
Water table
Notes: Image credit: Drip irrigation of new strawberry plants in Egypt. — usaid.gov https://www.usaid.gov/where-we-work/middle-east/merc-water-success-stories

## Slide 37: Baseline
The baseline situation is not just a snapshot in time.
This chart of groundwater levels shows both variability and a trend over time.
BOTH are part of the groundwater baseline situation.
Time
Water table
Notes: This shallow well features a raised enclosure and a cover, both of which help to reduce the possibility of contamination. Shallow wells provide an easy way to monitor groundwater levels.
Describing the baseline situation requires describing both the normal variability in environmental components and current trends in these components.
Baseline characterization is a description of environmental conditions in the absence of the proposed activities. The baseline characterization cannot be exhaustive. The environmental components most important when determining the baseline characterization are those components most likely to be affected by your activity and upon which your activity depends on for its success.
Provide an overview of topics for examining the environmental baseline, such as:
  Water: Quantity, quality, reliability, accessibility
  Soils: Erosion, crop productivity, fallow periods, salinity, nutrient concentrations
  Climate Change: unpredictable weather patterns, agriculture, and food production
  Fauna: Populations, habitat
  Environmental Health: Disease vectors, pathogens
  Public Health: Conflict over resources, vulnerable populations, access to resources
  Flora: Composition and density of natural vegetation, productivity, key species
  Key species, ecosystems
Determine the baseline situation by obtaining information from 3 sources:
  Your organization: Talk to staff who know the project, and know the sites. Obtain project documents and information
  Direct observation: Go to the site(s). Look up publicly available satellite imagery before you go.
  Utilize other local talent and knowledge: communities, government, counterparts, literature

## Slide 38
Impacts within an EIA Process Flow Chart
Where do impacts ‘sit’ within the EIA process?

## Slide 39: What is an activity?
ACTIVITY: market access road rehabilitation | ACTIONS: Survey, grading, culvert construction, compaction, etc. . .
a desired accomplishment or output
E.g.: a road, seedling production, or river diversion to irrigate land
An activity is:

Accomplishing an activity requires a set of actions
We are discussing the impacts of activities. What are activities?
A project or program may consist of many activities

## Slide 40: What about sub-activities?
A project or program usually consists of many activities.
Accomplishing an activity requires a set of sub-activities or tasks.
ACTIVITY: Market access road rehabilitation | SUB-ACTIVITIES OR TASKS: Survey, grading, culvert construction, compaction, etc..

## Slide 41: Activities and sub-activities
Market access road rehabilitation
Surveying
Grading
River diversion to irrigate land
?
?
Culvert construction
Compaction
Seedling production
?
?
Agricultural Enhancement Program
Project or Program
Activities
Sub-Activities or Tasks
Notes: Group activity – fill in the question marks on irrigation and seedling production. Emphasize that it is okay if they don’t know much about the topics; just do your best.

## Slide 42: Activity
Think about your select EIA report. Consider the following and report back to the group:
What key impacts are highlighted in your EIA? What main activity is being undertaken?

## Slide 43: Take a break
15mins

## Slide 44: EIA process

## Slide 45: EIA practice and outcomes
screens out environmentally unsound projects;
modifies the design of feasible proposals to reduce their environmental impact;
identifies the best practicable environmental option;
predicts the significant adverse effects of proposals with reasonable accuracy;
identifies mitigation measures that work successfully to avoid, reduce and offset major impacts;
influences decision making and approvals and the implementation of terms and conditions; and
results in environmental gains and benefits relative to other options.

## Slide 46: Costs and benefits of EIA
Although there are costs associated with undertaking EIA, experience has shown that the potential savings over the life of a project can repay the investment many times over.
The savings can be economic (e.g. identification of least cost alternative) as well as environmental (e.g. impact reduction, maintaining other resource use opportunities).
When EIA is integrated into the project preparation phase, environmental design considerations can be introduced in the first place rather than the proposal having to be modified later.
Generally the earlier EIA process is introduced in the project cycle, the greater the potential returns.

## Slide 47: Costs and benefits of EIA
Costs
Although many proponents complain that EIA causes excessive delays in projects, many of these are caused by poor administration of the process rather than by the process itself.
These occur when:
  the EIA is commenced too late in the project cycle;
  the terms of reference are poorly drafted;.
  the EIA is not managed to a schedule;
  the technical and consultative components of EIA are inadequate; and
  the EIA report is incomplete or deficient as a basis for decision making.

## Slide 48: Why?
With all developments, there is a potential impact on the environment and SD (not necessarily negative).
Notes: Partially from the herihly

## Slide 49: Impacts of Development
Introduction 3 mins
Direct loss of habitat - if only the footprint of the development.
Severance - this is where the development forms a barrier and possibly divides existing habitats. This leads to fragmentation.
Disruption to the local hydrology - including watercourse damage, polluted run-off, sedimentation and erosion.
Disturbance of particular notable species - eg badgers, bats, owls, etc.
Eden: environmental assessment
  ://www.youtube.com/watch?v=9xTxA4y6ctg

## Slide 50: Principles
The eight guiding principles...
There are eight guiding principles that govern the entire process of EIA and they are as follows:
Participation: An appropriate and timely access to the process for all interested parties.
Transparency: All assessment decisions and their basis should be open and accessible.
Certainty: The process and timing of the assessment should be agreed in advanced and followed by all participants.
Accountability: The decision-makers are responsible to all parties for their action and decisions under the assessment process.
Credibility: Assessment is undertaken with professionalism and objectivity.
Cost-effectiveness: The assessment process and its outcomes will ensure environmental protection at the least cost to the society.
Flexibility: The assessment process should be able to adapt to deal efficiently with any proposal and decision making situation.
Practicality: The information and outputs provided by the assessment process are readily usable in decision making and planning.

## Slide 51: Background
Historical Development
NEPA – National Environmental Policy Act 1969 in the USA
  Required federal agencies to carry out environmental assessment of policies and activities.
  Driving force of environmental law and assessment (Holder, 2007)
Notes: The National Environmental Policy Act (NEPA) was one of the first laws ever written that establishes the broad national framework for protecting our environment. NEPA's basic policy is to assure that all branches of government give proper consideration to the environment prior to undertaking any major federal action that significantly affects the environment.
NEPA requirements are invoked when airports, buildings, military complexes, highways, parkland purchases, and other federal activities are proposed. Environmental Assessments (EAs) and Environmental Impact Statements (EISs), which are assessments of the likelihood of impacts from alternative courses of action, are required from all Federal agencies and are the most visible NEPA requirements.

## Slide 52: Background
Historical Development
1973 – First Environmental Action Plan from the European Commission highlighted the importance of Environmental Impact Assessments (EIAs)
1985 – Directive (85/337/EEC) EIA procedures were mandated at project level
Previously EIAs were voluntary or carried out due to local authority request
  (Glasson et al, 2019)

## Slide 53: Process of conducting an EIA
ACBA 7004

## Slide 54: The EIA processes in sequences of application.
(UNEP, 2012)

## Slide 56
Stage | What’s involved
1. Screening | Deciding if an EIA is required
2. Scoping | Deciding what needs to be covered in the assessment and reported in the ES
3. Assessment and Report | The ES has to include the likely significant environmental effects of the development
4. Review of Application | The ES and development application must be publicised so interested parties and the public have the opportunity to give their views on it.
5. Decision | The ES and any comments made on it must be taken into account by the competent authority before they decide whether to give consent.
6. Implementation and monitoring | The developer must commence any monitoring required by the competent authority.
Source: United Nations University (2007)
https://wedocs.unep.org/bitstream/handle/20.500.11822/26503/EIA_Training_Resource_Manual.pdf
1. Screening | Deciding if an EIA is required
While the legislative guidelines varies slightly for each country, the process often follows similar steps / stages.
Notes: Environmental Impact Assessment - GOV.UK (www.gov.uk) - https://www.gov.uk/guidance/environmental-impact-assessment

## Slide 57
Screening
EIA is required for some types of development, but not others.
Deciding whether an EIA is required is known as “screening” and can be a source of major dispute between developers, communities and local authorities.
It is vital that this stage is carried out properly.
When undertaking screening, the regulations define two different types of project: those where EIA must take place or where it may be needed.
These are set out in two Schedules.
  Schedule 1 projects: an EIA must always be carried out
  Schedule 2 projects: an EIA must be carried out if the development is likely to have a significant impact on the environment by virtue of its nature, size or location.

## Slide 58
Phase 1 of the EIA Process
Screen the activity
Based on the nature of the activity what level of environmental review is indicated?
Conduct a Preliminary Assessment
A rapid, simplified EIA study using simple tools
ACTIVITY IS OF MODERATE OR UNKNOWN RISK
SIGNIFICANT ADVERSE IMPACTS POSSIBLE
SIGNIFICANT ADVERSE IMPACTS VERY UNLIKELY
ACTIVITY IS LOW RISK (Of its nature, very unlikely to have significant adverse impacts)
ACTIVITY IS HIGH RISK (Of its nature, likely to have significant adverse impacts)
Phase II
Phase I
Understand proposed activity
Why is the activity being proposed?
What is being proposed?
BEGIN FULL EIA STUDY
STOP the EIA process

## Slide 59
Schedule 1 developments
Examples include:
Major Power Plans
Chemical Works
Long Distance Railways
Waste Disposal Incineration
Major Road Schemes
Major Wastewater Treatment Works
Steel Works
Inland waterways/ports for inland waterway traffic
Dams
Quarries and open case mining
Intensive poultry / pig farm
Visit: https://www.legislation.gov.uk/uksi/2017/571/schedule/1/made
Mandatory EIA: an EIA must always be carried out.

## Slide 60
Schedule 2 developments
Examples include:
Visit: https://www.legislation.gov.uk/uksi/2017/571/schedule/2/made
An EIA must be carried out if the development is likely to have a significant impact on the environment by virtue of its nature, size or location.
All Schedule 2 developments are based on thresholds set out in the regulations. A proposed development only becomes a Schedule 2 development where it exceeds these thresholds
Quarries & Opencast Mines (not included in Schedule 1)
Deep Drilling
Surface Industrial Installations
Urban Development Projects
Intensive Agriculture
Surface Storage of Fuel
Foundries & Forges
Coke Ovens
Chemical Production (not included in Schedule 1)
Manufacture of Dairy Products
Brewing
Abattoirs
Rubber production
Wastewater Treatment Plants
Holiday Villages
Golf Courses
Large Scale / Groups of Wind Turbines

## Slide 61
Screening
QUESTION: Which of these projects do you think may require an EIA, and why?
a) Solar PV farm
b) Golf course
c) Afforestation
d) Domestic extension
e) Wind farm
f) Chemical works
g) Water treatment centre
h) Dairy factory
i) New shop

## Slide 62
Screening
QUESTION: Which of these projects do you think may require an EIA, and why?
Schedule 2, 3(a) – Energy industry: Industrial installations for the production of electricity
- Depends if greater than 0.5 ha
b) Schedule 2 – Golf course
- Depends if greater than 1 ha
c) Afforestation
- 2 ha if in AONB, else 0 ha if any sensitive area
- Else 5 ha
d) Domestic extension
No
e) Schedule 2: Energy Industry
(i) The development involves the installation of more than 2 turbines; or
(ii) the hub height of any turbine or height of any other structure exceeds 15 metres.
f) Schedule 1: 6. Integrated chemical installations
g) Schedule 1: 13. Waste water treatment plants with a capacity exceeding 150,000 population
h) Schedule 2 – 7. Food industry: Manufacture of dairy products
- New floorspace exceeds 1,000 sq.m
i) Schedule 2 – 10. Infrastructure projects (b) urban development project (i) More than 1 ha
Notes: Forestry: Natural Resources Wales / Planning my forestry project https://naturalresources.wales/permits-and-permissions/tree-felling-and-other-regulations/environmental-impact-assessment-for-forestry-activity/planning-my-forestry-project/?lang=en
Schedule 1: The Town and Country Planning (Environmental Impact Assessment) Regulations 2017 (legislation.gov.uk)
https://www.legislation.gov.uk/uksi/2017/571/schedule/1/made
Schedule 2: The Town and Country Planning (Environmental Impact Assessment) Regulations 2017 (legislation.gov.uk) https://www.legislation.gov.uk/uksi/2017/571/schedule/2/made

## Slide 63
Screening Schedule 2 developments
When screening a Schedule 2 proposal for EIA, a planning authority will consider the following:
  Is the proposed development within a category set out in Schedule 2?
  a) Does it exceed the threshold set out for that category in Schedule 2?

## Slide 64
Screening Schedule 2 developments
Due to the variability and uncertainty when determining whether a proposed project could significantly impact the environment, further guidance is given using indicative thresholds.
https://assets.publishing.service.gov.uk/media/5a75aa4440f0b67f59fcea7e/eia-thresholds-table.pdf
Source: https://www.gov.uk/guidance/environmental-impact-assessment#the-indicative-thresholds

## Slide 65
In April 2015, the thresholds for which the requirement for an EIA is excluded was updated for a number of development types.
After public consultation, the aim was to reduce the ‘red tape’, time, and expense, of the process.
Development types with changes included:
Residential developments
Urban developments
Industrial developments
Environment Bulletin: Recent changes to the Environmental Impact Assessment (EIA) Thresholds – Freeths - https://www.freeths.co.uk/2015/05/06/environment-bulletin-recent-changes-to-the-environmental-impact-assessment-eia-thresholds/

## Slide 66
Screening Schedule 2 developments
When screening a Schedule 2 proposal for EIA, a planning authority will consider the following:
  b) Is it in a ‘sensitive area’? e.g. Site of Special Scientific Interest (SSSI), Special Area of Conservation (SAC), National Park, Area of Outstanding Natural Beauty (AONB) etc.
  Is it likely to have significant effects on the environment by virtue of factors such as its nature, size or location?

## Slide 67: Activity
Visit the following website: https://datamap.gov.wales/maps/new#/
Add SSSI, SAC, SPI, and AONB to your map.

## Slide 68
Screening Schedule 3 developments
When a development is identified as surpassing the thresholds identified in Schedule 2, it is then screened against Schedule 3 criteria.
Development Characteristics
Location of Development
Type of impact
Visit: https://www.legislation.gov.uk/uksi/2017/571/schedule/3/made

## Slide 69
Schedule 3: Development Characteristics
Size and design of the development.
Cumulation with other development.
The use of natural resources, in particular land, soil, water and biodiversity.
The production of waste.
Pollution and nuisances.
The risk of major accidents and/or disasters, including those caused by climate change.
The risk to human health.

## Slide 70
Wetlands, riparian areas and river mouths.
Coastal zone and marine environment.
Mountain and forest areas.
Nature reserves and parks.
European sites and other areas classified or protected under national legislation
Areas in which there has already been a failure to meet the environmental quality standards.
Densely populated areas
Landscapes and sites of historical, cultural or archaeological significance.

## Slide 71
Schedule 3: Type of Impact
The magnitude and spatial impact.
The nature of the impact.
The transboundary nature of the impact.
The intensity and complexity of the impact.
The probability of the impact.
The expected onset, duration, frequency and reversibility of the impact.
The cumulation of the impact.
The possibility of reducing the impact.

## Slide 72
Who decides if an EIA is required?
A developer can submit an ES voluntarily with a planning application in recognition that their scheme falls under Schedule 1 or exceeds Schedule 2 thresholds and would have a significant effect.
Normally, however, the local planning authority (LPA) decides if an EIA is required in consultation with the applicant in the first instance.
The LPA will likely be asked by the applicant whether EIA is necessary for a Schedule 2 submission.
The proposal will then either be ‘screened in’ or ‘screened out’ by the LPA.

## Slide 73
Who decides if an EIA is required?
Regulations require the LPA to provide, on request, a formal opinion as to whether EIA should be carried out. This is called a Screening Opinion.
They have 21 days to provide this or not longer than 90 days as agreed with the applicant.
The LPA must be satisfied that it has received sufficient information to give an opinion, bearing in mind that the failure to require an EIA for a project subsequently found to have significant environmental impacts could be subject to costly legal challenge.
Where an application is submitted for a development falling within any of the Schedule 2 descriptions without an ES, the LPA may decide if an EIA is required and should refuse to consider the planning application until an ES is submitted.

## Slide 74
Who decides if an EIA is required?
The Secretary of State has powers to intervene in cases where the LPA has failed to give an opinion on whether an EIA is needed within the prescribed period, or where the applicant disagrees with the opinion given by the LPA.
Their decision is known as a Screening Direction.
They have up to 90 days to issue a screening direction under the EIA regulations.

## Slide 75
Screening Considerations
Screening Decisions have to be made publicly available.
Not following the legislation can lead to court action.
Some applicants try to negate EIA’s by ‘salami-slicing’ the overall proposed plan into smaller chunks which are more likely to get approval (Enríquez-de-Salamanca, Á., 2016)
Notes: Enríquez-de-Salamanca, Á. (2016). Project splitting in environmental impact assessment. Impact assessment and project appraisal, 34(2), 152-159.

## Slide 76
Submitting Screening application:
Screening decision application from (gov.wales)
Notes: Enríquez-de-Salamanca, Á. (2016). Project splitting in environmental impact assessment. Impact assessment and project appraisal, 34(2), 152-159.

## Slide 77: Activity
Visit a local council planning page and see if you can find screening requests / opinions / decisions

## Slide 78
Screening examples: Dean Quarry
Screening Decisions have to be made publicly available.
Not following the legislation can lead to court action.
Dean Quarry, Cornwall:
Initial proposal – minor development around old quarry
  Deemed ‘salami-slicing’
Council screening decision – Negative opinion, EIA not required
Public appeal: Cornwall Against Dean Superquarry
Secretary of State: Positive opinion, EIA required
High court action.
Swansea Bay Tidal Lagoon plan
Proposed plan to use Dean Quarry to supply material
Proposed plan at Dean Quarry
Notes: Lizard Quarry EIA trumping: https://www.localgovernmentlawyer.co.uk/index.php?option=com_content&view=article&id=28920%3Asocial-housing-real-estate-investment-trust-eyes-p250m-stockmarket-flotation&catid=60&Itemid=28
Permission for Dean “superquarry” quashed | UK (environment-analyst.com) https://environment-analyst.com/uk/44614/permission-for-dean-superquarry-quashed
High court reading: Roskilly, R (On the Application Of) v Cornwall Council And Others [2015] EWHC 3711 (Admin) (18 December 2015) (bailii.org) http://www.bailii.org/ew/cases/EWHC/Admin/2015/3711.html

## Slide 79
Screening examples: Parc Solar Caenewydd
Parc Solar Caenewydd, Swansea:
Large solar farm proposed for north-west Swansea
90 hectares of land to power 11,500 homes
Considered a project of ‘National significance’
Screening Opinion requested from Welsh Government:
Detailed Screening report provided outlining criteria for Schedules 1 to 3
Conclusion: No EIA required
Visit: https://www.parcsolarcaenewydd.co.uk/
Proposed plan for Parc Solar Caenewydd
Notes: https://www.parcsolarcaenewydd.co.uk/
https://www.walesonline.co.uk/news/solar-panels-swansea-energy-gorseinon-24916281

## Slide 80
Screening examples: Kittle Hill Poultry Farm
Kittle Hill Poultry Farm, Kittle, Swansea:
Chicken farm that produces eggs
In 2009 a proposal was put in to replace 3 sheds to meet new standards
  This was approved as it had no significant environmental impacts (same extent of sheds)
In 2011 the 2009 proposal was updated to increase the number of hens to 400,000, which required an EIA.
  Planning permission approved.
  Controversially appeared in media over conditions of the farm in 2016: https://www.itv.com/news/wales/2016-11-15/concerns-raised-about-welfare-of-caged-hens-at-south-wales-farm
Notes: https://property.swansea.gov.uk/online-applications/applicationDetails.do?activeTab=documents&keyVal=ZZZZRTEVXB489

## Slide 81
Screening examples: Gowerton Housing development
Gowerton, Swansea:
Proposal for a residential development of circa 230 dwellings
Development within a woodland that was previously a copper works.
Screening Opinion submitted and successful
Notes: https://property.swansea.gov.uk/online-applications/files/B58E222A2252670E4FBB530197C08A92/pdf/2022_2462_SCR-COVER_LETTER-1441335.pdf

## Slide 82
EIA Key Stages: Scoping
Stage | What’s involved
1. Screening | Deciding if an EIA is required
2. Scoping | Deciding what needs to be covered in the assessment and reported in the ES
3. Assessment and Report | The ES has to include the likely significant environmental effects of the development
4. Review of Application | The ES and development application must be publicised so interested parties and the public have the opportunity to give their views on it.
5. Decision | The ES and any comments made on it must be taken into account by the competent authority before they decide whether to give consent.
6. Implementation and monitoring | The developer must commence any monitoring required by the competent authority.
Source: United Nations University (2007)
https://wedocs.unep.org/bitstream/handle/20.500.11822/26503/EIA_Training_Resource_Manual.pdf
2. Scoping | Deciding what needs to be covered in the assessment and reported in the ES
After Screening comes Scoping.
Notes: Environmental Impact Assessment - GOV.UK (www.gov.uk) - https://www.gov.uk/guidance/environmental-impact-assessment

## Slide 83: Take a break
10mins

## Slide 84
Scoping
Scoping is the stage that sets out what needs to be assessed in the EIA to help define how to approach the assessment and what information may be needed to identify the likely significant effects from the development.
You can request a scoping opinion from the EIA decision-maker. A scoping opinion sets out what the decision-maker expects to be included and excluded from the EIA. Decision-makers will consult with consultation bodies, before issuing their scoping opinion.
To request a scoping opinion, you need to provide the decision-maker with a scoping report.

## Slide 85
A scoping report must include these legal requirements:
A description of the nature and purpose of the project and the possible effects on the environment.
Plans, charts or maps sufficient to identify the location of the activities to be carried out.
The structure of a scoping report should be the same as the intended final Environmental Statement.
the purpose is in effect to clarify what aspects / elements will need to be considered in the Environmental Impact Assessment, and therefore the topics / headings will be the same.
What to include in a Scoping report

## Slide 86
An Environmental Impact Assessment (EIA) needs to include:
Description of project, location and purpose, including construction, operation, maintenance, and decommissioning. ­Include ancillary works, such as any cable corridors and temporary structures
What to include in a Scoping report

## Slide 87
What to include in a Scoping report
An Environmental Impact Assessment (EIA) needs to include:
Description of reasonable alternatives
Current state of the environment (baseline)
Description of likely significant effects on these receptor topics:
  ­Population and human health
  ­Biodiversity, including protected species and habitats
  ­Land, soil, water, air and climate
  ­Material assets, cultural heritage and landscape
  ­In-combination effects

## Slide 88
What to include in a Scoping report
An Environmental Impact Assessment (EIA) needs to include:
Description of direct, indirect, secondary, cumulative, transboundary, short, medium and long-term, permanent and temporary, positive and negative effects.
Description of evidence and methods to be used, including any gaps or uncertainties
Description of measures to avoid, reduce and mitigate adverse effects

## Slide 89
An Environmental Impact Assessment (EIA) needs to include:
Monitoring measures
Risk of major accidents or disasters, such as extreme weather events.
EC guidance – Scoping Checklist:
Scoping Checklist
https://ec.europa.eu/environment/archives/eia/eia-guidelines/scoping_checklist.pdf
First part of the European Commission guidance Scoping Checklist
What to include in a Scoping report

## Slide 90
30/10/2023
Stage | What’s involved
1. Screening | Deciding if an EIA is required
2. Scoping | Deciding what needs to be covered in the assessment and reported in the ES
3. Assessment and Report | The ES has to include the likely significant environmental effects of the development
4. Review of Application | The ES and development application must be publicised so interested parties and the public have the opportunity to give their views on it.
5. Decision | The ES and any comments made on it must be taken into account by the competent authority before they decide whether to give consent.
6. Implementation and monitoring | The developer must commence any monitoring required by the competent authority.
Source: United Nations University (2007)
https://wedocs.unep.org/bitstream/handle/20.500.11822/26503/EIA_Training_Resource_Manual.pdf
3. Assessment and Report | The ES has to include the likely significant environmental effects of the development
Having determined the need for an EIA, a full assessment must be conducted, and the Environmental Statement (ES), or Environmental Impact Statement (EIS), produced.
Notes: Environmental Impact Assessment - GOV.UK (www.gov.uk) - https://www.gov.uk/guidance/environmental-impact-assessment

## Slide 91
Environmental Statement
The applicant is responsible for the preparation of the Environmental Statement.
In order to ensure completeness and quality, the applicant must ensure that it is prepared by competent experts.
It must be accompanied by a statement from the developer outlining the relevant expertise, or qualifications of such experts.

## Slide 92
What to include in an Environmental Statement
TBC
Schedule 4 provides guidance on what to include in the Environmental Statement
While the contents are stipulated, the specific methods and techniques are not, and therefore are left to the developer to determine (Glasson et al., 2012).
The reasoning is that each proposed development will be unique in setting and availability of information to the area.

## Slide 93
What to include in an Environmental Statement
The Environmental Statement must contain the following information:
A description of the development, including in particular:
  A description of the location of the development;
  A description of the physical characteristics of the whole development, including, where relevant, requisite demolition works, and the land-use requirements during the construction and operational phases;
  A description of the main characteristics of the operational phase of the development (in particular any production process), for instance, energy demand and energy used, nature and quantity of the materials and natural resources (including water, land, soil and biodiversity) used;
  An estimate, by type and quantity, of expected residues and emissions (such as water, air, soil and subsoil pollution, noise, vibration, light, heat, radiation and quantities and types of waste produced during the construction and operation phases.
Description

## Slide 94
What to include in an Environmental Statement
The Environmental Statement must contain the following information:
A description of the reasonable alternatives (for example in terms of development design, technology, location, size and scale) studied by the developer, which are relevant to the proposed project and its specific characteristics, and an indication of the main reasons for selecting the chosen option, including a comparison of the environmental effects.
Reasonable Alternatives

## Slide 95
What to include in an Environmental Statement
The Environmental Statement must contain the following information:
A description of the relevant aspects of the current state of the environment (baseline scenario) and an outline of the likely evolution thereof without implementation of the development as far as natural changes from the baseline scenario can be assessed with reasonable effort on the basis of the availability of environmental information and scientific knowledge.
Baseline

## Slide 96
What to include in an Environmental Statement
A description of the factors likely to be significantly affected by the development: population, human health, biodiversity (for example fauna and flora), land (for example land take), soil (for example organic matter, erosion, compaction, sealing), water (for example hydromorphological changes, quantity and quality), air, climate (for example greenhouse gas emissions, impacts relevant to adaptation), material assets, cultural heritage, including architectural and archaeological aspects, and landscape.
Factors affected

## Slide 97
What to include in an Environmental Statement
The Environmental Statement must contain the following information:
A description of the likely significant effects of the development on the environment resulting from, amongst other things:
  The construction and existence of the development, including, where relevant, demolition works;
  The use of natural resources, in particular land, soil, water and biodiversity, considering as far as possible the sustainable availability of these resources;
  The emission of pollutants, noise, vibration, light, heat and radiation, the creation of nuisances, and the disposal and recovery of waste;
  the risks to human health, cultural heritage or the environment (for example due to accidents or disasters)
Significant effects

## Slide 98
What to include in an Environmental Statement
The Environmental Statement must contain the following information:
A description of the likely significant effects of the development on the environment resulting from, amongst other things:
  The cumulation of effects with other existing and/or approved projects, accounting for any existing environmental problems relating to areas of particular environmental importance likely to be affected or the use of natural resources;
  The impact of the project on climate (for example the nature and magnitude of greenhouse gas emissions) and the vulnerability of the project to climate change
  The technologies and the substances used.
Effects on environment

## Slide 99
What to include in an Environmental Statement
The description of the likely significant effects on the factors specified should cover the direct effects and any indirect, secondary, cumulative, transboundary, short-term, medium-term and long-term, permanent and temporary, positive and negative effects of the development.
Indirect / transboundary

## Slide 100
What to include in an Environmental Statement
The Environmental Statement must contain the following information:
A description of the forecasting methods or evidence, used to identify and assess the significant effects on the environment, including details of difficulties (for example technical deficiencies or lack of knowledge) encountered compiling the required information and the main uncertainties involved.
Evidence?

## Slide 101
What to include in an Environmental Statement
A description of the expected significant adverse effects of the development on the environment deriving from the vulnerability of the development to risks of major accidents and/or disasters which are relevant to the project concerned.
Where appropriate, this description should include measures envisaged to prevent or mitigate the significant adverse effects of such events on the environment and details of the preparedness for and proposed response to such emergencies.

## Slide 102
What to include in an Environmental Statement
The Environmental Statement must contain the following information:
A non-technical summary of the information
A reference list detailing the sources used for the descriptions and assessments included in the environmental statement.

## Slide 103: Activity
Visit the following website: Blue Gem - Erebus - Virtual Exhibition (3dwtech.co.uk)
Visit the virtual Erebus exhibition.

## Slide 104: Activity
Is the virtual consultation useful?
What key information is provided?
How have they made this content accessible?
How did they assess impacts?
What key legislation is relevant here?

## Slide 105: Take a break
10mins

## Slide 106
EIA Key Stages: Review of Application
Stage | What’s involved
1. Screening | Deciding if an EIA is required
2. Scoping | Deciding what needs to be covered in the assessment and reported in the ES
3. Assessment and Report | The ES has to include the likely significant environmental effects of the development
4. Review of Application | The ES and development application must be publicised so interested parties and the public have the opportunity to give their views on it.
5. Decision | The ES and any comments made on it must be taken into account by the competent authority before they decide whether to give consent.
6. Implementation and monitoring | The developer must commence any monitoring required by the competent authority.
Source: United Nations University (2007)
https://wedocs.unep.org/bitstream/handle/20.500.11822/26503/EIA_Training_Resource_Manual.pdf
Having determined the need for an EIA, a full assessment must be conducted, and the Environmental Statement (ES), or Environmental Impact Statement (EIS), produced.
4. Review of Application | The ES and development application must be publicised so interested parties and the public have the opportunity to give their views on it.
Notes: Environmental Impact Assessment - GOV.UK (www.gov.uk) - https://www.gov.uk/guidance/environmental-impact-assessment

## Slide 107
Application submission
When an applicant intends to submit a planning application with an Environmental Statement, they should send the local planning authority (LPA) all the documents which must normally accompany a planning application as well as the Environmental Statement.
In addition, the applicant must also submit:
One further copy of the Environmental Statement for onward transmission by the local planning authority to the Secretary of State;
A note of the name of everybody to whom the applicant has already sent, or intends to send, a copy of the Environmental Statement and the date on which the Environmental Statement was so served, where relevant;
Sufficient further copies of the Environmental Statement as are needed to allow the local planning authority to send one to each of the consultation bodies who have not received a copy directly from the applicant.

## Slide 108
Publicity
The planning application and the Environmental Statement should be publicised according to the Town and Country Planning legislation.
The legislation contains the appropriate form for the notices to be published in the local press and posted on site, which must:
  State that a copy of the Environmental Statement is included in the documents which will be open to inspection by the public and give the address where the documents can be inspected free of charge;
  Give an address in the locality where copies of the Environmental Statement may be obtained;
  State that a copy may be obtained at that address while stocks last and the amount of any charge to be made for supplying a copy;
  Give details of a website maintained by or on behalf of the authority on which the environmental statement and the other documents have been made available;
  State the latest date by which any written representations about the application should be made to the local planning authority (being a date not less than 30 days later than the date on which the notice is published).

## Slide 109
EIA Key Stages: Review of Application
Stage | What’s involved
1. Screening | Deciding if an EIA is required
2. Scoping | Deciding what needs to be covered in the assessment and reported in the ES
3. Assessment and Report | The ES has to include the likely significant environmental effects of the development
4. Review of Application | The ES and development application must be publicised so interested parties and the public have the opportunity to give their views on it.
5. Decision | The ES and any comments made on it must be taken into account by the competent authority before they decide whether to give consent.
6. Implementation and monitoring | The developer must commence any monitoring required by the competent authority.
Source: United Nations University (2007)
https://wedocs.unep.org/bitstream/handle/20.500.11822/26503/EIA_Training_Resource_Manual.pdf
Having determined the need for an EIA, a full assessment must be conducted, and the Environmental Statement (ES), or Environmental Impact Statement (EIS), produced.
4. Review of Application | The ES and development application must be publicised so interested parties and the public have the opportunity to give their views on it.
Notes: Environmental Impact Assessment - GOV.UK (www.gov.uk) - https://www.gov.uk/guidance/environmental-impact-assessment

## Slide 110: Activity
EIA review is a key part of the EIA process. Using the handout and presentation provided (Guidelines for reviewing technical reports), write a short plan on how you would critique an EIA document.
Bullet points on key considerations?

## Slide 111
A number of core values and guiding principles for the practice of EIA have been identified:
Sustainability – EIA process result in environmental safeguards as it is anticipatory and preventive rather than curative (aids precautionary and preventive principle).
Integrity – the process will conform to agreed standards and be performed by multidisciplinary teams.
Utility – the process provides balanced, credible information for decision- making.
EIA Core Values
ACBA 7004

## Slide 112
Key Guiding Principles for EIA
Continuity - as an integral part of planning, designing and implementation cycle of and development initiative, EIA should run continuously and throughout project cycle.
Participatory - EIA provides a framework for stakeholders and all interested parties to participate in decision-making.
Transparency – EIA facilitates dialogue, predictions and responses in a forum where proponents, decision-makers, experts and the public interact in an open and accessible way in considering the potential impacts of a project on local community, natural resources and environmental quality. All assessment decisions and their basis, should be open and accessible.
Credibility – assessments are undertaken with professionalism and objectivity, using multidisciplinary skills.
Certainty – the process and timing of assessment must be agreed in advance and followed by all participants.
ACBA 7004

## Slide 113
Cost-effectiveness – the assessment process and its outcomes will ensure environmental protection at the least cost to society. It ensures fair and equitable distribution of project costs and benefit. As a minimum, local people in a project area must not be worse-off than they were before a project was implemented.
Flexibility – the assessment should be able to adapt to deal efficiently and effectively with any proposal or decision- making situation.
Practicality – the information and outputs are readily usable for planning, designing and in decision-making.
Accountability – decision-makers are responsible to all parties for decision and actions under the assessment process.
ACBA 7004

## Slide 114: EIA Good practice

## Slide 115
Reminder: Costs and Benefits of Using EIA
Benefits
There are both direct and indirect benefits of EIA.
More environmentally sustainable design or improvements in the design.
Better compliance with environmental standards.
Savings in capital and operating cost.
Reduces time and cost of approvals of development application.
Resolves conflict, solves problems and thus increase project acceptability.
Improves institutional co-ordination and inter-agency co-operation.
Improves accountability and transparency in planning and decision-making
For business and governments - EIA - important planning and management tool.
Environmental assessments good > good management > good business

## Slide 116: Limitations of EIA
EIA is also a way of ensuring that environmental factors are considered in decision-making process along with the traditional economic and technical factors.
Importantly EIA requires the scientific (technical) and value issues to be dealt with in a single assessment process.
This helps in the proper consideration of all advantages and disadvantages of a proposal.
Environmental considerations may, therefore, be set aside in favour of what are felt to be more important considerations.
Alternatively, predicted adverse effects on the environment might lead to strict conditions being imposed to avoid these effects or remedy any adverse effects, or perhaps lead to the complete abandonment of a proposal.

## Slide 117: Limitations of EIA
However, it is most important to recognise that EIA cannot be regarded as a means of introducing an environmental “veto” power into administrative decision-making processes.
Decisions that are unsatisfactory from an environmental point of view can still be made, but with full knowledge of the environmental consequences.
The final decision about a proposal depends upon the likely severity of the adverse effects, balanced against other expected benefits.

## Slide 118: Limitations of EIA
In other words, EIA is an administrative process that identifies the potential environmental effects of undertaking a proposal, and presents these environmental effects alongside the other advantages and disadvantages of the proposal to the decision-makers.
In the vast majority of EIA procedures this means that the outcome of the EIA process provides advice to the decision-makers – it does not provide a final decision.
So, by itself, the EIA procedures cannot be expected to stop a proposal – although this is an outcome that some members of the general community and environment groups may expect.

## Slide 119: Principles of EIA administration and practice
EIA is one of a number of policy tools that are used to evaluate project proposals.
It is also a relatively recent development when compared to use of economic appraisal methods.
A number of factors led to the introduction of EIA in different countries, including public concern about the quality of the environment and the increasing effects of new technologies and ever-larger development schemes.
In addition, then available economic appraisal techniques, such as benefit cost analysis, did not take account of the environmental and social impacts of major projects.
Today, EIA is applied in more than 100 countries, and by all development banks and most international aid agencies.
EIA has also evolved significantly, driven by improvements in law, procedure and methodology.

## Slide 120: Principles of EIA administration and practice
To date, EIA has been applied primarily at the project-level.
This ‘first generation’ process is now complemented by SEA (Strategic Environmental Assessment) of policies, plans and programmes, and both EIA and SEA are being adapted to bring a greater measure of ‘sustainability assurance’ to development decision making.
These trends have brought new perspectives on what constitutes EIA good practice and effective performance.

## Slide 121: EIA Legislation

## Slide 122: Legislation
The process of Environmental Impact Assessment in the context of town and country planning in England is governed by the Town and Country Planning (Environmental Impact Assessment) Regulations 2017 (the ‘2017 Regulations’). These regulations apply to development which is given planning permission under Part III of the Town and Country Planning Act 1990 (Gov.uk, 2018)

## Slide 123: Background
Requirements
An EIA is required from developers where projects may have significant affects on the environment.
Environmental impact assessments are designed to give due weight to issues of sustainability - environmental, economic and social factors, in relation to planning.
  (Department for Communities and Local Government, 2016)

## Slide 124: Background
Strategic Environmental Assessment (SEA)
  1970s -Environmental impact assessments to be carried out at the levels of policy, plan/program and project. Its application was to be for use in prevention of environmental detriment and integration of environmental aspects into the decision making process (Feldmann, 1998).
  EU Advice
    Overview
    http://ec.europa.eu/environment/eia/eia-support.htm

## Slide 125: Legislation affecting development
Town and Country Planning Regulations 1988 Act 1990.
Town and Country Planning Order 1995
The Environmental Impact Assessment Regulations 1999 (part of TCPR)
The Environmental Impact Assessment Regulations 2002 (dealing with uncultivated and semi-natural areas).
The Town and Country Planning (Environmental Impact Assessment) Regulations 2017 National Archive 2017

## Slide 126: Other Legislation
Conservation of Natural Habitats and of Wild Fauna and Flora Regulations 1994 (commonly Habitats and Species Directive)
Wildlife and Countryside Act 1981
Countryside and Rights of Way (CRoW) Act 2000
Protection of Badgers Act 1992
Hedgerow Regulations 1997
Tree Preservation Orders.
SEA Council Directive 2001/42/EC of 27 June 2001 on the assessment of the effects of certain plans and programmes on the environment (SEA Directive) etc Dutch case (10 mins)

## Slide 127: Difference to LCA (Crawley, 2015)

## Slide 128: Developing a Site
Be aware of what is present on the site and plan around it.
Environmental Assessment - broad-based term to describe the process of assessing or surveying land and the likely impacts of any development. From simple ecological survey looking at the presence or absence of a particular protected species through to a full-blown Environmental Impact Assessment survey.

## Slide 129: Environmental Impact Assessments (EIAs)
Used to:
Assess the potential impacts of an action such as the erection of a new building.
Look at the present situation and predict what changes the development may cause on the surrounding environment.
Provide an umbrella approach to facilitate the formulation of environmental statements and subsequent management strategies.

## Slide 130: Process 1
Project screening Not all development projects require EIA. Project screening will help identify the ones that actually do..
Scoping The process of scoping helps determine the coverage or 'scope' of the EIA.
Baseline data collection A brief explanation on the concept of baseline data collection and its purposes.
Identification of environmental impacts Various types of environmental impacts of development projects both beneficial and adverse.
Impact prediction comparison of alternatives and determination of significance considerations for impact prediction, uncertainties in impact prediction and comparison of alternatives for impact prediction.

## Slide 131: Process 2
Mitigation measures Described briefly under this section are the concept and objectives, types and interesting points, of mitigation measures.
Public consultation and participation Public participation is a necessary component of the EIA. "Who are the public?", "How to involve them?", and "What are the benefits/disbenefits?" The answers can be found under this section.
Environmental monitoring As one of the most important aspects of EIA, "Environmental Monitoring" is defined here along with explanations on monitoring principles, types and institutional aspects.
Environmental auditing You will find under this section, the various types of Environmental Auditing and when it should be carried out during the EIA.

## Slide 132: Critique of EIA Process
Benefits | Flaws
Provides systematic methods of impact assessment | Time-consuming
Estimates the cost/benefit trade-off of alternative actions | Costly
Facilitates the public participation | Little public participation in actual implementation
Provides an effective mechanism for coordination environmental integration negotiations feed back | Unavailability for reliable data (mostly in developing countries)
Top-level decision making | Too focused on scientific analysis (sometimes)
Triggers an institutional building | Poor presentation of EIA report (bulky volumes, scientific explanation, difficult to understand)
Achieve a balance between the impact of developmental and environmental concern | Compliance monitoring after EIA is seldom carried out
Notes: http://www.unescap.org/drpad/vc/orientation/m8_1.htm

## Slide 133
Summary
This week we have covered the definition and process of EIA
We have examined the Key Stages of an EIA
What Screening is:
  Schedules 1 and 2 projects
  Schedule 3 project considerations
Had a look at some case study examples which ranged in success and quality.
We have looked at the Scoping process and visited a virtual consultation for local wind farm development.

## Slide 134: Activity
On your laptops, create a new folder:
Conduct a literature search for your chosen EIA.
Make sub-folders:
Official Documentation
Feedback
Media

## Slide 135
Activities for next week:
Read and review: Government outlines plans to replace ‘over-complicated’ EIA regime (endsreport.com)
New legislation proposes radical changes, replacing EIA | UK (environment-analyst.com)
(2) Divergence Series | Divergence in environmental policy post-Brexit – YouTube
Additional suggested readings in Moodle (Week 2)

## Slide 136: References
City and County of Swansea (2008a) Unitary Development Plans: Post Enquiry Modifications. April 2008. p.i. City and County of Swansea. UK
City and County of Swansea (nd) Application Search
Accessed 27/07/08 http://www.swansea.gov.uk/index.cfm?articleid=4681)
Christensen, J. (2004) The Uneasy Chair: Why Good Governance Matters for Conservation. Conservation In Practice. Summer 2004/Vol 5 No 3
Countryside Council for Wales (2008) Personal Correspondence. 01/08/2008
Department for Communities and Local Government (2006) Environmental Impact Assessment: Guide to procedures. Thomas Telford. UK. Accessed 16/08/2008 http://www.communities.gov.uk/documents/planningandbuilding/pdf/157989.pdf
Evening Post (2008a) £15M Golf Plan Out of Bunker: Readers Comments. Accessed 27/07/2008 http://www.thisissouthwales.co.uk/displayNode.jsp?nodeId=161389&command=displayContent&sourceNode=161372&contentPK=20948800&moduleName=InternalSearch&formname=sidebarsearch

## Slide 137: References
Feldmann, L. (1998) The European Commission's Proposal for a Strategic Environmental Assessment Directive: Expanding the Scope of Environmental Assessment in Europe. Elselvia Science Inc
Glasson, J. Therivel, R. & Chadwick, A. (1999) Introduction to Environmental Impact Assessment. P. 401-402, p.423 fig 13.5. 2nd Edition. Principles and procedures, practice and prospects. UCL Press. London. UK
Holder, J. (2007) The prospects for ecological impact assessment. Edited by McGillivray, D. & Holder, J. (2007) Taking Stock of Environmental Assessment: Law, Policy and Practice. Roultledge Cavandish.
National Assembly for Wales (2005) Call in Section. Planning Division. Cardiff. UK
Newig J, Vob, J & Monstadt J (2007). Editorial Governance for Sustainable Development in the Face of Ambivalence, Uncertainty and Distributed Power: an Introduction. Journal of Environmental Policy & Planning Vol. 9, Nos. 3-4, September–December 2007, 185–192

## Slide 138: References
Soltys Brewster Consulting (2007) Royal Fern Development Project: Environmental Statement. NTS p.3 C8 p.5 NTS, p 2 (Not Published)
Sports Council for Wales (2004) Sport Update: Golf in Wales 2004. Research and Evaluation Section. Cardiff.
Surgess, P (2003) Royal fern Golf Course. Swansea Winter Ecological Surveys. (Not Published)
Stewart, B (2004) Ecological Surveys: Phase 2. Dillwyn Production Ltd. (Not Published)

## Slide 139: References
Tanner, R. & Gange, A. (2005) Effects of golf courses on local biodiversity. Landscape and Urban Planning 71 (2005) 137–146. p.1 Science Direct. Elsevier
Von Borgstede, C & Lundqvist, L. (2006) Organizational Culture, Professional Role Conceptions and Local Swedish Decision-makers’ Views on Climate Policy Instruments. Journal of Environmental Policy & Planning Vol. 8, No. 4, December 2006, 279–292.
Welsh Assembly Government (2008) People, Places, Future. The Wales Spatial Plan 2008 Update. p.30 Welsh Assembly Government. UK
Welsh Office (1999) Welsh Office Circular: Environmental Impact assessment. The Stationary Office. UK
Yakovleva, N (2007) Measuring the Sustainability of the Food System. Journal of Environmental Policy & Planning Vol. 9, No. 1, March 2007, 1–3

## Slide 140: Best practice for EIA
ACBA 7004

## Slide 141
Key Guiding Principles for EIA
Continuity - as an integral part of planning, designing and implementation cycle of and development initiative, EIA should run continuously and throughout project cycle.
Participatory - EIA provides a framework for stakeholders and all interested parties to participate in decision-making.
Transparency – EIA facilitates dialogue, predictions and responses in a forum where proponents, decision-makers, experts and the public interact in an open and accessible way in considering the potential impacts of a project on local community, natural resources and environmental quality. All assessment decisions and their basis, should be open and accessible.
Credibility – assessments are undertaken with professionalism and objectivity, using multidisciplinary skills.
Certainty – the process and timing of assessment must be agreed in advance and followed by all participants.
ACBA 7004

## Slide 142
Cost-effectiveness – the assessment process and its outcomes will ensure environmental protection at the least cost to society. It ensures fair and equitable distribution of project costs and benefit. As a minimum, local people in a project area must not be worse-off than they were before a project was implemented.
Flexibility – the assessment should be able to adapt to deal efficiently and effectively with any proposal or decision- making situation.
Practicality – the information and outputs are readily usable for planning, designing and in decision-making.
Accountability – decision-makers are responsible to all parties for decision and actions under the assessment process.
ACBA 7004

## Slide 143: EIA—Three core values
integrity - the EIA process will conform to agreed standards
utility - the EIA process will provide balanced, credible information for decision-making
sustainability - the EIA process will result in environmental safeguards
Source: Sadler, 1996
ACBA 7004

## Slide 144: EIA — guiding principles
The EIA process should be:
purposive – meeting its aims and objectives
focused – concentrating on the effects that matter
adaptive – responding to issues and realities
participative – fully involving the public
transparent – clear and easily understood
Source: Sadler, 1996; IAIA/IEMA 1999
ACBA 7004

## Slide 145: EIA — guiding principles (continued)
rigorous – employing ‘best practicable’ methodology
practical – establishing mitigation measures that work
credible – carried out with objectivity and professionalism
efficient – imposing least cost burden on proponents
Source: Sadler, 1996; IAIA/IEMA 1999
ACBA 7004

## Slide 146: Key operating principles of good EIA practice
EIA should:
be applied to all proposals with significant impacts
begin early in the project cycle
address relevant environmental, social and health impacts
identify and take account of public views
result in a statement of impacts and mitigation measures
facilitate informed decision making and condition setting
Source: Sadler, 1996
ACBA 7004