## Slide 1
Module Name : Electronics I
Module Code : ACDB5002
Lecture : 2
Topic : PN Junction & Zener Diodes
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk

## Slide 2
At the end of this lecture, the students can be able to understand the concepts of
Power Supply Blocks.
  PN junction
  PN junction diode
  Zener Diode
PN Junction & Zener Diodes
Learning Outcome:

## Slide 3
Basic Blocks of Power Supply
PN Junction & Zener Diodes

## Slide 4: PN junction
A junction formed between a sample of P type semiconductor and N type semiconductor is known as PN junction (or) Junction diode.
It has two electrodes
P region named as Anode
N region Named as Cathode
PN Junction & Zener Diodes

## Slide 5: PN - junction
PN Junction & Zener Diodes

## Slide 6: PN junction – Open circuited
When no supply is given to the PN junction diode.
PN Junction & Zener Diodes

## Slide 7: There are two forces regulating the PN junction:
Drift current
– Conduction of current happens due to drifting of majority charge particles.
Diffusion current
– conduction of current due to minority charge particles.
PN Junction & Zener Diodes

## Slide 8: PN junction – Biasing
Voltage can be applied in PN junction diode in two ways to control the width of the depletion region. They are
Forward biasing
Reverse Biasing
When an external voltage is applied to the PN junction in such a way that it cancels the potential barrier and permits the current flow, it is called Biasing
PN Junction & Zener Diodes

## Slide 9: PN junction – Forward biased
In Forward Bias condition, we work with drift and prevent diffusion
Hence, Depletion Region Shrinks and conductivity increases
PN Junction & Zener Diodes

## Slide 10: PN junction – Forward biased
Connecting, Positive of battery to P region and Negative of battery to N region is called Forward biasing.
This establishes an electric field opposite to potential barrier, So the potential barrier width decreases.
0.3V for Germanium and 0.7V for Silicon, is sufficient to eliminate the barrier potential, thus junction resistance becomes zero.
PN Junction & Zener Diodes

## Slide 11: PN junction – Reverse biased
In Reverse Bias condition, we work with diffusion and prevent drift.
Hence, Depletion Region widens, and conductivity decreased
PN Junction & Zener Diodes

## Slide 12: Diode Characteristics
PN Junction & Zener Diodes
PN – Junction Diode takes a certain amount of voltage in forward bias to collapse the depletion region and allow current flow.
This is the activation voltage and is generally ≈ 0.6V.
In reverse bias, the depletion region is expanded and current cannot flow.

## Slide 13
PN Junction & Zener Diodes

## Slide 14: Diode resistance
Ideal diode has zero resistance in forward biased and infinite resistance in reverse biased condition.
Diode acts as a switch.
PN Junction & Zener Diodes

## Slide 15: PN junction diode
Applications:
Used as switch.
Used in rectifier circuits.
Detector in RF circuits.
PN Junction & Zener Diodes

## Slide 16: Zener diode
A Zener diode is a type of PN-junction diode that, allows current to flow not only from its anode to its cathode, but also in the reverse direction when it reaches the "Zener voltage".
Zener diodes have a highly doped PN junction.
Also, normal diodes are not designed to operate in the breakdown region, but Zener diodes can reliably operate in this region.
PN Junction & Zener Diodes

## Slide 17
Zener effect:
Zener effect is a type of electrical breakdown.
It occurs in a reverse biased PN junction diode, where many free minority carriers suddenly increases the reverse current.
Diode which exhibits Zener effect is called Zener diode.
PN Junction & Zener Diodes

## Slide 18: VI Characteristics of Zener diode
PN Junction & Zener Diodes

## Slide 19: References
PN Junction & Zener Diodes
[1] P. Horowitz and W. Hill, The Art of Electronics, 3rd ed. Cambridge, UK: Cambridge University Press, 2015.
[2] "PN Junction Diode and Its Biasing Conditions," DDEScholar, [Online]. Available: https://ddescholar.acemap.info/field/2014194504.
[3] "PN Junction Diode Characteristics and Biasing," Electronics Tutorials, [Online]. Available: https://www.electronics-tutorials.ws/diode/diode_7.html.
[4] "P-N Junction Introduction," Physics and Radio Electronics, [Online]. Available: https://www.physics-and-radio-electronics.com/electronic-devices-and-circuits/semiconductor-diodes/p-n-junction-introduction.html.

## Slide 20
Thank You