## Slide 1
SUSTAINABLE PROCESSES
LIFE CYCLE COST
Juan A Ferriz-Papi
2018-2019

## Slide 2
LIFE CYCLE COST
LIFE CYCLE COST
Method for assessing the total cost of facility ownership
Consideration of costs of acquiring, owning and disposing of a building or building system
Different alternatives to fulfil the same performance
Assessment of initial costs, operating, maintenance and end of life costs
Comparison of costs at different stages of the life cycle
Choose the most cost-effective option

## Slide 3
LIFE CYCLE COST
LIFE CYCLE COST
Other techniques for economic evaluation:
Net savings (or net benefits)
Savings-to-investment ratio
Internal Rate of Return
Payback period

## Slide 4
LIFE CYCLE COST
LIFE CYCLE COST
Very different costs associated. Classification in categories:
Initial costs
Energy and water
Operation, maintenance and repair
Replacement costs
Residual value
Other costs
COSTS

## Slide 5
LIFE CYCLE COST
LIFE CYCLE COST
Initial Costs
Land acquisition
Construction
Installation
Purchase/procurement
Energy and Water
Energy usage (occupancy, building use, external consumptions, etc.)
Energy price and projections
Water costs (water supply and water discharge)
COSTS

## Slide 6
LIFE CYCLE COST
LIFE CYCLE COST
Operation, maintenance and repair
Historical data
Specifications from supplier
Statistical analysis
Waste management
Replacement costs and residual value
Other costs
Finance charges and taxes
Non-monetary benefits or costs (aesthetics, historic preservation, Security, safety, etc.)
COSTS

## Slide 7
LIFE CYCLE COST
LIFE CYCLE COST
Can you calculate the LCC of a heating system boiler for one building?
What costs should be considered?
QUESTIONS
Do you think the money we invest today has the same value 10 years later?
What risks/uncertainties can be identified in this procedure?

## Slide 8
LIFE CYCLE COST
LIFE CYCLE COST
Compare cash-flows incurred at different times during the life cycle.
Convert them to present values
Discount rate - Interest rate used– reflects the investor’s opportunity cost of money over time
PRESENT-VALUE ANALYSIS
F: Future value
P: Present value
i: discount rate (per year)
n: number of years

## Slide 9
LIFE CYCLE COST
LIFE CYCLE COST
Different scenarios because different variables can change:
Change of value/cost, market variation
Accident
Longer lifespan
Deflaction
Etc.
We need to evaluate uncertainty
Deterministic techniques
Probabilistic techniques
UNCERTAINTY ASSESSMENT IN LIFE-CYCLE COST ANALYSIS

## Slide 10
LIFE CYCLE COST
LIFE CYCLE COST
SENSITIVITY ANALYSIS
Identification of critical parameters that can take the greatest impact
Testing different scenarios to answer “what if” questions
Simply change the value of each input up and down, holding all others constant, and recalculate the economic measure to be tested.
UNCERTAINTY ASSESSMENT IN LIFE-CYCLE COST ANALYSIS

## Slide 11
LIFE CYCLE COST
LIFE CYCLE COST
BREAK-EVEN ANALYSIS
maximum cost of an input that will allow the project to still break even, or conversely, what minimum benefit a project can produce and still cover the cost of the investment.
UNCERTAINTY ASSESSMENT IN LIFE-CYCLE COST ANALYSIS

## Slide 12
LIFE CYCLE COST

## Slide 13
LIFE CYCLE COST
BS ISO 15686-5:2017
Performance Requirements

## Slide 14
DEFINITIONS (BS ISO 15686-5:2017)
LIFE CYCLE COST
LIFE CYCLE COST
Whole-life cost
All significant and relevant initial and future costs and benefits of an asset, throughout its life cycle, while fulfilling the performance requirements.
Life Cycle Cost
Cost of an asset or its parts throughout its life cyle, while fulfilling the performance requirements.
Operation cost
Costs incurred in running and managing the facility or built environment, including administration support services.
Maintenance cost
Total of necessarily incurred labour, material and other related costs incurred to retain a building or its parts in a state in which it can perform its required functions.

## Slide 15
WLC and LCC elements
LIFE CYCLE COST
BS ISO 15686-5:2017

## Slide 16
Typical decisions informed by Life Cycle Cost Analysis (LCCA)
LIFE CYCLE COST
BS ISO 15686-5:2017
Evaluation of different investment scenarios
Choices between alternative designs
Choices among alternative components
Comparison and/or benchmarking analysis of previous decisions
Estimation of future costs for budgetary purposes or investment approval

## Slide 17
Analysis at different stages of the life cycle
LIFE CYCLE COST
BS ISO 15686-5:2017

## Slide 18
Different levels of analysis at different stages of the life cycle
LIFE CYCLE COST
BS ISO 15686-5:2017

## Slide 19
LIFE CYCLE COST
BS ISO 15686-5:2017
Classification of costs
Typical scope of costs

## Slide 20
LIFE CYCLE COST
BS ISO 15686-5:2017

## Slide 21
LIFE CYCLE COST
BS ISO 15686-5:2017

## Slide 22
LIFE CYCLE COST
BS ISO 15686-5:2017