## Slide 1
Cameron Dickson
Managing a Professional Engineering Project & Engineering Design

## Slide 2: Project Introduction
Our brand AB Connectors which is a Sub Group under the TT Electronics Company Pola Power section. This section specialises in delivering highly complex electronic connectors and interconnection systems for aerospace & defence, industrial and rail applications.
The project that would be implemented in the company was set up to save the company money, time and overall making the company more efficient.
The Project that was chosen was implementing a Knurling Tool into our machine shop. This knurling tool was put in place to add cost saving, time saving and capacity to our machine shop. The problem was due to our capacity increasing and therefore we will be losing money in the future as the current process is not suitable. The current process is done with a slot milling tool to create serrations.

## Slide 3: Initial Ideas – Potting Bench
My Second Project idea was the Potting Bench. The potting bench is used to fill up and protect a PCB board. The connector mates with opposite mater.
This then holds the connector still and straight to be able to fill up with Black Epoxy Potting Fluid. This potting fluid is used to protect the PCB board within the connector.
The problem that is occurring with the bench is that it is very messy and nothing supports the cable straight meaning the compound may fill up unevenly in the connector.
My solution is to make a new bench with extra features to support the cable and wires better.

## Slide 4: Initial Ideas – Serrations Project
My final Idea was to overcome the serrations in Machine Shop. This project would consist of looking into a Knurling tool and other solutions to run on our Emco machines.
We will need to look into this project to find out how we could improve this process to increase efficiency, capacity and save the company money. The current machining method for these serrations is using a slot milling cutter which cuts one tooth at a time. The connectors that have serrations on are called “Heat Shrink Adaptor Shells”.
The initial problem that started this investigation was due to the fact that the capacity of these Heat Shrink Adaptor Shells was increasing by a very large amount. Due to the amount of time it takes to machine one tooth. The capacity and efficiency we could produce these parts at meant we would start to lose profit on these connectors.

## Slide 5: Research
I conducted research on my project idea to better the method of the serrations.
http://www.atmmt.com/ - ATM tooling mainly helps and supplies products to people with knurling problems. They provide knurling tools, tool holder and other types of knurls. I got into contact with someone from there company. I explained to them my problem and my possible solution ideas. They took these into account and gave me some help and a quote for 2 possible solutions I was looking into. One solution being a knurling tool. below I added a snippet of our emails which shows him explaining and showing me an option of a product they sell.

## Slide 6: Research
https://www.phorn.co.uk/ - I researched into Horn and looked at the solutions they could help me with. I spoke with a sales representative of Horn. I was able to get a lot of information about a solution I could have to put the serrations on the product. This idea was polygon milling with an end tooth cutter. They also had a video that they sent of the milling in action with a connector similar to ours.
Other websites I looked into:
http://www.ael-tooling.com/
https://www.cutwel.co.uk/

## Slide 7: Solutions
Solution 1 - Horn groove Milling Tool on Emco Machines
When looking at other solutions I looked into polygon milling. The idea was to put this method on the Emco machines. We had information from suppliers and also pictures and videos on how this would machine. Below shows the tool and how it would increase the time.
The issue with this method below is that our Emco machines do not run on a Y axis. This means we would only be able to use it on the x axis which will make no benefit in time for us.

## Slide 8: Solutions
Solution 2 - Horn Groove Milling Tool on Bumotech Machines (3)
We were then going to looking at adding this process below to the Bumotech machines. Our Bumotech machines run on a Y axis. The process below is how it is run on the y axis and the time savings we will gain.

## Slide 9: Feasibility
To be able to go ahead with this project we would need to justify the project and show that it was feasible.
We created a CEA to show a cost justification and payback time.
With using a spreadsheet and collecting data from last year we could justify the project. After a meeting and working out times I put in an estimate of our new times which we gathered from the supplier which shows it is a feasible option.
I then worked with my manager to put in place the CEA. Below you can see the justification and payback time. As you can see that the pay back would be completed within a year. We would have massive savings across the part with the average of 60% time saved per part.

## Slide 10: Data
Throughout the project I collected a lot of data. One of my main factor of data was through a Gantt Chart and using Critical Path Analysis.
When monitoring my Gantt chart I used Critical Path Analysis (CPA). CPA is a way of tracking the path of your project. Tracking this path is critical as you can see if you are on track to finish on the date you set or not. In the image below by making some of my tasks it tells me whether I am going to meet my deadline or not. In this case I was not going to meet my deadline by 3 days. I then had to investigate the problem and either reschedule or add more time to the overall project which is what I done in the end.

## Slide 11: Data
Another type of data I collected was timings. I had to conduct timings to work out how long the serrations take currently. I then needed to add the estimated new serration times to justify going forward with this project. I done this by working out how many parts last year we produced and compared hours and costs over what the hours and cost would be if they had the new serration estimates. You can see that the cost saving would be around £20,000 which we put in our CEA to justify the project.