## Slide 1
Fundamentals of Electrical
and Electronic Systems
(ACDA4018)
Lecture - 14

## Slide 2: Content
555 timer
Astable
Monostable
Bistable

## Slide 3: 555 Timer
The 555 timer IC is an integrated circuit (chip) used in a variety of timer, delay, pulse generation, and oscillator applications.
Introduced in 1972
Most widely used ICs due to its ease of use and flexibility.

## Slide 4: 555 Timer

## Slide 5: 555 Timer- Internal Schematic

## Slide 6: 555 Timer- Internal Schematic

## Slide 7: 555 Timer- Internal Schematic

## Slide 8: 555 Timer
Pin 1 (GND): Ground
  Connects to the ground or 0V reference.
Pin 2 (TRIG): Trigger
  Input for triggering the 555 timer. A low signal (below 1/3 of the supply voltage) applied to this pin initiates the timing process.
Pin 3 (OUT): Output
  Provides the pulse or square wave generated by the 555 timer. The waveform depends on the configuration mode (monostable, astable, or bistable).
Pin 4 (RESET): Reset
  A low signal (below 1/3 of the supply voltage) applied to this pin resets the internal flip-flop and stops the timer operation.

## Slide 9: 555 Timer
Pin 5 (CTRL): Control Voltage
  This pin allows control of the reference voltage for the internal comparators.
Pin 6 (THRS): Threshold
  The non-inverting input of the voltage comparator. When the voltage at this pin exceeds 2/3 of the supply voltage, the internal flip-flop is reset.
Pin 7 (DISCH): Discharge
  The collector of the discharge transistor that discharges the external capacitor (in monostable and astable modes).
Pin 8 (VCC): Supply Voltage
  Connected to the positive supply voltage.

## Slide 10: 555 Timer- Internal Schematic
Voltage Divider (Reference Voltage Network):
The 555 timer has an internal voltage divider network connected to the Control Voltage (CV) pin (Pin 5).
This network provides a reference voltage (​) for the internal comparators.
Voltage Comparators:
The 555 timer contains two voltage comparators: the Trigger (TRIG) comparator and the Threshold (THRS) comparator.
The Trigger comparator monitors the voltage at the Trigger input (Pin 2), and the Threshold comparator monitors the voltage at the Threshold input (Pin 6).
The outputs of these comparators control the internal SR flip-flop.

## Slide 11: 555 Timer- Internal Schematic
Comparator:
A comparator is an electronic circuit that compares the voltages at its two input terminals and produces an output indicating which input has a higher voltage.
The output of a comparator is typically a digital signal, indicating whether the voltage at the non-inverting terminal (V+​) is higher than the voltage at the inverting terminal (V−​).
If the voltage in V+ is higher, output is 1
If the voltage in V- is higher, the output is 0

## Slide 12: 555 Timer- Internal Schematic
SR Flip-Flop (Set-Reset Flip-Flop):
The flip-flop is controlled by the outputs of the Trigger and Threshold comparators.
It maintains its state until reset by an external trigger or when the voltage at the Threshold input exceeds​ of the reference voltage.
Output Stage:
The output stage of the 555 timer is connected to the OUT pin (Pin 3).
It is driven by the output of the flip-flop.
The output stage provides the final output waveform, whether in monostable, astable, or bistable modes.

## Slide 13: 555 Timer- Internal Schematic
Control Voltage (CV) Pin:
The Control Voltage (CV) pin (Pin 5) allows external control of the reference voltage for the internal comparators.

## Slide 14: 555 Timer- Internal Schematic
Flipflop – SR Flip Flop (SET-RESET Flip Flop)
When S is 1 & R is 0 => Q= 1 and =0
When S is 0 & R is 1 => Q= 0 and =1
When S is 0 & R is 0 => Q= NC and =NC
S | R | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
0 | 0 | NC | NC
S | R | Q | 
0 | 1 | 0 | 1
1 | 0 | 1 | 0
0 | 0 | NC | NC

## Slide 15: 555 Timer- Internal Schematic
Adjustable Timing Components:
The timing of the 555 timer is primarily controlled by two external resistors (R1 and R2) and an external capacitor (C). By adjusting these components, the user can set the timing characteristics of the 555 timer.

## Slide 16: 555 Timer- Internal Schematic
Applications:
The 555 timer is used in a wide range of applications, including pulse-width modulation (PWM), tone generation, LED flashers, pulse generators, timers, and more.

## Slide 17: 555 Timer
Three Operating Modes:
Monostable Mode (One-Shot): In this mode, the 555 timer operates as a one-shot timer, producing a single output pulse in response to an external trigger.
Astable Mode (Oscillator): In this mode, the 555 timer functions as an oscillator, generating a continuous square wave output.
Bistable Mode (Flip-Flop): The 555 timer can also operate as a flip-flop, maintaining a stable state until triggered to change.

## Slide 18: 555 Timer
The term "multivibrator" is used to describe a type of electronic circuit that can exhibit two distinct states or "vibrations.“
A multivibrator circuit typically alternates between two stable states, creating a waveform with a repeating pattern.

## Slide 19: 555 Timer

## Slide 20: 555 Timer- Monostable
Produces an output pulse for each trigger input

## Slide 21: 555 Timer- Monostable

## Slide 22: 555 Timer- Astable
Produces an output waveform without trigger input

## Slide 23: 555 Timer- Bistable
Produces an output pulse, the pulse starts at the first trigger and ends at the second trigger.

## Slide 24: 555 Timer- Bistable

## Slide 25: 555 Timer

## Slide 26: Thank You