## Slide 1: Investigation and Analysis of NVH (Noise, Vibration, and Harshness) in Road-Based Vehicles
Anandu Unnikirshnan Nair
2411630
Notes: My name is Anandu Unnikrishnan Nair, and today I will be presenting my assignment on Investigation and Analysis of NVH (Noise, Vibration, and Harshness) in Road-Based Vehicles

## Slide 2: Task 1: Introduction
NVH stands for (Noise, Vibration, and Harshness) (Horváth & Zelei, 2024).
NVH is important in road-based vehicle performance.
It has significance to vehicle comfort and driver experience.
NVH impact analysis is the Objective of this investigation.
Notes: NVH abbreviated as Noise, Vibration, and Harshness is an essential parameter for evaluating vehicle performance as well as satisfaction of the customers. NVH is a contraction of the words noise, vibration, and harshness and it relates to all the audible and felt sounds and vibrations occasioned by a vehicle's usage by both the passengers and drivers. Knowing NVH lets the engineers create vehicles not only rigid but rather noiseless with minimum vibrations. This research seeks to understand what NVH is how it impacts individuals, and how measured NVH data can be used to enhance ride comfort and safety.

## Slide 3: Component Harmonic Resonance Concept
Definition: Harmonic resonance in mechanical components.
Take place when natural frequencies line up with excitation orders.
Can cause unnecessary vibration and noise in vehicles.
Impacts several vehicle components, particularly engine parts.
Notes: engine order or Harmonic resonance is influenced by a force that is at the same frequency as a component an even a road frequency. This could lead to greater vibrations and the interior can become unbearable to touch or worse; they can tend to break apart. The effects such as these are evident when a component like an engine mount or bracket has not been isolated properly. It is significant to comprehend the circumstances in which resonance happens to establish mitigation measures like dampers or isolation mounts, to look into sound reduction, and to ensure that no fatal harm arises to the components of the structure.

## Slide 4: Components Affected by Excitation Orders
Engine components: Pistons, crankshafts, and cylinder heads.
Suspension components: Bushings, springs, and dampers (Barton & Fieldhouse, 2024).
Exhaust systems: Resonating at certain engine speeds.
Powertrain: Transmission and driveshaft components affected.
Notes: Many parts in a vehicle's structurally can be said to be susceptible to excitation orders. During combustion, the engine parts like pistons and crankshafts tend to vibrate at specific orders. Components such as bushings and dampers also go through periods of oscillation under damaging road conditions. Since exhaust techniques may generate drone sounds at given engine speeds, exhaust systems may also cause drone noises at those speeds. Likewise, the power train including the actual transmission and the driveshaft can transfer the vibrating energy to the rest of the vehicle structure. Knowing what areas are involved in dynamic response permits the engineers to focus on those areas when applying NVH fixes.

## Slide 5: Measuring Mechanical Vibration
Use of accelerometers for vibration measurement.
Placement: Main locations in the vehicle structure.
Frequency range: Low to high vibration investigation.
Data recorded helps recognize vibration sources and severity (Hassan et al., 2024).
Notes: When it comes to the measurement of mechanical vibration, the use of accelerometers is considered most useful. These are installed on the critical parts of the structure where the degree and frequency of vibration are likely to occur. They enable the engineers to determine whether the vibration levels are normal or if they require some form of control through damping. They include both low-frequency structure-borne vibrations and high-frequency contents within the given range. This enables the designers to identify the root cause of the noise or discomfort and have the chance to fix the issue with the vehicle's performance.

## Slide 6: Measuring Acoustic Air Pressure
Microphones perceive sound waves in the vehicle cabin.
Airborne noise produced by engine, tires, or exhaust.
Frequency analysis to separate particular noise sources.
Data helps in planning quieter vehicle systems.
Notes: Microphones are installed in the vehicles to capture sound in the airborne mode, especially cabin noise. These equipment measure pressure levels produced from the engine, tires, wind, or exhaust, among others. One point is that the use of microphones at various parts of the cabin creates a diagram of sounds. Since the noise data that is collected is usually time-variant, its frequency analysis will involve identifying regions of frequent occurrences by certain frequencies. This serves to help in the determination of specific regions of the noise, thus isolating specific sources of noise. This is important in the process of making quieter cabins and designing the in-cabin acoustics that raise the travelers' experience greatly.

## Slide 7: Sensor Operation for Mechanical Vibration
Accelerometers: Converts mechanical vibration to electrical signals.
Piezoelectric sensors: Measure energetic forces and accelerations (Szczerba et al., 2022).
Dynamic response caught in time-domain signals.
Filtered to recognize particular vibration frequencies.
Notes: Piezoelectric accelerometers are the most suitable to convert mechanical movements into electrical signals as mentioned above. These sensors work in a manner that they identify dynamic acceleration from structural vibrations. They provide information on the time and the frequency domain area which helps in determining distinct vibration incidences. Other techniques that are used to enhance the signals are averaged and filtered to drive out such noises by concentrating on the more important frequency areas. These sensors are inalienable in NVH testing since they provide engineers with the necessary information to achieve better ride comfort and to lessen the resulting vibration and wear.

## Slide 8: Sensor Operation for Acoustic Air Pressure
Microphones: Capture sound pressure disparities in the air (Fueldner, 2020).
Pressure microphones: Measure both sound level and frequency.
Signal processing used to separate particular frequencies.
Important for NVH-related design developments.
Notes: Microphones are used to measure changes in the pressure of air inside and outside the vehicle's cabins. These pressure microphones can be used to measure the sound pressure levels as well as the frequency content of noisy sources. Some of the essential uses of signal processing are to remove noise from a specific frequency range setting through enhancement and amplification. These provide engineers with valuable information on enhancing the current isolation of cabins, similar to those of engines, and the development of the enclosures as well as the efficient exhaust systems. Besides, it helps in increasing comfort levels and also informs regarding the exclusion or reduction of noise pollution by optimizing the materials, and design of buildings.

## Slide 9: Task 2: Order Locked Analysis Overview
Technique to examine vibration data in relation to engine speed.
Classifies particular orders of excitation frequencies.
Helps separate vibration sources at diverse engine speeds.
Essential for recognizing harmonic resonances in components.
Notes: Order Locked Analysis refers to the procedure used in mapping vibration levels with the engine speed. Instead of studying vibrations individually, this technique studies how specific "orders" of the vibrations fit into relation to the revolutions per minute of the engine. It is most advantageous in determining which part of the circuit oscillates at different speeds. Defining excitation frequencies about actual situations, Order Locked Analysis becomes a highly effective tool in identifying and eliminating NVH concerns toward the engine and drivetrain assemblies.

## Slide 10: NVH Data Analysis using DEWESOFT
RPM | Order 1 (m/s²) | Order 2 (m/s²) | Noise (dB) | Observations
1500 | 1.2 | 0.8 | 72 | Normal operation
2000 | 1.5 | 1.1 | 75 | Slight increase with RPM
2500 | 3.8 | 1.3 | 82 | Resonance detected (Order 1 spike)
3000 | 2.1 | 1.6 | 78 | Post-resonance stabilization
"At 2500 RPM, there’s a sudden spike in vibration at 83 Hz."
"Order 3 is louder in Test 2 compared to Test 1."
"A resonance appears at 4000 RPM in the waterfall plot."
Notes: The signal indicates normal vibrations below 2000 RPM, while the pronounced peak at 2500 RPM can be seen from the first harmonic (3.8 m/s²) and the noise level (82 dB). This correlates with the 83 Hz frequency which, again, indicates structural resonance. If there has been an increase in order 3 in Test 2 then it implies there is some wear and tear of gear or bearing. The 4000 RPM resonance in the waterfall plot should be looked into, which could possibly be a second or a third-order harmonic or a structural mode. One or two peaks may require balance or damping adjustments.

## Slide 11: Identifying Harmonic Resonances
Harmonic resonances occur when excitation orders contest normal frequencies .
Particular components experience amplified vibrations at these frequencies.
Resonance frequencies can lead to amplified noise and discomfort.
Analysis helps in fine-tuning components to avoid resonance.
Notes: When a component frequency matches the firing order of some source such as an engine, resonance results. This can cause more vibration, which leads to noise and further actions. They usually manifest themselves as variations or spike in vibration or acoustic signals. This makes it possible for engineers to analyze them to alter such characteristics as mass or stiffness that may cause a shift in natural frequency away from the operational rpm range to counter future resonance. I had tried my best to find the harmonic resonance from our mentioned value but I couldn’t find it

## Slide 12: Comparing Two Tests in NVH Analysis
Order Locked Analysis links test results at dissimilar conditions.
Classifies changes in vibration behavior across tests.
Helps distinguish discrepancies caused by design changes or wear.
Provides perception into vehicle NVH performance improvements.
Notes: Two test results from NVH tests enable an engineer to confirm changes in dynamic performance due to changes in the vehicle's design or due to wear and tear. As pointed out earlier, Order Locked Analysis is valuable when one aims to compare the vibration behavior in different conditions. It has developed and supplied systems sequencing by comparative analysis of such features that may not be apparent during isolated tests. They are essential to be used for performance improvement, when verifying changes of engineers, and when guaranteeing that the comfort and noise level of the finished product is the same with all the batches or the changes in the production line.

## Slide 13: Comparison of NVH
Parameter | Test A (Baseline) | Test B (Modified) | Delta (%) | Significance
Resonance RPM | 2500 | 2650 | +6% | Shift suggests stiffness change
Peak Order 1 | 3.8 m/s² | 3.2 m/s² | -16% | Improvement in balancing
Peak Noise | 82 dB | 79 dB | -3.7% | Reduced acoustic energy
Order 2 @3000 | 1.6 m/s² | 2.1 m/s² | +31% | New secondary vibration source
Notes: The analysis includes changes as follows: resonance moved +6% to 2650 RPM, showing alteration to stiffness; Order 1 vibration reduced by 16%, implying better balancing. Noise levels decreased by 3.7 dB. However, Order 2 increased by 31% at 3000 RPM, so there is another exciting frequency, which may be caused by bearing damages or its mispositioning. These mixed results demonstrate that the structural modifications contributed to the reduction of primary vibrations, though leading to emergence of new harmonics. Concerning the analysis of the Order 2 increase, it is recommended to continue its further research to avoid component wear.

## Slide 14: Observing Major Features in Data
Common features: Peak vibrations at certain frequencies
Major vibration modes recognized through analysis.
Frequency patterns and amplitude variations detected.
Resonance peaks link with mechanical problems in components.
Notes: One also notices that it is possible to detect critical problems analyzing NVH data and the main features which state them are the peak amplitudes at certain frequencies. It is possible to acknowledge major vibration modes, these are modes, where parts vibrate and amplitude fluctuations in motion would indicate its severity. Patterns of frequency always had a concern with mechanical practices or with a lack of them. Thus, analysis of resonance peaks in conjunction with components facilitates spotting of areas in the design that need improvement. Such comprehensive observation helps diagnose the problems in advance and optimize the performance of NVH design permanently.

## Slide 15: Conclusions and Further Research
Understanding NVH factors is critical for vehicle design.
Order analysis helps lessen NVH-related discomfort.
Further research desired on cultivating sensor accuracy.
Future work could discover material and design innovations.
Notes: In conclusion, NVH analysis helps the automotive industry in creating more silent, smoother, and comfortable cars. Such methods like Order Locked Analysis enable one to eliminate noise and vibrations as much at the source as possible. They will help to produce several critical design changes stemming from a better understanding of the material properties and the stresses experienced in the space environment. Nonetheless, to improve both the sensitivity of the sensors and the algorithms for data analysis further investigation is required. Potential future developments could extend to novel materials, AI-predictive models, and smart sensors for even better NVH performance in vehicles.

## Slide 16: References
Horváth, K., & Zelei, A. (2024). Simulating Noise, Vibration, and Harshness Advances in Electric Vehicle Powertrains: Strategies and Challenges. World Electric Vehicle Journal, 15(8), 367.
Barton, D. C., & Fieldhouse, J. D. (2024). Suspension systems and components. In Automotive Chassis Engineering (pp. 85-187). Cham: Springer International Publishing.
Hassan, I. U., Panduru, K., & Walsh, J. (2024). An in-depth study of vibration sensors for condition monitoring. Sensors, 24(3), 740.
Szczerba, Z., Szczerba, P., & Szczerba, K. (2022). Sensitivity of piezoresistive pressure sensors to acceleration. Energies, 15(2), 493.
Fueldner, M. (2020). Microphones. In Handbook of silicon based MEMS materials and technologies (pp. 937-948). Elsevier.
Bilal, N., Tripathi, A., & Bajaj, A. K. (2020). On experiments in harmonically excited cantilever plates with 1: 2 internal resonance. Nonlinear Dynamics, 100(1), 15-32.
Zhang, P., & Li, L. (2020). Vibration and noise characteristics of high-frequency amorphous transformer under sinusoidal and non-sinusoidal voltage excitation. International Journal of Electrical Power & Energy Systems, 123, 106298.