## Slide 1
Module Name : Electronics 1
Module Code : ACDB5002
Topic : Traffic Light- T junction
- A Practical Example
Lecture : 17
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk

## Slide 2: Traffic Light- T junction
At the end of this session, the students will be able to
Understand the requirements outlined in the assignment brief related to microcontroller-based circuit design.
UWTSD Lectures / ACDB5002 – Electronics 1
Learning Objectives

## Slide 3
UWTSD Lectures / ACDB5002 – Electronics 1
Defining the variables
sbit :used to declare a single bit variable.
LED_Red :name given to the single bit variable.
RB0_bit : the port and bit position to which the variable is assigned
Traffic Light- T junction

## Slide 4
UWTSD Lectures / ACDB5002 – Electronics 1
Declaring 7- segment Patterns
int i: Declares an integer variable named ‘i’.
unsigned seg_display[] : Declares an unsigned array named seg_display and initializes it with 10 hexadecimal values.
Traffic Light- T junction

## Slide 5
UWTSD Lectures / ACDB5002 – Electronics 1
Initialization of Ports and Pins
Declaring the Output Port : TRISB, TRISC , TRISD
Initialize PORTB, PORTC and PORTD to be ‘0’
The Port D is used to display the first value and Port C is used to display the second value. PORTB is used to assign Traffic Light Modules.
Traffic Light- T junction

## Slide 6
UWTSD Lectures / ACDB5002 – Electronics 1
Conditions in do- while Loop
This condition is to make Port D to display ‘0’
‘portd = 0xC0’ sets the value of the variable portd to 0xC0. (to display ‘0’)
‘portc = display[i]’ suggests that there is an array called display containing at least 10 elements. Also, it specifies the traffic Light sequence and the pedestrian LED. status
Traffic Light- T junction

## Slide 7
UWTSD Lectures / ACDB5002 – Electronics 1
Conditions in do- while Loop
This condition is to make Port D to display ‘1’
‘portd = 0xF9’ sets the value of the variable portd to 0xF9. (to display ‘1’)
Also, ‘portc = display[i]’ suggests that there is an array called display containing at least 10 elements.
Traffic Light- T junction

## Slide 8
UWTSD Lectures / ACDB5002 – Electronics 1
Conditions in do- while Loop
This condition is to make Port D to display ‘2’
‘portd = 0xA4’ sets the value of the variable portd to 0xA4. (to display ‘2’)
Also, ‘portc = display[i]’ suggests that there is an array called display containing at least 10 elements.
Traffic Light- T junction

## Slide 9
UWTSD Lectures / ACDB5002 – Electronics 1
Conditions in do- while Loop
This condition is to make Port D to display ‘3’
‘portd = 0xB0’ sets the value of the variable portd to 0xB0. (to display ‘3’)
Also, ‘portc = display[i]’ suggests that there is an array called display containing at least 10 elements.
Traffic Light- T junction

## Slide 10
UWTSD Lectures / ACDB5002 – Electronics 1
Conditions in do- while Loop
This condition is to make Port D to display ‘4’
‘portd = 0x99’ sets the value of the variable portd to 0x99. (to display ‘4’)
Also, ‘portc = display[i]’ suggests that there is an array called display containing at least 10 elements.
Traffic Light- T junction

## Slide 11
UWTSD Lectures / ACDB5002 – Electronics 1
Simulation
Traffic Light- T junction

## Slide 12
Thank You