## Slide 1: FIR Filters
Prepared by Prof. Ian Wells

## Slide 2: What do we Require for FIR Filter Design ?
FIR stands for Finite duration Impulse Response.
We want to find the N numbers that define the impulse response for the FIR filter i.e.
Equivalently,

## Slide 3: FIR Filter Structure
x(k)

y(k)
T
b0
X
T
T
T
b1
X
b2
X
bN-1
X
bN-2
X
Tapped Delay Line

## Slide 4: FIR Filter Design
We want to produce a desired transfer function and hope that it equals an achievable transfer function:

## Slide 5: FIR Filter Design
Alternatively, we can represent these functions as a z domain transfer function:

## Slide 6: FIR Filter Design
An FIR filter with N ‘coefficients’ , or N ‘impulse response values’, is an N-1st order filter and is completely characterised by:
    The N-1 zeroes of the z polynomial
    .
    the N-1 poles at the origin
Such a filter has no poles except those at the origin and is hence guaranteed to be stable.

## Slide 7: A Design Gift Example
h=[0.0361,0.0133,-0.019,0.0269,-0.0387,-0.2348,-0.1031,0.3173,0.3173,-0.1031,-0.2348,-0.0387,0.0269,-0.019,0.0133,0.0361];
k=[0:1:15];
subplot(2,1,2), stem(k,h)
xlabel('k');
ylabel('h(k)');
title('Impulse Response Sequence for a 15th Order FIR Filter');
[h,f]=freqz(h,1,512,1/200);
subplot(2,1,1), plot(f,abs(h));
xlabel('Frequency');
ylabel('Magnitude');
title('Frequency Response for a 15th Order FIR Filter');
15th order FIR bandpass filter
the sample frequency is arbitrarily set at 200Hz

## Slide 8: 15th Order FIR Bandpass Filter

## Slide 9: Phase and Frequency Responses (Decibels)
h=[0.0361,0.0133,-0.019,0.0269,-0.0387,-0.2348,-0.1031,0.3173,0.3173,-0.1031,-0.2348,-0.0387,0.0269,-0.019,0.0133,0.0361];
freqz(h,1,512,1/200);
This filter is a reasonably good filter with linear phase response.

## Slide 10: Zero Placement
The use of suitable PC software enables the design of filters by interactively placing poles onto a PZP.
The approach is to form:
with the ’s (for real filters normally) being either real or appearing in complex conjugate pairs.

## Slide 11: Zero Placement
PZP rules are used:
    zeroes on the unit circle fix to zero
    zeroes near the unit circle drag down towards zero
    conjugal zero pairs give a linear phase response
    zeros inside the unit circle give the
    same magnitude and phase response as their complex conjugates, but with minimum phase contribution

## Slide 12: Examples of Zero Patterns
x-axis is misleading
sample frequency was 500Hz
In normalised frequency the 250Hz value is equivalent to 0.5
between the 250Hz and the 500Hz values this is equivalent to the negative frequency axis
500Hz at 0
250 Hz also at –0.5
All points in between are proportionately divided.
(Its as if the right hand side of the diagram should be cut off and slid into the negative frequency axis with the 500Hz lining up with the 0Hz.)

## Slide 13: Filters Frequency Responses (Bandpass from  = 0.2 to 0.3)
b=fir1(26,[0.4 0.6]);
fs=500;
[h,f]=freqz(b,1,512,'whole',fs);
plot(f,abs(h))

## Slide 14: Filters PZP Diagram (Bandpass from  = 0.2 to 0.3)
[b,a]=fir1(15,[0.4 0.6]);
zplane(b,a)

## Slide 15: Filters PZP Diagram (Bandpass from  = 0.075 to 0.15)
[b,a]=fir1(15,[0.15 0.3]);
fs=500;
[h,f]=freqz(b,1,512,
'whole',fs);
subplot(2,1,1), plot(f,abs(h));
subplot(2,1,2), zplane(b,a);

## Slide 16: Filters PZP Diagram (Lowpass; c = 0.35)
[b,a]=fir1(15,0.7);
%set the sample frequency to 500Hz
fs=500;
%calculate the filter frequency response including the negative frequency axis
[h,f]=freqz(b,1,512,'whole',fs);
%plot the frequency response
subplot(2,1,1), plot(f,abs(h));
%plot the pole/zero diagram
subplot(2,1,2), zplane(b,a);

## Slide 17: Filters PZP Diagram (Lowpass; c = 0.15)
[b,a]=fir1(15,0.3);
fs=500;
[h,f]=freqz(b,1,512,
'whole',fs);
subplot(2,1,1), plot(f,abs(h));
subplot(2,1,2), zplane(b,a);

## Slide 18: Filters PZP Diagram (Lowpass; c = 0.075)
[b,a]=fir1(15,0.15);
fs=500;
[h,f]=freqz(b,1,512,
'whole',fs);
subplot(2,1,1), plot(f,abs(h));
subplot(2,1,2), zplane(b,a);

## Slide 19: Filters PZP Diagram (Highpass; c = 0.2)
[b,a]=fir1(16,0.4,'high');
fs=500;
[h,f]=freqz(b,1,512,'whole',fs);
subplot(2,1,1), plot(f,abs(h));
subplot(2,1,2), zplane(b,a);

## Slide 20: Impulse Invariant FIR Design
The impulse Invariant method is a non-optimal approach.
The idea is to start with the impulse response of prototype continuous time filter (usually ideal) and digitise it by sampling that impulse response.
We expect (and encounter) two problems:
    aliasing because it's a sampling
    Leakage, or finite Windowing effects because we are restricted to a finite number of impulse response samples.

## Slide 21: Impulse Invariant FIR Design
This last effect is usually suffered, because the desired design is frequency limited (e.g. a lowpass filter)
So the corresponding impulse response is required to spread over all time.
Not surprisingly, the time truncation causes a severe spectral smearing.
Nevertheless, the method is easy and effective.
It is simple when N is odd; we see here the first major distinction between N odd and N even.

## Slide 22: Practical design procedure
First select a desired ideal target filter , this is the analogue prototype having an impulse response .
This is harder than it seems, and is influenced by whether N is odd or even

## Slide 23: Practical design procedure
Simply form,
where,
T=Sample Interval
Usually was even or odd symmetric, so is linear phase

## Slide 24: Practical design procedure
The result is something like , but
  smeared through the effect of time truncation
  Aliased
  Has as a spectral modifier

## Slide 25: Design Example 1
Design an N=7 linear phase lowpass filter with a cut-off frequency of c=0.3.
Choose an analogue prototype:
assuming

## Slide 26: Design Example 1
Sinc Function Ideal Rectangular Function
t=[-10:0.01:10];
h=0.6*sinc(0.6*t);
plot(t,h)
ylabel('Magnitude');
xlabel('Time (sampled at 0.01)');
title('Sinc Function');

## Slide 27: Design Example 1
Find the value of the parameter  ;
The discrete impulse response is then given by;
Expanding the sinc function gives;

## Slide 28: Design Example 1
Mid point equal to the width of the ideal frequency response, 0.6 in this case
calculator will give an error if it is attempted by conventional means
use L'Hopitals Rule

## Slide 29: Design Example 1
Check the frequency response using the FST:

## Slide 30: Design Example 1
Magnitude,

## Slide 31: Design Example 1
This tells us that we have a rough lowpass response with poor DC gain. Using too few coefficients causes this.

## Slide 32: Frequency Response fs= 500Hz
x=[-0.0624,-0.0935,0.3027,0.6,0.3027,-0.0935,-0.0624];
[h,f]=freqz(x,1,512,500);
plot(f,abs(h))
xlabel('Frequency')
ylabel('Magnitude')
title('Filter Frequency response sampled at 500Hz')

## Slide 33: Frequency and Phase Response fs= 500Hz
x=[-0.0624,-0.0935,0.3027,0.6,0.3027,-0.0935,-0.0624];
freqz(x,1,512,500);
linear phase

## Slide 34: Matlab Generated Rectangular Function
t=[-1:0.1:1];
plot(t,rectpuls(t,0.6))
title('Rectangular
Frequency Domain Function')
ylabel('Magnitude');
xlabel('Frequency');

## Slide 35: Design Example 2
Design an N=7 linear phase filter with a cut on frequency and a sample frequency
This will give us a cut on, in normalised frequency, of

## Slide 36: Design Example 2
From a simple diagrammatic approach for the analogue prototype we can see:
f
f
-
300
-300
1
0
f
=
1
1
300
-300
Ideal Analogue Prototype for a Highpass Filter

## Slide 37: Design Example 2
From a mathematical point of view this could be shown as:
We don’t need to view this the same way in normalised frequency since the frequency range is only considered from –0.5 to 0.5

## Slide 38: Design Example 2
This gives us the following diagrammatic approach:
f
f
-
0.3
-0.3
1
0
f
=
1
1
0.3
-0.3
-0.5
0.5
0.5
-0.5
HA
HB
HC
0.6
1.0
Ideal Normalised Frequency Response for a Highpass Filter

## Slide 39: Design Example 2
The time domain equations for these filters are related by the equation:
Substitute for giving:

## Slide 40: Design Example 2
Expanding out this function gives:
Using the definition of sinc as
Where

## Slide 41: Design Example 2
Putting in numbers for this example gives:

## Slide 42: Design Example 2
We can tabulate the results for this example:
Take care with the Mid Point

## Slide 43: Design Example 2
k=[0,1,2,3,4,5,6];
h=[0.0624,0.0835,-0.3027,0.4,-0.3027,0.0835,0.0624];
[h1,f]=freqz(h,1,512,1000);
plot(f,abs(h1))
xlabel('Frequency(Hz)')
ylabel('Magnitude')
title('Highpass Filter Response')
Frequency Response for the Highpass Filter

## Slide 44: Design Example 2
plot(f,angle(h1))
xlabel('Frequency(Hz)')
ylabel('Phase')
title('Highpass Filter Phase Response')
Phase Response for the Highpass Filter
This filter has a linear phase response.

## Slide 45: Windowing
The frequency response of a filter is given by the function:
This is the general form of a Fourier series (however the periodic function is in time not  and the coefficients reside in frequency not time as in h(k) ).

## Slide 46: Windowing
We have an equivalent process for filter design therefore. This is particularly interesting when h(k) is finite (i.e. FIR) because these numbers are then explicitly the coefficients .
Hence an FIR’s frequency response:
can be used to approximate a desired frequency response

## Slide 47: Windowing
eg

## Slide 48: Why is Filter Design Usually Imperfect ?
The fact that N must be finite stops us matching the actual estimated response to the vertical edges of the rectangular response and also to the flat places on .
We must be able to compromise!

## Slide 49
Why is Filter Design Usually Imperfect ?

## Slide 50: Why is Filter Design Usually Imperfect ?
k=[-7,-6,-5,-4,-3,-2,-1,0,1,2,3,4,5,6,7];
x=0.3*sinc(2*pi*0.3*k*0.2);
subplot(3,2,1), stem(k,x);
rec=[0,0,0,1,1,1,1,1,1,1,1,1,0,0,0];
subplot(3,2,3), stem(k,rec);
trunc=rec.*x;
subplot(3,2,5),stem(k,trunc);
[h1,f1]=freqz(rec,1,512,'whole');
subplot(3,2,4), plot(f1,abs(h1));
[h2,f2]=freqz(trunc,1,512,'whole');
subplot(3,2,6), plot(f2,abs(h2));

## Slide 51: Windowing: A Solution
The struggle is to force to be more like . The imperfection resides in two things:
    ripples i.e. departures from flatness in pass-bands stop-bands or whatever
    transitions that roll more leisurely than the desired brick wall vertical edges
For a given N all that can be done is to re-apportion this imperfection!

## Slide 52: Windowing: A Solution
When designing filters our equations yields an infinitely long set of Fourier coefficients, h(k).
Obviously we cannot obtain all the values of such a set and so in practice the number of values of h(k) are truncated to an acceptable length.
The consequence of this process is a significant rippling effect in the filters magnitude response first identified by Willard Gibbs in 1899, while studying the effect of an abrupt transition of a function, and by Hamming in 1983 who applied these earlier mathematical calculations to modern systems.

## Slide 53: Windowing: A Solution
The effect is approximately 9 of the maximum magnitude regardless of the length of the truncated h(k).
This ripple is now called the Gibbs Phenomenon.
One way to smooth out existing ripples (as opposed to prevention) is to do Frequency () domain Convolution.
But this smearing while usually helping to make the ripples small inevitably spreads the transitions.
So the filter imperfection gets transferred into slovenly transitions

## Slide 54: Windowing: A Solution
The great virtually is simplicity; the Frequency domain Convolution is accomplished by time domain multiplication.
Windowing can be expressed by the following equation:
Where is the window sequence.

## Slide 55: Windowing: A Solution
This equation is relatively simple. What is not clear is how best to choose the correct , to do the job.
What makes a good window?
Generally, you want low sidelobe levels for the window functions frequency response, yet tight dispersion of it.

## Slide 56: Uniform Window
Features:
  Fastest transition possible in an N-length window
  Main lobe width is 2/N
  Leads to Gibbs phenomenon
  Highest sidelobe width is -13dB
Comments:
  Not really windowing, used as a comparison.

## Slide 57: Uniform Window
k=[0:1:9];
w=[0,0,1,1,1,1,1,1,0,0];
stem(k,w)
title('Uniform Window')
xlabel('k')
ylabel('Magnitude')

## Slide 58: Bartlett Window
Features:
  The two endpoint data values are lost this is bad!
  W (the frequency response) falls off twice as fast (dB/octave) as uniform window
  Highest sidelobe is -27dB
  Main lobe width is 2/N
Comments:
  Not used much because the harsh emphasis on centre points to the detriment of the endpoints

## Slide 59: Bartlett Window
k=[0:1:6];
w=1-abs((k-3)/3);
stem(k,w)
title('Bartlett Window')
xlabel('k')
ylabel('Magnitude')

## Slide 60: Bartlett Window
k=[0:1:24];
%Create a simple lowpass filter using the impulse invariant method
h=0.3*sinc(0.3*(k-12));
%create the Bartlett window coefficients
w=1-abs((k-12)/12);
%create h1 the new set of windowed coefficients
h1=w.*h;
%Find the frequency response of h1, the windowed filter
[h2,f]=freqz(h1,1,512);
%Find the frequency response of h, the original filter
[h3,f2]=freqz(h,1,512);
subplot(2,1,1), plot(f2,abs(h3));
title('Impulse Invariant Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');
subplot(2,1,2), plot(f,abs(h2));
title('Bartlett Windowed Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');

## Slide 61: Bartlett Window
Gibbs Phenomenon
Bartlett Window Applied to a Lowpass Filter

## Slide 62: Hanning Window
Features:
  Highest sidelobe is -23dB
  Main lobe width is 4/N

## Slide 63: Hanning Window
k=[0:1:6];
w=0.5*(1+cos(2*pi*(k-3)/7));
stem(k,w)
title('Hanning Window')
xlabel('k')
ylabel('Magnitude')

## Slide 64: Hanning Window
The end points although small are not zero as shown by the numerical values of the previous function:
w(k) = {0.0495, 0.3887, 0.8117, 1.0000, 0.8117, 0.3887, 0.0495}
It looks very triangular in shape until you increase the number of values as shown below:

## Slide 65: Hanning Window
Hanning (von-Hann) Window With More Values

## Slide 66: Hanning Window
k=[0:1:24];
%Create a simple lowpass filter using the impulse invariant method
h=0.3*sinc(0.3*(k-12));
%create the Hanning window coefficients
w=0.5*(1+cos(2*pi*(k-12)/25));
h1=w.*h;
[h2,f]=freqz(h1,1,512);
[h3,f2]=freqz(h,1,512);
subplot(2,1,1), plot(f2,abs(h3));
title('Impulse Invariant Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');
subplot(2,1,2), plot(f,abs(h2));
title('Hanning Windowed Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');
Hanning Window Applied to a Lowpass Filter

## Slide 67: Hamming Window
Features:
  Highest sidelobe is -43dB
  Main lobe width is 4/N
Comments:
  Just slight adjustments in values has given much more sidelobe cancellation.

## Slide 68: Hamming Window
k=[0:1:6];
w=0.54+0.46*cos(2*pi*(k-3)/7);
stem(k,w)
ylabel('Magnitude')
xlabel('k')
title('Hamming Window')

## Slide 69: Hamming Window
Hamming Window With More Values

## Slide 70: Hamming Window
k=[0:1:24];
h=0.3*sinc(0.3*(k-12));
%create the Hamming window coefficients
w=0.54+0.46*cos(2*pi*(k-12)/25);
%create h1 the new set of windowed coefficients
h1=w.*h;
[h2,f]=freqz(h1,1,512);
[h3,f2]=freqz(h,1,512);
subplot(2,1,1), plot(f2,abs(h3));
title('Impulse Invariant Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');
subplot(2,1,2), plot(f,abs(h2));
title('Hamming Windowed Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');

## Slide 71: Hamming Window
Hamming Window Applied to a Lowpass Filter

## Slide 72: Blackman Window
Features:
  Highest sidelobe is -58dB
  Main lobe width is 6/N
Comments:
  Higher order correction terms typical of Fourier style constructions.

## Slide 73: Blackman Window
k=[0:1:6];
w=0.42+0.5*cos(2*pi*(k-3)/7)+0.08*cos(4*pi*(k-3)/7);
stem(k,w)
ylabel('Magnitude')
xlabel('k')
title('Blackman Window')

## Slide 74: Blackman Window
Blackman Window With More Values

## Slide 75: Blackman Window
h=0.3*sinc(0.3*(k-12));
k=[0:1:24];
w=0.42+0.5*cos(2*pi*(k-12)/25)+0.08*cos(4*pi*(k-12)/25);
h1=w.*h;
[h2,f]=freqz(h1,1,512);
[h3,f2]=freqz(h,1,512);
subplot(2,1,1), plot(f2,abs(h3));
title('Impulse Invariant Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');
subplot(2,1,2), plot(f,abs(h2));
title('Blackman Windowed Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');

## Slide 76: Blackman Window
Blackman Window Applied to a Lowpass Filter

## Slide 77: Comparison of Hamming and Blackman Windows Applied to a Lowpass Filter
k=[0:1:24];
h=0.3*sinc(0.3*(k-12));
wh=0.54+0.46*cos(2*pi*(k-12)/25);
wb=0.42+0.5*cos(2*pi*(k-12)/25)+0.08*cos(4*pi*(k-12)/25);
h1=wh.*h;
h5=wb.*h;
[h2,f]=freqz(h1,1,512);
[h3,f2]=freqz(h,1,512);
[h4,f3]=freqz(h5,1,512);
subplot(2,1,1), plot(f2,abs(h3));
title('Impulse Invariant Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');
subplot(2,1,2), plot(f,abs(h2),f3,abs(h4));
title('Hamming and Blackman Windows Comparison');
xlabel('Frequency');
ylabel('Magnitude');

## Slide 78: Comparison of Hamming and Blackman Windows Applied to a Lowpass Filter
Blackman
Hamming

## Slide 79: Increasing the size of N
a=12;n=a*2+1;
k=[0:1:n-1];
h=0.3*sinc(0.3*(k-a));
w=0.54+0.46*cos(2*pi*(k-a)/n);
h1=w.*h;
[h2,f]=freqz(h1,1,512);
subplot(4,1,1), plot(f,abs(h2));
ylabel('N=25');
%
a=24;n=a*2+1;
k=[0:1:n-1];
h=0.3*sinc(0.3*(k-a));
w=0.54+0.46*cos(2*pi*(k-a)/n);
h1=w.*h;
[h2,f]=freqz(h1,1,512);
subplot(4,1,2), plot(f,abs(h2));
ylabel('N=49');
%
a=50;n=a*2+1;
k=[0:1:n-1];
h=0.3*sinc(0.3*(k-a));
w=0.54+0.46*cos(2*pi*(k-a)/n);
h1=w.*h;
[h2,f]=freqz(h1,1,512);
subplot(4,1,3), plot(f,abs(h2));
ylabel('N=101');
%
a=100;n=a*2+1;
k=[0:1:n-1];
h=0.3*sinc(0.3*(k-a));
w=0.54+0.46*cos(2*pi*(k-a)/n);
h1=w.*h;
[h2,f]=freqz(h1,1,512);
subplot(4,1,4), plot(f,abs(h2));
ylabel('N=201');

## Slide 80: Increasing the size of N

## Slide 81: Kaiser Window: Optimum Design Method
In 1974 Kaiser developed a formalised method for filter design using windows.
If we can obtain a window function that is maximally concentrated around=0 in the normalised frequency domain then the trade-off between the main lobe width and the sidelobe area can be quantified.

## Slide 82: Kaiser Window: Optimum Design Method
Kaiser found that an almost optimal filter design could be found by using the zeroth order modified Bessel function of the first kind.
He defined the window as below.
where is the zeroth order modified Bessel function of the first kind.

## Slide 83: Kaiser Window: Optimum Design Method
The central value of the window w(0) when k=0 is always unity; the parameter  controls the tapering of the function at its edges; if =0 there is no taper and the window reduces to a rectangular form.
The following figure shows the parameters that are considered in the Kaiser design method.

## Slide 84: Kaiser Window: Optimum Design Method

## Slide 85: Kaiser Window: Optimum Design Method
This design is for a lowpass filter with an ideal response given by the thick line in the figure.
An acceptable transition width  , given in normalised frequency terms, is chosen by the designer, together with an acceptable ripple level  in both the pass and stop bands.
The Kaiser window is based upon the fact that the parameter  is dependent upon the ripple level .
This is because  controls the window's tapering and hence sidelobe levels.
For a particular value of , and hence , the transition width  is related to window length.
Hence, if  is known then we can find M.

## Slide 86: Kaiser Window: Optimum Design Method
If  and M are known then the previous equation can be used to evaluate the coefficients.
Ripple level is initially specified as an attenuation, A, given in decibels by:

## Slide 87: Kaiser Window: Optimum Design Method
The value of  is found from:
The value of M is found from:

## Slide 88: Kaiser Window: Optimum Design Method
If a fractional result is produced then the value of M must obviously be rounded up to the nearest integer.
The values of  and M are then used to evaluate the equation. The term can be expanded as a power series as below:

## Slide 89: Kaiser Window: Optimum Design Method
%design a Kaiser filter that has a transition
%region from 1500Hz to 1550 Hz [1500 1550],
%that is lowpass [1,0],
%that has a passband ripple of 0.001 and a stop-band
%ripple of 0.01 [0.001 0.01],
%that has a sample rate of 8000Hz
c = kaiserord( [1500 1550], [1 0], [0.001 0.01], 8000, 'cell' );
%pass the design parameters to a filter design
b = fir1(c{:});
%find the frequency response of the filter
[h,f]=freqz(b,1,512,8000);
plot(f,abs(h))
title('Kaiser Windowed Lowpass Filter');
xlabel('Frequency');
ylabel('Magnitude');

## Slide 90: Kaiser Window: Optimum Design Method
This is a superb filter!

## Slide 91: Other Optimum Design Methods
Other optimal designs exist such as the Parks-McLellan method but will not be dealt with here.
The Parks-McLellan method attempts to minimise the ripple throughout the spectrum which can lead to some significant ripple in the filter's pass band.

## Slide 92: Filter Design Using Fourier Series Coefficients
The frequency response and the unit impulse response h(k) for a linear time invariant system are related to each other by the equation:
-Synthesis Equation

## Slide 93: Filter Design Using Fourier Series Coefficients
For an analogue signal, which is sampled at intervals of T then, we obtain:
Where
It can be shown that:

## Slide 94: Filter Design Using Fourier Series Coefficients
The synthesis equation is extremely important in filter design.
This equation means that the impulse response sequence is in fact the set of coefficients for the FIR system.
When we design filters we start with the desired filter response characteristics.

## Slide 95: Filter Design Using Fourier Series Coefficients
We need a relationship for the filter coefficients in terms of the frequency response and this is given by:
-Analysis Equation

## Slide 96: Filter Design Using Fourier Series Coefficients
The integral is needed because the spectrum has a continuous variable  but we are only interested in the region where
This is because of the spectrum repeating itself outside this range.

## Slide 97: Filter Design Using Fourier Series Coefficients
Our equations constitute a Fourier series pair known as a synthesis expression and an analysis expression.
They are written together as:

## Slide 98: Filter Design Using Fourier Series Coefficients
The corresponding pair of equations for the sampled analogue case can be written as the pair:
where is the sampling frequency in radians per second.

## Slide 99: Filter Design Using Fourier Series Coefficients
We begin the design procedure by deciding upon a desired frequency response:
We desire the unit impulse response h(k).

## Slide 100: Filter Design Using Fourier Series Coefficients
Multiply both sides of the equation by giving:
or

## Slide 101: Filter Design Using Fourier Series Coefficients
Integrate both sides of the equation from =-0.5 to 0.5
i.e. one period; we arrive at:
Interchanging the summation and integration order yields:
-equation A

## Slide 102: Filter Design Using Fourier Series Coefficients
The Euler relationship can now be used:
to give:

## Slide 103: Filter Design Using Fourier Series Coefficients
For the case when km then the terms
cos[(k-m)2] and sin[(k-m)2 ]
are periodic sinusoidal functions that are being integrated over a whole period.
The integral of such a function is zero except when the case k=m exists and the equation becomes:

## Slide 104: Filter Design Using Fourier Series Coefficients
The right hand side of the equation A has only a value when k=m and hence only the term h(k) remains.
We consequently arrive at the relationship:
This result allows us to use this expression to calculate the Fourier series coefficients.

## Slide 105: Lowpass Filter Design Using Fourier Series Coefficients
The equation used for a lowpass design is shown below:
The frequency response part of the equation = 1 in the passband and 0 elsewhere and so our equation becomes:

## Slide 106: Lowpass Filter Design Using Fourier Series Coefficients
Evaluating the integral gives:
Applying the Euler relation gives:

## Slide 107: Lowpass Filter Design Using Fourier Series Coefficients
Our expression needs to be causal (i.e. k 0) however, and so the expression is shifted along the time axis to satisfy this constraint

## Slide 108: Lowpass Filter Design Using Fourier Series Coefficients
Note that this expression is the same as the Impulse Invariant equation and the examples done previously are applicable here.
Another thing to remember is that we must truncate this expression to a finite number since it is clearly impractical to have an infinite series.

## Slide 109: Frequency Transformation of Ideal Fourier Series Coefficients
This design method starts from the design of a simple low pass filter and then uses a transformation method to produce other types of filters.

## Slide 110: Frequency Transformation of Ideal Fourier Series Coefficients

## Slide 111: Design Procedure
Represent the desired filter in terms of a low pass design.
Find the filter coefficients
Select a value for N.Select a window function
Window the low pass filter.
Perform the appropriate frequency transformation.
Verify the filters frequency response.

## Slide 112: Design Example
Design a high-pass filter with a cut on frequency of 200 Hz. The sampling frequency is 1000 Hz and let N=7.
Firstly convert any frequencies to normalised frequency:
c = fc/fs = 200/1000 = 0.2

## Slide 113: Design Example
The ideal frequency response for a high pass filter is shown below:
The equation that is needed for the low pass prototype is:
0.5-c
-(0.5-c)
1
-0.5
0.5

## Slide 114: Design Example
The cut on frequency from the diagram is 0.5-c which is equal to 0.2 our specified frequency.
0.2= 0.5-c
Rearranging gives c = 0.3.
It is therefore this value that we use in the low-pass prototype filter equation.

## Slide 115: Design Example
Put numerical values into the equation:

## Slide 116: Design Example
The frequency response of the lowpass prototype and the final high pass filter

## Slide 117: Frequency Sampling Filter Design
We are usually more interested in the frequency domain behaviour of a filter.
This method involves the use of the Inverse Discrete Fourier Transform (IDFT) to approximate that behaviour.

## Slide 118: Frequency Sampling Design Procedure
The frequency response is:
this Discrete Fourier Transform (DFT) has N values from =-0.5 to 0.5.

## Slide 119: Frequency Sampling Design Procedure
Next we evaluate the IDFT find the N unit sample response values.

## Slide 120: Frequency Sampling Design Procedure
An appropriate window is chosen of length M and applied to the sample response values
Note: there are M windowed weights. The value N should be much larger that M.

## Slide 121: Frequency Sampling Design Procedure
Finally, the filter is implemented using any of the previously discussed methods.

## Slide 122: Design Example
Design a high-pass filter with cut-on of 10kHz with a sampling frequency of 50kHz.
Use the IDFT approach:
    Find the approximate Fourier coefficients by using 101 frequency samples.
    Use a 21 sample rectangular window to reduce the number of coefficients to 21 and plot the frequency response.
    Use a 21 sample Hamming window and plot the frequency response.

## Slide 123: Design Example
The sample values of are described by the following:
With N=101 the spacing between samples is :

## Slide 124: Design Example
Find the IDFT of the 101 samples:
Apply a 21 sample rectangular window as below,
to the 101 coefficient sample response.
This gives the results below.

## Slide 125: Design Example
fs=50000;
%Set up the 101 samples (N) of the ideal high-pass
%filter response. BUT REMEMBER TO MOVE YOUR
%NEGATIVE FREQUENCY SECTION TO FOLLOW ON AFTER
%THE POSITIVE PART OF THE SPECTRUM !!!
H(1:21)=0;
H(22:81)=1;
H(82:101)=0;
%find the IDFT of the response
h=ifft(H);
htim(1:50)=h(52:101);
htim(51:101)=h(1:51);
%apply a 21 sample rectangular window to the IDFT response
w(1:21)=htim(41:61);
%look at its frequency response
[h1,f1]=freqz(w,1,512,fs);
subplot(2,1,1), plot(f1,abs(h1));
title('Frequency Sampled Highpass Filter');
% CONTINUED
%
ylabel('Magnitude');
%produce a set of time values
k=[0:1:20];
%apply a Hamming window
wham=0.54+0.46*cos(2*pi*(k-10)/21);
%create hwin the new set of windowed coefficients
hwin=wham.*w;
%look at its frequency response
[h2,f2]=freqz(hwin,1,512,fs);
subplot(2,1,2), plot(f2,abs(h2));
title('Hamming Windowed Frequency Sampled Highpass Filter');
xlabel('Frequency');
ylabel('Magnitude');

## Slide 126: Design Example
Frequency Sampled High-Pass Filter

## Slide 127: Important Points Regarding the Frequency Sampling Method
The ideal frequency response that is used will be something like
Before you can sample this response you must make the function causal.
c
-co
1
-0.5
0.5

## Slide 128: Important Points Regarding the Frequency Sampling Method
In other words the negative frequency axis is moved so that it continues on from the maximum value in the positive frequency axis.
This will give:
c
-co
1
-0.5
0.5
1.0
previously at -co
previously at 0

## Slide 129: Important Points Regarding the Frequency Sampling Method
Then you are able to sample this frequency response and perform the IDFT.
It is advisable to choose an odd number of samples since an even number causes all sorts of problems.
['Discrete Systems and Digital Signal Processing' by R.D. Strum and D.E. Kirk (Addison-Wesley,1988)]