## Slide 1
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
Authors:
Maria Reyes Mula-Molina
Mariareyes.mm@gmail.com
Juan Antonio Ferriz-Papi
Juan.ferriz-papi@uwtsd.ac.uk
ICABE 2016 London

## Slide 2
1. Introduction
2. Aim and Objectives
3. Methodology
4. Results and analysis
5. Conclussions
1
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
0. Index
ICABE 2016

## Slide 3
Universities as centres of knowledge and research excellence
Society expectative about environment protection and sustainable development
Solutions for our challenging world
2
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
1. Introduction
ICABE 2016

## Slide 4
Environment awareness of Spanish Universities
2007. Creation of ECOCAMPUS office at the University of Alicante
Necessity of environment assessment
Know present situation – scarce or non-existing information
Some actions already carried out. Others to put in practice
CRUE. Environment Quality and Sustainable Development Workgroup
3
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
1. Introduction
ICABE 2016

## Slide 5
Aim:
Develop a simplified methodology to calculate and compare carbon emissions per user at the University campus.
Objectives:
Study other methodologies applied in different campuses in Spain;
Establish own methodology considering building operations and transport;
Compare and analyse these results.
4
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
2. Aim and objectives
ICABE 2016

## Slide 6
INFORMATION COMPILATION
+
REFERENCES
METHODOLOGIES FOR ASSESSMENT
DEFINITION OF OWN METHODOLOGY
University of Santiago de Compostela
University of Barcelona
Polytechnic University of Cataluña
Miguel Hernández University
Ecological footprint
Carbon footprint
Corporate ecological footprint
Sustainable development
Environment assessment
Indicators
UN publications
ISO,BSI, AENOR
EU Directives
World Resources Institute
etc.
5
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
3. Methodology
ICABE 2016

## Slide 7
6
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
3. Methodology
ICABE 2016

## Slide 8
7
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
3. Methodology
ICABE 2016

## Slide 9
8
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
3. Methodology
ICABE 2016

## Slide 10
ESTIMATION OF CARBON FOOTPRINT
DUE TO BUILDING AND URBAN SERVICES IN THE CAMPUS
OBTAIN ENERGY CONSUMPTION
ESTIMATION OF ELECTRICITY
CARBON EMISSIONS
ESTIMATION OF NATURAL GAS CARBON EMISSIONS
ESTIMATION OF TOTAL CARBON FOOTPRINT
ELECTRICITY
+
NATURAL GAS
EMISSION FACTOR:
ELECTRIC MIX
EMISSION FACTOR:
IDAE
RATE
PER M2 BUILT
OVER THE CAMPUS
PER USER
9
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
3. Methodology
ICABE 2016

## Slide 11
ESTIMATION OF CARBON FOOTPRINT
DUE TO TRANSPORT
DIFFERENT SITUATIONS
ESTABLISH % OF DAILY ATTENDANCE
ASIGN AVERAGE CONSUMPTION
TRANSPORT SURVEY
UNIVERSITY USERS
SPANISH FLEET
ACADEMIC CALENDAR
TERM TIME
OUTSIDE TERM TIME
FUEL TYPE
VEHICLE TYPE
ESTIMATION OF USERS PER TYPE OF VEHICLE
NUMBER OF TRIPS
ASSIGN AVERAGE DISTANCE
ESTIMATION OF DAILY km
(L) OF DAILY FUEL
CONVERSION FACTORS: IDAE
RATE PER USER
10
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
3. Methodology
ICABE 2016

## Slide 12
CARBON FOOTPRINT DUE TO USE
CARBON FOOTPRINT DUE TO TRANSPORT
FINAL CARBON FOOTPRINT
11
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
3. Methodology
ICABE 2016

## Slide 13
2011 |  | 
Kg CO2 |  | TOTAL
Carbon Footprint due to Use | Carbon Footprint due to Transport | 
4,716,481 | 28,938,875 | 33,655,356
RATE PER USER
12
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
4. Results and Analysis
ICABE 2016

## Slide 14
Pie chart
13
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
4. Results and Analysis
ICABE 2016
Chart: CO2 emissions
| Due to Use | Due to Transport
CO2 emissions | 0.1401 | 0.8599

## Slide 15
Chart: Tons of CO2 emissions in a year
| UA | UB | USC | UPC
Toneladas de CO2 anuales | 33655.356 | 30885 | 20601 | 25100
Chart: Tons of CO2 emissions per user and day
| UA | UB | USC | UPC
Toneladas de CO2/persona/día | 3.91 | 2.29 | 4.2 | 4.94
14
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
4. Results and Analysis
ICABE 2016

## Slide 16
15
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
4. Results and Analysis
ICABE 2016
Chart: TOTAL CARBON FOOTPRINT DUE TO USE
 | 19.5647 | 21.9084 | 15.711 | 15.2886 | 21.8606

## Slide 17
16
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
4. Results and Analysis
ICABE 2016
Chart: CO2 EMISSIONS PER BUILDING IN USE
TOTAL SPORTIVE ZONE | 23.2101 | 24.367 | 21.5684 | 12.099 | 24.7345
SCIENCE FACULTY III | 53.0678 | 46.8522 | 34.7253 | 34.3834 | 46.1884
DATA PROCESS CENTRE | 196.6543 | 205.0989 | 142.2919 | 138.1781 | 186.6375
LAW FACULTY - AUDITORIUM | 14.2521 | 19.2184 | 15.2899 | 12.4135 | 15.5535
SOCIAL CLUB I | 6.9151 | 28.6406 | 19.3596 | 19.624 | 28.8202
GENERAL LECTUREROOM BUILDING I | 11.0869 | 12.0608 | 8.3806 | 8.0328 | 11.7622
GENERAL LIBRARY | 43.4223 | 37.5537 | 28.6784 | 28.9521 | 27.7241
COMMERCIAL CENTRE | 9.3632 | 9.7901 | 5.9476 | 4.3868 | 5.9083
POLYTECHNIC FACULTY IV | 14.4344 | 13.8264 | 9.4513 | 9.038 | 12.4029

## Slide 18
17
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
5. Conclussions
ICABE 2016
Methodology established for carbon footprint estimation
  Consideration of use and transport footprints
  Aspects not considered: water consumption, paper or other consumables, waste management, etc.
No apparent decrease of carbon footprint
  Energy meters since 2010
  It was reduced in 2013 and 2014. What happened?
  No evolution comparison per user, only per m2
  New buildings have been incorporated, not analysed
No possibility to split per use inside the building
  Global meters, not per zones or use
Different uses in each building, difficult to compare
Transport Report only in 2011
  No later information. Change in bus lanes and new tram lane
CONCLUSSIONS

## Slide 19
18
Carbon footprint of Educational Establishments:
The Case of the University of Alicante
5. Conclussions
ICABE 2016
Evolution of carbon footprint along time
  Per user and per m2
  Consideration of new buildings
  Extension to other campuses of the UA
Consideration of other carbon footprints
  Water consumption
  Paper and other consumables
  LCA of buildings
Action Plan to reduce the carbon footprint in this campus
  Reduction of energy consumption
  Separate energy meters per use
  Use of renewable energies
  New Transport Study
  Analysis of uses in each building
  Energy efficiengy, LED technology, Smart buildings
Comparison to other universities. Network
FURTHER RESEARCH

## Slide 20
Thank you
for your attention
Maria Reyes Mula-Molina
Mariareyes.mm@gmail.com
Juan Antonio Ferriz-Papi
Juan.ferriz-papi@uwtsd.ac.uk
Carbon footprint of Educational Establishments:
The Case of the University of Alicante