## Slide 1
Module Name : Electronics I
Module Code : ACDB5002
Lecture : 5
Topic : Voltage Regulators
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk

## Slide 2
For low current power supplies - a simple voltage regulator can be made with a resistor and a zener diode connected in reverse.
Zener diodes are rated for their breakdown voltage Vz and maximum power Pz
Zener diode regulator
Voltage Regulators

## Slide 3
Two basic categories of voltage regulation are:
  line regulation(input varies)
  load regulation(load varies)
The purpose of line regulation is to maintain a nearly constant output voltage when the input voltage varies.
The purpose of load regulation is to maintain a nearly constant output voltage when the load varies
Voltage Regulators

## Slide 4: Line Regulation
Line regulation can be defined as the percentage of change in the output voltage for a given change in the input voltage.
Δ means “a change in”
Voltage Regulators

## Slide 5: Load Regulation
Load regulation can be defined as the percentage change in the difference of output voltage from no-load (NL) to full-load (FL) to the full-load.
Where:
VNL = the no-load output voltage
VFL = the full-load output voltage
Voltage Regulators

## Slide 6: Types of Regulator
Fundamental classes of voltage regulators are linear regulators and switching regulators.
Two basic types of linear regulator are the
  Series regulator and
  Shunt regulator
Voltage Regulators

## Slide 7: Types of Regulator
The series regulator is connected in series with the load
The shunt regulator is connected in parallel with the load.
Voltage Regulators

## Slide 8: IC Voltage Regulators
Regulation circuits in integrated circuit form are widely used.
Generally, three terminal devices that provide a positive or negative output.
A typical 7800 series voltage regulator is used for positive voltages.
The 7900 series are negative voltage regulators.
Voltage Regulators

## Slide 9: Fixed Voltage Regulator
The fixed voltage regulator has an unregulated dc input voltage Vi applied to one input terminal, a regulated output dc voltage Vo from a second terminal, and the third terminal connected to ground.
Fixed-Positive Voltage Regulator
The series 78XX regulators are the three-terminal devices that provide a fixed positive output voltage.
Voltage Regulators

## Slide 10: Fixed Voltage Regulator
An unregulated input voltage Vi is filtered by a capacitor C1 and connected to the IC’s IN terminal.
The IC’s OUT terminal provides a regulated +12 V, which is filtered by capacitor C2.
The third IC terminal is connected to ground (GND)
Voltage Regulators

## Slide 11: Fixed Voltage Regulator
IC Part | Output Voltage (V) | Minimum Vi (V)
7805 | +5 | +7.3
7806 | +6 | +8.3
7808 | +8 | +10.5
7810 | +10 | +12.5
7812 | +12 | +14.5
7815 | +15 | +17.7
7818 | +18 | +21.0
7824 | +24 | +27.1
Positive-Voltage Regulators in the 78XX Series
Voltage Regulators

## Slide 12: Fixed Voltage Regulator
Fixed-Negative Voltage Regulator
The series 79XX regulators are the three-terminal IC regulators that provide a fixed negative output voltage.
This series has the same features and characteristics as the series 78XX regulators except the pin numbers are different.
Voltage Regulators

## Slide 13: Fixed Voltage Regulator
IC Part | Output Voltage (V) | Minimum Vi (V)
7905 | -5 | -7.3
7906 | -6 | -8.4
7908 | -8 | -10.5
7909 | -9 | -11.5
7912 | -12 | -14.6
7915 | -15 | -17.7
7918 | -18 | -20.8
7924 | -24 | -27.1
Negative-Voltage Regulators in the 79XX Series
Voltage Regulators

## Slide 14
Thank You