## Slide 1
Aim: To understand the scientific principles associated with an SAU.
Learning Outcomes: Upon the successful completion of this module, the student should be able to:
Specify the role of an SAU;
Recognise the main safety requirements of an SAU; and
Understand the advantages and disadvantages of in-line and out-of-line systems to the OME designer
Safety & Arming Technology

## Slide 2
CHEMISTRY
PHYSICS
MATHEMTATICS

## Slide 3
SAU Schematic

## Slide 4
Role of the SAU
The role of the SAU is to:
Prevent the unintentional initiation of the explosive train of a munition
Allow the initiation of the explosive train once the sequential functions of arming have taken place by which time the missile must have reached a safe separation distance from the launch platform
Ensure the weapon is safe until after launch and separated by a sufficient distance
Closes path between fuze and warhead
Can cause weapon to revert to safe or self-destruct/neutralise

## Slide 5
Safety requirements of the SAU
Must be safe under all conditions and throughout the life of the munition
Arming process must be as simple as possible
Must be checkable during and after assembly
Not possible to assemble mechanism in an unsafe condition
Must be possible to determine if armed or unarmed
An interruptor device should normally be used and must be kept positively locked until arming has taken place.

## Slide 6
Safety requirements of the SAU
7. The system must remain safe until a safe separation distance or time has been achieved
8. Before this, it must be impossible to function the weapon (<1 in 106)
9. Must utilize at least one feature whose operation depends on sensing the environment which is unique to the weapon after initiation of the deployment cycle
10. If in-line fuzing is used, no energy must be present in the fuzing system before arming
11. It must not be possible to arm or initiate any electro-explosive devices during munition testing or setting operations

## Slide 7
Mk 15 Mortar - Crossmaglen

## Slide 8
Safety and Arming Stimuli
Launch acceleration (set-back)
Spin
Spin decay
Time
Deceleration

## Slide 11
Out-of-Line Systems
Advantages | Disadvantages
Long and reliable history Can be very small Low cost Use little electrical power | Use primary explosives Require special precautions when dismantled Arming mechanism not easy to test and reset Requires shutter sealing trials Susceptible to RF interference

## Slide 12: Impact Sensitivity of Primary Explosives
Key: SF = silver fulminate; MF = mercury fulminate; SA = silver azide; LA = lead azide; LS = lead styphnate; DDNP = diazodinitrophenol; GNGT = tetracene; TATP = tri-acetone tri-peroxide; HMTD = Hexamethylene triperoxide diamine; PETN = pentaerythritol tetranitrate
Notes: Initiating substances (primaries) are chemical compounds or mixtures used in improvised igniters or detonators to bring about burning or detonation. The successful initiation begins with a small external stimulus, which is non-explosive (flame, impact, heat, electric spark, friction etc), and where the energy from combustion is magnified. As such, primary compositions are the key to the success of the explosive train whereby the non-explosive impulse is either transferred from the primer to the output charge by flame, or turned into a detonation wave by an intermediary transfer element. Examples of primary explosives of interest are in table. Where known from literature or by experiment, their ‘worst case’ TNT equivalence (TNTe), velocity of detonation (Vd) and friction sensitivity are annotated to provide comparison.
In terms of sensitivity to impact, friction, and electrostatic discharge, the variation in experimental results for primary compositions can be significant. Figures could be quoted from a huge variety of texts but it would be difficult to draw useful comparison. For flame, the comparison is not as difficult since primary explosives can be split into two specific groups: the first group (known as the mercury fulminate group) burn when initiated by flame and may, if required, transition to detonation; the second group (the lead azide group) do not exhibit a pre-detonation zone and initiation by flame produces instantaneous detonation. The following graphical representations are academic summaries which attempt to provide an understanding of trends in relation to impact, friction and electrostatic initiation.
Figure demonstrates that impact sensitivity cannot be reliably quoted without an exact statement of experimental conditions (data taken from numerous sources). For example, lead azide (LA) displays impact energies between 0.6 and 4, whereas DDNP lies between 0.8 and 1.1

## Slide 13: Electrostatic Sensitivity of Primary Explosives

## Slide 14: Friction Sensitivity of Primary Explosives

## Slide 20: Delayed Arming Unit (DAU)
Stored & Safe Position.
Axial Detent Down on Setback. Radial Plunger spun out.
DAU shown is from a HESH round Fuze

## Slide 21
Safety and Arming In-Line

## Slide 22
In-Line Systems
Advantages | Disadvantages
No moving parts Only secondary explosives May be tested and reset many times Does not require special handling precautions Can be fully encapsulated High resistance to RF | Uses high voltage components Cannot be made very small Higher unit cost Uses significant electrical power

## Slide 23: High Voltage DDT initiator
(See earlier Perchlorate Composition CP)

## Slide 24: Exploding Bridgewire Detonator
Notes: All the igniters and detonators described thus far in this chapter contain primary explosives, which can be easily initiated by physical mishaps or by stray electric currents even of low magnitude. Although protection against accidental functioning is provided as far as possible, no explosive train containing primary explosives is as safe as one which contains only secondary explosives. Moreover, an electric circuit which is designed to initiate a train only when powered by a high voltage is clearly safer than one intended to operate from a low-power source. An initiator which provides both of these safety features is the exploding bridgewire (EBW) detonator. EBWs are high voltage devices which consist of a low resistance bridgewire in intimate contact with a low density secondary explosive. To activate, a large amount of energy is dissipated into the bridgewire in a small time interval (typically less than 1 μs). The resultant high power causes the bridge wire to explode and detonate the explosive. In contrast to the hot-wire initiator, the exploding bridgewire (EBW) device uses shock to initiate a reaction. The shock wave produced by the explosion of the bridgewire initiates detonation directly in a secondary explosive. Because of this, primary explosives are not required. When the initiation characteristics of secondary explosives are considered, only pentaerythritoltetranitrate (PETN) pressed at low densities can be initiated by the relatively low shock output of an EBW. Therefore, PETN is the current explosive used in EBWs. EBW initiation of other secondary explosives can be achieved but the energy input requirements necessitate relatively large firing systems.
The EBW detonator which has been commonly used in UK Service is the N1 Mk2. This is a small device, 17.4 mm long, with a moulded thermoplastic body. The bridgewire is of gold, approximately 0.9 mm long and 0.4 mm in diameter. The bridgewire is secured to the insulating body of the detonator and spot welded at each end to a nickel wire contact pin in a similar way to that in a low-tension bridgewire detonator. A filling of low-density PETN is in contact with the wire, and another layer of PETN, pressed to a higher density, is contiguous with the first layer. To initiate the detonator a pulsed current is passed from a 6.5 pF capacitor charged to 2000 V. The current which can rise to more than 700 A heats the bridgewire through the melting, boiling and vaporisation phases. A rapid explosive reaction is initiated which builds up to full detonation throughout the length of the low density filling. Detonation is transferred to the high density pellet, which results in a very powerful output providing reliable detonation of the secondary explosive stemming.
The EBW detonator is safe from initiation by low currents applied accidentally but is prone to “dudding” if a discharge raises the temperature of the explosive. in contact with the wire to a level which modifies its physical condition or melts the bridgewire. EBW detonators can be used in any weapon system in which a high voltage source is available, and have found use in Guided Weapon systems. Since an EBW detonator contains no primary explosive it can be incorporated in an ‘in-line’ fuze. The functioning time of an EBW detonator, being a few microseconds, is far faster than that of any other electrical type except the exploding foil initiator (EFI) detonator and faster than that of any mechanical type. The drawbacks of EBWs are generally due to the thermal stability properties of the PETN, which has a melting point 141.3 °C. However, it is not sufficiently stable above 71 °C limiting the temperature at which EBWs can be used for military requirements, to the range -50 °C to +71 °C. HNS cannot be initiated in EBWs at practical firing energies and therefore the safety advantages conferred by this material are unavailable for EBW applications. However, EBWs can be initiated with longer firing pulses than EFIs and control of fireset inductance is less stringent.

## Slide 25: Exploding Foil Initiator Detonator (Slapper)
Notes: Exploding foil initiator (EFI) detonators often referred to as “Slapper” detonators are safe and reliable high voltage detonators, which can replace Exploding bridgewire (EBW) detonators in explosive trains. They were first devised by J Stroud at Lawrence Livermore National laboratory in the USA in the early 1970’s. Since that time their development has continued in the USA and Europe and they are now used as in-line detonators for use in electronic safety and arming units (ESAUs) in several UK Service munitions including Sea Wolf missiles and the Spearfish and Sting Ray torpedoes. The EFI detonator like the EBW, depends upon direct shock initiation of secondary explosives.
The EFI contains a thin film metal bridge, usually copper deposited on a thin film of polyimide plastic, creating a foil/flyer assembly which is in turn attached to a thin stripline firing cable with copper conductors and to a barrel which consists of an annulus of plastic about 0.25 mm thick. The firing cable, foil/flyer and barrel are laminated together to form a single assembly just a few millimetres thick. This assembly is offered up to a high explosive pellet of either HNS or PETN to form a complete detonator. Because of the space saving method of stripline construction and the simple, reproducible functioning mechanism, EFI detonators are smaller than EBW detonators and give better timing simultaneously between detonators. Firing times are much less affected by variations in fireset parameters.

## Slide 26: Comparison of Detonator Types

## Slide 30: Questions?

## Slide 31
The foundation:
ACDA 4005 – POSE. ACDB 4010 – Study Skills
ACDA 4008 – Mathematics. ACDB 4007 – Physics OME
ACDB 4011 – Chemistry OME. ACDA 4018 – Fundamentals of Electronics
ACDA 4019 – Principles of OME
Understand:
ACDA 6017 – OME Major Project
ACDA 5009 - EMR
ACDA 5007 – Computer Aided Engineering
ACDA 6021 – Data Capture & Evaluation
ACDA 5013 – Safety & Hazard Assessment
ACDA 5021 – Systems Engineering
ACDA 5022 – Work-Based Group Project
ACDA 6022 – OME Safety Management & Law
ACDB 5011 – I & C
ACDB 5011 –
Instrumentation & Control
ACDA 5021 - Advanced Chemistry of OME
ACDB 5015 – Advanced Physics OME
ACDA 6008 – Scientific Principles of OME
ACDA 5009
ACDB 5011
OME Level 4 to Level 6
OME
CADMID
Notes: Typical missile structure (Lockheed Martin)