## Slide 1: Materials Handling
Andrew Thorn

## Slide 2: Materials Handling
Three main aspects
Physical
Management
Technology

## Slide 3: Types of Material Handling System
Manual
Mechanised
Automated

## Slide 4: Materials Handling
Equipment Selection equation
What + Where + When = Equipment selection

## Slide 5: Equipment Selection
What: - type of material being handled in the facility
Where: - routing the material throughout the facility
- type of movement
- length of movement
- limitations of movement
- building limitations
- mobility requirements
- transfer requirements
When: - material in right place at right time

## Slide 6: Rules of Equipment Selection
Use mechanical equipment
Use existing equipment whenever possible
Keep cost considerations in mind
Standardise equipment
Integrate equipment
Provide alternative methods
Check facility limitation
Consider unit cost
Plan for the future
Maintenance

## Slide 7: Symptoms of inefficient Material Handling
Material handling can account for 30 to 70% of manufacturing cost
Symptoms
Aisles cluttered
Over handling of products
Lack of gravity flow movement
Lack of standardisation
Excess scrap

## Slide 8: Symptoms of inefficient Material Handling (2)
Flow inefficiencies
High loss and damage
Idle cube storage
Dirty facilities

## Slide 9: Material Handling Checklist
Is equipment more than 10 years old?
Are breakdowns a result of poor preventative maintenance
Are there excessive employee accidents due to manual handling of materials
Are materials weighing more than 23kg handled manually
Are there many handling tasks that require two or more employees?
Are skilled employees wasting time handling materials

## Slide 10: Material Handling Checklist (2)
Is high storage space being wasted
Are high demurrage charges experienced
Is material being damaged during handling

## Slide 11: Ten Principles of Material Handling
Planning Principle
Standardisation Principle
Work Principle
Ergonomic Principle
Unit load Principle
Space Utilisation Principle
System Principle
Automation Principle
Environmental Principle
Life Cycle Cost Principle

## Slide 12: Material Handling Productivity Ratios
Manual Handling Labour ratio
Handling Equipment Utilisation ratio
Storage Space Utilisation ratio
Movement Operation ratio
Manufacturing Cycle Efficiency ratio
Damaged loads ratio

## Slide 13: Material Handling Ratios
MHL = Persons assigned to material handling duties
Total operating personnel
HEU = Items moved per hour
Theoretical capacity
SSU = Storage space occupied
Total available storage space

## Slide 14: Materials Handling Ratios
M/O = Number of moves
Number of productive operations
MCE = Time spent in facility structure operations
Time spent in the facility structure
DL = Number of damaged loads
Total number of loads

## Slide 15: Manual V Automated
Question
What are the arguments for and against the choice of manual v automated materials handling system

## Slide 16: Issues in Material Handling Systems
Reliability
Total integration
Flexibility and modularity
Upgradeability
Automated identification
Ease of use
maintainability

## Slide 17: Types of Material Handling Equipment
Handtrucks
Powered trucks
Cranes and hoists
Conveyors
AGVS
Other handling equipment

## Slide 18: Material handling analysis techniques
Used to represent the material handling problem for visualisation and analysis purposes
Graphical techniques
Quantitative approaches
- flow rates
- operation & times
- efficiency

## Slide 19: From-to-Charts
Showing the number of deliveries required between different stations in a layout
To
From 1 2 3 4 5
1 0 9 5 6 0
2 0 0 0 0 9
3 0 0 0 2 3
4 0 0 0 0 8
5 0 0 0 0 0

## Slide 20: From-to-Charts
Showing distances between different stations
From 1 2 3 4 5
1 0 200 400 700 N/A
2 N/A 0 N/A N/A 300
3 N/A N/A 0 300 600
4 N/A N/A N/A 0 300
5 N/A N/A N/A N/A N/A

## Slide 21: Quantitative Measures
Transport Work (TW)
TW = Rf Ld
Rf = Flow rate
Ld = Length of delivery
Units for TW are components/h multiplied by the distance (m)

## Slide 22: Quantitative Measures
Total Transport Work (TTW)
TTW = ∑ Rf Ld
TTW is the sum of the individual TW values for each delivery
TTW provides a measure of the total requirements that must be satisfied by the material handling system.

## Slide 23: Quantitative Measures
Total Transport Work Example
Using the data in slides 19 and 20 TTW can be calculated
TTW = 9 x 200 + 5 x 400 + 6 x 700 + 2 x 300 + 9 x 300 + 3 x 600 + 8 x 300
= 15,500 parts m/h

## Slide 24: Inefficiencies in handling
Reasons for
Lost time
Capacity constraints
Loading and unloading time
Return trips with no loads
Downtime for maintenance
Traffic congestion
Scheduling problems

## Slide 25: Explanation of losses
Distance between origination point and destination point is represented by Ld
If Vc represents speed of handling system then the time of delivery is Ld / Vc. This is considered as the productive time of the handling system.
Each delivery may involve unloading and loading taking time away from the available time for transporting materials
Loading and unloading activities can be combined into a single term Th

## Slide 26: Explanation of losses
For a considerable amount of time the carriers are travelling without a load and this is considered an inefficiency
Empty travelling time can determined. If distance moved empty is Le then empty travelling time is Le / Vc
This assumes no stops along route

## Slide 27: Explanation of Losses
Additional inefficiencies in material handling system include traffic congestion and poor scheduling and are sometimes defined by a term called the traffic factor Ft
Systems with negligible losses have a traffic factor of 1.0

## Slide 28: Efficiency of Material Handling System
The various losses can be incorporated into a measure of efficiency for a material handling system, as follows
Eh = Ld / Vc Ft
Ld / Vc + T + Le / Vc
Eh = Overall efficiency of the handling system

## Slide 29: Effect of plant Layout
New or existing
New plant handling system should be considered as part of the layout

## Slide 30: Conveyor Question
A re-circulating conveyor has total length of 50m. Its speed is 10 m/min and spacing of part carriers along its length is 2.5m. Each carrier can hold two parts. Robots are used to load and unload the conveyor at its load and unload stations. The time required to load a part is 0.20min and the unloading time is the same. The required loading and unloading rates are both 1 part/min

## Slide 31: Conveyor Question (2)
What is the maximum possible flow rate of parts on the conveyor system?
How many parts could be contained on the conveyor system if every carrier were filled to capacity?
How much time is required for the conveyor to make one complete loop?
Evaluate the conveyor system design with respect to the three principles developed by Kwo

## Slide 32: Automated Guided vehicle Systems
Three types
Driverless trains
AGVS pallet trucks
AGVS unit load carriers

## Slide 33: Applications
Storage distribution systems
Assembly line operations
Flexible manufacturing systems
Driverless train operations

## Slide 34: Vehicle guidance
Guidance system refers to the method by which the AGVS pathways are defined and the vehicle control systems that follow the pathways
Two principal methods currently in use to define the pathways along the floor: embedded guide wires and paint strips

## Slide 35: Vehicle guidance
Guide wire method: -wires are usually embedded in a small channel cut into the surface of the floor. A frequency generator provides the guidance signal carried in the wire. This signal level creates a magnetic field along the pathway that is followed by sensors on board each vehicle.

## Slide 36: Vehicle guidance
Paint strips: - are used to define the vehicle pathways, the vehicle possesses an optical sensor system that is capable of tracking the paint. The strips can be taped, sprayed or painted on the floor

## Slide 37: Quantitative Analysis
Assumptions
Vehicle operates at a constant velocity throughout its operation
Ignore the effects of acceleration & deceleration
Ignore speed differences that might result from the load carried and other factors that would affect speed

## Slide 38: Quantitative analysis
Time elements
The loading operation at the pickup station and unloading operation at drop-off station to obtain (Th) the (total handling time)
The travel time to the drop-off station
(Ld / Vc)
3. The empty travel time of the vehicle between deliveries (Le / Vc)

## Slide 39: Quantitative analysis
Ignoring any effect of traffic congestion, the total time per delivery per vehicle is given by:
T = Ld + Th + Le
Vc Vc

## Slide 40: Quantitative analysis
The sources of inefficiency in an AGVS that are accounted for by the traffic factor Ft include blocking of vehicles waiting in line, poor scheduling, inefficient routing of vehicles and poor layout of the guide path. The number of vehicles waiting at intersections, and vehicles waiting in line in the system relative to the size of the layout

## Slide 41: Quantitative analysis
To estimate the number of deliveries that can be made per hour by a single vehicle, we assume the Tv is given in minutes and the traffic factor is expressed as a decimal fraction
Number of deliveries/hour/vehicle = 60F
Tv

## Slide 42: Quantitative analysis
The total number of vehicles required in the system can be estimated based on number of deliveries per hour that each vehicle can make and the total number of deliveries that must be made by the system.
No of AGVS =
Number of deliveries required/hour
Number of deliveries/hour/vehicle