## Slide 1
ACBA 4022 | FUNDAMENTALS OF CONSTRUCTION TECHNOLOGY
TRADITIONAL
WALLS & FLOORS
Session 4 • 2-hour interactive class
Understand how older buildings were built —
and how to investigate them today.
• Discuss • Sketch • Diagnose
ACBA 4022 • Fundamentals of Construction Technology
01

## Slide 2
SESSION 4
what can an old floor or wall tell us?
ACBA 4022 • Fundamentals of Construction Technology
02
THINK — 30 seconds
Imagine a house built around 1900.
What clues might tell you how its walls and floors were constructed?
PAIR — 90 seconds
Compare ideas with the person beside you.
Choose one clue and explain what it might tell you.
SHARE — invite 3 quick answers
Wall thickness, stone/brick pattern or mortar
Floorboard direction, movement or creaking
Damp marks, cracks, ventilation grilles or finishes

## Slide 3
SESSION 4
By the end of the session, you should be able to
ACBA 4022 • Fundamentals of Construction Technology
03
Describe common traditional wall materials and construction features.
Explain solid ground floors, suspended ground floors and suspended upper floors.
Recognize common risks and defects: damp, cracking, spalling, decay, noise and heat loss.
Compare traditional solutions with modern expectations for comfort and performance.
Use a simple annotated sketch to explain how a construction works.
You can explain not just what a component is, but why it was used and what can go wrong.

## Slide 4
SESSION 4
Recap: traditional or modern?
ACBA 4022 • Fundamentals of Construction Technology
04
The previous session introduced the difference between traditional and modern construction.
TRADITIONAL — often
Solid masonry; local stone or brick;
lime mortar; timber floors;
methods shaped by local materials and craft.
MODERN — often
Cavity wall construction; engineered components; insulation and moisture control designed into the build-up.
Quick vote: which clue would you investigate first in a 1900s house?
A. Wall thickness
B. Mortar type
C. Floor ventilation
D. All three — and the building context

## Slide 5
SESSION 4
Traditional walls: materials
ACBA 4022 • Fundamentals of Construction Technology
05
Stone
• Long-lasting when suitable stone is used
• Random rubble: irregular pieces
• Ashlar/dressed stone: more regular, worked blocks
Brick + mortar
• Brick sizes support repeatable courses
• Mortar bonds units and accommodates some movement
• Traditional walls commonly used lime mortar
Why local materials matter
Availability and transport costs shaped local building styles.
Local stone and brick can give buildings a strong regional character.
Repair materials should be compatible with the original wall.
what might happen if a very hard modern mortar is used on soft historic brick or stone?

## Slide 6
SESSION 4
Three wall forms to recognise
ACBA 4022 • Fundamentals of Construction Technology
06
outer masonry
inner masonry
1 Random rubble
Irregular stone, often bedded in lime mortar.
2 Ashlar / brickwork
More regular blocks or repeated brick courses; bond affects appearance and arrangement.
3 Solid wall section
One thick masonry wall rather than two leaves with a cavity.
describe one visible difference between rubble stone, ashlar and brickwork without using the word “old”.

## Slide 7
SESSION 4
What must an external wall do?
ACBA 4022 • Fundamentals of Construction Technology
07
Weather
Limit rain penetration and help the building dry.
Structure
Carry loads and remain stable.
Fire
Provide appropriate fire resistance.
Thermal
Limit unwanted heat loss.
Acoustic
Reduce sound transmission.
Durability
Resist wear and remain repairable.
Pair task (2 min): rank the three functions you think matter most in a traditional solid wall. Be ready to defend your top choice.

## Slide 8
SESSION 4
Mortar matters: lime versus cement
ACBA 4022 • Fundamentals of Construction Technology
08
Lime mortar — common historically
• Softer and more vapor-permeable
• Can accommodate small movements
• Helps moisture evaporate from traditional masonry
• Often appropriate for compatible historic repairs
Portland cement mortar — widely used later
• Generally stronger and faster-setting
• Useful in many modern construction contexts
• Can be too hard or less permeable for some soft historic masonry
• Compatibility matters more than “stronger is better”
Key concept: if mortar is much harder than the masonry unit, the brick or stone face may deteriorate (spalling).
Question: in a repair, should the mortar always be the strongest material? Why or why not?

## Slide 9
SESSION 4
Older solid walls: clues, not absolute rules
ACBA 4022 • Fundamentals of Construction Technology
09
outer masonry
inner masonry
Features noted in the material
• Thick solid masonry
• Random rubble or brickwork
• Lime mortar
• Shallow or limited foundations in some older properties
• Often no damp-proof course (DPC)
Important caution
These are clues, not a guaranteed checklist. Buildings vary by region, date, alterations and repair history. Inspect rather than assume.
why is it risky to diagnose a building from its age alone?

## Slide 10
SESSION 4
Activity 1 — diagnose the wall
ACBA 4022 • Fundamentals of Construction Technology
10
In groups of 3
Choose one possible defect from the image panel. Discuss:
1. What can you observe?
2. What might be causing it?
3. What further evidence would you need?
4. What would you avoid doing immediately?
Report back
One person reports the observation; one gives a possible cause; one names the evidence needed before recommending a repair.
Timing: 5 minutes group discussion + 3 minutes feedback.

## Slide 11
SESSION 4
Now look down: what does a floor do?
ACBA 4022 • Fundamentals of Construction Technology
11
Supports occupants, furniture and the floor’s own weight.
Resists or manages moisture, heat and sound transmission.
Provides a surface finish that affects appearance, feel and acoustics.
May be built directly on the ground or suspended from walls / supporting structure.
Quick check
Which floor type would you expect to have an air space beneath it? What might that space be for?

## Slide 12
SESSION 4
Three traditional floor arrangements
ACBA 4022 • Fundamentals of Construction Technology
12
A Solid ground floor
Built up from the ground; often compacted earth with a stone/concrete layer and a finish.
B Suspended ground floor
Timber joists and floorboards above a ventilated void; ventilation is essential.
C Suspended upper floor
Timber joists and boards supported by walls or beams; ceiling below may be open or plastered.
concrete / stone layer
compacted earth
quarry tile finish
Floorboards
Timber joists
Ventilated void
Solid ground floor
Suspended timber ground floor

## Slide 13
SESSION 4
Traditional solid ground floors
ACBA 4022 • Fundamentals of Construction Technology
13
concrete / stone layer
compacted earth
quarry tile finish
Typical historic build-up
Compacted earth/ground → stone or concrete layer → finish such as quarry tiles.
Possible disadvantages
• Can feel cold and hard
• Moisture may move through the floor
• Often lacks modern damp and thermal layers
Discuss
How might the room feel in winter? What signs might suggest moisture?

## Slide 14
SESSION 4
Suspended timber ground floors
ACBA 4022 • Fundamentals of Construction Technology
14
Floorboards
Timber joists
Ventilated void
How it works
Floorboards span across timber joists. Joists transfer loads to supporting walls or other structure.
Why ventilation matters
Air movement beneath the floor helps control moisture. Blocked or inadequate vents can contribute to timber decay.
Modern performance
Insulation may be added carefully, but the design must not block ventilation or trap moisture.

## Slide 15
SESSION 4
Suspended upper floors: what can go wrong?
ACBA 4022 • Fundamentals of Construction Technology
15
Typical features and issues
• Timber joists support floorboards
• Joists may bear on internal walls or beams
• Older floors may have little acoustic or thermal insulation
• Loose nails / board movement can cause creaking
• Deflection, decay or alterations may need investigation
Think like a building surveyor
A creak is a clue, not a diagnosis.
Check moisture, support, fixings and movement before recommending work.
Do not assume every uneven floor is unsafe — assess it properly.

## Slide 16
SESSION 4
Floorboards, quarry tiles and parquet
ACBA 4022 • Fundamentals of Construction Technology
16
Tongue-and-groove boards
• Boards fit together at the edges
• Traditionally nailed at right angles to joists
• Nails can loosen over time, creating creaks
• Sound boards may be sanded and refinished
Quarry tiles
• Common traditional finish on solid floors
• Hard-wearing and visually distinctive
• Inspect for loose tiles, cracks and moisture staining
Parquet
• Short timber pieces arranged in geometric patterns
• Adds visual character
• Can be sensitive to moisture and movement
what clues would help you decide whether a floor finish is original or a later addition?

## Slide 17
SESSION 4
Ceilings below timber floors
ACBA 4022 • Fundamentals of Construction Technology
17
Open ceiling
• Joists and floorboards may be visible from below
• Cheapest finish
• Little inherent sound or thermal insulation
• Sometimes painted or wallpapered
Lath and plaster
• Narrow timber laths fixed across joists/studs
• Wet plaster pushed through gaps to form “keys”
• Traditionally applied in multiple coats
• Used widely from the 1700s until the mid-20th century
Inspection clue
Cracks, bulging or loose plaster may indicate failure of the plaster keys or movement. Avoid disturbing unknown older materials without appropriate checks.

## Slide 18
SESSION 4
Activity 2 — design a floor for a small room
ACBA 4022 • Fundamentals of Construction Technology
18
Scenario: you are advising on a small ground-floor room in an older Welsh house.
Your team must decide
1. Solid floor or suspended timber floor?
2. What materials and layers would you expect?
3. How will you manage moisture?
4. What finish would suit the room?
Deliverable
Draw a simple section sketch and label at least 4 components. Add one advantage, one risk and one question you would investigate on site.
Roles: sketcher • materials expert • defect detective • spokesperson
Timing: 7 minutes to design + 1 minute per team to share. Reward clear reasoning, not artistic skill.

## Slide 19
SESSION 4
Traditional and modern: compare carefully
ACBA 4022 • Fundamentals of Construction Technology
19
Traditional examples
• Solid masonry walls
• Lime mortar
• Solid earth-based floors or suspended timber floors
• Often fewer designed-in insulation layers
• Repairs rely on understanding existing materials
Modern approaches — broad comparison
• Cavity walls with ties and insulation
• Engineered timber / concrete floor systems
• Designed damp-proofing and insulation layers
• Performance requirements set through current standards
• Still need correct detailing and maintenance
Important: traditional does not automatically mean better, and modern does not automatically mean defect-free. Suitability depends on context, condition and performance needs.

## Slide 20
SESSION 4
Exit ticket — show what you learned
ACBA 4022 • Fundamentals of Construction Technology
20
1. Name one material commonly used in traditional solid walls.
2. Why might lime mortar be more suitable than hard cement mortar for some historic masonry?
3. What is the purpose of ventilation beneath a suspended timber ground floor?
4. Give one likely cause of a creaking floorboard.
5. Name one clue you would investigate before recommending a repair.
How to answer
Write short answers independently for 3 minutes. Then compare with a partner and correct one answer in a different colour.

## Slide 21
SESSION 4
Five ideas to take away
ACBA 4022 • Fundamentals of Construction Technology
21
Traditional construction varies by location, materials, age and later alterations.
Wall materials and mortar work as a system — compatibility matters.
Solid floors and suspended floors behave differently, especially around moisture and ventilation.
Defects should be observed and investigated before a repair is prescribed.
Annotated sketches help explain construction clearly and professionally.
Next session link
You will build on this by looking at cavity walls and modern floors.