## Slide 1
Risk Assessment

## Slide 2: Objectives of this Section
Introduce the concept of risk assessment and risk management and its role within UK health and safety legislation.
Define the principle components of risk management.
Outline advanced risk assessment methodologies
To outline a practical risk assessment process.

## Slide 3: Principals of Risk Management
Risk management can be defined as:
The eradication or minimisation of the adverse affects of risks to which an organisation is exposed.

## Slide 4: Stages in Risk Management
Identifying the hazards.
Evaluating the associated risks.
Controlling the risks.

## Slide 5
Regulation 3(1) of the ‘Management of Health and Safety at Work Regulations 1992 states:-
‘Every Employer shall make a suitable and efficient assessment of:-
a) The risks to the health and safety of his employees to which they are exposed whilst they are at work.
b) The risks to the health and safety of persons not in his employment arising out of or in connection with the conduct by him or his undertaking;
For the purpose of identifying the measures he needs to take to comply with the requirements and prohibitions imposed on him by or under the relevant statutory provisions.’

## Slide 6
Hazard :
The potential to cause harm. Harm including ill health and injury, damage to property, plant, products or the environment, production losses or increased liabilities.

## Slide 7
Risk:
The likelihood that a specified undesired event will occur due to the realisation of a hazard by, or during work activities or by the products and services created by work activities.

## Slide 8: Major Hazards
Major hazards associated with complex chemical or nuclear plants, may ‘warrant the need of such techniques as Quantitative Risk Assessment’.
In Quantitative Risk Assessment (QRA) a numerical estimate is made of the probability that a defined harm will result from the occurrence of a particular event.

## Slide 9
Major Hazards:
Quantitative risk assessment
  Commonly used in the high technology industries
  QRA tends to deal with the avoidance of low probability events with serious consequences to the plant and the surrounding environment.

## Slide 10
Risk assessment can be a
‘very straightforward process based on judgement requiring no specialist skills or complicated techniques.’
This approach is commonly known as qualitative or subjective risk assessment.

## Slide 11: Assessing the Risks Subjective risk assessment
Qualitative risk assessment involves making a formal judgement on the consequence and probability using:
Risk = Severity x Likelihood

## Slide 12: Assessing the Risks
The likely effect of a hazard may for example be rated:
1. Major
Death or major injury or illness causing long term disability
2. Serious
Injuries or illness causing short-term disability
3. Slight
All other injuries or illnesses

## Slide 13: Assessing the Risks
The likelihood of harm may be rated
1. High
Where it is certain that harm will occur
2. Medium
Where harm will often occur
3. Low
Where harm will seldom occur

## Slide 14: Assessing the Risks
Risk
=
Severity of Harm
x
Likelihood of occurrence
This simple computation gives a risk value of between 1 and 9 enabling a rough and ready comparison of risks.
In this case the lower the number, the greater the risk, and so prioritises the hazards so that control action can be targeted at higher risks.

## Slide 15: Controlling Risk
Risk Avoidance – This strategy involves a conscious decision on the part of the organisation to avoid completely a particular risk by discontinuing the operation producing the risk e.g. the replacing a hazardous chemical by one with less or no risk potential.
Risk Retention – The risk is retained in the organisation where any consequent loss is financed by the company. There are two aspects to consider here, risk retention with knowledge and risk retention without knowledge.

## Slide 16: Controlling Risk
Risk Transfer – This refers to the legal assignment of the costs of certain potential losses from one party to another. The most common way is by insurance.
Risk Reduction – Here the risks are systematically reduced through control measures, according to the hierarchy of risk control described in earlier sections.

## Slide 17: ALARP
Legislation requires employers to reduce risks to a level that is as low as is reasonably practicable (sometimes abbreviated as ALARP).
To carry out a duty so far as is reasonably practicable means that the degree of risk in a particular activity or environment can be balanced against the time, trouble, cost and physical difficulty of taking measures to avoid the risk.

## Slide 18: Types of Risk Assessment
Within Industry, three types of risk assessment can be distinguished:
Assessments of large scale complex hazard sites, such as those found in the process and nuclear industries. These require QRA’s
General assessments of the complete range of workplace risks – as required under the Management of Health & Safety at Work Regulations, 1999.
Risk Assessments required under specific legislation – for example for hazardous substances (COSHH Regulations, 1998), Manual Handling (Manual Handling Operations Regulations, 1992).

## Slide 19: Advanced Risk Assessment Techniques
Quantitative Risk Assessment
QRA is most commonly used in the process industries to quantify the risks of ‘major hazards’.
QRA used in the offshore oil and gas industries, the transport of hazardous materials, the protection of the environment, mass transportation (rail) and the nuclear industry.

## Slide 20: Quantitative Risk Assessment (1)
Individual Risk is defined as ‘the frequency at which an individual may be expected to sustain a given level of harm from the realisation of specific hazards’.
Societal Risk

## Slide 21: Quantitative Risk Assessment: Acceptance Criteria
The HSE state that ‘broadly, a risk of death of 1 in 1000 is about the most that is ordinarily accepted under modern conditions for workers in the UK and it seems to be the dividing line between what is tolerable and what is intolerable’.

## Slide 22: Hazard & Operability Studies
A HAZOP study is a systematic search for hazards which are defined as deviations within these parameters that may have dangerous consequences.

## Slide 23: Hazard & Operability Studies
HAZOP is a team approach, involving a team of people representing all different functions in a plant.
They identify all the deviations by ‘brain-storming’ to a set of guide words which are applied to all parts of the system.

## Slide 24: Practical Risk Assessment (from BS8800)

## Slide 25: Classify Work Activities
Possible ways of classifying work activities include:
Geographical areas within/outside the organisation's premises.
Stages in the production process, or in the provision of a service.
Planned and reactive work.
Defined tasks (mixing mortar).
BS8800:1996

## Slide 26: Identify Hazards
Broad categories of hazard
To help with the process of identifying hazards it is useful to categorise hazards in different ways, for example by topic, e.g.:
Noise.
Electrical.
Manual handling.
Substances.
Fire and explosion.

## Slide 27
Hazards prompt-list
During work activities could the following hazards exist?
Slips/falls on the level.
Falls of persons form heights.
Falls of tools, materials, etc., from heights.
Inadequate headroom.
Hazards associated with manual lifting/handling of tools, materials, etc..
Hazards from plant and machinery associated with assembly, commissioning, operation, maintenance, modification, repair and dismantling.
BS8800:1996

## Slide 28
Hazards prompt-list
Vehicle hazards, covering both site transport, and travel by road.
Fire and explosion.
Violence to staff.
Substances that may be inhaled.
Substances or agents that may damage the eye.
Substances that may cause harm by coming into contact with, or being absorbed through, the skin.
Substances that may cause harm by being ingested (i.e., entering the body via the mouth).
Harmful energies (e.g., electricity, radiation, noise, vibration).
BS8800:1996

## Slide 29
Hazards prompt-list
Work-related upper limb disorders resulting from frequently repeated tasks.
Inadequate thermal environment, e.g. too hot.
Lighting levels.
Slippery, uneven ground/surfaces.
Inadequate guard rails or hand rails on stairs.
Contractors' activities.
BS8800:1996

## Slide 30: Determine risk
The risk from the hazard should be determined by estimating the potential severity of harm and the likelihood that harm will occur.

## Slide 31
Severity of harm
Information obtained about work activities is a vital input to risk assessment. When seeking to establish potential severity of harm, the following should also be considered:
Part(s) of the body likely to be affected;
Nature of the harm, ranging from slightly to extremely harmful:
  1) Slightly harmful, e.g.:
    Superficial injuries; minor cuts and bruises; eye irritation from dust.
    Nuisance and irritation (e.g. headaches); ill-health leading to temporary discomfort.
BS8800:1996

## Slide 32: Severity of harm
  2) Harmful, e.g.
    Lacerations; burns; concussion; serious sprains; minor fractures.
    Deafness; dermatitis; asthma; work related upper limb disorders; ill-health leading to permanent minor disability.
  3) Extremely harmful, e.g.
    Amputations; major fractures; poisonings; multiple injuries; fatal injuries.
    Occupational cancer; other severely life shortening diseases; acute fatal diseases.
BS8800:1996

## Slide 33
Likelihood of harm
When seeking to establish likelihood of harm the adequacy of control measures already implemented and complied with needs to be considered.
Issues considered:
Number of personnel exposed.
Frequency and duration of exposure to the hazard.
Failure of services e.g. electricity and water.
Failure of plant and machinery components and safety devices.
Exposure to the elements.
BS8800:1996

## Slide 34
Likelihood of harm
Protection afforded by personal protective equipment and usage rate of personal protective equipment;
Unsafe acts (unintended errors or intentional violations of procedures) by persons, for example, who:
  1) May not know what the hazards are.
  2) May not have the knowledge, physical capacity, or skills to do the work.
  3) Underestimate risks to which they are exposed.
  4) Underestimate the practicality and utility of safe working methods.
BS8800:1996

## Slide 35
Quantitative Risk Rating
A favoured method to rate risks is to assign a numerical score for hazard effects, likelihood and severity.
This example is known as a 5 x 5 matrix where scores from 1 to 5 are given to the likelihood and the severity of each hazard. These are then multiplied to give the hazard’s overall risk rating, whilst taking into account the controls in place.
BS8800:1996

## Slide 36
Likelihood | Score | Severity | Risk
Very Unlikely (difficult to see how this can occur) | 1 | Minor Injury (no treatment or absence from work) | 1
Unlikely (not expected to happen, but can’t be ruled out) | 2 | Minor Injury (requiring first aid / possible absence up to 3 days) | 2
Likely (could happen at some stage) | 3 | Injury (requiring over three days absence) | 3
Very Likely (may occur on a regular basis) | 4 | Major Injury (RIDDOR reportable injury / long term absence / health effect) | 4
Certain (no doubt about it – it will happen) | 5 | Death | 5

## Slide 37
The table below indicates how severity and probability combine to produce a risk score.
Ratings are assigned as follows:
1 – 8 = Low risk green – risk is being controlled
9 – 15 = Medium risk orange – risk is controlled but needs further
controls to reduce risk further
16 – 25 = High risk red – risk is high and should stop or immediate
controls implemented

## Slide 38
 | Severity |  |  |  | 
 | Minor Injury (no treatment) | Minor Injury (up to 3 days absence) | Injury (requiring over 3 days absence) | Major Injury (RIDDOR reportable, long term absence or health effects) | Death / multiple deaths
Very unlikely (difficult to see how this can occur) | 1 | 2 | 3 | 4 | 5
Unlikely (but can’t be ruled out) | 2 | 4 | 6 | 8 | 10
Likely (could happen at some stage) | 3 | 6 | 9 | 12 | 15
Very likely (may occur on a regular basis) | 4 | 8 | 12 | 16 | 20
Certain (no doubt about it – it will happen) | 5 | 10 | 15 | 20 | 25

## Slide 39
Risk assessment is a simple process that analyses the hazards present in the workplace and combines the potential severity of each hazard with its probability to produce a measure of the danger, the risk.
The assessments need to be reviewed on regular planned timescales, with the lower risks needing less attention that those that pose a greater threat. Reviews should be carried out on:
• The review date assigned
• Change in legislation
• Change of personnel
• Change of substance
• Change of machinery
• Any changes directed by the manufacturers
• Following an accident / incident
• A complaint
• Any new guidance published

## Slide 40
Prepare risk control action plan
Risk categories shown form the basis for deciding whether improved controls are required and the timescale for action.
The outcome of a risk assessment should be an inventory of actions, in priority order, to devise, maintain or improve controls.
BS8800:1996

## Slide 41
Prepare risk control action plan
The action plan should be reviewed before implementation, typically by asking:
Will the revised controls lead to tolerable risk levels?
Are new hazards created?
Has the most cost-effective solution been chosen?
What do people affected think about the need for, and practicality of, the revised preventive measures?
Will the revised controls be used in practice, and not ignored in the face of, for example, pressures to get the job done?
BS8800:1996

## Slide 42
Changing Conditions and Revising
Risk assessment should be seen as a continuing process. Thus, the adequacy of control measures should be subject to continual review and revised if necessary.
BS8800:1996