## Slide 1
Module Name : Signals and System
Module Code : ACDA4009
Topic : Classification of Signals
Lecture : 3
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk

## Slide 2: Classification of Signals
LEARNING OUTCOMES
Upon the successful completion of this lecture, the student should be able to know:
How the Signals are Classified.
ACDA4009 – Signals and System

## Slide 3
Classification of Signals
ACDA4009 – Signals and System
Signals could be classified as
    Continuous Time and Discrete Time Signals
    Deterministic and Non-deterministic Signals
    Even and Odd Signals
    Periodic and Aperiodic Signals
Classification of Signals

## Slide 4: Classification of Signals
Continuous Time Signals
A signal is said to be continuous when it is defined for all instants of time.
ACDA4009 – Signals and System
x(t)
t
Discrete Time Signals
A signal is said to be discrete when it is defined at only discrete instants of time.
x[n]
n

## Slide 5: Classification of Signals
Continuous Time Signals
‘t’ is used to denote the continuous-time independent variable which is enclosed in parentheses ( )
ACDA4009 – Signals and System
Discrete Time Signals
‘n’ is used to denote the discrete time independent variable which is enclosed in square brackets [ ]

## Slide 6: Classification of Signals
Examples of Continuous Time Signals
ACDA4009 – Signals and System

## Slide 7: Classification of Signals
ACDA4009 – Signals and System
Example of Unit Step Function
When a voltage is switched ON or OFF in an electrical circuit at a specified value of time t.
The switching process can be described mathematically by the function called the Unit Step Function

## Slide 8: Classification of Signals
ACDA4009 – Signals and System
Example of Unit Step Function
u is a function of time t, and u has value zero when time is negative (before we flip the switch); and value one when time is positive (from when we flip the switch).

## Slide 9: Classification of Signals
ACDA4009 – Signals and System
Example of Unit Rectangular Signal
A common situation in a circuit is for a voltage to be applied at a particular time (say t = a) and removed later, at t = b (say).
We write such a situation using unit step functions as:
This voltage has strength (amplitude) 1, duration (𝑏−𝑎)

## Slide 10: Classification of Signals
ACDA4009 – Signals and System
Example of Unit Rectangular Signal
Plot the unit rectangular function for the time a = 1.2 and b = 3.8
We know that V(t) could be obtained for the rectangular signal by utilizing the equation,
The graph of 𝑉(𝑡)= 𝑢(𝑡−1.2) − 𝑢(𝑡−3.8)
Here, the duration is 3.8−1.2 = 2.6.

## Slide 11: Classification of Signals
ACDA4009 – Signals and System
Example of Unit Ramp Signal
Ramp signals are used in the fields of power electronics and testing of power system components.
Breakdown voltage test which is normally conducted on transformer oil, insulators, bushings, etc where the voltages could be in kV

## Slide 12: Classification of Signals
ACDA4009 – Signals and System
Exercise 1
Write the following functions in terms of step function. Sketch the waveform.
A 12-V source is switched on at t = 4 s.
Solution
      Since the voltage is turned on at t = 4, we need to use u(t − 4).
      We multiply by 12 since that is the voltage/Amplitude.
      We write the function as follows:
      𝑉(𝑡)=12⋅𝑢(𝑡−4)

## Slide 13: Classification of Signals
Variations of Sine and Cosine Functions
A cosine curve is graphed similarly to a sine curve but is out of phase with it.
A sine wave crosses the centre line at each interval of π, whereas a cosine wave peaks at intervals of π and crosses the centre line at intervals of ½π
ACDA4009 – Signals and System

## Slide 14: Classification of Signals
Variations of Sine and Cosine Functions
The general forms of sinusoidal functions are
and
where A is the voltage / Amplitude, is the phase shift and
is the vertical shift.
ACDA4009 – Signals and System

## Slide 15: Classification of Signals
Exercise 2
Sketch the wave form for the function
ACDA4009 – Signals and System

## Slide 16: Classification of Signals
Exercise 3
Sketch the wave form for the function
In the general, y = A sin (Bx−C)+D
The phase shift is which is which indicates there is no phase shift
The Value of Vertical shift D = 2
ACDA4009 – Signals and System

## Slide 17: Classification of Signals
ACDA4009 – Signals and System
Examples of Discrete Time Signals

## Slide 18: Classification of Signals
Deterministic Signals
A signal is said to be deterministic if there is no uncertainty with respect to its value at any instant of time. (or)
Signals which can be defined exactly by a mathematical formula are known as deterministic signals.
Example Sine or cosine function.
ACDA4009 – Signals and System

## Slide 19: Classification of Signals
ACDA4009 – Signals and System
Non-deterministic Signals
A signal is said to be non-deterministic if there is uncertainty with respect to its value at some instant of time.
Non-deterministic signals are random in nature hence they are called random signals. Example: Noise

## Slide 20: Classification of Signals
ACDA4009 – Signals and System
Even Signals
A signal x(t) or x[n] is referred to as an even signal if it is identical to its time-reversed counterpart, i.e., with its reflection about the origin.[1]
  In continuous time, a signal is Even if x(-t) = x(t)
  while a discrete-time, signal is Even if x[- n] = x[n].
  It can be written as

## Slide 21: Classification of Signals
ACDA4009 – Signals and System
Odd Signals
A signal is referred to as Odd if x( -t) = - x(t) for continuous or x[-n] = -x[n] for discrete.
An Odd signal must necessarily be 0 at t = 0 or n = 0 that is x(0) = - x(0) and x[0] = - x[0].
It can be written as

## Slide 22: Classification of Signals
ACDA4009 – Signals and System
Even and Odd Signals
+ = ----------(1)
--------(2)
--------(3)
Adding (2) and (3),

## Slide 23: Classification of Signals
ACDA4009 – Signals and System
Ex1: Draw and Plot the even signals for the given discrete time signal given below.
Solution

## Slide 24: Classification of Signals
ACDA4009 – Signals and System
Example:
Find the Even and Odd signal for the function given below

## Slide 25: Classification of Signals
ACDA4009 – Signals and System
Example:
We know that can be written as
Therefore, can be drawn as
X[-n] can be drawn as
Given X[n] is

## Slide 26: Classification of Signals
ACDA4009 – Signals and System
Example:
Also, We know that can be written as
Therefore, can be drawn as
X[-n] can be drawn as
Given X[n] is

## Slide 27: Classification of Signals
ACDA4009 – Signals and System
Ex 3: Find the correct discrete time function for the plot given below
a. b.
c. d. None

## Slide 28: Classification of Signals
Periodic Signals
ACDA4009 – Signals and System
A periodic signal is a signal that repeats itself at regular intervals of time.
A periodic signal can be represented as a sum of sinusoidal functions with frequencies that are integer multiples of the fundamental frequency of the signal.

## Slide 29: Classification of Signals
Aperiodic or non- Periodic Signals
ACDA4009 – Signals and System
A non-periodic signal is a signal that does not repeat itself at regular intervals. This means that it does not have a fundamental frequency.
Examples of non-periodic signals include white noise

## Slide 30: Classification of Signals
ACDA4009 – Signals and System
Exercises

## Slide 31: Classification of Signals
ACDA4009 – Signals and System
Exercises

## Slide 32: Classification of Signals
ACDA4009 – Signals and System
Exercises

## Slide 33: Classification of Signals
References
[1] A. V. OPPENHEIM and A. S. WILLSKY, Signals and System, SECOND ed., UPPER SADDLE RIVER, NEW JERSEY: PRENTICE HALL, 1996.
[2] S. Haykin and B. V. Veen, Signals and System, SECOND ed., USA, 2002.
[3]"tutorialspoint," [Online]. Available: https://www.tutorialspoint.com/signals_and_systems/signals_and_systems_overview.htm.
[4] “lumenlearning,”[Online]. Available: Graphs of the Sine and Cosine Functions | Algebra and Trigonometry
ACDA4009 – Signals and System

## Slide 34
Thank You