## Slide 1: Input and Output
Graham Rees-Evans

## Slide 3: Introduction
Without Input/Output the computer is worthless
Without it
  No Keyboard Input
  No Screen Output
  No Print Output
  No Disk Storage or Retrieval
  No Network or Internet Access

## Slide 4: Input and Output
Managed by I/O Module
Both Handled in a similar way
Information passes between Registers
Particular Registers  Particular Devices
Technique is Programmed I/O

## Slide 5: Factors for Handling I/O
Method of Data Transfer
Simultaneous Operation
Speed of Devices
Time Consuming

## Slide 6: External Devices
Broadly classified into three categories.
Human Readable
Machine Readable
Communication

## Slide 7: Keyboard
Most common computer/user interaction
ASCII
7 bits
128 combinations (27) (000 0000)
Two types of characters
  Printable
  Control

## Slide 8: ASCII
Binary | Oct | Dec | Hex | Glyph
100 0001 | 101 | 65 | 41 | A
100 0010 | 102 | 66 | 42 | B
100 0011 | 103 | 67 | 43 | C
100 0100 | 104 | 68 | 44 | D
100 0101 | 105 | 69 | 45 | E
100 0110 | 106 | 70 | 46 | F

## Slide 9: I/O Module
Control and timing
Processor communication
Device communication
Error detection

## Slide 10: Control and Timing
The processor interrogates the I/O module to check the status of the device.
The I/O module returns the device status.
If ready to transmit processor requests transfer of data, by means of a command.
The I/O module obtains a unit of data from the external device.
The data is transferred from device to processor.
Notes: During any period of time the processor may communicate with one or more external devices in unpredictable patterns, dependant on the need for a programs need for I/O. As internal resources are shared processor, mem etc. the buses must be shared, so timing is needed

## Slide 11: Processor Communication
Command decoding
  The I/O module accepts commands from processor.
Data
  Data is exchanged over the data bus.
Status reporting
  I/O devices are slow, so the readiness will have reported.
Address recognition
  Each I/O device has an address so each address needs to be identified.

## Slide 12: Device Communication
Similar to Processor communication
Devices at different speeds

## Slide 13: Error detection
Two general classes:
Reported by the device
  Mechanical, e.g. paper jam
  Electrical, e.g. bad disk track
Transmit Error
  Unintentional change in bit pattern.

## Slide 14: Error Detection
Simplest is odd or even parity.
The binary number has 1 or 0 added
0 | 0 | 1 | 1 | 1 | 0 | 1 | 0
Binary Value
Parity Bit
1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
Binary Value
Parity Bit

## Slide 15: Modes of Transfer

## Slide 16: Modes of transfer
Three basic ways to transfer of data.
Programmed
Interrupt driven
Direct Memory Access (DMA)

## Slide 17: Modes of Transfer - Programmed
Polling
Processor is total control
Constantly checking port status to see if its ready.
Disadvantage is waste of processing time.
  Often polled 1000 times.
Read Port State
Device Ready?
Transfer Data
Notes: Polling – Check the status of a device

## Slide 18: Modes of Transfer - Interrupt driven
All processors have interrupt pins.
  More efficient.
Allows device to signal processor when ready.
Eliminating needless waiting.
Allows processor to carry on processing.

## Slide 19: Interrupt Sequence
Interrupt signal is sent to processor
  Current instruction is finished
Processor Sends an Acknowledgment
Current program state is saved
Loads pc with address of interrupt handling program.
Interrupt handler processes the interrupt.
Interrupted program resumes.

## Slide 20: Interrupt Prioritisation
Interrupts can be prioritised.
  Fire alarm over a phone call
Some interrupts are more important.
  System timer over a printer
Some processors have few interrupt pins.
If two processes interrupt then who take priority.
Further interrupts are ignored unless there is a higher priority
Notes: Interrupts can come form hardware or a running program

## Slide 21: Disadvantage
Disadvantage of interrupt driven.
  All data is moved to and from CPU registers
  Overhead of preserving and recovering interrupted programs status.
This can slow down the data transfers.
Large volumes of data need to be moved we need better speeds.

## Slide 22: Modes of Transfer – Direct Memory Access
DMA requires an additional module – Direct Memory Controller
Capable of mimicking the CPU.
Takes control over system bus.
CPU must not be utilising the bus.
Cycle stealing.
Notes: DMA transfers can either occur one word at a time, allowing the CPU to access memory on alternate bus cycles - this is called cycle stealing since the DMA controller and CPU contend for memory access.

## Slide 23: DMA Process
When the CPU wishes to R/W a block of data, a command is sent to the DMA controller, and information about the data.
  Read or Write.
  The address of the I/O device.
  The location in memory to R/W. stored then in address register.
  The size of the data.

## Slide 24: Advantages DMA
Entire block of data transferred.
No CPU involvement.
After transfer control is handed back.
It is not an interrupt, no context is stored.
CPU pauses for 1 bus cycle.

## Slide 25: Types of Interfaces

## Slide 26: Parallel
Transfers several bits at one clock cycle.
Been used for higher speed peripherals
    Disks and tape
Parallel Interface | 1 | Parallel Device
 | 0 | 
 | 1 | 
 | 0 | 
 | 1 | 
 | 0 | 
 | 1 | 

## Slide 27: Serial
Serial Interface |  | Serial Device
 | 1010101 | 
Transfers 1 bit at one clock cycle
Traditionally used for digital cameras and device control
Interfaces getting faster

## Slide 29: Recap
Handling Input and Output
Control and Timing
Processor Communication
Device Communication
Errors
Modes of Transfer
Interrupts
Types of Interface