## Slide 1
Prepared By,
- Jenifer Prince Devaraj M.E., M.Ed.
Module Name: Electronics II
Module Code: ACDA6001
Lecture – 1- PART 2

## Slide 2
Logic Gates
Logic gates perform logical operation.
Each gate has one or more input and only one output. OR, AND & NOT are basic gates.
NAND and NOR gates are known as universal gates, from which basic gates can be derived.

## Slide 3: Logic Gates
AND Gate
The AND gate performs a logical multiplication commonly known as AND function.
The output is high when both the inputs are high.
The output is low when any one of the inputs is low.
Truth table
Pin Diagram
Logic symbol

## Slide 4: Logic Gates
OR Gate:
The OR gate performs a logical addition.
The output is high when any one of the inputs is high.
The output is low when both the inputs are low.
Truth table
Pin Diagram
Logic symbol

## Slide 5: Logic Gates
NOT Gate:
The NOT gate is called an inverter.
The output is high when the input is low and the output is low when the input is high.
Truth table
Pin Diagram
Logic symbol

## Slide 6: Logic Gates
NAND Gate:
The NAND gate is a contraction of AND-NOT.
The output is high when both inputs are low and any one of the input is low .
The output is low level when both inputs are high.
Truth table
Pin Diagram
Logic symbol

## Slide 7: Logic Gates
NOR Gate:
The NOR gate is a contraction of OR-NOT.
The output is high when both inputs are low.
The output is low when one or both inputs are high.
Truth table
Pin Diagram
Logic symbol

## Slide 8: Logic Gates
X-OR Gate:
The output is high when any one of the inputs is high.
The output is low when both the inputs are low, and both the inputs are high.
Truth table
Pin Diagram
Logic symbol
=

## Slide 9: Logic Gates
X-NOR Gate:
The output is low when any one of the inputs is high.
The output is high when both the inputs are low, and both the inputs are high.
Truth table
Pin Diagram
Logic symbol
=

## Slide 10: Boolean Algebra - laws
Laws in Boolean Algebra:
The three laws in Boolean Algebra are as follow
Commutative law
Associative law
Distributive law
Boolean algebra simplify the output Boolean expression of the combinational network.

## Slide 11: Boolean Algebra - laws
Commutative law
Law 1: This law states that the order in which the variables are ORed makes no difference in the output.
Eg: A+B=B+A
Input |  | Output | 
A | B | LHS | RHS
 |  | A+B | B+A
0 | 0 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 1 | 1
1 | 1 | 1 | 1

## Slide 12
Commutative law
Law 2: This law states that the order in which the variables are ANDed makes no difference in the output.
Eg: A.B=B.A
Input |  | Output | 
A | B | LHS | RHS
 |  | A.B | B.A
0 | 0 | 0 | 0
0 | 1 | 0 | 0
1 | 0 | 0 | 0
1 | 1 | 1 | 1
Boolean Algebra - laws

## Slide 13
Associative law
Law 1: This law states that ORing of several variables, the result is the same regardless of the grouping of the variables.
Eg: (A+B)+C =A+(B+C)
Input |  |  |  |  | Output | 
A | B | C | A+B | B+C | LHS | RHS
 |  |  |  |  | (A+B)+C | A+(B+C)
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1
Boolean Algebra - laws

## Slide 14
Associative law
Law 2: This law state that ANDing of several variables, the result is the same regardless of the grouping of the variables.
Eg: ((AB).C) =A.(BC)
Input |  |  |  |  | Output | 
A | B | C | AB | BC | LHS | RHS
 |  |  |  |  | (AB).C | A.(BC)
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1 | 1 | 1
Boolean Algebra - laws

## Slide 15
Distributive law
This law state that ORing several variables and ANding the result with a single variables is equivalent to ANDing the result with a single variable with each of the several variables and then ORing the products.
Eg: A.(B+C)=AB+AC
Input |  |  |  |  |  | Output | 
A | B | C | B+C | AB | AC | LHS | RHS
 |  |  |  |  |  | A(B+C) | AB+AC
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Boolean Algebra - laws

## Slide 16
Rules in Boolean Algebra
Any single variables (or) function of several variables can have either 1 (or) 0. Its value depends on the Boolean algebra.
Complement of a variable is represented by a bar (ˉ) or dash (‘ ) over the letter. Eg: Complement of A=0, is (or) A’=1
Logical AND operator of two variables is written by a dot (.) between two variables (or) simply writing together. Eg: A.B (or) AB
The logical OR operator of two variables is written by putting a plus (+) sign in between the variables. Eg: A+B, A+B+C
Boolean Algebra - laws

## Slide 17: Boolean Algebra - Rules
The logical OR operator in Boolean algebra gives following results
  0+0=0
  0+1= 1
  1+0 = 1
  1+1=1
The logical AND operator in Boolean algebra gives following results
  0×0=0
  0×1= 0
  1×0= 0
  1×1=1

## Slide 18
The NOT Operator in the Boolean algebra with variables having either 0 (or) 1 gives
Boolean Algebra - Rules

## Slide 19
The following rules are formulated from the above statement
Rule 1:
0+A=A (or) A+0=A
(ie) 0+0=0 ; 0+1=1
Rule 2:
1+A=1 (or) A+1=1
(ie) 1+0=1 ; 1+1=1
Rule 3:
A+A=A
(ie) 0+0=0 ; 1+1=1
Boolean Algebra - Rules

## Slide 20
0+1=1 (or) 1+0=1
Rule 5:
0.A=0 (or) A.0=0
0.0=0 ; 0.1=0
Rule 6:
1.A=A (or) A.1=A
1.0=0 ; 1.1=1
Boolean Algebra - Rules

## Slide 21
Boolean Algebra - Rules

## Slide 22
Boolean Algebra - Rules

## Slide 23
Theorems in Boolean Algebra
Demorgan’s Theorem
Theorem 1: This theorem states that the complement of a product is equal to the sum of the complements.
Boolean Algebra - Rules

## Slide 24
Demorgan’s Theorem
Theorem 2: The complement of a sum is equal to the product of the complements.
Boolean Algebra - Rules

## Slide 25
Boolean Algebra - Rules

## Slide 26: ACTIVITY Verify the Following Gates with its truth table using Proteus
AND
OR
NOT
NAND
NOR
XOR
XNOR

## Slide 27: Proteus - Procedure
Step 1: Open Proteus 8.6

## Slide 28: Proteus - Procedure
Step 2: Open File  New Project

## Slide 29: Proteus - Procedure
Step 2: Open File  New Project

## Slide 30: Proteus - Procedure
Step 2: Open File  New Project File Name

## Slide 31: Proteus - Procedure
Step 2: Open File  New Project File Name

## Slide 32: Proteus - Procedure
Step 2: Open File  New Project File Name

## Slide 33: Proteus - Procedure
Step 2: Open File  New Project File Name

## Slide 34: Proteus - Procedure
Step 3: Worksheet

## Slide 35: Proteus - Procedure
Step 3: To Add a Component

## Slide 36: Proteus - Procedure
Step 4: To Add a terminal

## Slide 37: Proteus - Procedure
Step 4: To Run the Circuit

## Slide 38
Thank You