## Slide 1: Lighting Energy Useage in UK

## Slide 2: UK Lighting Useage
Chart: UK Lighting
| 1st Qtr | 2nd Qtr | 3rd Qtr
UK Lighting | 70 | 26 | 4

## Slide 3: Why is Lighting Important?
It uses up nearly 1/5th of UK’s energy
Correct lighting relates directly to H and S
Correct lighting improves productivity
Smart Lighting reduces energy requirement

## Slide 4: The light vision of the future

## Slide 5: Recommended lighting Levels

## Slide 6: Colour Theory

## Slide 7: Colour Additive Theory

## Slide 8: 1 Candela Lighting Intensity
Notes: The candle's lighting intensity is equal to 1 candela

## Slide 9: Definition of a Lumen

## Slide 10: Lumens (Brightness)
Lumens (denoted by lm) are a measure of the total amount of visible light (to the human eye) from a lamp or light source. The higher the lumen rating the “brighter” the lamp will appear.

## Slide 11: Definition of a Lumen
The lumen is a significant entity: it measures the total amount of visible light emitted by a given source. All other measurements are based on the lumen.
The lumen measurement originated from the basic concept of foot-candles; it might be illustrated, more or less, by the image shown next. A more scientific definition exists today, but this drawing helps visualize the lumen.
Picture a candle set in the middle of a sphere measuring 0.60 meters (2 feet) in diameter; when we cut a hole that measures 0.09 square meters (1 square foot) in the centre of this sphere, the light that shines through is what we define as a lumen.

## Slide 12: Luminous Flux and Intensity

## Slide 13: Illumination of a Surface

## Slide 14: Typical Illuminance levels (lx)
Mid day the Equator (clear Sky) = 100,000 Lx
Heavily Overcast day in the open = 5,000 Lx
Artificial Light in well lit office = 800 Lx
Full Moon on a clear night = 0.25 Lx

## Slide 15: Laws of Illumination
The illumination on a surface depends on:
The luminous intensity.
The distance between the source and the surface being illuminated.
The direction of the rays of light.
This is governed by the following laws:
Inverse square law
Lambert’s cosine law

## Slide 16: Inverse Square Relationship
E1 d12 = E2 d22

## Slide 17: Inverse square calculations
You measure 10.0 lm/m2 from a light bulb at 1.0 meter. What will the flux density be at half the distance?
What will be the flux density at twice the distance?
If the flux density = 20 lm/m2 what is the distance from the light source.

## Slide 18: Lambert’s Cosine law
Notes: In simple terms, the maximum amount of light reflected from a surface will occur when the light is applied perpendicularly to that surface. This reduces as the angle is made more obtuse and varies in relation to the cosine of the angle.

## Slide 19: Required Lighting Scheme Factors

## Slide 20: Recommended Work Illumination Levels

## Slide 21: Lighting Depreciation Factor

## Slide 22: Artificial Lighting Types

## Slide 23: Incandescent Bulbs & HID

## Slide 24: Sodium Vapour Lamps

## Slide 25: Sodium Vapor Lamps

## Slide 26: Luminous Efficiency

## Slide 27: Colour Rendering

## Slide 28: Colour Rendering Index

## Slide 29: Colour Temperature (K)

## Slide 30: Colour Temperatures (Kelvin scale)

## Slide 31: Examples of Colour Temperatures

## Slide 32: Lighting Classification

## Slide 33: Neon Lighting

## Slide 34: Light Emitting Diodes (LED’s)

## Slide 35: Organic light-emitting Diode(OLED’s)

## Slide 36: OLED’S Lighting (Advantages)

## Slide 37: OLED’S Lighting (Disadvantages)

## Slide 38: Space Illumination

## Slide 39: Localised (Task) Lighting

## Slide 40: Accent Lighting

## Slide 41: Lighting Fixtures

## Slide 42: Direct & Indirect Light Fixtures

## Slide 43: Shielded Light Fixtures

## Slide 44: Linear & Volumetric Sources

## Slide 45: Visual Tasks Illumination Levels

## Slide 46: Lighting Levels

## Slide 47: Lighting in Office

## Slide 48: Lighting Distribution Classification

## Slide 49: Optimum Mean Office Illuminations

## Slide 50: Lighting Symbols

## Slide 51: Lighting Diagrams

## Slide 52: Lighting Design

## Slide 53: Lighting Options & Electric Lighting

## Slide 54: Statistical Exercise
The life expectancy of a sample of 10 light bulbs on a stretch of M4 is
as follows:
8000, 7900, 8100, 7950, 8050, 7800, 7900, 8200, 8100, 8000 hours.
Calculate the mean, and standard deviation for this sample.
What proportion of lights have a life in excess of 8100 hours?
If you want to guarantee that 95% of the lights are on when would you
replace all the lights?
If you want to guarantee that 99% of the lights are on when
would you replace all the lights?