## Slide 1
Fundamental Mechanics of Materials

## Slide 2
Mechanical properties of materials
Hardness – resistance to indentation or scratching
Strength – resistance to applied forces
Brittleness/toughness – resistance to impact loads
Elasticity/stiffness – temporary deformation under load
Plasticity – permanent deformation under load

## Slide 3
Properties of materials
Isotropic
Anisotropic
Orthotropic

## Slide 4
Types of loading
Typical loading types including:
Static – non-fluctuating loads
Live – produced by, for example, cars crossing over a bridge
Impact or shock loads caused by sudden blows
Fatigue, fluctuating or alternating loads – the magnitude and sign of the load changing with time

## Slide 5
Simple (direct) stress
F
F
F
F
Area
Stress σ = F
A
Tension
Compression
Stress is measured
in Nm-2 or pascals
(Pa)

## Slide 6
Direct strain
F
F
δL
L
Strain ε = change in length = δL
original length L
Strain is a dimensionless ratio i.e. it has no units

## Slide 7
Elastic materials – Hooke’s law
Stress = E
Strain
Where E = modulus of elasticity or Young’s modulus
E = stress = P/A = PL
strain δL/L AδL

## Slide 8
Typical tensile test
Load or
stress
Extension or Strain
σy
σt
Yield point
σy = yield stress
σt = ultimate tensile strength
O
A
B
C
OA = elastic behaviour
ABC = plastic behaviour

## Slide 9
More tensile curves
Stiff, brittle
material
Low stiffness, highly elastic
High plasticity material
Typical carbon steel

## Slide 10
Poisson’s Ratio
P
P
Poisson’s ratio ν = lateral strain .
longitudinal strain

## Slide 11
Example 1:
A steel wire AB of length 0.6 m and cross-sectional area 1.5x10-06 m2 is attached at B to a copper wire, BC, of length 0.39m and cross-sectional area 3.0x10-06 m2. The combination is suspended vertically from a fixed point at A, and supports a weight of 250N at C. Find the extension of each section of the wire . (Young’s modulus of steel= 2.0x1011Pa, Young’s modulus of copper=1.3x1011 Pa)
Exercise 1
An aluminium wire of length 0.35 m and radius 0.2mm is stretched by 1.4mm. Young’s modulus of aluminium is 7.0 x1010 Pa.
Find the strain in the wire.
Find the stress in the wire
Find the cross-sectional area of the wire.
Find the tension of the wire

## Slide 12
Sequence of Modules in ABAQUS
File: Set Working Directory
PART - Create individual parts that might be copied multiple times in an assembly
PROPERTY- assign material properties to Sections and assign Sections to regions of parts
ASSEMBLY- create ‘instances’ of each part
INTERACTIONS- eg create contact between two colliding surfaces
STEP- define initial and solver steps - and what type of problem
LOAD- eg add applied forces/tractions to surfaces and add boundary conditions (BCs)
MESH- define a mesh over part and assign finite elements to mesh
JOB- create a job for subsequent submission
VISUALIZER- display results

## Slide 13: Beyond the simple bi-linear elastic-plastic stress strain model
For high strain rate (> 103 s-1 ) situations that we commonly find with explosive loading of ductile materials, a very popular model is the Johnson Cook model that is better for modelling plastic behaviour under dynamic loading:

## Slide 14: Damage initiation and evolution

## Slide 15: J-C damage initiation criterion
When does the plastic strain start the damage?
This will calculate onset of damage

## Slide 16: Damage evolution …can be defined in abaqus as either the displacement or energy required for complete failure after damage initiation