## Slide 1: GIS B Holland 2014
Spatial data
Understanding Maps

## Slide 2: Introduction
The Geographical Information System provides only a computer representation of the read world.
This is a simplified view of reality, but hopefully containing the features important to your study.
The GIS should be populated with ideas about how these data interact and this can be termed a spatial model.
Chorley et al suggest that a spatial model places emphasis on reasoning about the real world by means of translations in space.
Thus we can solve geographical problems that would be otherwise difficult to model.

## Slide 3: Topographic, Thematic etc..
There are many different types of maps. However (Robinson et al..) the following processes need to be considered:
Establish the purpose
Define the scale
Select the feature (spatial entities) from the real world that you want to portray
Choose a method to represent the features point line area
Generalize the feature to provide a two dimensional representation
Use a map projection
Apply a spatial referencing system to locate features relative to each other
Annotate your map with keys Legends and appropriate text.

## Slide 4: Data on the Earths Surface

## Slide 5: Examples of (a) paper maps Source: (a) Maps reproduced by permission of Ordnance Survey on behalf of HMSO. © Crown Copyright 2006. All rights reserved. Ordnance Survey Licence number 100030901; image shown on map brochure courtesy of Peter Baker / International Photobank

## Slide 6: Scale
Virtually all maps and spatial data are smaller than the reality they represent.
Scale gives us an indication of their real size.
We could think of scale as an order of magnitude or the level of Generalisation applied to the objects.

## Slide 7: Expressions of scale

## Slide 8: Spatial Entities
Usually represented by point line or area
This could depend on the scale of the mapped area you are trying to model
OS used different methods of representation depending on the scale

## Slide 9
OS Superplan, Landplan, Explorer, Landranger, Tour, Route maps Crown copyright 2006

## Slide 10
What is scale?
Scale is what makes map drawing possible. It takes real life things and
reduces them in size many times so they can be shown on a map.
Every map has a scale printed on the front and you should always check this
figure before you start reading it. It will tell you how much smaller the area
shown on the map is compared to the same area in real life.
1:25 000
This means that every one unit of measurement on the map (like a
centimetre) is the same as 25 000 of those units (in this case 25 000 cm or
250 metres) in real life.
Ordnance Survey produces maps drawn to many different scales,
depending on what people want to use them for.
Large scale maps
Large scale maps are better for showing individual buildings in detail
because they only cover a small area of land.

## Slide 11: Scale-related generalization
the process of reducing detail on a map as a consequence of
reducing the map scale

## Slide 12: Understand Longitude and Latitude Coordinates
& Map projections

## Slide 13: X and Y
There are two major axes that separate the world. Vertical lines are called Longitude lines, and they refer to the X-coordinate. Horizontal lines are called Latitude lines, and they refer to the Y-coordinate .
The location of the Equator is identified by the X-axis at zero degrees Latitude (wrapping around the globe like a horizontal belt). The Location of the Prime Meridian is identified by the Y-axis at zero degrees Longitude (wrapping around the globe from top to bottom vertically).
The place where the Equator and Primer Meridian intersect creates four quadrants
The first quadrant has both positive X and Y coordinates, the 2nd quadrant has negative X and positive Y coordinates. The third quadrant has negative X and negative Y coordinates, and the 4th has positive X and negative Y.
These basic concepts will help you understand how to get your records with coordinate information on the map.

## Slide 14: Create Points
Some of the data you use may contain X and Y coordinates for the location of that record. If this is the case, MapInfo can read those coordinates and create a point at that location using the “Create Points” command.
Before plotting the data on the map, you should have an understanding of the basics of longitude/ latitude coordinates and how they relate to the surface of the earth.

## Slide 15: The Earth from space and some commonly used global map projections

## Slide 17: Projections: (a) cylindrical; (b) azimuthal

## Slide 18: Projections: (c) conic (Continued)

## Slide 19: Latitude and longitude

## Slide 20
The first quadrant has both positive X and Y coordinates, the 2nd quadrant has negative X and positive Y coordinates. The third quadrant has negative X and negative Y coordinates, and the 4th has positive X and negative Y.

## Slide 21: a) Latitude and longitude of Moscow; (b) calculating the latitude; (c) calculating the longitude