## Slide 1: Routing Concepts Lecture 1

## Slide 2: 1.1 Router Initial Configuration

## Slide 3: Characteristics of a Network

## Slide 4: Why Routing?
The router is responsible for the routing of traffic between networks.

## Slide 5: Routers are Computers
Routers are specialized computers containing the following required components to operate:
  Central processing unit (CPU)
  Operating system (OS) - Routers use Cisco IOS
  Memory and storage (RAM, ROM, NVRAM, Flash, hard drive)

## Slide 6: Routers are Computers (cont.)
Routers use specialized ports and network interface cards to interconnect to other networks.

## Slide 7: Routers are Computers
Router Memory

## Slide 8: Routers Choose Best Paths
Routers use static routes and dynamic routing protocols to learn about remote networks and build their routing tables.
Routers use routing tables to determine the best path to send packets.
Routers encapsulate the packet and forward it to the interface indicated in routing table.

## Slide 9: Packet Forwarding Methods
Process switching – An older packet forwarding mechanism still available for Cisco routers.
Fast switching – A common packet forwarding mechanism which uses a fast-switching cache to store next hop information.
Cisco Express Forwarding (CEF) – The most recent, fastest, and preferred Cisco IOS packet-forwarding mechanism.
Notes: Process Switching
  Process switching is the slowest form of routing because the processor must route and rewrite using software.
Fast Switching
  Is a faster method by which the first packet in a flow is routed and rewritten by a route processor using software, and each subsequent packet is then handled by hardware.
Cisco Express Forwarding (CEF)
  The CEF method uses hardware forwarding tables for most common traffic flows, with only a few exceptions. If you use CEF, the route processor spends its cycles mostly on other tasks.

## Slide 10: Connect to a Network

## Slide 11: Default Gateways
To enable network access devices, must be configured with the following IP address information:
  IP address - Identifies a unique host on a local network.
  Subnet mask - Identifies the host’s network subnet.
  Default gateway - Identifies the router a packet is sent to when the destination is not on the same local network subnet.

## Slide 12: Document Network Addressing
Network documentation should include at least the following in a topology diagram and addressing table:
Device names
Interfaces
IP addresses and
subnet masks
Default gateways

## Slide 13: Enable IP on a Host
Statically Assigned IP address – The host is manually assigned an IP address, subnet mask and default gateway. A DNS server IP address can also be assigned.
  Used to identify specific network resources such as network servers and printers.
  Can be used in very small networks with few hosts.
Dynamically Assigned IP Address – IP Address information is dynamically assigned by a server using Dynamic Host Configuration Protocol (DHCP).
  Most hosts acquire their IP address information through DHCP.
  DHCP services can be provided by Cisco routers.

## Slide 14: Enable IP on a Host

## Slide 15: Enable IP on a Host

## Slide 16: Device LEDs

## Slide 17: Console Access
Console Access

## Slide 18: Enable IP on a Switch
Network infrastructure devices require IP addresses to enable remote management.
On a switch, the management IP address is assigned on a virtual interface called a switched virtual interface (SVI)

## Slide 19: Configure Router Basic Settings
Name the device – Distinguishes it from other routers
Secure management access – Secures privileged EXEC, user EXEC, and Telnet access, and encrypts passwords .
Configure a banner – Provides legal notification of unauthorized access.
Save the Configuration

## Slide 20: Configure an IPv4 Router Interface
To be available, a router interface must be:
Configured with an address and subnet mask.
Activated using no shutdown command. By default LAN and WAN interfaces are not activated.
Configured with the clock rate command on the Serial cable end labeled DCE.
Optional description can be included.

## Slide 21: Configure an IPv6 Router Interface
Configure interface with IPv6 address and subnet mask:
Use the ipv6 address ipv6-address/ipv6-length [link-local | eui-64]interface configuration command.
Activate using the no shutdown command.

## Slide 22: Configure an IPv6 Router Int (cont.)
IPv6 interfaces can support more than one address:
Configure a specified global unicast – ipv6address ipv6-address /ipv6-length
Configure a global IPv6 address with an interface identifier (ID) in the low-order 64 bits - ipv6address ipv6-address /ipv6-length eui-64
Configure a link-local address - ipv6address ipv6-address /ipv6-length link-local

## Slide 23: Configure an IPv4 Loopback Interface
A loopback interface is a logical interface that is internal to the router:
It is not assigned to a physical port, it is considered a software interface that is automatically in an UP state.
A loopback interface is useful for testing.
It is important in the OSPF routing process.

## Slide 24: Verify Interface Settings
Show commands are used to verify operation and configuration of interface:
show ip interfaces brief
show ip route
show running-config
Show commands that are used to gather more detailed interface information:
show interfaces
show ip interfaces

## Slide 25: Verify Interface Settings (cont.)

## Slide 26: Verify IPv6 Interface Settings
Common commands to verify the IPv6 interface configuration:
show ipv6 interface brief - displays a summary for each of the interfaces.
show ipv6 interface gigabitethernet 0/0 - displays the interface status and all the IPv6 addresses for this interface.
show ipv6 route - verifies that IPv6 networks and specific IPv6 interface addresses have been installed in the IPv6 routing table.

## Slide 27: Filter Show Command Output
Show command output can be managed using the following command and filters:
Use the terminal length number command to specify the number of lines to be displayed.
To filter specific output of commands use the (|)pipe character after show command. Parameters that can be used after pipe include:
  section, include, exclude, begin

## Slide 28: Command History Feature
The command history feature temporarily stores a list of executed commands for access:
To recall commands press Ctrl+P or the UP Arrow.
To return to more recent commands press Ctrl+N or the Down Arrow.
By default, command history is enabled and the system captures the last 10 commands in the buffer. Use the show history privileged EXEC command to display the buffer contents.
Use the terminal history size user EXEC command to increase or decrease size of the buffer.

## Slide 29: 1.2 Routing Decisions

## Slide 30: Router Switching Function

## Slide 31: Send a Packet

## Slide 32: Forward to Next Hop

## Slide 33: Packet Routing

## Slide 34: Reach the Destination

## Slide 35: Routing Decisions

## Slide 36: Best Path
Best path is selected by a routing protocol based on the value or metric it uses to determine the distance to reach a network:
  A metric is the value used to measure the distance to a given network.
  Best path to a network is the path with the lowest metric.
Dynamic routing protocols use their own rules and metrics to build and update routing tables:
  Routing Information Protocol (RIP) - Hop count
  Open Shortest Path First (OSPF) - Cost based on cumulative bandwidth from source to destination
  Enhanced Interior Gateway Routing Protocol (EIGRP) - Bandwidth, delay, load, reliability

## Slide 37: Load Balancing
When a router has two or more paths to a destination with equal cost metrics, then the router forwards the packets using both paths equally:
  Equal cost load balancing can improve network performance.
  Equal cost load balancing can be configured to use both dynamic routing protocols and static routes.

## Slide 38: Administrative Distance
If multiple paths to a destination are configured on a router, the path installed in the routing table is the one with the lowest Administrative Distance (AD):
  A static route with an AD of 1 is more reliable than an EIGRP-discovered route with an AD of 90.
  A directly connected route with an AD of 0 is more reliable than a static route with an AD of 1.

## Slide 39: 1.3 Router Operation

## Slide 40: The Routing Table
A routing table is a file stored in RAM that contains information about:
  Directly connected routes
  Remote routes

## Slide 41: Routing Table Sources
The show ip route command is used to display the contents of the routing table:
  Local route interfaces - Added to the routing table when an interface is configured. (displayed in IOS 15 or newer for IPv4 routes and all IOS releases for IPv6 routes.)
  Directly connected interfaces - Added to the routing table when an interface is configured and active.
  Static routes - Added when a route is manually configured and the exit interface is active.
  Dynamic routing protocol - Added when EIGRP or OSPF are implemented and networks are identified.

## Slide 42: Routing Table Sources (cont.)

## Slide 43: Remote Network Routing Entries
Interpreting the entries in the routing table

## Slide 44: Directly Connected Interfaces
A newly deployed router, without any configured interfaces, has an empty routing table.

## Slide 45: Directly Connected Routing Table Entries

## Slide 46: Directly Connected Example

## Slide 47: Directly Connected IPv6 Example

## Slide 48: Static Routes
Static routes and default static routes can be implemented after directly connected interfaces are added to the routing table:
  Static routes are manually configured.
  They define an explicit path between two networking devices.
  Static routes must be manually updated if the topology changes.
  Their benefits include improved security and control of resources.
  Configure a static route to a specific network using the ip route network mask {next-hop-ip | exit-intf} command.
  A default static route is used when the routing table does not contain a path for a destination network.
  Configure a default static route using the ip route 0.0.0.0 0.0.0.0 {exit-intf | next-hop-ip} command.

## Slide 49: Static Route Example

## Slide 50: Static Route Example (cont.)
Entering and Verifying a Static Route

## Slide 51: Static IPv6 Route Examples

## Slide 52: Static IPv6 Route Examples

## Slide 53: Dynamic Routing
Dynamic routing is used by routers to share information about the reachability and status of remote networks.
It performs network discovery and maintains routing tables.
Routers have converged after they have finished exchanging and updating their routing tables.

## Slide 54: IPv4 Routing Protocols
Cisco routers can support a variety of dynamic IPv4 routing protocols including:
  EIGRP – Enhanced Interior Gateway Routing Protocol
  OSPF – Open Shortest Path First
  IS-IS – Intermediate System-to-Intermediate System
  RIP – Routing Information Protocol
Use the router ? Command in global configuration mode to determine which routing protocols are supported by the IOS.

## Slide 55: IPv4 Dynamic Routing Examples

## Slide 56: IPv6 Routing Protocols
Cisco routers can support a variety of dynamic IPv6 routing protocols including:
  RIPng (RIP next generation)
  OSPFv3
  EIGRP for IPv6
Use the ipv6 router ? command to determine which routing protocols are supported by the IOS
IPv6 Routing Protocols

## Slide 57: IPv6 Dynamic Routing Examples

## Slide 58: 1.4 Chapter Summary

## Slide 59: Section 1.1 New Terms and Commands
Topology
Speed
Cost
Security
Availability
Scalability
Reliability
Point-to-Point Protocol (PPP)
Process Switching
Fast switching
Cisco Express Forwarding (CEF)
Wireless access points (WAPs)
Edge router
Gateway of Last Resort
Topology diagram
Secure Shell (SSH)
Hypertext Transfer Protocol Secure (HTTPS)
Console cable
Terminal emulation software - Tera Term, PuTTY, HyperTerminal
Secure management access
Ipv6 address ipv6-address/ipv6-length [link-local | eui-64] interface configuration command.
no shutdown command
loopback interface
interface loopback number command
show ip route command
show running-config interfaceinterface-id
show ip interface brief command
show running-config interface command
show ip interfaces command
Show ipv6 interface command
Notes: New Terms and Commands

## Slide 60: Section 1.1 (cont.) New Terms and Commands
show interfaces command
show ipv6 interface brief command
show ipv6 route command
pipe (|) character
Ctrl+P
Ctrl+N
show history
terminal history
Notes: New Terms and Commands

## Slide 61: Section 1.2 New Terms and Commands
Metrics
Routing Information Protocol (RIP)
Open Shortest Path First (OSPF)
Enhanced Interior Gateway Routing Protocol (EIGRP)
load balancing
IS-IS - Intermediate System-to-Intermediate System
RIPng (RIP next generation)
OSPFv3
Notes: New Terms and Commands

## Slide 62: Section 1.3 New Terms and Commands
Administrative Distance (AD)
Local Route interfaces
Static routes
Route timestamp
Route source
ip route network mask { next-hop-ip | exit-intf }
ip route 0.0.0.0 0.0.0.0 { exit-intf | next-hop-ip }
ipv6 unicast-routing
ipv6 route ::/0 {ipv6-address | interface-type interface-number}
ipv6 route ipv6-prefix/prefix-length {ipv6-address|interface-type interface-number}
Router ? command
Ipv6 router ? command
Notes: New Terms and Commands