## Slide 1: Total Productive Maintenance (TPM)
By
Andrew Thorn

## Slide 2: 1. Avoid wastage in a quickly changing economic environment 2. Producing goods without reducing product quality 3. Reduce cost 4. Produce a low batch quantity at the earliest possible time
Why TPM

## Slide 3: 1. Adoption of the life cycle approach for improving the overall performance of production equipment 2. Improving productivity by highly motivated workers which is achieved by job enrichment 3. The use of voluntary small group activities for identifying the cause of failure, possible plant and equipment modifications
Motives of TPM

## Slide 4: To maximise the overall equipment effectiveness of individual and natural groups of assets within the factory To establish a thorough system of preventative maintenance for the economic lifetime of the equipment To integrate other business departments with the implementation of TPM including the internal customers and internal suppliers To involve every employee from the managing director to the newest apprentice To promote the TPM process and objectives through highly motivated empowered, and autonomous
TPM Objectives

## Slide 5: Step 1: Proper understanding, commitment and active involvement of the top management is needed for this step Step 2: Training for TPM. Training is be done based on the need. Some need intensive training and some just an awareness
Steps in Introducing TPM

## Slide 6
Pillars of TPM

## Slide 7: 1. TPM starts with 5S. Problems cannot be clearly seen when the workplace is disorganised 2. Cleaning and organising the workplace helps the team to uncover problems 3. Making problems visible is the first step of improvement
Pillar 1 5S

## Slide 8
Pillar 1 5S
Japanese Term | Translation | Equivalent ‘S’
Seiri Seiton Seiso Seiketsu Shitsuke | Organisation Tidiness Cleaning Standardisation Discipline | Sort Systematise Sweep Standardise Self-Discipline

## Slide 9: This means sorting and organising the items as critical, important, frequently used items, useless or items not needed as of now
Seiri- Sort Out

## Slide 10
Seiri- Sort Out
Priority | Frequency of use | How to use
Low | Less than once per year. Once per year ≤ | Throw away Store away from the workplace
Average | At least 2/6 months, Once per month Once per week | Store together but offline
High | Once per day | Locate at the workplace

## Slide 11: Seiton - The concept here is that “Each item” has a place, and only one place - The items should be placed back after usage at the same place - To identify items easily, nameplates and coloured tags are used Seiso - Involves cleaning the workplace free of dirt, grease, oil waste, scrap etc.
Seiton/Seiso

## Slide 12: Seiketsu: - Standardisation - Employees discuss together and decide on standards for keeping the workplace/machine/pathways neat and clean - Standards are implemented for the whole organisation and tested regularly Shitsuke: - Self discipline - Considering 5S as a way of life and bringing about self- discipline among employees of the organisation
Seiketsu/Shitsuke

## Slide 13: This pillar is geared towards developing operators to be able to take care of small maintenance tasks freeing up the skilled maintenance people to spend time on more value-added activity and technical reports
Pillar 2 Jishu Hozen (JH)

## Slide 14
Steps in Jishu Hozen
Preparation of employess Initial clean up of machines Take countermeasures Fix tentative JH standards General inspection Autonomous inspection Standardisation Autonomous management

## Slide 15: Step 1: Train employees: - Educate employees about TPM and JH and its advantages Step 2: Initial clean-up of machines: - Arrange items needed for cleaning, employees should clean the equipment completely with the help of maintenance department Dust, stains, oils and grease are removed. Take care of oil leaks, loose wires, loose nuts and worn-out parts
Steps in Jishu Hozen

## Slide 16: Step 3 Countermeasures: - Modify parts to prevent accumulation of dirt and dust and to prevent wear out of machine parts necessary action must be taken Step 4 Tentative standards: - JH schedule followed strictly, including details like when, what and how inspection and lubrication should be done
Steps in Jishu Hozen

## Slide 17: Step 5 General Inspection: - Employees are trained to improve technical skills and to use inspection manuals correctly Step 6 Autonomous Inspection: - New methods of cleaning and lubricating are used, each employee prepares his own autonomous schedule in consultation with supervisor Parts which have never given any problem or don’t need inspection are removed from the list permanently based on experience
Steps in Jishu Hozen

## Slide 18: Step 6 Autonomous Inspection: Inspection that is made in preventive maintenance is included in JH and the frequency of clean up and inspection is reduced based on experience. Step 7 Standardisation: The surroundings of machinery are organised. Items should organised such that there is searching and searching time is reduced. Work environment is modified such that here is no difficulty in getting any item and necessary spares for equipment is planned and procured
Steps in Jishu Hozen

## Slide 19: - “Kai” means change, and “zen” means good (for the better) - Basically, kaizen is for small improvements, but carried out on a continual basis and involving all people in the organisation - The pillar is aimed at reducing issues in the workplace that affect our efficiency - By using a detailed and thorough procedure we eliminate losses in a systematic method using various kaizen tools
Pillar 3 Kaizen

## Slide 20: - The objective of TPM is maximisation of equipment effectiveness - TPM aims at maximisation of machine utilisation and not merely machine availability maximisation - Kaizen pursues efficient equipment, operator and material and energy utilisation that are at extremes of productivity and aims at achieving substantial effects - Kaizen activities try to thoroughly eliminate 16 major issues
Pillar 3 Kaizen

## Slide 21
16 Major Losses in Organisations
Loss | Category
Failure losses- Breakdown loss Set up/adjustment losses Cutting blade loss Start-up loss Minor stoppage/idling loss Speed loss- operating at low speeds Defect/rework loss Scheduled downtime loss | Losses that impede equipment efficiency

## Slide 22
16 Major Losses in a Organisation
Loss | Category
9. Management loss 10. Operating motion loss 11. Line organisation loss 12. Logistics loss 13. Measurement and adjustment loss | Losses that impede human work efficiency
14. Energy loss 15. Die, jig and tool breakage loss 16. Yield loss | Losses that impede

## Slide 23
Classification of Losses
Aspect | Sporadic Loss | Chronic Loss
Causation | Causes for this failure can be easily traced. Cause-effect relationship is simple to trace | This loss cannot be easily identified and solved. Even if various counter measures are applied
Remedy | Easy to establish a remedial measure | This type of losses are caused because of hidden defects
Impact/Loss | A single loss can be costly | A single cause is rare- a combination of causes tends to be a rule

## Slide 24
Classification of Losses
Aspect | Sporadic Loss | Chronic Loss
Frequency of occurrence | The frequency of occurrence is low and occasional | The frequency of loss is more frequent
Corrective action | Usually, the line personnel in production can attend to this problem | Specialists in process engineering, quality assurance and maintenance people are required

## Slide 25: - It aimed to have trouble free machines and equipment producing defect free products for total customer satisfaction - With planned maintenance we evolve our efforts from a reactive to proactive and use trained maintenance staff to help train the operators to better maintain the equipment
Pillar 4 Planned Maintenance

## Slide 26: 1. Zero equipment failure and breakdown 2. Improve reliability and maintainability by 50% 3. Reduce maintenance cost by 20% 4. Ensure availability of spares all the time
Planned Maintenance Aims

## Slide 27: 1. Equipment evaluation and recording present status 2. Restore deterioration and improve weakness 3. Building up information management system 4. Prepare time-based information system select equipment, parts and members/and map out plan 5. Prepare predictive maintenance system by introducing equipment diagnostic techniques 6. Evaluation of planned maintenance
Six Steps in Planned Maintenance

## Slide 28: - Aimed towards customer delight through highest quality through defect free manufacturing - Focus is on eliminating non-conformances in a systematic manner, much like focused improvement gain an understanding of what parts of the equipment affect product quality and begin to eliminate current quality concerns, then move to potential quality concerns
Pillar 5 Quality Management

## Slide 29: - Quality management activities are set to equipment to prevent quality defects, based on basic concept of maintaining perfect equipment to maintain perfect quality of products - The conditions are checked to verify that measured values are within specifications to prevent defects - The conditions are checked to verify that measured values are within specifications to prevent defects
Pillar 5 Quality Management

## Slide 30: - Aims to have a multi-skilled revitalised employees whose morale is high and who are eager to come to work and perform all required functions effectively and independently - Education is given to operators to upgrade their skills - It is not sufficient to know only “know-how” but they should also learn “know-why.”
Pillar 6 Training

## Slide 31: - By experience they gain, “know-how” to overcome problems - This they do without knowing the root cause of the problem and why they are doing so - Hence it becomes necessary to train them on knowing “know-why.” - The goal is to create a factory full of experts
Pillar 6 - Training

## Slide 32: The employees should be trained to achieve the four phases of skill Phase 1: Do not know Phase 2: Know the theory but cannot do Phase 3: Can do but cannot teach Phase 4: Can do and also teach
Pillar 6- Training

## Slide 33: 1. Setting policies and priorities and checking present status of education and training 2. Establishment of training system for operational and maintenance skills 3. Training the employees for upgrading the operational and maintenance skills 4. Preparing the training schedule 5. Start off the systems for training 6. Evaluation of activities and future approach
Steps in Educating and Training Activities

## Slide 34: - Office TPM must be followed to improve productivity, efficiency in the administrative functions and identify and eliminate losses - This includes analysing processes and procedures towards increased office automation. - Office TPM addresses twelve major losses
Pillar 7- Office TPM

## Slide 35: 1. Processing loss 2. Cost loss industry areas such as procurement, accounts, marketing, sales leading to high inventories 3. Communication loss 4. Idle loss 5. Set-up loss 6. Accuracy loss 7. Office equipment breakdown
Office TPM Major Losses

## Slide 36: 8. Communication channel breakdown 9. Time spent on retrieval of information 10. Non-availability of correct online stock status 11. Customer complaints due to logistics 12. Expenses on emergency dispatches/purchases
Office TPM Major Losses

## Slide 37: 1. Providing awareness about office TPM to all support departments 2. Helping them identify PQCDSM in each function in relation to plant performance 3. Identify the scope for improvement in each function 4. Collect relevant data 5. Help them to solve problems in their areas
How to Start Office TPM

## Slide 38: 6. Make up an activity board where progress is monitored on both sides- results and actions along with Kaizens 7. Expand out to cover all employees and circles in all functions
How to Start Office TPM

## Slide 39: - Inventory reduction - Lead time reduction of critical processes - Motion and space losses - Retrieval time reduction - Equalising workload
Kaizen topics for Office TPM

## Slide 40: P – Production output lost due to want of materials, manpower productivity, production output loss Q – Mistakes in preparation of payments, invoices, payroll, customer returns C – Buying cost/unit produced, cost of logistics – inbound/outbound, cost of carrying inventory, cost of documentation, demurrage cost
PQCDSM in Office TPM

## Slide 41: D – Logistics losses (Delay in loading/unloading) - Delay in delivery due to support functions - Delay in payment to suppliers - Delay in information S – Safety in material handing/stores/logistics. Safety of soft and hard data M – Number of Kaizens in office areas
PQCDSM in Office TPM

## Slide 42: - This area focuses to create a safe workplace and surrounding area that is not damaged by our processes or procedures - This pillar will play an active role in each of the other pillars on a regular basis
Pillar 8- Safety, Health and Environment