## Slide 1
EXAM GENERAL TOPICS FOR REVISION:
6 Questions in all…chose any 4….2 hours
One ‘Geological Mapping’ Question
To Know:
Apparatus studied and Use of the test.
Methodologies for the Test Procedures
Associated Calculation
Soil Mechanics Equations, Parameters
and their Use.
Permeability
Compaction and Consolidation
4. Constant Head apparatus and Atterburg Limits
have already been covered by the Assignment.

## Slide 2: Shear Strength
Revision Questions

## Slide 3
The following observations were taken in a series of tests in a 60 mm×60 mm Direct Shear Box
Normal load (KN/m2) | Max. shear load (KN/m2)
100 | 150
200 | 230
300 | 308
400 | 380
Find:
1. The position of the Failure Envelope.
2. The value of cohesion and the angle of friction ϕ
for the soil.

## Slide 4
Shear box results for a clayey soil sample
t
s
N1
N2
Shear Stress
Normal ( Confining) Stress
Failure Envelope
C
f
KN/m2
KN/m2
C = 68 KN/m2
F = 39o

## Slide 5
 |  | Cell pressure (Effective Stress) | Deviator stress | Major Principal stress (Axial Stress) (Confining + deviator)
 |  | s3 | (s1 - s3) | s1
 | Test 1 | 200 | 281.7 | 481.7
 | Test 2 | 400 | 319.6 | 719.6
 | Test 3 | 600 | 383.0 | 983.0
A series of Tri-axial tests were performed on a soil. Each test was carried out until the sample sheared. The principal stresses for each test were as follows.
Plot the Mohr’s stress circles for the soil and hence determine:
The position of the failure envelope
The Angle of Internal Friction of the soil
The Cohesion value
The values of shear and normal stress on the plane of failure for Test 3
s3 KN/m2
s1 KN/m2

## Slide 6
Chart: Normal stress
 | 97.0103 | 208.5915
 | 0 | 0
 | 0 | 0
 | 0 | 0
 | 0 | 0
 | 0 | 0
 | 0 | 0
 | 0 | 0
 | 0 | 0
Mohr’s Circle Diagram
Cohesion = | 97 | KN/m2
Angle of Friction = | 6.9° | 
Shear
Stress
KN/m2
KN/m2

## Slide 7
Soil Parameters
Revision Question

## Slide 8
In its natural condition, a soil sample has a mass of 2300g and a volume of 1.15 x 10 -3 m3.
After being completely dried in an oven, the mass of the sample is 2185g.
The value of Gs for the soil is 2.66.
Determine the following:
1. The bulk density
2. Unit weight
3. Water content %
A second sample was found to have Void Ratio of .50 and a moisture content of 14% determine:
4. The Porosity of this second sample
5. The Degree of Saturation for this sample

## Slide 9
1) Bulk density ρ = M = 2.300 = 2000 kg/m3
V 1.15 x 10⁻3
2) Unit weight ϒ = Mg = ρ x g = 2000 x 9.8 = 19600 N/m3 = 19.6kN/m3
V
3) Water content w = Mw = 2300-2185 = 0.052 or 5.2%
Ms 2185

## Slide 10
5) Porosity n = e = 0.5 = 0.5 = 0.33 or 33%
1+ e 1+ 0.5 1.5
6) Degree of saturation ST = wGs = 0.14 x 2.66 = 0.744 or 74.4 %
e 0.5