## Slide 1: Systems Engineering by Google Maps.
Level 4 …………………….Only Worry about the blue.
The Orange will be the transition to level 5.

## Slide 2
Operational Requirements
Concise statement of purpose with key constraints

## Slide 3
Requirements
NF System
Requirements
NF System
What the whole system has to do……Normally what the customer tell us. But we must build on these. Gemba visits, put yourself in the customer’s shoes, customer complaints

## Slide 4
Requirements
NF-Performance
Requirements
NF System
How well the system has to do it. Target values. Often not sepecified but given as “as low as possible” etc.
Requirements
NF-Performance

## Slide 5
Functional Requirements
What the system has to do, Rarely given by the customer and have to be determined by the designer.
Use a use case a functional flow or examination of an existing design to find the functions.
Functional requirements have a verb / noun relationship. Paint The fence. Wash the car. The noun must be a “Concrete” noun! Something you can touch
Requirements
NF System
Requirements
NF-Performance
Functional Requirements
Paint the fence. BAD CHOICE OF WORDS -> Suggests a solution!
Protect fence (Against moisture ingress) better.
Now we can include dipping, wood preservatives, galvanising etc. as solutions
(Note……fence may not be wooden……)
Functions!
Give the opportunity to perform an FFMEA early in the design.

## Slide 6
More NF Performance Requirements
Rarely given by the customer. Often have to be derived by us.
These performance requirements relate to the function specifically.
How do we pick between two options? What do we measure? What is the target value FOR THE FUNCTION.
Requirements
NF System
Requirements
NF-Performance
Functional Requirements
More NF Performance Requirements
Relationships go in here
9 = Strong
3 = Medium
1 = Week
Prioritise
Ranking
QFD 1

## Slide 7
More NF Performance Requirements
Rarely given by the customer. Often have to be derived by us.
These performance requirements relate to the function specifically.
How do we pick between two options? What do we measure? What is the target value FOR THE FUNCTION
Requirements
NF System
Requirements
NF-Performance
Functional Requirements
More NF Performance Requirements
This well
In order to meet this requirement
I have to perform this
To this level

## Slide 8
Solutions
Developed from our list of functional requirements
How do we want to achieve our functions?
What are the means at our disposal?
Sensible? Futuristic? “Out there”?
Functional
Requirements
Work out solutions
Select
De-select
Make combinations to develop concepts
Pick winning concept
Pugh or other Multi Criteria Analysis.
Solutions

## Slide 9
Solutions
Select our “winning “ means from FMA
Functional Requirements
Requirements
NF-Performance
Solutions
Target Specification
To This Level
In order to perform this function
I have to use this solution,
To this Specification

## Slide 10
Functional Requirements
Requirements
NF-Performance
Solutions
Target Specifications
Relationships go in here
9 = Strong
3 = Medium
1 = Week
Prioritisation
Carried forward
Ranking
QFD 2

## Slide 11
Solutions analysed via P diagrams
System has an input and output
What can we control?
What are noises (Environmental …..Including humans, Unit to Unit, and deterioration. )

## Slide 12
Control FACTORS
Control factors…..Factors we control as designers.
Dimensions, materials etc.
Noise Factors
Noise factors…..Factors from the outside world that upset or affect the output of the system.
3 Flavours, Unit to Unit, Deterioration, Environmental.
Control FACTORS
Noise Factors
Noise Factors
Noise Factors
What Why table. Indicates where noises “Hit” our controls.
Controls with a lot of hits need care.
Noises that hit a lot of controls need reducing.

## Slide 13
Functional Requirements
So far we’ve only got the generic functionality. Top level
There is more detail we need to uncover by looking at our designs.
Performing a functional analysis on the design will reveal……………
Emergent Functionality
Functions required to hold the structure of the device together
Architectural Functionality
Functions that prevent undesirable emergent behaviour
Solution Dependant Functionality
Those functions which are dependent upon the solution selected
Legislative
Functionality
That necessitated by the law of the land

## Slide 14
QFD 1 will grow and start to become unmanageable!
Suggest and architecture
Decompose into sub systems
Use QFD 2 to identify critical sub systems and components

## Slide 15
Design of the manufacturing system.
A “Rinse and repeat” exercise of the design of your object
EXCEPT
The FUNCTIONS are the PROCESS STEPS in your manufacturing process.
We can apply PFMEA here to identify the issues.

## Slide 16
Function Means analysis again gives us our process Means
The specific routes or techniques we are going to use.
It is these means we are going to carry forward into our next phase of analysis….
Together with Important stuff, New stuff and difficult stuff from our design analysis.
Need to determine what makes the list above so……….
…………..Enter QFD 3

## Slide 17
Manufacturing
Solutions
Our winning manufacturing solutions from FMA
Design Solutions
Target Specification
Manufacturing Solutions
Target Process Controls
To This Level
In order make this solution
I have to use this manufacturing solution,
To these settings
Relationships
Ranking
QFD 3

## Slide 18
Control FACTORS
Control factors…..Factors we control as designers.
Dimensions, materials etc. From P Diagram.
Noise Factors
Noise factors…..Factors from the outside world that upset or affect the output of the system. From P- Diagram
3 Flavours, Unit to Unit, Deterioration, Environmental.
Control FACTORS
Noise Factors
Noise Factors
Noise Factors
What Why table. Indicates where noises “Hit” our controls.
Controls with a lot of hits need care.
Noises that hit a lot of controls need reducing.

## Slide 19
Control Measures
Things we put in place to reduce reject and limit noise.
Manufacturing Solutions
RPN Calculation
Control Measures
Target Process Controls
Relationships
Ranking
QFD 4