## Slide 1
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk
Module Name : Electronics II
Module Code : ACDA6001
Topic : Xilinx VIVADO Experiments
Lecture : 11

## Slide 2
Xilinx VIVADO
Xilinx VIVADO
Vivado is the Hardware Development suite used to create a VHDL, Verilog, or any other HDL design on the latest Xilinx FPGA.
In other words, when you need to translate your VHDL design into a configuration file to be downloaded into a Xilinx FPGA, you need Vivado framework.

## Slide 3
Xilinx VIVADO
Xilinx VIVADO
Vivado is an integrated tool that allows you to perform the complete design flow for a Xilinx FPGA:
Simulate
Synthesize
Map
Route
Analyze Timing
Create a bit-stream FPGA configuration File
Configure FPGA
Debug the FPGA using ILA (Integrated Logic Analyzer)

## Slide 4
Xilinx VIVADO
Xilinx VIVADO
Vivado is an integrated tool that allows you to perform the complete design flow for a Xilinx FPGA:
Simulate
Synthesize
Map
Route
Analyze Timing
Create a bit-stream FPGA configuration File
Configure FPGA
Debug the FPGA using ILA (Integrated Logic Analyzer)

## Slide 5
Xilinx VIVADO
  Starting a new Vivado project
Every FPGA hardware development tool needs to create a project.
A project contains all the information the different development FPGA software need to realize a design in FPGA.

## Slide 6
Xilinx VIVADO
  Starting a new Vivado project

## Slide 7
Xilinx VIVADO
  Starting a new Vivado project
Project Name and the project folder. If you select the “Create project subdirectory”, Vivado will create a subfolder named as the Project name under the Project location folder.

## Slide 8
Xilinx VIVADO
  Starting a new Vivado project
“Project Type”. To create a project based on a VHDL design entry, select the “RTL Project” selection.

## Slide 9
Xilinx VIVADO
  Add Source files in Vivado Project
By clicking next on the “Project Type” window will open a new “Add source” window as shown here.

## Slide 10
Xilinx VIVADO
  Add Source files in Vivado Project

## Slide 11
Xilinx VIVADO
  Add Source files in Vivado Project
Every design should have a constraint file. The constraint files are related mainly to
Timing
Mapping, when you need to fix a location of your design inside the FPGA
Pin

## Slide 12
Xilinx VIVADO
  Add Source files in Vivado Project
In the first run of your design can be done without considering this step and complete the design to understand is the design flow works fine.
Design can be created and add the design constraint file in a second step after the first trial layout.
In this case, Vivado GUI can be used to create and add design constraints.
But if set timing constraints are not created, Vivado does not provide the timing analysis.

## Slide 13
Xilinx VIVADO
  Vivado Project Part selection
The last step to create a project on Vivado is the Device selection of as shown in the figure .

## Slide 14
Xilinx VIVADO
  Vivado Project Part selection
By clicking finish, Vivado initializes the project and is ready to start compiling the VHDL design..

## Slide 15
Xilinx VIVADO
  Vivado Run Project Implementation
To start compiling the design just click on the “play” button
Vivado ML Overview (xilinx.com)

## Slide 16
Synthesis
Xilinx VIVADO
In Synthesize process, VHDL codes are compiled and translated into netlist by a program called a synthesis tool. Synthesis will convert the RTL code to the netlist.
As the synthesis tool is running, the program will print out a lot of information about what the program is doing at the moment. All the errors occurring during the synthesis process are all described in the log.

## Slide 17
Implementation
Xilinx VIVADO
After the design is synthesized, you need to run the Implementation process. Implementation tool will take the netlist as input and does optimization, placement and routing.
The implementation process maps the synthesized design onto the FPGA chip targeted by the design.
When implementation is running, select log panel which is located at the bottom of Project Manager All the errors occurring during the implementation process are all described in the log.

## Slide 18
Simulation
Xilinx VIVADO
It describes the behaviour of the circuit in terms of input signals, output signals and the knowledge of delays.
It is described in terms of occurrence and waveforms in a circuit and is based on discrete event simulation.
Each event is described by the type of event and the time it is to occur.

## Slide 19
Test Bench Code for Simulation
Xilinx VIVADO
VHDL Testbench is important part of VHDL design to check the functionality of Design through simulation waveform.
A test bench is HDL code that allows you to provide a documented, repeatable set of stimuli that is portable across different simulators.
Testbench consist of entity without any IO ports, Design instantiated as component, clock input, and various stimulus inputs.

## Slide 20
Thank you