## Slide 1
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk
Module Name : Electronics II
Module Code : ACDA6001
Topic : State Reduction Example
Lecture : 11

## Slide 2: (i) Determine the reduced state diagram for the state diagram given below. (ii) Also, for the obtained reduced state diagram answer the following and design a synchronous Sequential Circuit using D Flip Flop.
State Reduction - Example
Show the Reduced State Table
Show its state Assignment.
Obtain the PS- NS Table.
Obtain Excitation Table.
Output Expressions
Logic Circuit
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 3: (i) To draw the Reduced State Diagram Step 1: State Table
 | Next State |  | Output(z) | 
Present State | x = 0 | x = 1 | x = 0 | x=1
a | a | b | 0 | 0
b | c | d | 0 | 0
c | a | d | 0 | 0
d | e | f | 0 | 1
e | a | f | 0 | 1
f | g | f | 0 | 1
g | a | f | 0 | 1
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 4: To draw the Reduced State Diagram Step 2: Reduced State Table
 | Next State |  | Output(z) | 
Present State | x = 0 | x = 1 | x = 0 | x =1
a | a | b | 0 | 0
b | c | d | 0 | 0
c | a | d | 0 | 0
d | e | f | 0 | 1
e | a | f | 0 | 1
f | e | f | 0 | 1
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 5: To draw the Reduced State Diagram Step 2: Further Reduced State Table
 | Next State |  | Output(z) | 
Present State | x = 0 | x = 1 | x = 0 | x =1
a | a | b | 0 | 0
b | c | d | 0 | 0
c | a | d | 0 | 0
d | e | d | 0 | 1
e | a | d | 0 | 1
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 6: To draw the Reduced State Diagram Step 3: Reduced State Diagram
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 7: (ii) From Reduced State Diagram Step 1: Show its Reduced state Table
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 8: (ii) From Reduced State Diagram Step 2: Show its state Assignment
a ---> 000
b ---> 001
c ---> 010
d ---> 011
e---> 100
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 9
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2
Present State | Input | Next State | Output
q2 q1 q0 | X | Q2 Q1 Q0 | Z
0 0 0 | 0 | 0 0 0 | 0
0 0 0 | 1 | 0 0 1 | 0
0 0 1 | 0 | 0 1 0 | 0
0 0 1 | 1 | 0 1 1 | 0
0 1 0 | 0 | 0 0 0 | 0
0 1 0 | 1 | 0 1 1 | 0
0 1 1 | 0 | 1 0 0 | 0
0 1 1 | 1 | 0 1 1 | 1
1 0 0 | 0 | 0 0 0 | 0
1 0 0 | 1 | 0 1 1 | 1
1 0 1 | 0 | d d d | d
1 0 1 | 1 | d d d | d
1 1 0 | 0 | d d d | d
1 1 0 | 1 | d d d | d
1 1 1 | 0 | d d d | d
1 1 1 | 1 | d d d | d
 | Next State |  | Output (z) | 
Present State | x = 0 | x = 1 | x = 0 | x =1
000 | 000 | 001 | 0 | 0
001 | 010 | 011 | 0 | 0
010 | 000 | 011 | 0 | 0
011 | 100 | 011 | 0 | 1
100 | 000 | 011 | 0 | 1
OR
Step 3: PS – NS Table

## Slide 10: Step 4: Obtain Excitation Table using D Flip- flop.
Present State | Input | Next State | Output | D Flip-flop
q2 q1 q0 | X | Q2 Q1 Q0 | Z | D2 D1 D0
0 0 0 | 0 | 0 0 0 | 0 | 0 0 0
0 0 0 | 1 | 0 0 1 | 0 | 0 0 1
0 0 1 | 0 | 0 1 0 | 0 | 0 1 0
0 0 1 | 1 | 0 1 1 | 0 | 0 1 1
0 1 0 | 0 | 0 0 0 | 0 | 0 0 0
0 1 0 | 1 | 0 1 1 | 0 | 0 1 1
0 1 1 | 0 | 1 0 0 | 0 | 1 0 0
0 1 1 | 1 | 0 1 1 | 1 | 0 1 1
1 0 0 | 0 | 0 0 0 | 0 | 0 0 0
1 0 0 | 1 | 0 1 1 | 1 | 0 1 1
1 0 1 | 0 | d d d | d | d d d
1 0 1 | 1 | d d d | d | d d d
1 1 0 | 0 | d d d | d | d d d
1 1 0 | 1 | d d d | d | d d d
1 1 1 | 0 | d d d | d | d d d
1 1 1 | 1 | d d d | d | d d d
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 11: From the Reduced State Diagram Step 5: K Map Expressions
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 12
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 13: Step 6 : Logic Diagram
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 14: Reference [1] S. Salivahanan and S. Arivazhagan, Digital Circuits and Design, Paperback ed. New Delhi, India: Vikas Publishing, Jan. 2018.
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 15
Thank you