## Slide 1
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk
Module Name : Electronics II
Module Code : ACDA6001
Topic : State Reduction Example
Lecture : 13

## Slide 2: Determine the reduced state diagram for the state diagram given below. Also, for the obtained reduced state diagram answer the following
State Reduction - Example
Show its state Assignment.
Obtain the State Table.
Obtain Excitation Table using any Flip- flop.
Output Expressions
Logic Circuit
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 3: To draw the Reduced State Diagram Step 1: State Table
 | Next State |  | Output | 
Present State | x = 0 | x = 1 | z = 0 | z =1
a | a | b | 0 | 0
b | c | d | 0 | 0
c | a | d | 0 | 0
d | e | f | 0 | 1
e | a | f | 0 | 1
f | g | f | 0 | 1
g | a | f | 0 | 1
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 4: To draw the Reduced State Diagram Step 2: Reduced State Table
 | Next State |  | Output | 
Present State | x = 0 | x = 1 | z = 0 | z =1
a | a | b | 0 | 0
b | c | d | 0 | 0
c | a | d | 0 | 0
d | e | f | 0 | 1
e | a | f | 0 | 1
f | e | f | 0 | 1
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 5: To draw the Reduced State Diagram Step 2: Further Reduced State Table
 | Next State |  | Output | 
Present State | x = 0 | x = 1 | z = 0 | z =1
a | a | b | 0 | 0
b | c | d | 0 | 0
c | a | d | 0 | 0
d | e | d | 0 | 1
e | a | d | 0 | 1
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 6: To draw the Reduced State Diagram Step 3: Reduced State Diagram
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 7: From Reduced State Diagram Step 1: Show its state Assignment
a ---> 000
b ---> 001
c ---> 010
d ---> 011
e---> 100
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 8: From the Reduced State Diagram Step 2: Obtain the state Table
a ---> 000
b ---> 001
c ---> 010
d ---> 011
e---> 100
Present State | Input | Next State | Output
P Q R | X | P Q R | Z
0 0 0 | 0 | 0 0 0 | 0
0 0 0 | 1 | 0 0 1 | 0
0 0 1 | 0 | 0 1 0 | 0
0 0 1 | 1 | 0 1 1 | 0
0 1 0 | 0 | 0 0 0 | 0
0 1 0 | 1 | 0 1 1 | 0
0 1 1 | 0 | 1 0 0 | 0
0 1 1 | 1 | 0 1 1 | 1
1 0 0 | 0 | 0 0 0 | 0
1 0 0 | 1 | 0 1 1 | 1
1 0 1 | 0 | d d d | d
1 0 1 | 1 | d d d | d
1 1 0 | 0 | d d d | d
1 1 0 | 1 | d d d | d
1 1 1 | 0 | d d d | d
1 1 1 | 1 | d d d | d
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 9: From the Reduced State Diagram Step 2: Obtain Excitation Table using any Flip- flop.
Present State | Input | Next State | Output | D Flip-flop
R S T | X | R S T | Z | D1 D2 D3
0 0 0 | 0 | 0 0 0 | 0 | 0 0 0
0 0 0 | 1 | 0 0 1 | 0 | 0 0 1
0 0 1 | 0 | 0 1 0 | 0 | 0 1 0
0 0 1 | 1 | 0 1 1 | 0 | 0 1 1
0 1 0 | 0 | 0 0 0 | 0 | 0 0 0
0 1 0 | 1 | 0 1 1 | 0 | 0 1 1
0 1 1 | 0 | 1 0 0 | 0 | 1 0 0
0 1 1 | 1 | 0 1 1 | 1 | 0 1 1
1 0 0 | 0 | 0 0 0 | 0 | 0 0 0
1 0 0 | 1 | 0 1 1 | 1 | 0 1 1
1 0 1 | 0 | d d d | d | d d d
1 0 1 | 1 | d d d | d | d d d
1 1 0 | 0 | d d d | d | d d d
1 1 0 | 1 | d d d | d | d d d
1 1 1 | 0 | d d d | d | d d d
1 1 1 | 1 | d d d | d | d d d
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 10: From the Reduced State Diagram Step 3: K Map Expressions
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 11: From the Reduced State Diagram Step 4: Logic Diagram
State Reduction - Example
UWTSD Lectures / ACDA6001 – Electronics 2

## Slide 12
Thank you