## Slide 1: Principles of OME Level 4 ACDA4019 Fuzing

## Slide 3: Subjects.
Types of Fuze.
Functionality
Environment
Construction
Explosive Train
Safety Mechanisms.
Future.

## Slide 4
Fuse
Fuze
13 Amp
X


## Slide 5: Ammunition natures.
Most types of projectile, Medium Calibre upwards.
Artillery.
Mortar.
Missiles, inc torpedoes.
Bombs.
Special applications eg anti-structures.
Mines

## Slide 7: Generic Functions of a Fuze
Maintain safety of the shell/warhead filling during storage, transport, handling and firing until after deployment or launch and the target is sensed.
Function the payload/filling reliably at the required time.
It is a one-shot device with a 20 year shelf-life.

## Slide 8: Design for Safety.
Premature function of ammunition leads to casualties of our own troops, civilians and equipment.
Numerous Design Safety Principles, usually governed by OB Procs, DefStan, Stanags, Mil Specs.
Typically probability of accidental arming or function of a fuze < ‘1 in a million.’
= NEVER.
Key Features
Must remain Safe under all anticipated conditions.
Arming is distinct from initiation, sensing.
Use of proven materials, explosives, compositions.
Safe to assemble, for user and manufacturer – an ability to check safety.
Out of line system usually.
No single mode failure – implies minimum 2 safety locks.

## Slide 9: Reliability.
Usually defined by system requirement.
Typically 97 – 99.9%
  Influenced by system requirement.
  Overall cost of system delivery.
  1st shot reliability - (lets the bad guys know where you are !)
NB. Reliability has an implicit safety requirement and is becoming increasingly important particularly in training.
  A blind or dud round creates a hazard;
  An off-course missile normally requires S/Destruct.
  Also anti-aircraft ~25mm (missed target)
An added safety device can degrade reliability.

## Slide 10: Fuze Output
2 Main types.
HE/Detonating output.
  To function a HE shell or warhead.
Igniferous Output.
  Initiate Carrier Shell with sub-munitions
    – eg warhead or bomblets. (each with fuze)
  May simultaneously ignite payload (illuminating rounds, smoke)

## Slide 11: Typical Fuze construction.
3 main elements –
Sensing and initiation.
  Mechanical (Striker- Nail) and/or Electronic (RF, magnetic).
  Time.
Arming/Safety mechanism.
  Conventionally out of line mechanical systems favoured, occasionally in-line systems.
Explosive train
  To suit system function.

## Slide 12: Putting it all together – Exocet SAU.

## Slide 13: Proximity Fuze - schematic
Battery
Sensing and initiation.
  RF transmitter/detector.
  Processing Electronics.
Arming mechanism.
Explosive train

## Slide 14: Types of Fuze. - By Position.
Nose - Most common.
Base – Often to prevent interference with system effect, eg HESH or shaped charge.
Distributed – Typically in a missile warhead system where arming, initiation and target sensing may be remote from each other.
Design principles essentially same for all.

## Slide 15: Class of Fuze. (by functionality) cont.
Proximity.
  Initiates close to rather than by contact – usually RF transmitter, could be magnetic.
Time.
  Chemical time – generally obsolete
  Mechanical Clockwork – obsolescent, some in service.
replaced by
  Electronic Time – more accurate.
All require datum time, normally shot-start as the reference time. Fuze is set normally before loading.
Time may also be used to determine a proximity event - hence term Variable Time for proximity.

## Slide 16: Typical Explosives.
Detonator. Sensitive to Stab, Flash, Electric. 100-150 mg. Sometimes 2 for multi-function.
Stemmed Charge, Debrix, CE.
Booster, Debrix, PETN, Rowanex, Gunpowder

## Slide 17: System Launch Environment
High ‘g’ thrust – ‘set-back’
Angular Acceleration.
Spin.
Velocity
Spin Decay.
Yaw.
Impact.

## Slide 18
System Launch Environment
Flick Ramming.
High ‘g’ thrust – ‘set-back’
Low ‘g’ thrust – (rocket)
Angular Acceleration.
Balloting
Spin.
Velocity.
Low ‘g’ retardation.
Spin Decay.
Yaw.
Manouver (eg apogee)
Rain/Hail
Impact.

## Slide 19
System Launch Environment
Flick Ramming.
High ‘g’ thrust – ‘set-back’
Low ‘g’ thrust – (rocket)
Angular Acceleration.
Balloting
Spin. – centrifugal force.
Velocity - Air turbine.
Low ‘g’ retardation.
Spin Decay.
Yaw.
Manouver (eg apogee)
Rain/Hail
Impact.
Useful Energy Sources

## Slide 20: Other Energy sources.
System Energy.
  Batteries. (Reserve Cells)
  Gas Pressure (rocket motor)
  Compressed springs.
  Pyrotechnics (gas-motors & delays)
  User (Safety Pins !)
  Lanyards
Stored Energy is generally not favoured for safety mechanisms; best practise is to draw energy from the (unique) launch environment.

## Slide 21: Concept of ‘Safe-sealing’
A Primary explosive (more sensitive than Tetryl) must be out of line and must not function or degrade the explosive train if accidentally initiated.
Exceptions. High Energy Devices. Operate at 500V+.
Slapperplates, EFI’s. Usually contain secondary explosive (eg HNS)
NB These require intrinsically safe circuits, safety is determined by control of independent electro-mechanical safety breaks. (high integrity switches)
SAFE ARMED

## Slide 22: Arming
Must be unique to launch .
ie Not affected by Drop, Vibration, normal Manufacture To Target Sequence.
Safety Mechanism is a ‘combination lock’,
  - launch environment is the key.
Armed when safety devices are overcome, awaiting receipt of a firing signal.
Required to cope with a variety of charges.

## Slide 23: Safe – Arming Delay.
A system is normally required to have an arming delay to ensure safe-separation from the user.
Prevents premature function in the vicinity of the launch platform.
Often a distance measuring device to cope with varying projectile velocity.
Protects the ‘Goodies.’

## Slide 24: Arming Devices
Shear Devices – prevent movement until a threshold load.
Springs - prevent movement until a threshold load (for a finite time).
Arming Sleeves – eg for Ball Release
Detents – a catch
Shutters. – a barrier to the explosive chain.
Escapements – control movement.
Switches – for electrical power.
Gas motors – for powered movement.

## Slide 25: Function of a Mechanical Fuze

## Slide 26: Delayed Arming Unit (DAU)
Stored & Safe Position.
Axial Detent Down on Setback. Radial Plunger spun out.
DAU shown is from a HESH round Fuze

## Slide 27
Locking Arm Set Forward
Shutter Rotated to Arm.
Locking Lever Out
Detonator In-Line
View of Rear with cover removed to show Pallet Mechanism (delays shutter motion.)
See SAU animation

## Slide 28: An Electronic Proximity Fuze
4.5”HE. IA
NOSE
ASSEMBLY
FOAM
FILLING
LOCKING
RING
CIRCUIT
BOARD
BODY
PROTECTIVE CAN
CONTACT
RING
LOCKING RING
END CAP
DEBRIX PELLET
DEBRIX STEMMING
GAINE (Mech + booster)
ENERGISER

## Slide 29: Electronics Ruggedness.
Solid-state
Surface Mount
Low mass – large footprint
Avoid flexing – usually supported in a potting medium. (beware dielectric effects).
Crystals can be problematic, rely on RC timers.
Firing circuits encased if PID required. – Functionality after impact.

## Slide 30: Energiser (Battery)
See Battery animation
Also known as
‘reserve cell’

## Slide 31
INTERNAL BALLISTICS
FIRING VEHICLE
TARGET
Ballistic Phases (1)
Initial Projectile Motion –’Shot start’
Fuze axial detents Set-back
Batteries energised

## Slide 32
TARGET
INTERNAL BALLISTICS
FIRING VEHICLE
Ballistic Phases (2)
A 1gram component ‘weighs’ 20kg !
Peak Pressure and High Acceleration.
Spin increases.
Thrust ‘freezes’ fuze mechanism.

## Slide 33
INTERMEDIATE BALLISTICS
FIRING VEHICLE
TARGET
Ballistic Phases (3)
Axial detents held back by ‘ spin locks’. Radial detents out
Fuze mechanism free to move. Final arming begins
Battery power >50%
(Muzzle shock)
Acceleration decreasing , maximum spin.

## Slide 34
EXTERNAL BALLISTICS
FIRING VEHICLE
TARGET
Ballistic Phases (4)
At arming distance (c. 200m)
mechanical arming complete.
Batteries at full power.
Will function in PD or Graze mode.
Target approach.
Proximity circuits switched on.
Target detection mode.

## Slide 35
TERMINAL BALLISTICS
FIRING VEHICLE
TARGET
Ballistic Phases (5)
Detonation at optimum distance above target in Proximity mode.
Impact function in PD mode or as ‘back-up’

## Slide 36: Proximity Fuzes
Selectable sensitivity for burst height.
  Target signatures vary
  Optimum height varies
RF environment
  Radars.
  TV, Radio,Mobile,
  ECM
Solutions to interference.
  Choice of Frequency.
  Detection Algorithm (Pattern)
  Sensor & Transmitter Disabled until target.

## Slide 37: Setting.
Function - Proximity, Sensitivity, Time, PID
Hand, inbuilt switch. (cheap, easier logistics)
Contact Setters.
Inductive Setting
Feedback to confirm setting.
Interface with battlefield comms.
Often a default setting, eg Medium Height Proximity with PD back-up.

## Slide 38: Inductive Setter

## Slide 39: Typical testing methods.
Development
  Environmental stressing – On system unless simulation data available. – representative of MTTS.
  ETIT. Safe-Seal.
  ETD. Take-over.
  Jumble, Jolt,
  Spin Testing.
  Ballistic matching.
  Safe-Arming Distance
  Recovery; Overwater, Vertical, Aerobutt.
  (Components, assemblies or full fuze)
  Overpressure Gun Firings.
Production Tests.
  Function Tests; eg Electrical, Spin.
  Proof. Usually gun-firing, may include some elements of above.
  In Service Surveillance

## Slide 40: Future.
Safety + High cost of proving (a relatively low cost system) leads to slow development by maturity rather than step change/novel design.
Today’s trend is for Multi-function, standardised, interoperable fuzes.
  Minimises re-fuzing, reduced logistic burden.
  IM. - little overall impact on reaction but ALARP.
Future.
  Increased functionality. Smart weaponry, GPS, course correction, reduces space for conventional function, power supplies an issue.
  Integrated systems, function selection after launch, distributed, multi-point initiaition.
  MEMS. (Micro-Electro-Mechanical Systems)
  RPV’s – New environments, new requirements.

## Slide 41: Future.
Mag
Power Supply
Processor
Antenna
SAU
Mechanical
Proximity
GPS/Course correction/ Processing
Inductive set
Smart
Technology
~100
~400
~1-2k

## Slide 42: Course Correction
Pros –
Accuracy – Less rounds.
Interchangeable.
Consider-
Complimentary not replacement.
Complexity v Cost v Need
Correct for range.
Correct for range & bearing.

## Slide 43: Miniaturisation
105/155mm
25mm
5% of payload
30% of payload

## Slide 44: Questions?