## Slide 1
HOT AND COLD WATER SYSTEMS
Faculty of Architecture, Computing and Engineering
School of The Built and Natural Environments
Allan Nantel
2018

## Slide 2
Plumbing Systems Fundamentals
COPY DOWN
WATER USE CYCLE
TREATMENT

## Slide 4
Source: Lakes, Rivers, Reservoirs

## Slide 5
Water Sources ??
95% of the Earth’s water is either saltwater or glacial.
Rain Water – Collected in natural ‘water sheds’ (areas of land where all of the water that is under it or drains off of it goes into the same land area), and is stored in lakes or ponds
Advantages – Water is soft and pure
and is suitable for the hot water supply
system
Disadvantages-
Only a source when it is precipitated.
‘Collection’ points may not be clean.
Squam Lakes, USA.

## Slide 6
2.
Water Sources (contd.)
Ground Water – Part of the natural rainwater that falls on the land will sink into permeable ground. It will percolate or ‘seep’ by gravitation to lower levels, until impervious stratum is reached. Ground water will then build up in quantity and pressure.
Aquifers - Large solution cavities in Limestone and layers of sandstone provide natural strata for the storage of water.
Clays and fine grained soils of low permeability (cohesive layers) will ‘adsorb’ (?) and obstruct the movement of water, or serve to contain it from flow.
This water can be drawn from springs and artesian wells.
Advantages – Abundant supply
Requires less treatment because of natural filtering through strata.
Disadvantages- May have organic matter or chemical elements.... such as ???

## Slide 7
Flow of Ground
Water
Impervious strata
Geological interference
by fault
Out falling of the natural
water table due to
topography

## Slide 8
The void spaces between particles of soil are continuous throughout the soil mass.
Ground water will percolate through soils which are permeable.
Permeability is the measure of the rate of flow of that groundwater.
The rate at which this happens differs widely.
Permeability of Soils
Solid
Air
Water

## Slide 9
Seepage velocity (V)
Assume a column of soil and water flowing through from one section to another.
The volume of water flow q through total cross sectional area A in the time of 1 second is calculated
q = v x A
where v = Velocity of water flow
A = Cross sectional area of tube

## Slide 10
Seepage velocity (V)
Flow line
At the particulate level the water follows a laboured path through the pores.
The ratio of volume flow rate ‘q’ to the average area of voids A on a cross section normal to the direction of flow is called the seepage velocity (v)
v = q
A
In general, the velocity of water through soil has been found to be relatively small e.g. less than 0.61 m/min

## Slide 11
Piezometric Level and Hydraulic Head
If a stand pipe is installed to penetrate below the ground water table, water rises into it to find its own level. These standpipes are called Piezometric tubes and the level to which the water rises is the Piezometric Level.
The out of balance head of water that is causing flow downhill is called the Hydraulic Head (h). The hydraulic head is given up in pushing the water along its flow path
Height difference

## Slide 12
Hydraulic Gradient
Average Hydraulic Gradient (i) is defined as:
i = Δ h
L
Where
h = hydraulic head difference
L = The length of the flow line

## Slide 13
Henry Darcy was a French engineer who studied the movement of water through sand in 1856.
He found that the rate of water flow through a tube is proportional to the difference in the height of the water between the two ends of the tube, and inversely proportional to the length of the tube.
He also discovered that flow was proportional to a coefficient, K, which is called the…
Hydraulic Conductivity or the
Coefficient of Permeability
Henry Darcy

## Slide 14
Darcy’s Law & Coefficient of Permeability
The Coefficient of permeability ‘K’ may vary from as large as 1 m/s for clean gravels to a small value of the order of 10-10 m/s for very fine soil such as clay and silt.
The values of k are influenced by….?
Pore size
Soil structure
(grain size and cohesion)
Viscosity of the pore fluid
Gravels
Clay silt

## Slide 15
Water Sources (contd.)
3. Natural Surface Water - A mixture of surface run off and ground water.
Surface sources include rivers, lakes, ponds.
Advantages – Usually easy to acquire and in large quantities.
Used for irrigation, industrial supply and community water
supply
Disadvantages - Contains large amounts of bacteria, organic and inorganic
substance. Purification and treatment is necessary.
Surface / Ground water makes up the majority of our supply.

## Slide 16
Water Quality
Pesticides, solvents and seepage from landfills pollute groundwater (Steel, paper and textiles are the most polluting industries).
Organics and natural chemicals in the rocks also affect it.
Community councils will regularly check the quality of municipal water supplies… and will look at:
Mineral content
Acidity,
Alkalinity
Contamination
Turbidity
Biological purity.
(pH level)
How we obtain good ….
HAND OUT
Physical Defect
Chemical Defect
Biological Defect

## Slide 17
Hand out

## Slide 18
http://www.youtube.com/watch?v=9z14l51ISwg
THE WATER TREATMENT PROCESS
How we obtain good water quality
The Water Supply (Water Quality) Regulations 2016

## Slide 19
1. Intake Crib Raw water from a surface water lake or reservoir is drawn into the plant through intake structures. Large debris like logs are prevented from entering.
2. & 3. Screens Smaller debris like fish, vegetation and garbage are removed from the raw water by protective bar and travelling screens before the water enters the low lift pumps.
4. Low Lift Pump Well These pumps lift the water to flow through the treatment processes.
Water Treatment System

## Slide 20
5. Pre-oxidation & Primary Disinfection Disinfectants or other oxidants are added to disinfect or control tastes and odours. The specific processes used are determined by the chemical and biological raw water characteristics.
6. Coagulation Coagulants rapidly add electrochemical charges that attract the small particles in water to clump together as a “floc”. This initial charge neutralization process allows the formed floc to agglomerate but remain suspended.
7. Flocculation By slower mixing, turbulence causes the flocculated water to form larger floc particles that become cohesive and increase in mass. This visible floc is kept in suspension until large enough to settle under the influence of gravity.
Water Treatment System (contd.)

## Slide 21
8. Sedimentation Flocculated water is applied to large volume tanks where the flow speed slows down and the dense floc settles. Settled floc is removed and treated as a waste product that is discharged to the sewer system.
9. Media Gravity Filtration Relatively floc free, settled water flows through a media filter by gravity. Filter media are made from layers of anthracite or granular activated carbon and sand. Gravel or synthetic materials support the media. Physical straining removes the remaining floc. Filters are periodically backwashed to clean off accumulated floc and other trapped impurities.
10. Clear Well Filtered water in the clear well is used to backwash filters and kept in storage to ensure that disinfectants are in contact with the water long enough to inactivate disease causing organisms.
11. Secondary Disinfection Supplemental chlorine is added to maintain disinfection concentrations while the water is pumped through the distribution system. The purpose is to ensure minimum residual disinfectant levels at the farthest points of the system.
Water Treatment System (contd.)

## Slide 22
13. High Lift Pump Well Treated drinking water is pumped through large pressure pumps to other pumping stations, reservoirs or points of supply within the local distribution system.
14a & 14b Elevated Water Storage Towers and Ground Level Reservoirs Water distributed to water towers and storage reservoirs ensures stable water pressure. An adequate supply of water is maintained to meet peak water demands or emergencies such as fires, water main breaks, power outages and pump failures.
Distribution System Distribution systems are comprised of large pipes known as trunk mains to deliver drinking water. Smaller diameter branch mains feed individual streets. Service connections to branch mains deliver water into residences. Pumping stations are used to increase pressure and to maintain adequate supply flows.
12. Fluoridation A process where silico-fluoride compounds are added to treated drinking water to artificially raise the fluoride concentration to within a specified range; for example between 0.5 to 0.8 mg/L (ppm). Fluoridation is an optional public health dental policy
Water Treatment System (contd.)

## Slide 23
Water Treatment System

## Slide 24
1. COLD WATER SUPPLY

## Slide 25: Introduction
Plumbing is the engineering and technique of installing pipes, fixtures and apparatus for delivery of potable water, liquids and gases.
It also provides the fittings for removing
these substances in the form of
water-borne wastes.
Plumbing is from the word ‘plumbum’,
Ancient Latin name for the metal LEAD,
which was the original material from which all pipes were made.
Pompeii, Italy

## Slide 26
Plumbing Systems Fundamentals
SYSTEM COMPONENTS

## Slide 27
Riser is a supply pipe that supplies water vertically one full storey or more.
Basic Definitions
Water Mains are large piping networks that carry potable water for the public system from treatment plant to an community area.
Service Pipe runs from the main to the property, far enough underground to
prevent freezing in cold winters.
Water Meter inside or outside the building. This measures and records the
quantity of water passing through the service pipe.
This meter may also measure sewage disposal services.
Distribution pipes deliver the water to the point of use within the property.
Control (Cut Off) valve is located outside the building to cut off the
supply to the building in case of emergency.
Shut Off valve located inside the building allows owner to control the supply.

## Slide 28
Cold Water –Regulations
All materials i.e. pipes, fittings and appliances as well as the manner in which they are installed, are covered by the:
Water Supply (Water Fittings) Regulations 1999. (WRAS)
The Regulations are framed by various Government bodies and give the guidance about materials and the method of installation.
The main reason for their implementation :
• Prevent contamination of a water supply
• Prevent the waste of water
• Prevent misuse of a water supply
• Erroneous measurement (fiddling the meter)
No legal requirement for a person working on water services to be a qualified plumber, but anyone who carries out such work can be prosecuted for an offence against the Water Regulations and if convicted of an offence can be liable to a fine.

## Slide 29
Cold Water Distribution
1
2
3

## Slide 30
Dura - Blue PVC Trunk main piping
MDPE Alkathene water piping –
25mm standard
Caution…older water piping was Black and hard to distinguish from electrical cabling.
Only the water companies make connections onto the principle mains water supply.
Mains supply pipes are laid to a minimum depth of 900mm below the ground level.
Connection onto the local main is usually by use of a screw down gun metal stop valve.
The mains pipe is made of PVC…the connecting pipework to the building stop-tap is in MDPE
Cold Water – Mains Connection
100mm to 350mm standard

## Slide 31
COLD WATER MAINS CONNECTION
(BY THE LOCAL WATER AUTHORITY)
Screw down gun metal stop valve
FERRULE
900 mm
minimum

## Slide 32
COLD WATER MAINS CONNECTION TO THE DWELLING
Prevention of pulling on underground joints
A ‘Gooseneck’ or offset is used to provide slack in the pipe length.
This prevents strains on joints when the trench is backfilled after the pipework has been tested.

## Slide 33
COLD WATER MAINS CONNECTIONS
Services in Trenches
If the above dimensions are not possible in practice, additional protection for cold service will be required

## Slide 34
SKETCH
Cold Water – Incoming Water Supply
Pipe must be insulated
If Less than 750mm
Gooseneck MDPE

## Slide 35
STOP TAP
An externally operated valve regulating the flow of a liquid (or gas) through a pipe, in particular one on the water main supplying a building.
Restricts or isolates the flow of a liquid (or gas) through a pipe.
Know where it is !

## Slide 36
COLD WATER – INCOMING WATER MAIN SUPPLY

## Slide 37
COLD WATER – WATER METERS
Supplementary, or cross bonding (10mm2) is usually found.
Unlike earthing it is not designed to clear a fault. What it does is electrically tie together all accessible conductive parts (pipes, taps, electrical appliances etc.) that could under fault conditions introduce a dangerous potential (voltage) into the room.

## Slide 38
If the water pressure is too low…this must be reported to water authority to adjust.
If water pressure is too high, a water pressure reducing valve or FLOW REGULATOR is integrated into the system. This simply reduces a high pressure to a lower one.
COLD WATER– PRESSURE AND FLOW
Pressure gauge used to measure the pressure of the water supply
Mains Water pressure throughout the UK varies from below 1 bar (sufficient for most dwellings) to above 10 bar. ( where 1 bar = 100kPA) (around 10m head)

## Slide 39
In older properties, mains pressure is supplied to all cold water taps and WC’s ‘directly’. Hot water is delivered via a hot water cylinder, fed from a cistern. The big advantage of this system is that drinking water can be drawn from any cold water tap in the building.
1. The Two main types of Cold water supply
DIRECT
INDIRECT
Modern buildings are plumbed with the indirect system.
Water enters the building under mains pressure through the service pipe and proceeds via the rising main directly to the cold water storage cistern, normally in the roof-space.
Apart from the kitchen sink (first point of entry), all cold water taps and appliances are fed indirectly under gravity pressure from the storage cistern.
The hot water storage cylinder is also fed with cold water from the same cistern.
There it is heated by emersion heater or gas boiler and drawn off to supply the hot water taps and appliances.

## Slide 40
1. DIRECT COLD WATER SUPPLY
Sanitary systems are supplied direct from the mains supply, and a cold water feed (cistern) is utilised to feed the hot water storage cylinder.
The capacity in litres of the feed cistern is required to be at least equal to the capacity of the hot water cylinder.
Water Regulations require a cistern of 115 litres minimum capacity.
This is small enough to be accommodated in the top of a cupboard.
In older properties, mains pressure is supplied directly to all cold water taps and WC’s. Hot water is fed via the hot water storage cylinder.
Problems with large cisterns !

## Slide 41
Hot Water
Cylinder
SKETCH
COLD WATER – DIRECT SUPPLY

## Slide 42
INDIRECT
COLD WATER SUPPLY
In this system, all the sanitary fittings, except drinking water draw offs at kitchen sinks, are supplied indirectly from the cold water storage cistern.
Since the cistern supplies baths, basins, showers etc. and also feeds the hot water cylinder, its capacity in litres will be approx. double that of the direct water supply system.
The Regulations require a cistern of 230 litres minimum, and this will be located in the loft space.
For larger buildings, the storage size will be estimated from the number of sanitary fittings and the estimated head count of users.
Draw this yourself

## Slide 43
Hot Water
Cylinder
COLD WATER – INDIRECT SUPPLY

## Slide 44
COLD WATER – Storage Cistern installation requirements – pipework connections
Ball Valve
(If Indirect system)

## Slide 45
COLD WATER – Storage Cistern Requirements – Installation of the Cistern
Cold Feed
Overflow to outside
RISING MAIN

## Slide 46
Overflow Pipe
Designed to take discharge from the cistern when the inlet valve is running full bore. It prevents the tank from over filling and flooding the building.
Pipe is taken through the external skin and terminates outside the building in a conspicuous position to alert the user to the problem.
This can be outflowing into the guttering at roof level, or as an outlet pipe just below roof level.
COLD WATER – Storage Cistern Requirements – overflow pipework

## Slide 47
COLD WATER – Storage Cistern Requirements – Installation of the cistern
Overflow pipes must be suitable to carry the water temperature that may discharge through them. When would we see a possible rise in temperature?
Cisterns for Solid Fuel/Gas heating may discharge boiling water as a vented overflow. In this instance, the overflow must be of copper piping.
Overflow must be one size larger than the supply pipe it protects, with a minimum size of 22mm being stipulated
Overflow pipe must have a suitable fall to the discharge point and must be well supported.

## Slide 48
COLD WATER – Storage Cistern Requirements – Installation of the cistern
Water Regulations state a minimum gap of 350mm between cistern and roof underside.
Storage Cisterns and pipe work must meet minimum distances required by regulations – this prevents frost damage and allows servicing of the cistern.

## Slide 49
COLD WATER – Protection Requirements
Where pipework is at risk from freezing it must be protected using approved pipework insulation
This should be resistant to or protected from:
Rain
Condensation
Mechanical Damage
Vermin
Thermal Insulation material for pipework should comply with BS5422 and should be installed in accordance with BS5970 and the manufacturers instructions.

## Slide 50
Advantages and Disadvantages of each system
Direct System:
Less pipework
Smaller storage
Cheaper to install as a result
Drinking water is available at basins
Possibility of smaller cold water cistern sited below the ceiling (airing cupboard)
Indirect System:
Large capacity storage cistern supplies a reserve of water if the mains water fails.
The water pressure on the taps supplied from the cistern is reduced.
This minimises noise and the wear on the fittings.
When the installation is complete, all services are sterilised before use. They are thoroughly flushed through with a chlorine dose of 50 parts per million of water. The chlorinated system is left for three hours before being thoroughly flushed through again.
COPY DOWN
Look at your two sketches of Direct and Indirect Systems…..

## Slide 51
SEE :
BS EN 806-2:2005 - Installations inside buildings conveying water for human
consumption.
BS 6700 - Design, installation, testing and maintenance of services supplying water for
domestic use within buildings
Low Level buildings – Possible Block of Flats cold supply
Separate Supply Pipes
Common Supply Pipes
Common Distributing Pipes
Problems?
Noise, leaking pipes, access, water quality, communal area routing, pressure drop, inadequate storage, maintenance, peak demand periods.

## Slide 52
Water supplies for High Rise
For high rise building where the mains pressure is low it is necessary to pump the water from inside the building.
The pressure on the water main required would be estimated for the peak demand period.
Normal mains pressure of around 300 k Pa would supply water to a height of 30m.
In buildings of more than twenty storeys, boosting header pipe pressure by pumping will put too much pressure on the taps on lower floors. To prevent this, the floors are ‘zoned’ with their own drinking water cistern, so that the head of water above the lowest fitting does not exceed 30m.
Boosted Cold Water System

## Slide 53
DIRECT SYSTEM
DIRECT COLD WATER SUPPLY
Water Authority’s stop cock.
Service Pipe
Main Stop cock
Rising Main
Storage Cistern
Hot water cylinder
7-10 Waste systems

## Slide 54
INDIRECT SYSTEM
INDIRECT COLD WATER SUPPLY
Handout

## Slide 55
Copper PIPES
Used for Hot and cold water, heating, gas and drainage installations.
Moderate tensile strength and can be of thin wall.
Cheap and light.
Some acid soils attack it.
If this is a danger, they can be coated in
plastic.
Smooth internal bore, no resistance to flow.
Can easily be bent into shapes to allow for cornering.
Jointed by brazing with tin/copper alloys.
See BS 2871
Solder jointed
or
Compression
jointed
Tin/Copper alloy melted to 450 C
PTFE tape added
MATERIALS

## Slide 56
MILD STEEL PIPES
May be galvanised or not.
Galvanised used for industrial hot and cold water install (coated with zinc to prevent rusting)
Cheap… with high tensile strength. Because of this, they can resist high pressures and mechanical damage.
Internal surfaces are rougher and can therefore offer greater resistance to the flow of fluids.
Easily bent to shape by hydraulic bending machine.
Jointed by means of screwed or flanged joints.
PTFE tape is used
between the
threads to
prevent leaks.
See BS 1387

## Slide 57
LEAD PIPES – Older properties
Very prone to splitting in cold weather!
Still found as the main supply pipe to older buildings.
Lead poisoning from water which has passed through pipes is a major hazard.
Lead is now banned on new installations
Existing pipework, which is still abundant on older properties will need replacing with copper or plastic upon refurbishment.

## Slide 58
Wiped Lead Ball Joint
Lead pipe cannot be threaded because it is too soft, so a special brass fitting called a ‘wiped nipple’ is butted up against the lead pipe.
More lead would then be melted and ‘wiped’ around the joint sealing the connection, with a leather pouch.

## Slide 59
PVC PIPES
PVC (Polyvinyl chloride) is used for cold water and distributing pipes, mains water and drainage pipe systems.
Not suitable for hot water pipes (as softening temperature is low), but can be used for short periods of discharge of hot waste water.
Pipe is manufactured by extrusion moulding and cut to 10m lengths.
Smooth internal surface, light and easy to handle.
Various colours available.
Jointed by solvent cements or ‘o’ ring rubber seal
(Push-fit) or by screwed
compression.
Polythene pipe is used for cold water services, especially underground mains
See BS 3505
See BS 3506
Size ranges 9mm to 150mm
See BS 6572
See BS 6730

## Slide 60
GLOBE VALVE
Types of Valve
Used for High Pressure systems
Used for Heating systems
Stem washer acts as a non return valve to prevent back flow.
Valves : start or shut down the system, regulate pressure, check backflow, control direction of the flow.

## Slide 61
GATE VALVE
Used for control of fluids in low pressure systems… allows the system to be serviced.
Typically used for distribution systems from storage cisterns, or low pressure heating systems.
They offer much less resistance to flow than the Globe Valve.

## Slide 62
BALL VALVE
Used to control the supply of water to larger storage vessels
Flotation device (‘Portsmouth’) type is an automatic shut off using a plastic ball float.

## Slide 63
DRAIN VALVE
MANY different types
Used to drain Boilers, cylinders and sections of pipework for maintenance work.

## Slide 64
SAFETY VALVE
Used to relieve excess pressure on boilers, tanks and pipework.
Come in spring and dead-load type.

## Slide 65
TAP OR BIB

## Slide 66
2. HOT WATER SUPPLY

## Slide 67
The idea of being able to heat all the rooms in a house was first contemplated in the 1950s. Up until then, which room was heated depended on which room was going to be used. The normal heat source was an open coal fire.
Central heating has developed into an efficient and sophisticated system that allows full control to suit individual lifestyles.
The purpose of central heating is to:
• provide thermal comfort inside the building or home
• be economical to operate and ensure maximum efficiency in energy use.
A newly installed central heating system must meet all the requirements as set out in:
British Standard BS EN 14336:2004
Heating systems in buildings: Installation and commissioning of water based heating systems.
HEAT SUPPLY
The ‘Combination Boiler’ now dominates new installs…..but MANY buildings will still utilise older
methods and technologies (old boilers + pipework systems)

## Slide 68
Electric Water Heating
Is a system which uses an immersion heater installed into the hot water storage vessel, usually cylindrical. It behaves in much the same way as an electric kettle in that when the required temperature is reached, the electric element is automatically switched off.
The element reaches low down to the bottom of the vessel, to 75mm from its base.
In some models….two heaters will be fitted. ….One at high level and one low.
The power comes directly from the main electrical consumer unit

## Slide 69
Hot Water – Stratification
Layering of water within the cylinder.
Hotter (less dense) water sits on top of cooler (more dense) water.

## Slide 70
HOT WATER – IMMERSION HEATERS
Immersion Heater Thermostats must incorporate an overheat safety cut-out so that water within the cylinder does not overheat, which would cause scolding water to be delivered through the taps.
Cold Water Cistern
Cold Water Feed
The hot store vessel may be a water cylinder or a combination unit, encased or lagged
Hot water distribution
Immersion Heater
Open Safety Vent
Vented immersion heater systems
Hot Water
Storage
Vessel

## Slide 71
CYLINDER INSULATION AND VENTILATION
CYLINDER INSULATION JACKET FOR UNINSULATED CYLINDER
Immersion heater left exposed to prevent overheating of contacts
Cylinders can be ‘pre-lagged’ in the manufacturing process with expanded foam
Lagging jackets are the alternative, which are strapped to the tank with bands
ECONOMICAL ??

## Slide 72
Electric Water Heating
Cost of heating water using electricity is expensive and rising, so conservation of the heat produced by this system becomes even more important.
What can we do to conserve this heat?
We must observe the following points.
Insulation of the hot water storage vessel to a minimum of 50mm , but preferably 75mm, of good insulation.
The length of draw off points from the storage vessel must be reduced to a minimum.
Thermostatically control the temperature of the water to 60 degree C…..this is perfectly adequate for hot water supply.

## Slide 73
ASSIGNMENT 1

## Slide 74
HOT WATER SYSTEMS

## Slide 75
Is one in which the water is heated and stored centrally within the building, supplying a system of pipework to the various draw-off points. The water is fed to the boiler by ‘primary flows’ and ‘return’ pipes, with circulation either by convection current or by pump.
As the water expands on heating, it is drawn off from the top of the storage vessel. The cold feed is supplied low down in the vessel, preventing the unnecessary cooling of previously heated water.
At the highest point in the vessel, a vent pipe is run up to terminate in the feed storage cistern. This pipe allows air and excess pressure to escape from the system and also allows air in if the system is to be drained down.
The temperature of the stored water should not exceed 60 degrees C. Anything above this is uncomfortable and dangerous.
A Centralised system
HOT WATER SUPPLY
Two types : ‘Centralised’ and ‘localised’

## Slide 76
2. A localised system …
Is a system in which the water is heated locally to specific needs…
for example at a single point heater located above a sink. The water may be heated in the vessel itself, or heated in a boiler and circulated to that position.
This option may be chosen when a long distribution pipe would mean an unnecessarily long wait for hot water to be drawn off at the tap.
There are two types, ‘instantaneous’ (heated by gas) and ‘storage types’( heated by electric element).
In each case the heater will only serve one sink.
(maybe 2 if in very close proximity)

## Slide 77
Heat Recovery Period
This is the amount of time required to heat up a quantity of water.
It varies depending upon the power rating of the heat source used, but basically the higher the power rating, the shorter the time taken. It is possible to calculate the heat recovery period of the water using the following formula:
SH x kg x temperature rise
Available time (seconds)
Where: SH = Specific Heat Capacity of water (4.186 kJ)
kg = The weight of water to be heated
(where 1Litre = 1kg)
=
POWER
REQUIRED
COPY DOWN
The specific heat is the amount of heat per unit mass required to raise the temperature by one degree Celsius.

## Slide 78
Exercise 1 :
Find the power required to heat 100 litres of water in 2.5 hours from 4 degrees C to 60 degrees C
POWER =
SH x kg x temperature rise
Seconds in 2.5 hours
=
4.186 x 100 x 56
9000
=
2.6 kW of power

## Slide 79
Note that this example does not take into account any heat loss from the system or for the heating up of the storage vessel itself.
We usually add 10 % for this…..
Thus our result would be 2.6 +10% = 2.86 kW
Therefore a 3kW heater would be chosen.
Of course…the incoming temperature of the water would also have a bearing on recovery time.

## Slide 80
Often, we require to know the time it will take to heat the water using an existing immersion heater power capacity.
Exercise 2 :
Find how long it would take to increase the temperature of 136 litres of water from 10 degrees C to 60 degrees C, using a 3kW immersion heater.
Ignore heat losses in the system itself

## Slide 81
Solution
SH x kg x temperature rise
Available time in seconds
=
POWER
=
4.186 x 136 x 50
3
=
9488 seconds or
2hrs 38 minutes
We can use a ‘Recovery Chart’ to give an approximate time for heating the water and this proves a useful guide when sizing up heaters or boilers for efficiency.

## Slide 82
To heat 150 litres of water from 5 degree C to 60 degree C in
2 hours 24 minutes ….
a boiler with a energy rating of what would be required?
4 KW

## Slide 83
Boiler Sizing Method
The required boiler output for the system is determined as follows:
Total up the fabric Heat Losses for all the rooms of the building.
Add half the sum total of the ventilation heat losses (Qv) for the rooms.
Add the minimum domestic heat requirement (considering hot water cylinder capacity) ( 1kW for every 50 litres heated)
Add a 10% margin for heat losses from pipes and from the
initial ‘warm up’ of the system.
(Note: in 2 above the total ventilation heat loss is not included because some air change will be the result of warm air passing from one room to another)
Calculate Heat Losses (as previously calculated), with consideration to temperature differences, Area and U values.
Calculate the Heat Emitter (radiator) size to hold constant temperatures at desired levels (as previously calculated).

## Slide 84
How did we calculate the Radiator Size required?
AREA = Total Heat Losses (W)
Heat Emission of the Radiator (W/m2)

## Slide 85
How did we calculate the Total Fabric Heat Loss?
Heat loss= U value x Area x temperature difference

## Slide 86
Qv =
0.33 x N x V x
(Tai – Tao )
Where N = Rate of air change per hour
V = Volume of the room in M3
Tai = Inside air temperature (in degree C)
Tao = Outside air temperature (in degree C)
Where 0.33 was our ‘ventilation allowance’ in the question.
This is a ‘factor’ that relates to the specific heat capacity of air and its density. For our calculations we will use this value.
How did we calculate the Ventilation Heat Loss?

## Slide 87
Exercise 3:
From the table below, calculate the boiler output required for the bungalow under study. This building’s heating system contains a hot water cylinder of 150 litre capacity.
ROOM | VENTILATION LOSS ( W) | Average U value | AREA | TEMP DIFFERENCE | FABRIC LOSS (W)
Lounge Bedroom Kitchen Hall Bathroom | 313.63 270.86 294.94 124.15 188.18 | 1.24 .88 .70 .42 .82 | 48.5 44.8 38 15 36 | 20 19 18 20 20 | 
COPY DOWN

## Slide 88
ROOM | VENTILATION LOSS ( W) | FABRIC LOSS (W)
Lounge Bedroom Kitchen Hall Bathroom | 313.63 270.86 294.94 124.15 188.18 | 1202.80 749.056 478.80 126.00 590.40
Solution: Exercise 3
Total 1191.76 | Total 3147.056
Half Heat Ventilation Loss | 595.88
 | 3742.936
DHW requirement | 3000.00
 | 6742.936
Add 10 % margin | 674.294
Boiler output capacity of | 7.417 kW

## Slide 89
HOT WATER SUPPLY
Heated by gas, solid fuel or oil, and positioned as close as possible to the hot water storage cylinder, so heat losses from primary flow and return are reduced to a minimum.
Water is circulated by gravity or pump with pipes insulated to conserve heat.
‘Centralised’ Boiler systems:
Type 1 : Direct systems
In the direct system, the central heating is not combined with hot water supply. The heating and hot water are kept separate because the storage feed is from the cistern which brings gasses into the system from the cistern and draw off points (taps). This could cause corrosion to ferrous metals.
This system is cheaper to install than the ‘indirect’, and the water in the cylinder can be heated quickly, with direct circulation between the boiler and the cylinder.

## Slide 90
Direct systems
There are 4 types:
1. Electric Water heating
2. Storage heating (electric)
3. Instantaneous gas systems
4. Boiler / Cylinder systems
Boiler / Cylinder systems
In this system a small boiler (gas fired) conveys the hot water by primary flow and return.
It is not possible to include radiators on the primary pipework, unless they are made of non ferrous metals.
The water passing to the boiler is supplied from a feed cistern and is passing through pipework drawn off at taps.
This brings gases into the system which may cause corrosion to radiators (ferrous metal).

## Slide 91
HOT WATER – DIRECT SYSTEM
Gas Boilers are purpose made vessels with gas burners installed directly below the stored water. The system incorporates an open flue which discharges into the Cold Water Storage cistern (CWSC), a pressure release (if needed) for the cylinder.
To Hot Water outlets

## Slide 92
HOT WATER SUPPLY
Type 2: In-Direct systems:
This system is used when heating is combined with hot water supply provision.
A ‘Heat Exchanger’ (calorifier) allows water from the boiler to pass through, but not mix with, the water in the cylinder itself. In effect, it is two systems which appear to join at the hot storage vessel.
The water from the boiler circulates through
this heat exchanger and heats the water in
the cylinder indirectly.
The movement occurs by convection, or it
can be pumped. Again, pressure is vented
into the cistern in the loft.
This water can circulate through the required
number of radiators.
Boiler

## Slide 93
HOT WATER – INDIRECT SYSTEM or Double Feed System
Most indirect systems are of the double feed design, using two cisterns in the roof space, and having a coil heat exchanger fitted into the cylinder. The water in the ‘Primary Flow’ is never changed and should therefore be free of lime-scale or gasses, and being ‘neutralised’ it is suitable for central heating purposes.

## Slide 94
Comparative Running Costs
Looking at these hot water systems, what will affect our running costs??
Local costs
Level of use
Fuel type
System type
Size of the building
How well the system is insulated
Considerable savings to be made by an efficient system and a well insulated one.
Solid Fuel, oil and electric are available to every building, but the first two require a separate physical storage facility.
Mains gas may not be available everywhere (all districts).
Generally, in running costs, there is little difference between the types. In efficiency…there is…… So what is the best fuel ??
Efficiency Considerations
On balance, mains gas is probably the best fuel if available. It is clean and offers infinitely more controllable heat output, needs no storage and its supply is secure.

## Slide 95
SYSTEM COMPARISONS – ‘STORED’ versus ‘INSTANTANEOUS’?
10 Minutes

## Slide 96
CENTRAL HEATING SYSTEMS

## Slide 97
DOMESTIC
CENTRAL
HEATING
Is the heating of the building from a central heat source.
WARM AIR EXAMPLES ??
Ductwork
Curtain Heaters
Warm Air Convectors
COPY DOWN

## Slide 98
WET CENTRAL HEATING
The most popular form of heating is the
wet system in which water is heated by
a boiler and pumped through small bore pipes to radiators or convector heaters.
The heat from the water is released into the rooms and the water circulates back to the boiler for re-heating in a continuing cycle
of flow and return.
Parts of the system can be shut down if rooms
are unoccupied.
An extra advantage of this system is that it
can be used jointly to heat a hot water and radiator
supply for the building.
The boiler can be heated by gas, solid fuel
oil, or electricity.
Double (Two Pipe) feed system

## Slide 99
The controls for this system are very flexible. Thermostats and valves allow the output of individual heat emitters to be automatically adjusted.
A thermostatic radiator valve (TRV) is a self-regulating valve
fitted to the (flow) hot water heating system radiator, to control the temperature of a room by changing (regulating) the flow of hot water to the radiator. It senses the internal air temperature. Building Regulations require thermostatic radiator valves (TRVs) to be installed on new systems or for there to be some other means of controlling an individual room’s temperature
Programmer / Timer – Controls the boiler (on and off) and controls the flow of heated water to the hot water cylinder and radiators.
Cylinder thermostat – It measures when the water in the cylinder storage is warm enough (depending on what you set it to). As the cylinder cools down it will tell the programmer to turn back on again (if left constantly on).

## Slide 100
One Pipe System
Two Pipe System
WET CENTRAL HEATING
Reduces installation costs as less piping is required. Has disadvantages to the two pipe principally in that the pump forces water around the main flow and not through individual radiators.
Water is pumped around the circuit and through radiators, giving a much faster heating up time.
Two Pipe Reverse
Length of heating circuit to each heat emitter is about the same.

## Slide 101
One-pipe Central Heating system (Vented)
This works using a one-pipe run (a complete ring of pipework) with a flow and return from the boiler. They are no longer installed in domestic properties . However, you may come across them in older properties. Disadvantages ???
Has disadvantages to the ‘two pipe’ system principally in that the pump forces water around the main flow and not through individual radiators, so heat up time is longer. It is however a lower install and maintenance cost.
Hot water supply

## Slide 102
Two-pipe Central Heating system (Vented)
Water is pumped around the circuit and through radiators, giving a much faster heating up time.
Hot water supply
(Feed and Expansion)

## Slide 103: Fully pumped systems Y - plan
Fully pumped Central Heating system (Vented)
In this system, the hot water and the heating circuits are operated completely by the pump. The boiler can be sited above the height of the cylinder, giving more design options. Installation supplies are controlled by motorised valves.

## Slide 104
UNVENTED HOT WATER SYSTEMS
The water is taken directly from the mains supply.
There is no open vent or storage cistern where the expansion of heated water can escape to.
Therefore some expansion vessel needs to be incorporated. Should the expansion vessel not function correctly, the water will be forced out through the expansion relief valve.
These systems are far more complicated, and have many more parts to them, but do allow near mains pressure hot water supply. They are designed to do away with the storage cistern and operate at a much higher pressure than the open vented system.
Installed in pressurised system to provide an air gap and a window that identifies flow

## Slide 105
Expansion Vessel Installed
Tundish

## Slide 107
The boiler is the heart of the heating system and modern
varieties are compact and efficient.
1. GAS Boilers have pilot lights that burn constantly and light the boiler on ignition. They work manually or by electronically controlled timer set. You can also link the boiler to room thermostat so that the heating can be
turned on and off in specific areas. A thermostatic valve
within the boiler itself prevents the water overheating.
2. OIL Fired Boilers with the same efficient controls as gas fired, come in two types; ‘Pressure jet’ and ‘Vaporising’.
This refers to whether the oil is reduced to tiny droplets or
turned to vapour to be burnt. Average 2,000 L/yr
Pressure jets are too noisy for use indoors and must
be housed outside (in a boiler house).
Vaporisers are much quieter. A drawback is that this system
needs a large storage tank, sited outside for delivery tanker
access.
Central Heating Boilers

## Slide 108
Solid Fuel Boilers also need a suitable storage place for the fuel, and they produce waste which needs to be removed daily. The rate of burning is controlled by a damper or fan.
Instant control of the heat is not possible, so the heat needs a way to escape in the case of pump failure to avoid damage. This is achieved by a draining expansion pipe between the boiler and the heat exchanger.
Central Heating Boilers
These boilers must be connected to venting chimneys.
Boiler outputs are usually quoted in BTU/hour (British Thermal Units)
or Kilo Watts (kW) where 10,000 BTU/h = 3kW

## Slide 109
Combination (Combi) Boiler
Combines the heating of hot water supply and a central heating system
instantly (Plate heat exchanger – very efficient) (some have 35L water store)
so are therefore considered a ‘Direct’ supply. All boilers need a flue to
discharge products of combustion.
The ventilation access may affect the choice of location for the boiler and the
ventilation requirements.
Reduces installation costs as no feed or storage vessels are required for the
supply of hot water
Omitting the large quantity ‘storage’ of domestic hot water saves money,
which might have been previously spent heating the water unnecessarily if using
the central storage method.
Suitable for low energy homes with limited hot water demand.
Many variations of combination boilers, all working on different design concepts.
All new installations and ‘re-fittings’ now require ‘Condensing’ boiler types.
The most common method to heat water instantaneously is the use of a combination boiler.
This type of boiler works by using the circuit that powers the central heating and diverting it
to another ‘water to water’ heat exchanger (heat swapping).
This part ‘swaps out’ the heat from the heating water to the hot water outlets of the building.
Features

## Slide 110
Why are condensing boilers more efficient?
A condensing boiler has a large heat exchanger (or, in some designs, a second heat exchanger) that extracts more heat from the flue gases.
In a non-condensing boiler, the flue gases are at a temperature of 120-200°C.
In a condensing boiler, more heat is removed and the temperature falls to below 100°C and as low as 50°C for the most efficient boilers operating at reduced boiler return temperature.
The water vapour in the gases ‘condenses’ (hence the name) and the resulting liquid has to be drained away. As the ‘flue gas’ side of the heat exchanger gets wet in the process, it is more susceptible to corrosion.
To avoid this, it has to be constructed from corrosion-resistant materials e.g. stainless steel or aluminium
It is now a requirement of the building regulations that newly installed gas-fired boilers should be condensing (excludes range-cooker boilers), with a SEDBUK (Seasonal Efficiency of a Domestic Boiler in the UK) efficiency of 86% or more.

## Slide 111
Filling loop
How to restore the pressure in a sealed heating systems ?
Sealed heating systems with combi boilers need to have their pressure checked and topped up from time to time. In most cases the pressure gauge will be on the front of the boiler and should register 1.0 to 1.5 Bar of pressure.
Over time the pressure will fall. How quickly depends on how leaky the system is. Very small leaks often occur on radiator valve spindles, Automatic Air Vents (AAVs) and other components.
Often you will not notice the leak since the small amount of water will evaporate. (Every time fresh water is introduced, further scaling and corrosion may occur in the system, so you should not leave an excessively leaky system to continue)
Recharging the pressure once a year is probably normal.
To recharge the system pressure you need to locate the filling loop. This is usually a silver coloured, flexible braided connection with a small valve at each end. Usually under the boiler or nearby, but sometimes incorporated into the boiler.

## Slide 112
Exercise:
From discussions and using the template provided, sketch a typical simple Combination boiler piping layout. This will be a
Sealed system, vented for combustion gas.
Your sketch should include the positions of:
Boiler (Lower or Upper floor)
Piping layout for hot and cold water to supply both water fittings
and radiators (FLOW and RETURN)
3. Two radiators on the ground floor and two on the first floor.
TRV positions on radiators
An exterior thermostatic control adjacent to the Boiler
Note:
A. The cold feed to the first floor is direct, as a flow regulator is fitted to the rising main.
B. Indicate your water flow direction with arrows. (preferably red for HOT, blue for COLD)

## Slide 113
COMBINATION BOILER LAYOUT EXERCISE
RISING MAIN

## Slide 114
Combination Boiler – sealed system
Accounts for 80% of modern domestic supply systems
Combination boilers are only really suitable for low energy domestic applications in which the demand for hot water is limited.
It relies on the efficiency and capacity of the boiler in the volume of water heated… and the speed at which this can happen.

## Slide 115
Test Yourself
1. Name the three most common fuel sources used to run central heating systems.
2. What term is used to define all new boilers (either in new installations or as a replacement in an existing system), as defined in Part L1 of the Building Regulations?
3. What is the key difference between combination boilers and system boilers?
If a two-pipe system is being installed in a dwelling, which of the following statements
will be true?
a Water in the flow and return pipe work will be mixed.
b The return water will be at the same temperature as the flow.
c The water in the flow and return pipe work must be kept separate.
d The temperature of the return water will be higher than the flow.
What is the main purpose of the vent pipe on a heating circuit?
a To provide hot water
b To introduce air into the system
c To provide protection in the event of overheating
d To allow filling up of the system

## Slide 116
6. According to SEDBUK, what is the minimum percentage efficiency required on new boiler system installations?
a 66%
b 70%
c 76%
d 86%
7. What are combination boilers designed to do?
a Provide hot water and heating
b Work with oil and gas at the same time
c Provide hot water from a storage cylinder
d Pressurise cold water
What is the main purpose of the fill loop on a boiler?
a To provide hot water
b To introduce air into the system
c To provide increased pressure
d To allow ventilation of the system
9. What should be done to the system before opening the air-release valve at the top of
a radiator panel?

## Slide 117
Test Yourself
1. Name the three most common fuel sources used to run central heating systems.
2. What term is used to define all new boilers (either in new installations or as a replacement in an existing system), as defined in Part L1 of the Building Regulations?
3. What is the key difference between combination boilers and system boilers?
If a two-pipe system is being installed in a dwelling, which of the following statements
will be true?
a Water in the flow and return pipe work will be mixed.
b The return water will be at the same temperature as the flow.
c The water in the flow and return pipe work must be kept separate.
d The temperature of the return water will be higher than the flow.
What is the main purpose of the vent pipe on a heating circuit?
a To provide hot water
b To introduce air into the system
c To provide protection in the event of overheating
d To allow filling up of the system
Solid Fuel, Oil, Gas
Condensing
System boilers supply domestic hot water indirectly
Combination boilers are designed to heat up a cold water supply instantaneously for domestic hot water, so it is classed as direct hot water supply. When required, it will also supply hot water for the central heating system.

## Slide 118
7. What are combination boilers designed to do?
a Provide hot water and heating together
b Work with oil and gas at the same time
c Provide hot water via a storage cylinder
d Pressurise cold water
What is the main purpose of the fill loop on a boiler?
a To provide hot water
b To introduce air into the system
c To provide increased pressure
d To allow ventilation of the system
9. What should be done to the system before opening the air-release valve at the top of
a radiator panel?
Ensure the system is not in operation for risk of hot water and steam scold
6. According to SEDBUK, what is the minimum percentage efficiency required on new boiler system installations?
a 66%
b 70%
c 76%
d 86%