## Slide 1
BIPOLAR TRANSISTOR ( PRACTICAL BEHAVIOUR )
A transistor can be considered to act like a variable resistor between its Collector and Emitter terminals.
IC
IB
IE
Lamp
B
C
E
RT
IB
Lamp fully on
Lamp off
Lamp dim
IBmax
If IB switches from 0 to IBmax then RT will switch between Hi to Lo and the lamp will switch from off to on as if controlled by a mechanical switch.
Hi
Lo
12 V
RT

## Slide 2
We may therefore consider the transistor as having two modes of operation:
1) switch mode
2) linear, amplification mode
The Bipolar transistor may be considered to be a current controlled device, not all transistors are, some may be considered to be voltage controlled devices, such as the Field Effect transistor ( FET ).
Transistors operating in switched mode are suitable for digital electronic circuits whilst when operating in linear mode they may be used in analogue circuits.

## Slide 3
The base current IB controls the collector current IC. In what’s called the “linear region” the following relationship holds true:
IC = hFE . IB where hFE is a multiplication factor.
Suppose we want to control the illumination of a lamp by means of a transistor. Assuming we have a 9V lamp, a 12 V supply and a transistor with a hfe of 100. Assume also that the lamp is rated at 6W.
IC
IB
IE
Lamp
b
c
e
12V
6W
9V
In order for the lamp to be fully illuminated ( 9V across it )
then Vce, the collector/emitter voltage, must = 12-9 = 3V.
IC = P/V = 6W/9V = 2/3 A
But IC = hFE . IB therefore, re-arranging the expression we get;
IB = IC / hFE = (2/3) / 100 = 6.66 mA

## Slide 4
This means that the transistor will now have a resistance of
RT = Vc/IC
Therefore RT = 3 / (2/3) = 4.5Ω
RT forms a potential divider with the resistance of the lamp and thus controls the voltage and current available to illuminate the lamp.
By adjusting IB between 0 and 6.66 mA we can control the full range of lamp illumination.
In practice IB flows into the base and out of the emitter and therefore adds to IC which enters the collector and exits via the emitter as well.
Therefore IE = IB + IC
However, since IC >> IB (usually) we may say:
IE = IC approximately.