## Slide 1: Basement Construction & Waterproofing
Rhodri Thomas

## Slide 2: Definition:
Part of a building that is either partially or completely below ground level.
Approved document B of the UK building regulations, Fire Safety, Volume 1 Dwellinghouses, defines a ‘basement storey’ as:
‘A storey with a floor which at some point is more than 1,200 mm below the highest level of ground adjacent to the outside walls.’

## Slide 3: Basement or Cellar?
The term ‘basement’ is sometimes used interchangeably with the term ‘cellar' and may refer to any sort of below ground space used to provide accommodation, storage, car parking, services spaces, and so on.

## Slide 4
However, Approved Document F, 'Ventilation' suggests that, in relation to dwellings…
a basement = a dwelling or a usable part of a dwelling (i.e. a habitable room), that is situated partly or entirely below ground level.’
a cellar = part of a dwelling which is situated partly of entirely below ground level, and is distinct from a basement in that it is used only for storage, heating plant or purposes other than habitation.'

## Slide 5
Benefits of a Basement?

## Slide 6
Benefits of a Basement?
More ‘living’ space
Storage, utility room etc…
Make use of uneven ground
Temperature more stable?

## Slide 7
Negatives of a Basement?

## Slide 8
Negatives of a Basement?
Cost of more materials
Associated damp problems
Cost of damp solutions
Damp proofing can fail – difficult to remedy
Building regs/planning?

## Slide 9: Construction of Basements
Excavation – Temporary hoarding – retaining walls

## Slide 10: Construction of Basements

## Slide 11: Construction of Basements
Brick/Block masonry walls
This tends to be the most economical option for small-scale basement construction and often requires less time. However, concrete blocks are not suited to soil conditions that are prone to swelling as this applies lateral pressures to the basement wall which can weaken joints.

## Slide 12: Construction of Basements
Brick/Block masonry walls

## Slide 13: Poured Concrete
The external structure of the basement is poured into formwork, with reinforcing steel bars included if required. Form/Shuttering is then stripped away after curing. This type of construction tends to be stronger than others and is much more resistant to water infiltration.

## Slide 14: Poured Concrete
Offer High Strength
Poured concrete walls are hard to beat when it comes to their strength. They are super durable and offer a higher amount of flexural and compressive strength than block walls.
More Resistant to Lateral Water Pressure
It is imperative to construct a strong structure that offers as much water resistance as possible. No matter how bad the climate gets. Poured concrete walls are free from joints and are much denser than block foundation walls. They will not give in as quickly to buckling or bowing.
Fire Resistant
Poured concrete walls have the highest fire safety rating when compared to blocks.
They Offer Design Flexibility
Poured concrete walls offer more design flexibility for builders. They can opt for a change at the last moment regardless of the foundation type. Builders start with a liquid form, build a mold into any shape and design. This is hard to achieve with cinder block walls.
They Are Low Maintenance
Poured concrete walls are lower maintenance. They have fewer joints, better at withstanding lateral pressure, and fire-resistant. It is possible to have no signs of cracks or water leaks in the first 5 to 10 years with exterior waterproofing.
5 Reasons Why Poured Concrete Walls Are Better (americandry.com)

## Slide 15: Insulated Concrete Form

## Slide 16: Precast Panels
Precast concrete panels can be transported to the site and assembled on footings. This method is not as common but can be economical where there are multiple basements being constructed at the same time. If the joists between panels are not properly sealed then moisture can get trapped in the panels or penetrate to the interior and cause problems.
Precast Concrete Basements - Lakeland Log & Timber Frame Homes (lakelandloghomes.com)

## Slide 17: Methods Of Tanking Walls
The solution you require will depend on the extent and severity of the damp problem, and how you intend to use your underground space - whether it is simply for storage or if you want cellar tanking to create a habitable room or basement conversion in the property.
Bituminous bonded sheet tanking membranes
Bituminous paint tanking membranes
Polyurea tanking membranes
Epoxy coatings
Cementitious tanking membranes
Expanding clay sheet tanking membranes

## Slide 19: Tanking
A continuous waterproof barrier is applied to the inside or outside of the basement structure. The most common form is a bituminous ‘stick-on’ plastic sheet. While this is relatively inexpensive, it can lose adhesion and is easily damaged during backfilling.

## Slide 20: Drained Cavity
Cavities are formed within between the internal and external wall and floor constructions to collect and drain away water entering the basement using a sump and pump. As well as the internal drain, a perimeter drain may also be included. This runs around the external perimeter of the building just below the level of the foundation, removing water from the building’s external face.
https://www.youtube.com/watch?v=P_xjvhiiKJI

## Slide 21: Palace Hotel basement - Swansea

## Slide 22: Any Questions? Useful Resources
Inside London's Mega-Basements (businessinsider.com)
Grand Designs - Tracy Fox and Steve (Urban Shed) (South East London) Available on BoB, aired Friday 22/9/23