## Slide 1: UWTSD Motorsports Engineering
BMW Rally Group Project – Aerodynamics
Yash Patani (2306509) Kairan Bennett (2305389) Rhodri Jones (2305734) Jeremi Gumapos (2305861)

## Slide 2: Introduction
Yash

## Slide 3: Timing Plan and Team Organisation
Yash
Report Co-Ordinator – Yash
Research and Development – Rhodri
CAD Modeller – Jeremi
CFD Simulator - Kairan

## Slide 4: Literature Survey
ANSYS Inc., 2023. ANSYS Discovery and SpaceClaim User Guide. Available through ANSYS Help
McBeath, S., 2011. Competition Car Aerodynamics: A Practical Handbook. 3rd ed. Yeovil: Haynes Publishing.
Bernoulli / velocity-pressure relationship
(Anderson, 2017)
Anderson, J.D., 2017. Fundamentals of Aerodynamics. 6th ed. New York: McGraw-Hill Education.
Tudor, T., n.d. CFD External Aerodynamics 1: Introduction. Watch video.
(YouTube). Produced by the University of Wales Trinity Saint David, Swansea.
Tudor, T., n.d. CFD External Aerodynamics 2: Domain and Geometry. Available at: https://youtu.be/9OU2ySg0XS8
Tudor, T., n.d. CFD External Aerodynamics 3: Meshing Grid Creation (Octree). Available at: https://youtu.be/ezU-IceMndU
Tudor, T., 2025–2026. Vehicle Dynamics and Aerodynamics Lectures. University of Wales Trinity Saint David, Swansea. Delivered September 2025 – January 2026.
Sandford, M., 2025–2026. Engineering Management Lectures. University of Wales Trinity Saint David, Swansea. Delivered September 2025 – present day.
AUTODOC (2026) BMW E87 Body parts [Photograph]. AUTODOC. Available at: https://www.auto-doc.ie/car-parts/body/bmw/1er-reihe/1-e87 (Accessed: 18 March 2026).
sunyon-2024 (2026) For BMW 1 Series E81 E87 2005-11 118i 120i Top Wing Spoiler ABS Black Decoration [Photograph]. eBay. Available at: https://www.ebay.com/itm/365065632538 (Accessed: 18 March 2026).
Drawing Database (2014) BMW 1 Series (E87) Blueprint [Blueprint/Technical drawing]. Drawing Database. Available at: https://drawingdatabase.com/bmw-1-series-e87/ (Accessed: 18 March 2026).
MCG Autostyling (2025) BMW 1 Series Spoiler – Maxton Design [Photograph]. MCG Autostyling. Available at: https://shop.mcgautostyling.com/product/bmw-1-series-spoiler/ (Accessed: 18 March 2026).
Plastics 4 Performance (no date) BMW – E87 1 Series 5dr – Lexan Polycarbonate window kit [Photograph]. Plastics 4 Performance. Available at: https://www.plastics4performance.com/bmw-e87-1-series-5-dr-hatch-lexan-polycarbonate-window-kit (Accessed: 19 March 2026).
Hulsey, K. (1994-2015) Exploded illustrations and diagrams [Technical illustration]. Kevin Hulsey Illustration. Available at: https://www.khulsey.com/exploded-illustrations.html (Accessed: 20 March 2026).
​​Airfoil Tools (2026) Airfoil Tools. Available at: http://airfoiltools.com/ (Accessed: March 21, 2026).
​“Basic Wing Lofting in SolidWorks” (2021) Aircraft Breakdown [Preprint]. Available at: https://www.youtube.com/watch?v=p6WxZmhK4w0 (Accessed: March 21, 2026).
​Xfoil (2026) Airfoil Tools. Available at: http://airfoiltools.com/airfoil/details?r=polar/index/#xfoil (Accessed: March 21, 2026).
​​Tudor, T., 2026. 25_26 Vehicle Aerodynamics, Swansea: UWTSD.
​​​
Building a simple aerofoil rear wing for a sports car | Bucks Composites (no date). https://www.bucks-composites.com/how-to-do/building-simple-aero-foil-rear-wing-sports-car (Accessed: November 20, 2025).
Carbon, S. (2025) Cost Guide: Custom carbon fibre parts pricing explained. https://www.supreemcarbon.com/cost-guide-custom-carbon-fiber-pricing-explained.html (Accessed: November 20, 2025).
How to make a carbon fibre rear wing, mouldless method - Easy Composites (no date). https://www.easycomposites.co.uk/learning/mouldless-carbon-fibre-aero-wing (Accessed: November 20, 2025)

## Slide 5: Design and Research
Research into existing wing designs
Circuit rally regulations state body modifications cannot exceed the silhouette of the vehicle
https://www.motorsportuk.org/wp-content/uploads/2019/12/145-154-Vehicles-J.pdf
Rhodri

## Slide 6: Scanning
Scanned real wing in workshop
Modelled wing CAD models onto car model for CFD
Attempted full car scan

## Slide 7: 3D Model from scan
Full wing CAD model was produced from the 3D scan
Imported file to SolidWorks
Areas with imperfections

## Slide 8: Wing assembly process - Design 1
Aerofoil from car no.40
Low attack angle
Wing was modified to fit BMW model
Showed results but were minor differences

## Slide 9: Adjusted Design 1
Adjusted attack angle to roughly 10 degrees
Showed significantly better results

## Slide 10: S1223 Wing mount
Designed and moulded mount for the wing
Fixed to window
Proof of concept

## Slide 11: Skid plate design
Designed skid plate to streamline underbody airflow
Double use of protecting components as well
Proof of concept design – not tested

## Slide 12: Mounted to car model
Underbody of car model isn’t detailed
Skid plate put in place as proof of concept

## Slide 13: Modelling
Individual investigation on aerofoils conducted
Jeremi

## Slide 14: Airfoiltools.com

## Slide 15: Filtering & Viable Aerofoil
NACA4412 | NACA4415 | NACA6409 | SELIG S1210 | SELIG S1223 | EPPLER E423

## Slide 16: Graphs
Parameters:
Reynold number = 200,000 (green line) and 500,000 (blue line)
Ncrit value = 5

## Slide 17: Values
 | @ 10° | @ 10° | @ 10° | @ 10° | @ 10° | @ 10°
 | NACA4412 | NACA4415 | NACA6409 | SELIG1210 | SELIG1223 | EPPLER423
Cl | 1.40 | 1.30 | 1.43 | 1.99 | 2.20 | 1.90
Cd | 0.02 | 0.02 | 0.025 | 0.026 | 0.025 | 0.022
 | @ 10° | @ 10° | @ 10° | @ 10° | @ 10° | @ 10°
 | NACA4412 | NACA4415 | NACA6409 | SELIG1210 | SELIG1223 | EPPLER423
Cl | 1.30 | 1.25 | 1.38 | 1.82 | 2.09 | 1.85
Cd | 0.029 | 0.022 | 0.032 | 0.033 | 0.033 | 0.028
@ 200,000 Re, Ncrit 5 [34mph]
@ 500,000 Re, Ncrit 5 [85mph]

## Slide 18: Dimensions
Chord = 200mm and Span = 1690mm

## Slide 19: Calculations
Reynold number transition from laminar to turbulent on a flat plate 500,000.
@ 80mph | 476,474
@ 70mph | 414,175
@ 60mph | 354,708
Aspect Ratio =
To calculate the overall wing’s coefficient of lift given the aerofoil coefficient of lift, the formula used is:
= Cl of wing
AR = 8.45
Cl of wing = 1.633
Calculating the lift of a wing uses the formula: 0.5 x Pressure x Vel^2 x Cl of wing x chord x span
@ 80mph | 437.426N
@ 70mph | 324.356N
@ 60mph | 242.420N
Sensitive Data

## Slide 20: CFD and Model
Aims
Geometry fix
Creating a domain
Completed multiply CFD runs with different wing configurations
Analysis
Real world
Further CFD work
Kairan

## Slide 21: Analysis
First CFD run
No wing
Baseline for further CFD work
key areas (rear boot lip flow separation and high pressure and low-pressure points )
Vortex and turbulent wake reign

## Slide 22: CFD 2 Neutral Wing
Wake reduction Air flow characteristics Vortex reduction Pros and cons of neutral wing
The streamlines also become closer together, indicating flow acceleration
Velocity is low (blue region).

## Slide 23: CFD 3 HIGH ATTACK ANGLE
10° attack angle
Biggest wake reduction of all CFD runs
Improvements in rear stability at high speeds Direction flow improvements
Increase in high pressure at the top face of wing
Pros and cons of the high attack wing

## Slide 24: Improvements and reflection
What our CFD showed
The conclusion we came to in the context of the rally competitions and regulations
How the CFD could have been better
Further CFD work, we are looking into doing (improved model, better CFD software, run CFD on more aerodynamic devices

## Slide 25: Results

## Slide 26: Conclusions

## Slide 27
Thank You For Listening