## Slide 1: Simple Digital Communications System
Dr John Rees

## Slide 2: Simple Comms System
Input Transducer
Transmitter
Channel
Receiver
Output Transducer
Input
Output

## Slide 3: Digital Communications System?
Input transducer
  Conditions the input
  Sample the input
  Convert it into a binary number
  Conditions the input
  Line code the binary number
Transmitter
  Key the binary number
  Modulate the binary number
  Amplify the signal
  Send it to the air interface (or transmission channel)

## Slide 4: Digital Comms System?
Channel
  Attenuates the signal
  Distorts the signal
  Reflects and diffracts the signal
Receiver
  Conditions the signal
  Samples the signal
  Conditions the signal
  Demodulates the signal
  Conditions the signal
  Passes the binary number

## Slide 5: Digital Comms System?
Output transducer
  Converts the output back to a signal (if appropriate)
  Conditions the output
  Amplifies the output (if appropriate)

## Slide 6: So, More Digital?

## Slide 7: More Digital?
We can move our analogue approach entirely into numbers
Sample the input signal at an appropriate rate
Use the numbers? E.g.
  A low pass filter is an average of samples
  A high pass filter is the difference of samples
Send the sample as a number
Receive the number
Digital to analogue conversion (back to analogue)

## Slide 8: So We Have to Sample?
Think audio, .wav files, etc.
  Often sampled at 44,100 samples per second, 8bit or 16 bit samples
  (There is a lot of information in an audio signal)
Television/video (actually camera!)
  Each pixel is individually a sample (three samples if colour RGB)
  Updated whole screen 25x per second (whole picture capture – all pixels sampled – 25/sec)

## Slide 9: What About Problems?
Sampling too slow
  Aliasing
Sampling synchronised to a harmonic of the signal?
Sampling too fast?
Noise?
  On the input signal
  Quantisation noise

## Slide 10: Simple Digital Filter
Uses two concepts
  Windows
    The sequence of samples over which it will apply
  Summing weighted delayed samples
    Adding together the samples in the window with weights applied to each
    The output is the resulting sum

## Slide 11: Example Simple Digital Filter
Low pass filter
  Window size 6
  Equal weights
x(n)
x(n-1)
x(n-2)
x(n-3)
x(n-4)
x(n-5)
x
∑
1/6
1/6
1/6
1/6
1/6
1/6
Filtered
Output
Unfiltered
Output

## Slide 12: Example Cont.
If input sample sequence is
{10, 20, 26, 30, 33, 35, 35, 35, 35, 35, …..}
Filtered output is
  Delayed by six sample periods, then:
{26, 30, 32, 33, 34, 35, ….}
(10+20+26+30+33+35)/6
(30+33+35+35+35+35)/6
(35+35+35+35+35+35)/6
Called a moving average filter, or a
rolling mean filter

## Slide 13: Example Cont.
Length of filter defines degree of smoothing
  Shorter window, less filtering effect
Uses only delayed samples of our signal
  Digital numbers, simply stored in memory
Uses only trivial mathematics
  Necessarily quick in processing
But delayed output (by the window size)
  Affects all windowed filters
Linear filter – can recover the original sequence

## Slide 14: Take the Same Sequence with Noise
Input sample sequence is
{10, 20, 50, 30, 33, 35, 35, 35, 35, 35, …..}
  Noise picked up on sample 3 (in red)
Filtered output is
  Delayed by six sample periods, then:
{30, 34, 36, 34, 35, 35, ….}
As expected, the averaging has spread the noise effect and reduced its peak value

## Slide 15: Average Filter