## Slide 1
Traditional walls
ACBA 4022: Fundamentals of Construction Technology

## Slide 2
Lesson objectives
Objectives:
Describe the construction methods and materials used for traditional wall construction.
State common defects associated with this type of construction.

## Slide 3
Traditional construction
Today many processes have been modernised in order to increase efficiency and drive down costs. Modern methods also aim to overcome some defects associated with traditional construction.
Traditional methods are considered a slower form of construction. Most usually with the added downside of increased cost.
However some still consider traditionally built buildings to be higher quality because of the extra time and cost. This is coupled with the fact that older buildings have stood the “test of time”.

## Slide 4
In the UK traditional construction usually refers to solid masonry walls (brick or stone) although old timber frame was also used, for the purposes of this module we will focus on solid masonry walls.

## Slide 5
Stone construction
Stone has been used as a building material for thousands of years. It has long been recognised as a material of great durability and superior artistic quality, the foremost choice for buildings associated with status, power and religion.
The pyramids in Giza, burial chambers in the UK and temples in Malta were all built from stone 4000-6000 years ago and are still standing. The use of stone in construction has declined over the last hundred years, but it remains an aristocrat of building materials.

## Slide 6
Brick
Although stone is the oldest method of masonry construction, the brick method of construction has been used for many years. In fact it was first used in 5000BC.
Pompei
Rome
Egyptian brick mould

## Slide 7
Activity – Take 10 minutes to think of potential advantages & disadvantages of masonry (brick/stone) as a construction material
Advantages | Disadvantages

## Slide 8
FUNCTIONAL REQUIREMENTS OF EXTERNAL WALLS
Weather protection
Fire resistance
Thermal resistance
Strength and stability
Durability
Buildability
Noise insulation

## Slide 9
SOLID WALLS
Traditional construction. Pre 1919 solid walls
1919?

## Slide 10
The thickness of a stone wall can vary, typically thicker in older buildings, an average thickness of a circa 1900’s house could be 750mm on the ground floor and tapering to a thinner wall upstairs.

## Slide 11
SOLID WALLS
Traditional construction. Pre 1919 solid walls
Characteristics:
Thick walls
Random rubble
Lime mortar
Shallow foundations
No DPC

## Slide 12
SOLID WALLS
Traditional construction. Pre 1919 solid walls
Random rubble
The inclusion of ‘tie stones’ which bind the inner and outer layers of stone improves strength

## Slide 13: Ashlar or ‘Dressed Stone’
By working stone into more regular shapes, it allows more standardised construction and more predictable properties with many benefits from appearance to easier estimating of quantities.
There is more manufacturing involved in machining these stones which means increased cost and time.
Traditional construction. Pre 1919 solid walls

## Slide 14
SOLID WALLS
Traditional construction. Pre 1919 solid walls
Brickwork

## Slide 15
SOLID WALLS
Brickwork. Materials

## Slide 16
SOLID WALLS
Traditional construction. Pre 1919 solid walls
Brickwork. Bonds

## Slide 17
SOLID WALLS
Traditional construction. Pre 1919 solid walls
Brickwork. Bonds

## Slide 18
SOLID WALLS
Traditional construction. Pre 1919 solid walls
Brickwork. Bonds

## Slide 19
SOLID WALLS
Traditional construction. Pre 1919 solid walls
Brickwork. Bonds

## Slide 20
Traditional construction
Solid masonry walls of brick or stone.
Construction materials varied depending on location such as rural or in a larger town.

## Slide 21
Traditional construction
Foundations were sometimes stone or brick or concrete in more affluent areas. Sometimes in older rural properties there wasn’t much of a foundation at all

## Slide 22
What about mortar?
Lime Mortar – Lime, Sand and Water
Cement Mortar – Cement, Sand and Water

## Slide 23
With the introduction of modern Portland cement during the 19th century, the use of lime mortar in new constructions gradually declined.
This was largely due to the ease of use of Portland cement, its quick setting, and high compressive strength. However, the soft and porous properties of lime mortar provide certain advantages when working with softer building materials such as natural stone and terracotta.
For this reason, while Portland cement continues to be commonly used in new brick and concrete construction, in the repair and restoration of brick and stone-built structures originally built using lime mortar, the use of Portland cement is not recommended.
A wall system needs a balance between the mortar and brick that allows the mortar to be the weak part of the unit. When mortar is stronger than the brick, it prevents any natural movement in the wall and the faces of the brick will begin to deteriorate, a process known as Spalling.

## Slide 24
Defects

## Slide 25
Defects

## Slide 26
Masonry Wall - Exterior Protection
Solid masonry walls had a few options for external protection:
Sometimes left bare to rely on the natural density of the material to repel water and the breathability of the lime based mortar to release moisture.
Whitewash / Limewash – a traditional, breathable finish made from slaked lime, water, and natural pigments. Applied to porous surfaces like lime render and stone, creating a soft, matte, and textured look that allows moisture to evaporate from the wall
External lime render – Used up to the 1920’s
Gradually replaced by Cement. Still considered
most suitable for solid Masonry walls due to its
breathability.

## Slide 27
Internal Partition Walls - Traditional
Partition walls aren’t load bearing and are used to form rooms and spaces. As such, they don’t necessarily need to be built in the same way as structural walls.
Brick – solid wall then a lime based plaster
Timber Stud – Could be covered with Lath and Plaster
Timber Stud – With brick infill then plastered, usually lightweight hollow clay bricks

## Slide 28
Lesson objectives
Objectives:
Describe the construction methods and materials used for traditional wall construction.
State common defects associated with this type of construction.

## Slide 29
Any questions?