## Slide 1: HANDOUT: ARM Thumb-16 Assembly

## Slide 2: Data Types
ARM processors support the following data types in memory:
Byte 8 bits
Halfword 16 bits
Word 32 bits
Doubleword 64 bits

## Slide 3: Thumb 16-bit Instruction Set Encoding

## Slide 4
Rd: Destination register
Rn: Source OR an operand in a register for an arithmetic operation
Rm: An operand in a register for an arithmetic operation.
Ra: A value in a register to be used in an addition or subtraction. Think "accumulator“
Example: add Rd, Rn, Rm is equivalent to Rd = Rn + Rm

## Slide 5: LDR Immediate
LDR |  |  |  |  | 
 | Clock Cycles |  |  | Examples | Equivalent
ldr Rd, =<imm> | 1 | Load an immediate value to a register | Rd = imm | ldr r0, =3 ldr r0, =0x12 | r0 = 3 r0 = 0x12
For Thumb, Rd, Rn and Rm = r0 to r7 (the Lo registers)

## Slide 6: Literal Pool
When using LDR immediate, the assembler places the large values in a literal pool
  By default this follows the “.end” directive
  Alternatively place an LTORG assembler directive near the code using the LDR instruction (there is a 4Kbyte (or 1Kbyte for Thumb) distance limit)
For example: ldr r0, =0x1234567 ldr r1, =0x1345567 in psuedocode looks like this:
ldr r0, [literal pool + 0]
ldr r1, [literal pool + 4] // Skip first 4 bytes(32-bits) literal pool: .word: 0x1234567 // 32-bit values .word: 0x1345567 // stored in memory
Actually it uses offset addressing from PC, hence the offset limit when placing pool

## Slide 7: MOV
MOV -- Move Value to Register |  |  |  |  | 
 | Clock Cycles |  |  | Examples | Equivalent
mov Rd, #<imm> | 1 | Copy an 8-bit immediate value to a register Max immediate value is 255 (Thumb limit) | Rd = imm | mov r0, #3 mov r0, #0x12 | r0 = 3
mov Rd, Rs | 1 | Copy contents of source register into destination register | Rd = Rs | mov r0, r1 | r0 = r1
For Thumb, Rd and Rs = r0 to r7 (the Lo registers)

## Slide 8: LDR vs MOV
Actually LDR is a pseudo-instruction provided by the assembler
  The assembler actually converts it into one or more assembler instructions, although eventually it boils down to a mov instruction
Use LDR to load immediate values into registers instead of MOV
Use LDR when reading data from memory (See later notes)
Use MOV copy the value from one register to another

## Slide 9: Add/Subtract
ADD |  |  |  |  | 
 | Clock Cycles |  |  | Examples | Equivalent
add Rd, #<imm> | 1 | Add an 8-bit immediate value to a register Max immediate value is 255 (Thumb limit) | Rd = Rd + imm | add r0, #3 add r0, #0x12 | r0 = r0 + 3
add Rd, Rn | 1 | Add two registers together and store result in first register | Rd = Rd + Rn | add r0, r1 | r0 = r0 + r1
add Rd, Rn, Rm | 1 | Add two registers together and store result in third register | Rd = Rn + Rm | add r0, r1, r2 add r0, r0, r1 | r0 = r1 + r2 r0 = r0 + r1
add Rd, Rn, #<imm> | 1 | Add register and 3-bit immediate and store result in second register Max immediate value is 7 Thumb limit) | Rd = Rn + imm | add r0, r1, #2 | r0 = r1 + 2
Subtract is identical e.g. sub r0, #3
For Thumb, Rd, Rn and Rm = r0 to r7 (the Lo registers)

## Slide 10: Mutliply
MUL -- Multiply |  |  |  |  | 
 | Clock Cycles |  |  | Examples | Equivalent
mul Rd, Rn | 1 or 32 | Multiply two registers and store result in the first one | Rd = Rd * Rn | mul r0, r1 | r0 = r0 * r1
mul Rd, Rn, Rd | 1 or 32 | Multiply two registers and store result in the second one | Rd = Rn * Rd | mul r1, r0, r1 | r1 = r0 * r1
Thumb Does Not Provide a Divide Instruction
For Thumb, Rd, Rn and Rm = r0 to r7 (the Lo registers)

## Slide 11: Left Shift Operations
LEFT SHIFT |  |  |  | 
 | Clock Cycles |  |  | Examples
lsl Rd, #<shift> | 1 | Left shift the contents of register by the shift length (0 to 31). | Rd = Rd << shift | lsl r0, #3
lsl Rd, Rm, #<shift> | 1 | Left shift the contents of register by the shift length (0 to 31) and store result in first register. | Rd = Rm << shift | lsl r0, r1, #3
lsl Rd, Rs | 1 | Left shift the contents of register by the shift length contained in the register Rs (0 to 31). | Rd = Rm << Rs | lsl r0, r1
For Thumb, Rd, Rn and Rm = r0 to r7 (the Lo registers)

## Slide 12: Right Shift Operations
SHIFT/ROTATE |  |  |  | 
 | Clock Cycles |  |  | Examples
lsr Rd, #<shift> | 1 | Right shift the contents of register by the shift length (1 to 32). | Rd = Rd >> shift | lsr r0, #3
lsr Rd, Rm, #<shift> | 1 | Right shift the contents of register by the shift length (1 to 32) and store result in first register. | Rd = Rm >> shift | lsr r0, r1, #3
lsr Rd, Rs | 1 | Rightshift the contents of register by the shift length contained in the register Rs (0 to 31). | Rd = Rm >> Rs | lsr r0, r1
For Thumb, Rd, Rn and Rm = r0 to r7 (the Lo registers)

## Slide 13: Rotate Right Operation
SHIFT/ROTATE |  |  |  | 
 | Clock Cycles |  |  | Examples
ror Rd, Rs | 1 | Rotate ight the contents of register by the shift length (1 to 31) and store result in first register. | Rd = Rm << Rs | ror r0, r1
For Thumb, Rd, Rn and Rm = r0 to r7 (the Lo registers)

## Slide 14: Labels
To avoid using memory addresses, especially when referring to lines of code, we use a text label
The linker will calculate the correct address for each label during the linking process
loop:
b loop // Loop forever

## Slide 15: Unconditional Branching
BRANCH – Jump to a specific location |  |  | 
 | Clock Cycles |  | Examples
b label | 1 | Always branch to the address specified by the label | forever: b forever

## Slide 16: Conditional Branching
BRANCH – Jump to a specific location |  |  |  | 
 | Clock Cycles |  | Status Flag | Examples
beq label | 1 | Branch when equal to the address specified by the label when | Z set | ==
bne label | 1 | Branch when not equal to the address specified by the label when | Z clear | !=
bgt label | 1 | Branch when greater than to the address specified by the label when | Z clear, N and V the same | >
bge label | 1 | Branch when greater than or equal to the address specified by the label when | N and V the same | >=
blt label | 1 | Branch when less than to the address specified by the label when | N and V differ | <
ble label | 1 | Branch when less than or equal to the address specified by the label when | Z set, N and V differ | <=
bcs label bvs label | 1 | Branch when carry/overflow set to the address specified by the label when | C set V set | 
bcc label bvc label | 1 | Branch when carry/overflow clear to the address specified by the label when | C clear V clear | 

## Slide 17: Condition Flags
Flag | Logical Instruction | Arithmetic Instruction
Negative (N=1) | No meaning | Bit 31 of the result has been set. Indicates a negative number in signed operations
Zero (Z = 1) | Result is all zeroes | Result of operation was zero
Carry (C = 1) | After Shift operation ‘1’ was left in carry flag | Result was greater than 32 bits. Operation results in a carry, or when a subtraction results in no borrow
oVerflow (V = 1) | No meaning | Result was greater than 31 bits Operation causes an overflow (or an underflow). May indicate a possible corruption of the sign bit in signed numbers

## Slide 18: Comparing Values (Are they the same?)
COMPARE POSITIVE/NEGATIVE VALUES |  |  | 
 | Clock Cycles |  | Status Flags Set
cmp Rn, #<imm> | 1 | Compare the register value with the 8-bit immediate value | N, Z, C, V
cmp Rn, Rm | 1 | Compare the register values | 
cmn Rn, Rm | 1 | Compare the register values assuming values are negative | 
For Thumb, Rn and Rm = r0 to r7 (the Lo registers)

## Slide 19: Loading Value/Address into Register
LOAD – Load Value/Address into Register |  |  |  | 
 | Clock Cycles |  |  | Examples
ldr Rd, =<imm> | 1 or 2 | Load immediate value into register (see previous notes, also see literal pool). The equals operator tells the assembler this is a value not an address. | Rd = 0x252626 | ldr r0, =0x62727
ldr Rd, =label | 1 or 2 | Load the address of the labelled memory into the register. The assembler actually calculates offset from this instruction to the memory i.e. the PC relative address | Rd = addr(label) | ldr r0, =label
For Thumb, Rd = r0 to r7 (the Lo registers)

## Slide 20: Loading Value into Register from Memory
LOAD – Load Register From Memory |  |  |  | 
 | Clock Cycles |  |  | Examples
ldr Rd, [Rs] | 1 or 2 | INDIRECT ADDRESSING Load value from memory at address specified by Rs into the register Rd | Rd = [Rs] | ldr r0, [r1]
ldr Rd, [Rs, <offset>] | 1 or 2 | INDIRECT OFFSET ADDRESSING Load value from memory at address specified by Rs (plus an 5-bit positive offset 1-31) into the register Rd | Rd = [Rs + 3] | ldr r0, [r1, #3]
ldr Rd, [Rs, Rn] | 1 or 2 | INDIRECT REGISTER OFFSET ADDRESSING Load value from memory at address specified by Rs (plus offset specified in register Rn) into the register Rd | Rd = [Rs + Rn] | ldr r0, [r1, r2]
For Thumb, Rd, Rs and Rn = r0 to r7 (the Lo registers)
Word addresses must be 32-bit aligned
NO DIRECT ADDRESSING MODE
i.e. ldr Rd, [label]  doesn’t work

## Slide 21: Loading Value into Register from Memory (Halfword and Byte)
LOAD – Load Register From Memory |  |  |  | 
 | Clock Cycles |  |  | Examples
ldrb Rd, [Rs] ldrh Rd, [Rs] | 1 or 2 | INDIRECT ADDRESSING Load byte/halfword value from memory at address specified by Rs into the register Rd | Rd = [Rs] | ldrb r0, [r1] ldrh r0, [r1]
ldrb Rd, [Rs, <offset>] ldrh Rd, [Rs, <offset>] | 1 or 2 | INDIRECT OFFSET ADDRESSING Load byte/halfword value from memory at address specified by Rs (plus an 8-bit offset) into the register Rd | Rd = [Rs + 3] | ldrb r0, [r1, #3] ldrh r0, [r1, #4]
ldrb Rd, [Rs, Rn] ldrh Rd, [Rs, Rn] | 1 or 2 | INDIRECT REGISTER OFFSET ADDRESSING Load byte/halfword value from memory at address specified by Rs (plus offset specified in register Rn) into the register Rd | Rd = [Rs + Rn] | ldrb r0, [r1, r2] ldrh r0, [r1, r2]
For Thumb, Rd, Rs and Rn = r0 to r7 (the Lo registers)
Halfword addresses must be 16-bit aligned

## Slide 22: Loading Signed Value into Register from Memory (Halfword and Byte)
LOAD – Load Register From Memory |  |  |  | 
 | Clock Cycles |  |  | Examples
ldrsb Rd, [Rs] ldrsh Rd, [Rs] | 1 or 2 | INDIRECT ADDRESSING Load signed byte/halfword value from memory at address specified by Rs into the register Rd | Rd = [Rs] | ldrsb r0, [r1] ldrsh r0, [r1]
ldrsb Rd, [Rs, Rn] ldrsh Rd, [Rs, Rn] | 1 or 2 | INDIRECT REGISTER OFFSET ADDRESSING Load signed byte/halfword value from memory at address specified by Rs (plus offset specified in register Rn) into the register Rd | Rd = [Rs + Rn] | ldrsb r0, [r1, r2] ldrsh r0, [r1, r2]
For Thumb, Rd, Rs and Rn = r0 to r7 (the Lo registers)
Halfword addresses must be 16-bit aligned

## Slide 23: Store Register Value In Memory
STORE– Store Register Into Memory |  |  |  | 
 | Clock Cycles |  |  | Examples
str Rs, [Rd] | 1 or 2 | INDIRECT ADDRESSING Store value in R from memory at address specified by Rs into the register Rd | [Rd[ = Rs | str r0, [r1]
str Rs, [Rd, <offset>] | 1 or 2 | INDIRECT OFFSET ADDRESSING Load value from memory at address specified by Rs (plus an 8-bit offset) into the register Rd | [Rs + 3] = Rs | str r0, [r1, #3]
str Rs, [Rd, Rn] | 1 or 2 | INDIRECT REGISTER OFFSET ADDRESSING Load value from memory at address specified by Rs (plus offset specified in register Rn) into the register Rd | [Rs + Rn] = Rd | str r0, [r1, r2]
For Thumb, Rs and Rd = r0 to r7 (the Lo registers)
Word addresses must be 32-bit aligned
Versions are also available for storing bytes and halfwords
strb Rs, [Rd], etc store byte
strh Rx, [Rd], etc  store halfword

## Slide 24: Variables
Example:
int number1 = 22;
int number2 = 33;
int result;
…. Some other code …..
result = number1 + number2;
number1 + number2
result = r3
[r0]
.section .data
number1: space 4
number2: space 4
result: space 4
.section .text
ldr r0, =result
ldr r1, =number1
ldr r3, =#22
str r3, [r1]
ldr r2, =number2
ldr r3, =#33
str r3, [r2]
… Some other code ….
ldr r1, [r1]
ldr r2, [r2]
add r3, r1, r2 str r3, [r0]

## Slide 25: Array (Equivalent)
An array in a higher level language is just a block of space
.section .data
array: .space 4 * 10  an array of 10 words (4 bytes each, 32-bits)
label

## Slide 26: Fill array
ldr r1, =array
ldr r0, =#0  Initialise index
b exitloopbody:
loopbody:
ldr r2, =#0
str r2, [r1]  Set array element to 0
add r1, #4  Move to next array pos
add r0, #1 Increment index
exitloopbody:
cmp r0, #10  index < 10
blt loopbody

## Slide 27: Call Function
BL– Long Branch with Link |  |  |  | 
 | Clock Cycles |  |  | Examples
bl label | 3 | Branch to label. The contents of the program counter(PC) register is placed in the link register (LR) . |  | bl label
For Thumb, Rd, Rs and Rn = r0 to r7 (the Lo registers)

## Slide 28: PC and LR
R15 is the Program Counter (PC)
R14 is used as the subroutine Link Register (LR) and stores the return address when Branch with Link operations are performed, calculated from the PC.
Thus to return from a linked branch (i.e. function call), use either:
  mov r15,r14
or
  mov pc,lr
pc = Program Counter (r15)
lr = Link Register (r14)

## Slide 29: Function/Subroutine Calls
Functions are just blocks of code that we branch to, but with one big difference. The return address following the branch “call” is automatically placed in the ARM processor link register (r14)
A branch and link (BL) instruction is required to achieve this
…. More Code …. bl function
…. More Code ….
function:
…. Body of function ….
mov pc, lr
label
Branch instruction “call”
Simple Return (usually use “pop”)

## Slide 30: Passing Arguments to a Function and Returning Results
First four arguments should be passed into the function in registers r0, r1, r2 and r3
Any additional arguments to be passed into the function should be pushed onto the stack
Result should be returned in r0
In function use r0, r1, r2, and r3 as you wish
  If you need more registers then push the register values onto the stack first but remember to pop them off again before returning

## Slide 31: PUSH
PUSH – Push Register Values Onto Stack |  |  |  | 
 | Clock Cycles |  |  | Examples
push { <reglist> } | 1+N | Push the contents of each register in the list onto the stack |  | push { r0 } push { r0, r1, r2 } push { r0 - r2, r7 }
push { <reglist>, lr } | 1+N | Push with link register. Push the contents of each register in the list onto the stack with contents of link register |  | push { lr } push { r0, r1, lr }
For Thumb, Rd, Rs and Rn = r0 to r7 (the Lo registers)
<reglist> = comma separated list of registers which may include a range e.g. r0-r5

## Slide 32: POP
POP – Pop Register Values From the Stack |  |  |  | 
 | Clock Cycles |  |  | Examples
pop { <reglist> } | 1+N | Pop the contents of each register in the list from the stack |  | pop { r0 } pop { r0, r1, r2 }
pop { <reglist>, pc } | 3+N | Pop and return. Pop the contents of each register in the list from the stack and the return address into the program counter |  | pop { pc } pop { r0, r1, pc }
For Thumb, Rd, Rs and Rn = r0 to r7 (the Lo registers)
<reglist> = comma separated list of registers which may include a range e.g. r0-r5

## Slide 33: Full Descending Stack
Increasing Memory Addresses
Registers are ALWAYS stored on the stack in numerical order, with the highest register numbers pushed first i.e. lowest numbered register at the lowest memory address
push {r0,r1,r3-r5, lr}
SP
Old SP
r0
r5
r4
r3
r1
lr (r13)
r0
Decrement Before Save
pop {r0,r1,r3-r5, lr}
SP
Old SP
r5
r4
r3
r1
r0
lr (r13)
Increment After Load
r4
Register number
Notes:   Lowest register mapped to lowest memory address.
  ‘!’ causes stack pointer updated in all these cases.

## Slide 34: Stack Example
ldr r4, =#5
push {r4}
ldr r4, =#6
push {r4}
ldr r5, =#0x11111111
push {r4-r5, lr}
Memory Address | Bytes (32-bits) |  | Stack Pointer
0x20000018 | 06 00 00 00 | r4 | sp
0x2000001C | 11 11 11 11 | r5 | sp + 4(0x04)
0x20000020 | 33 00 40 00 | lr | sp + 8(0x08)
0x20000024 | 06 00 00 00 | #6 | sp + 12(0x0C)
0x20000028 | 05 00 00 00 | #5 | sp + 16(0x10)
Descending Addresses
Note: For push{r4-r5, lr} lr is pushed then the register list starting with highest reg numbers first i.e. r5 then r4
r4 ends up at lowest memory address following push

## Slide 35: Function Example
Passing 6 arguments
Using r0 to r3 are used so save r7 so we can use it (demo, could just as easily just used r0)
AddSixNumbers:
push {r7, lr}
mov r7, r0
add r7, r1
add r7, r2
add r7, r3
ldr r1, [sp, #0x0C]
add r0, r1
ldr r1, [sp , #0x08]
add r0, r1
pop {r7, pc}
ldr r0, =#1
ldr r1, =#2
ldr r2, =#3
ldr r3, =#4
ldr r4, =#23
push {r4}
ldr r4, =#45
push {r4}
bl AddSixNumbers // Call function
Use r0-r3
Push values 23 and 45 onto stack
Save r7 and lr on stack (2 x 4 bytes)
Use r0-r3
Get value 23 from stack (skip 12 bytes)
Get value 45 from stack (skip 8 bytes)
r7
sp
lr
sp + 4
#45
sp + 8
#23
sp + 12
Restore r7 and return, result in r0

## Slide 36: Calling Assembler Function From C
Three things you need to do are:
  Export the function in the assembler file to make it externally linkable using .global
  Specify the type of the symbol in the assembler file using .type and indicating that the symbol is a function by setting the value to %function
    %function for a function
    %object for a data object
  Import the function into the C file by using an extern
1
2
3

## Slide 37: Linking to an Assembler Function
.section .text
.global AddNumbers
.type AddNumbers, %function
AddNumbers:
push {lr}
add r0, r1
pop {pc}
.end
LTORG
extern int AddNumbers(int number1, int number2);
int result = AddNumbers(2, 3);
3
2
1

## Slide 38: Pass Value by Reference (e.g. Pass Address of Array)
extern unsigned int AddArrayNumbers(unsigned int *array, int arrayLen);
unsigned int numbers[] = { 3, 4, 5, 6, 7 };
result = AddArrayNumbers(numbers, 5);
.global AddArrayNumbers // Make it externally linkable
.type AddArrayNumbers, %function
AddArrayNumbers: // r0 = array, r1 = array length
push {r4, lr}
ldr r2, =#0 // Set index
ldr r3, =#0 // Running total
b numbersloopend
numbersloopstart:
ldr r4, [r0] // Read value from array element
add r3, r4 // Add read value to running total
add r0, #4 // Move to next array element (+4 bytes)
add r2, #1 // Increment index
numbersloopend:
cmp r2, r1 // index < arraylenght
blt numbersloopstart
mov r0, r3 // Return result(r0)
pop {r4, pc}
unsigned int = 32-bits (4 bytes)