## Slide 1
Manufacturing Quality
(Planning, Assurance, Control & Improvement)
Jordan R. Jenkins

## Slide 2: Recap – JIT (Right Products, Right Quantities, Right Time, Right Quality)
Takt Time
Heijunka – Uniform Plant Loading
Continuous Flow
Total Quality Management (TQM)
Layouts & Cellular Design
Reduce Changeover Time (SMED)
Respect for People:
Worker, Customer & Supplier Relationships
Total Productive Maintenance (TPM)
Pull Systems

## Slide 3: Session Overview
Session Aim
“To gain an understanding of the fundamental principles of quality in manufacturing”
Lecture Summary
Defining quality (not as straight forward as it seems!)
Introducing the quality gurus
Traditional vs contemporary approaches to quality
The 8 dimensions of quality
Cost of Quality (COQ), Cost of Poor Quality (COPQ) and 1-10-100 rule
What is quality management?
Introduction to Total Quality Management (TQM)
Overview of the 7 basic tools of quality
Overview of the Kano model

## Slide 4: Question – Definition of Quality
How do you (or your organisations) define the quality of a product / service?
Take a few minutes to think about the ways in which you could define good/bad quality

## Slide 5: The Many Ways to Define Quality
We are all familiar with the premise of quality, but narrowing it down to a single definition is often a difficult or elusive task.
Textbooks, journals and technical standards documents (ISO, BSI, ASME) contain a diverse (and often conflicting) range of definitions.
Although there are common themes: excellence, continuous improvement, and customer focus etc, different organisations will inevitably emphasise different things.

## Slide 6: Some Common Quality Definitions
Transcendent quality – excellence, best in class, “You’ll know it when you see it”.
Product-based quality - precise and measurable variable/attribute of a product (quantitative) “fastest, biggest, smallest, strongest, fit, form, function” etc.
Production/process-based quality - conformance specifications / variation (quantitative), products that deviate from this specification are considered defective and thus poor quality.
Customer-based quality - focuses exclusively on the customer in the determination of quality (qualitative) . Involves meeting (and exceeding) their needs & wants to improve satisfaction.

## Slide 7: Traditional Quality – Product/Process Orientation
Many traditional approaches to quality rely on measuring a products conformance to specifications/standards.
A common approach is the concept of acceptable quality levels (AQLs) - lowest quality level that is still considered satisfactory.
A risk of this approach is that we may start aiming for this lowest level of quality (encourages complacency).
Question – In the current climate, is “the worst quality we can get away with” a benchmark we should setting?

## Slide 8: The Quality Gurus
Eight quality gurus, known for their key contribution to the quality:
Walter A. Shewhart
William E. Deming
Joseph M. Juran
Kaoru Ishikawa
Armand Feigenbaum
Genichi Taguchi
Shigeo Shingo
Philip Crosby
Not an Exhaustive List!

## Slide 9: How do the Quality Gurus Define Quality?
Walter A. Shewhart
William E. Deming
Joseph M. Juran
Kaoru Ishikawa
Armand Feigenbaum
Genichi Taguchi
Shigeo Shingo
Philip Crosby
Customer focus: Meeting the customers Needs
Customer Focus: Fitness for use
Holistic Quality: Product, people, process & service.
Customer focus: Satisfaction of customers
Product focus;
Designed in quality / robustness
Customer focus:
Conformance
To
customer
requirements
Process focus: Quality at source & zero defects
Process focus: Free from
defects

## Slide 10: Contemporary Quality – Customer Focus
Most modern approaches recognise the significance / importance of considering the customers requirements in defining quality.
Whilst many traditional approaches rely on AQLs there is no such measure in Lean philosophy, rather it states that no level of poor quality or defective product (other than zero) is acceptable.
Further, total quality management (TQM) philosophy suggests that quality is defined by the wants and needs (requirements) of the customer, and that the quality of a product / process / service is the measure of how closely it meets these requirements.
It recognises that even a ‘technically excellent’ product should be considered poor quality if it doesn’t meet the customers requirements (wants & needs).

## Slide 11: 8 Dimensions of Quality (Developed by David Garvin)
Garvin proposed eight critical dimensions or categories of quality (common customer requirements) that can serve as a framework for quality:
Performance
Features
Reliability
Conformance
Durability
Serviceability
Aesthetics
Perceived Quality

## Slide 12: Cost of Quality (COQ) (Money spent to avoid and as a result of failures)
Costs of Conformance
Prevention Costs (Producing a quality product)
Planning activities (audits, supplier evaluations, risk assessments, design reviews)
Training
Equipment required
Time to do it right
Appraisal Costs (Assessing the quality)
Inspection & testing
Quality audits
Destructive testing losses (calibration, test setup, materials & product losses)
Costs of Nonconformance
Internal Failure Costs (failures found in process)
Scrap & rework
Retest & redesign
Unplanned downtime
Time spent problem solving
External Failure Costs (failures found by customers)
Liabilities
Warranty work / charges
Returns & recalls
Late delivery penalties
Lost business / opportunities

## Slide 13: The 1-10-100x Rule
Prevention Cost – Catching & fixing problems Early, i.e. before or during production.
Correction Cost – Catching & fixing problems late, i.e. internally but after the first time through.
Failure Cost – Cost of fixing problems once they have reached the customer.

## Slide 14: Costs of Poor Quality (COPQ) – Iceberg Analogy (“Poor quality will be remembered long after low prices are forgotten” – Charles Royce)
Visible Costs – Tangible
≈ 15%
Hidden Costs – Intangible
≈ 85%
Defects (yield)
Rework
Scrap
Field Repairs
Inspection
Reduced Profitability
Costly engineering changes
Additional setups
Expediting costs
Excess inventory
Increased cycle times
Risk to safety
Late delivery
Costly overtime
Scheduling conflicts
Investigations
Lost sales
Degraded company image
Lost customer loyalty

## Slide 15: Customer Focus – Challenges
The customer defined quality approach presents us with a series of challenges
Customer requirements are often subjective (and qualitative), how do we capture them?
So many different preferences – how do we prioritise them?
How do we measure how closely we are meeting these requirements?
Some customers may not know what they want/need or may not be able to articulate it.
What challenges do you think may occur as a result of customer defined quality?

## Slide 16: What is Quality Management?
Quality Management
Can be defined as all of the activities involved in planning, assurance, control and improvement of quality.
Quality Planning
Defining customer quality requirements and developing the capability/resources to meet them.
Quality Assurance
Applying planned, systematic quality activities to prevent defects and generate confidence that we are meeting the quality requirements.
Quality Control
Monitoring production to check we are meeting quality requirements (i.e. testing & inspections)
Quality Improvement
Increasing the capability to meet and exceed the quality requirements and then standardising these improvements.
Plan – Quality Planning
Are we doing the right things?
Do – Quality Assurance
(Before) Are we doing things right?
Check – Quality Control
(After) Have we done the right things correctly?
Act – Quality Improvement
Can we do things better?

## Slide 17: Quality Improvement – Deming’s 14 Points (Deming laid the ground work for TQM)
Deming’s 14 Points |  |  | 
1. | Create constancy of purpose | 8. | Drive out fear
2. | Adopt the new philosophy and take on leadership | 9. | Eliminate silos / barriers between departments. Encourage interdepartmental collaboration / teamwork
3. | Stop depending on / eliminate inspections, build in quality | 10. | Eliminate slogans, exhortations and arbitrary targets for the workforce
4. | Use a single supplier for any one item | 11. | Eliminate numerical standards / quotas for the workforce.
5. | Aim to improve constantly and forever | 12. | Encourage and celebrate pride of workmanship
6. | Institute training on the job (education and progression opportunities) | 13. | Institute a vigorous program of training and self improvement.
7. | Supervision should help people, not monitor performance. | 14. | Involve all workers in the transformation, and commit to ever-improving quality

## Slide 18: What is Total Quality Management?
TQM is a organization-wide management strategy that emphasises continuous improvements in order to improve product / service quality. Goals of TQM:
Achieve the continuous improvement mindset
Prevent defects and reduced process variation
Improve customer satisfaction
Improve employee engagement and training
Streamline supply chain management

## Slide 19: Total Quality Management (TQM)
Total – Conveys the idea that all employees, throughout every function and level of the organisation, must work together in the pursuit of quality / Improvement.
Quality – Implies that quality is defined by the customer, and that we must constantly aim to meet or exceed their wants & needs (requirements).
Management – All of the activities undertaken to plan, assure, control and improve the level of quality, and further, to sustain this high level of quality.

## Slide 20: The Quality Movement – History of TQM (How quality evolved with Time)
Evolution of Quality Over Time
Process (manufacturing)
Product
Influence of Management
Customers / people / culture
Breadth of Quality Focus

## Slide 21: Total Quality Management - Lean/JIT
TQM wasn’t specifically developed at Toyota like many of the Lean principles we have come to recognise.
It’s a broad and systematic philosophy based on a series of principles developed by the likes of Deming, Juran and Feigenbaum.
However, it was quickly adopted and proven by many Japanese companies, such as Toyota.
Nowadays, TQM is considered intrinsic to Lean/JIT manufacturing.
Remember, JIT is about producing what customers want, when they want it and in the right quantities.

## Slide 22: TQM Implementation - 7 Key Principles
1. Customer focus
2. Continuous improvement
3. Involving people / empowering employees
4. Process centred approach
5. Data-Driven decisions (using 7 quality tools)
6. Leadership driven / systematic management
7. Mutually beneficial supplier relationships

## Slide 23: Typical TQM Implementation Workflow
Top management learns about and decides to commit to TQM (TQM is identified as the organization’s new QM strategy).
The organization assesses current culture, customer satisfaction, and quality management systems (scope for improvement).
Top management identifies core values and principles to be used, and communicates them to all employees.
A TQM master plan is developed on the basis of steps 1, 2, and 3.
The organization identifies and prioritizes customer requirements and aligns products and services to meet them.
Management maps the critical processes through which the organization meets its customers’ needs.

## Slide 24: Typical TQM Implementation Workflow (Cont.)
Management oversees the formation of teams for process improvement efforts (kaizen teams).
The momentum of the TQM effort is managed (sustained) by the steering committee (multiskilled / interdepartmental team).
Managers contribute individually to the effort through hoshin planning, training, coaching etc.
Daily process management, improvement & standardization take place.
The progress of the TQM implementation is evaluated and the plan is revised as needed.
Constant employee awareness and feedback on status are provided and a reward/recognition system is established.

## Slide 25: TQM – All Encompassing
As stated above, TQM required broad sweeping changes that have a much wider impact than to engineering/manufacturing alone:
Management | Change management, kaizen culture, sustaining improvements
R&D | Quality by design (customer requirements to technical specifications)
Purchasing | Sourcing quality supplies and building supplier relationships
Marketing | Determining the customer requirements through market research
Accounting & Finance | Evaluating / monitoring financial impacts & providing exact costings
HR | Hiring the right people (skills) and providing training opportunities
Information systems | Access and reliability of all required information across all departments.

## Slide 26: The Many Benefits of Implementing TQM
Improved product / service quality
Improved yield
Decreased quality costs
Increased customer satisfaction
Increases employee satisfaction / participation / teamwork
Increased productivity & profitability
Better understanding of process interactions in the value stream.
Better supplier relationships (cost & quality)
Increased competitive advantage
Increased market share

## Slide 27: Barriers to TQM
Lack of management commitment / leadership
Lack of constancy of purpose
Inability to change organizational culture
Focus on short term gains
Improper planning for quality
Lack of training and education
Lack of recognition and rewards
Failure to continuously improve

## Slide 28: 7 Basic Quality Tools – Brief Overview (Ishikawa's 7 Tools to solve 95% of problems)
The 7 basic quality tools:
Pareto analysis / diagrams
Histograms
Scatter diagrams
Control charts
Process Flow charts
Cause & effects analysis / Ishikawa Diagrams
Check lists / sheets

## Slide 29: 7 Basic Quality Tools – Brief Overview (Ishikawa's 7 Tools to solve 95% of problems)
Simple graphical (visual) techniques to:
Track quality performance & trends
Identify any existing quality problems
Analyse an gain insight into the causes / sources or quality problems
Figure out (prioritise) which issues to address
Help eliminate the quality problems (prevention, not just detection & correction).
Note: Basic knowledge for anyone interested / working in quality, general engineering problem solving and systems design. You are probably already familiar with most of them!

## Slide 30: Why seven tools?
Kaoru Ishikawa promoted the 7 basic tools as a simplistic means of addressing quality (simplistic solutions are often the most effective)
They are largely designed for manufacturing settings, but are also applicable to engineering and management.
There are also many more advanced statistical methods, such as:
Survey sampling
Acceptance sampling
Statistical hypothesis testing
Design of experiments
Multivariate analysis (MVA)

## Slide 31: Check sheets
Tool for collecting & organising measured / counted defect data
Data collected is used as input data for the other quality tools
Data collections are based on answering: what, where, who and how
When to use a check sheet?
Generally to collect data from anywhere in production process.
To collect data repeatedly by the same person or at the same location
To collect data on: frequency or pattern of events, problems, defects, defect location, defect cause etc.

## Slide 32: Histograms
Simple bar charts showing frequency of occurrence data.
Used to visualise centring, dispersion (deviation/spread), and shape (relative frequency) of a dataset
Often used to identify how the output of a process relates to a target / specification (customer requirement)
Answers the question is this process currently capable of meeting the specification
Often compared with historical examples to identify changes in process capability.

## Slide 33: Cause & effects (Ishikawa / fishbone diagrams)
Visual tool to show the hierarchical structure of causes that contribute to a problem/outcome.
  Problem of interest forms the back bone
  Spines are the causes that contribute to the problem
  Spines may have individual bones that represent sub-factors.
Often used to brainstorm / identify various possible contributing factors and group casual sequences (A causes, B causes, C causes)
Very simple tool but extremely useful.
Initially, Its important to list all minor and major contributing factors! (minor factors can concatenate into major failures).

## Slide 34: Pareto Analysis
Essentially histograms arranged by decreasing Frequency.
Used to identify which causes contribute to a problem / outcome the most.
  Based on Pareto's 80 / 20 rule
  Uses Juran’s vital few & trivial many
Often performed after C&E analysis to determine the significance of causes.
Allows us to prioritise our corrective action.
Greater cost-benefit from addressing significant problems – some may barely be worth addressing

## Slide 35: Scatter diagrams
Used to Analyse the correlations between a given quality characteristic and a factor that may (may not) be driving it.
if variables are correlated, when one changes the other will also change.
Data points (dots) that looks as though they are forming a line are strongly correlated
Sometimes, the scatter plot may show little correlation when all the data is plotted (considered) at the same time. We may need to stratify or filter data.

## Slide 36: Control Charts
Control charts are used to monitor how the outputs of a process are changing over time (process stability).
Often used to identify and eliminating common cause variation (special cause is more tricky!).
Control charts include:
Centre line (mean average).
Upper control limit (UCL) and lower control limit (LCL).
These lines are used to identify if process variation is stable (in control) or unpredictable (out of control)

## Slide 37: Process flow charts
Process flow charts are tools used to visualise the sequence of activities and decisions.
Used to streamline the flow of activities by applying logic.
Gain insight into how to perform activities effectively.
Eliminate and prevent problems due to missing or poor sequencing of process activities.
Often used in process design and improvement to analyse new ideas:
Well planned processes avoid problems and eliminate waste.
Almost zero cost for improving quality.

## Slide 38: Summary
Check sheets are used to record problem / defect data.
Histograms are used to identify the frequency of problems defects.
Ishikawa diagrams are used to identify possible causes.
Scatter plots are used to analyse whether there is any relationship between the potential causes and effects (problems).
Pareto analysis allows us to prioritise which causes to address
Flow chart Eliminate & prevent problems due to missing or poor sequencing of process activities.
Control charts allow us to monitor process stability and identify new problems.

## Slide 39: Kano Model for Quality – Overview
Quality measurement tool used to prioritise quality characteristics (customer requirements) based on their impact to customer satisfaction.
Ranking requirements between customer groups to work out which have priority.
Based on the principle that there are 3 types of customer reaction to any given product characteristic / attribute.

## Slide 40: Kano Model for Quality – Overview
Delighters – Exciting Quality
Satisfiers – Wants / normal quality
Dissatisfiers – Must haves / expected quality

## Slide 41: Summary of Kano model benefits
Helps us define quality from the customers perspective.
Prevents time / effort / money wasted working on features or attributes that will not please customers or leave them indifferent.
Prioritises product features / attributes to create most value.
Improves customer satisfaction by better understanding of needs.
Provides opportunities for competitive differentiators (USPs) and can thus improves market share.
Helps determine when a product attribute moves from attractive to becoming a must-have.