## Slide 1: Building Owners Manual or Operation & Maintenance (O&M) Manual

## Slide 2: Purpose
Contains the information required for the operation, maintenance, decommissioning and demolition of a building.

## Slide 3
The Inclusive Design Overlay to the RIBA Plan of Work published by the RIBA in 2023, states:
‘The Building Manual helps to ensure that operations and maintenance activities are effectively implemented. It includes a summary of all key information about a building, including the Health and Safety File and Fire Safety Information, which are regulatory requirements and might contain tasks that the users must consider to get the most out of the building.’
RIBA (2024)

## Slide 4: Prepared by the contractor or the sub-contractor with additional information from the designers (in particular, the services engineer) and suppliers. It is a requirement that is generally defined in the preliminaries section of the tender documentation where its contents will be described, although there may be additional requirements regarding mechanical and electrical services in the mechanical and electrical specification.

## Slide 5
A draft version of the document should be provided for the client as part of the handover procedure prior to certifying practical completion.
The final document is not usually available in full form until several months after practical completion, as commissioning information often needs to include summer and winter readings taken in the fully occupied building.
The preliminaries may require several copies of the building owner's manual and might require an electronic version.

## Slide 6: What information might be useful in a building operating & maintenance manual?
https://www.designingbuildings.co.uk/wiki/Building_owner's_manual_-_O_and_M_manual

## Slide 7: A description of the main design principles.
Types of Ventilation including Controls
Heating and Cooling Methods
Active or Passive Methods being used
Insulation or Thermal Mass utilisation
Intended use and layout
Orientation and shading
HMC Architects (2019)

## Slide 8: Details of the building's construction (such as finishes, cladding, doors and windows, roof construction, and so on).
Maintenance work – Paint/Render types/colours
Specification of materials – performance metrics i.e. slate will last longer than concrete tiles
To help plan for retrofit

## Slide 9: As-built drawings and specifications.
To allow planning of future alteration work
Identification of service locations
Help plan maintenance work
Useful for energy calculations

## Slide 10: Instructions for its operation and maintenance (including health and safety information and manufacturers' instructions).
Passed on by installers and testers
Allow for efficient operation and safe use
Plan for maintenance
Essential to comply with warranties/guarantees

## Slide 11: An asset register of plant and equipment.
List of equipment used in the building
Essential for planning maintenance
Often required to comply with legislation – Display Energy Certificates, Operational Ratings, Recommendation reports and Air conditioning inspection certificates/reports.
https://www.gov.uk/get-your-air-conditioning-system-inspected
https://find-energy-certificate.service.gov.uk/energy-certificate/1586-9914-5062-5690-2396#other_certificates_and_reports

## Slide 12: Commissioning and testing results. Guarantees, warranties and certificates.
Dates of repeat maintenance included
Maintenance required to maintain warranties
Information about guarantees and claims

## Slide 13: Particular requirements for demolition, decommissioning and disposal.
Identification of Hazardous material
Safe systems of work
Information on waste disposal procedures and locations

## Slide 14: Details of how measures included in the Security Strategy are incorporated into the Building Systems and how these will be operated.
Outline measure for building access
Digital security measures
The Security Strategy outlines what security measures have been incorporated into the design based on the Security Risk Assessment and the Security Requirements.
Evacuation and Emergency Procedures
Fire Control Systems

## Slide 15
Much of this information will already exist in one form or another, so preparing the building owner's manual might simply be a matter of compiling and assembling its components.
Over the life of the buildings, the building owner's manual may be developed to reflect changes that take place to the fabric of the building or its systems, along with details of maintenance that has taken place .

## Slide 16
The building owner's manual is different from the health and safety file which only needs to include information important to health and safety and does not need to include information about the construction process, contractual information or information about the normal operation of the completed structure.
The building owner's manual may also include a non-technical 'building user's guide' with information for users about environmental controls, access, security and safety systems, etc.

## Slide 17
Building Log-book
Part L of the Building Regulations (conservation of fuel and power) requires that the building owner is issued with information about the building services to help them operate the building properly and efficiently.
It is suggested that this is done by issuing a building log-book to the building's facilities manager.
These are required for new buildings and for existing buildings where the services have changed.

## Slide 18: Building Log-Book
This is different to, but may draw upon information in the Building Owner's (O&M manual), and the Health and Safety File.
Unlike the building owner's manual it should be a concise document (20-50 pages for larger buildings and 5-10 pages for buildings under 200 sqm. Carbon Trust (2003)
It should be easy to understand, giving an overview of the way in which the building was originally intended to operate and any changes that have been made.

## Slide 19
Building log books can be prepared following the guidance in the Chartered Institution of Building Services Engineers (CIBSE) TM 31 Log Book Toolkit. They may include:
Maintenance requirements.
Metering and monitoring strategy.
The data used to calculate the TER (target CO2 emission rates) and BER (building CO2 emission rates), see emissions rates.
The recommendations report produced along with the construction energy performance certificate.
Building performance in use investigations and targets.
References to other documents.
A description of key responsibilities.
A schedule of contacts.
A description of the overall building, including zoning and occupancy.
A description of the building's operational strategy.
A description of the building's services plant, controls and management systems.
Changes that have been made to the building.
Health and safety considerations.

## Slide 20
In addition to a building owner's manual and building log book, it may also be prudent to prepare a non-technical 'building user's guide' (BUG) with information for users about:
The principles behind the design of the building and how these affect its operation.
The building's standard of performance.
Energy efficiency measures.
Water-saving measures.
Means of operating heating, lighting and cooling systems, and the consequences of incorrect operation.
Access, security and safety systems.
Methods for reporting problems.
Car parking and cycling provision, local public transport, car sharing schemes, etc.
Waste management.
Training.

## Slide 21: References
Royal Institute of British Architects (RIBA) 2024 Inclusive Design Overlay to the RIBA Plan of Work. Available At: https://www.architecture.com/knowledge-and- resources/resources-landing-page/inclusive-design-overlay-to- riba-plan-of-work (Accessed: 12th February 2025)
HMC Architects 2019. Architecture and Facility Management Work Together to Extend a Building’s Lifecycle. Available at: https://hmcarchitects.com/news/architecture-and-facility- management-work-together-to-extend-a-buildings- lifecycle2019-08-14/ (Accessed: 12th February 2025)
Carbon Trust 2003 Good Practice Guide 348 Building log books - a user’s guide. Available at:
https://www.thenbs.com/PublicationIndex/documents/details?Pub=CARBONTRUST&DocID=292269 (Accessed 12th February 2025)