## Slide 1: Su-Field Analysis
By
Andrew Thorn

## Slide 2: The Substance Field Model
Is a TRIZ analytical tool for modelling problems related to existing technological systems
Every system is created to perform some functions
The desired function is the output from an object or substance (S1), caused by another object (S2) with the help of some means (types of energy, F)

## Slide 3: When to use Su-Field Analysis
To zoom in on the zone of interest
The analysis can be applied to a system as well as component levels of abstraction, interface between the two substances
For complex systems there is a Su-Field model for all the zones of interest
Two substances and a field are necessary and sufficient to define a working technical system

## Slide 4: Four Basic Models
Effective complete system
Incomplete system (requires completion or a new system)
Ineffective complete system (requires improvement to create the desired effect)
Harmful complete system (requires elimination of the negative effects)

## Slide 5: Su-Field Analysis
If there is a problem with an existing System and any of the three elements are missing, Su-field analysis indicates where the model requires completion and offers directions for innovative thinking
If there is an innovative problem and the system has three required elements, Su-field analysis can suggest ways to modify the system for better performance

## Slide 6: Making a Model
The field, which is itself often some form of energy, provides some energy, force or reaction to guarantee an effect
The effect could be on S1 or the output of the field information
The term field is used in the broadest sense, including the fields of physics, thermal, chemical

## Slide 7: Steps in Su-Field Model
Identify the elements: - The field is either acting upon both substances or is within substance 2 as a system
Construct the model: - After completing these two steps, stop to evaluate the completeness and effectiveness of the system
Consider solutions from the 76 standard solutions
Develop a concept to support the solution

## Slide 8: Sufield Analysis
Effect not evaluated
Desired effect
Insufficient effect
Harmful effect
Results in changed model
Field types Ftype
Useful effect U
Harmful effect H

## Slide 9: Sufield Analysis
The identification of substances (S1 and S2) depends upon the application
Either substance could be a material, tool, part, person or environment
S1 is the recipient of the systems action
S2 is the means by which some source of energy is applied to S1
Relationships between the elements in the Su-field model are depicted by five different connecting lines shown in the previous slide

## Slide 10: Su-field Analysis
the source of energy, or field (F), which acts upon the substances is often:
(Me) Mechanical
(Th) Thermal
(Ch) Chemical
(E) Electrical
(M) Magnetic
(G) Gravitational

## Slide 11: Identify the Elements
Task is to break a rock
Function = Break rock
Rock = S1
Hammer = S2

## Slide 12: Construct the Model Incomplete System
In these incomplete models the desired effect does not occur
Completing the system will at the very least, make the useful function possible
One complete system is a pneumatic hammer, which provides pulsed mechanical force upon the rock with the hammer
The performance of the system is not considered at this time

## Slide 13: Construct the Model
Once a complete system has been defined, performance can be analysed
The evaluation of a completed system’s performance gives three possible
(1) Effective complete system
(2) A harmful effect occurs
(3) The results are ineffective

## Slide 14: Complete System
FMe FMe
Rock Hammer
S1
S2
S1
S2
S1

## Slide 15: Harmful Complete System
FMe H (rock too small)
Hammer Rock
FMe U (rock broken)
Hammer Rock H (flying particles)
S2
S1
S2
S1

## Slide 16: Consider 76 Standard Solutions
Depending upon the application there may be the option of a new system by replacing S2 by S3 and/or using a different field
For example S2 could be a large vise still using a Fme but the mechanical field is created by a human while in the example it is created by pulsed air

## Slide 17
S2
S1
S3
F Me

## Slide 18: Develop a Concept to Support the Solution
The changes made are based only on the original form of the problem, new directions to search for design solutions are considered
Some of the directions may not be fruitful, but the important function of the model is to create global concepts
The challenging task is to supply detail to the global concept

## Slide 19: Develop a Concept to Support the Solution
Two ways of applying a standard solution are introduction of another substance or introduction of another field
Insights come from considering different substances for S and different fields for F

## Slide 20: Develop a Concept to Support the Solution Example
The harmful effect is flying pieces, a metal mesh covering the rock could be an added substance (S) used to eliminate the harmful effect
If the rock contains moisture freezing (F Th) could cause cracks produced by the expansion of the moisture when it freezes
The breaking will occur as these cracks gradually expand, reducing the explosive release of fragments