## Slide 1
Lecture By,
Mrs. Jenifer Prince Devaraj,
Lecturer - Embedded Electronics,
Faculty of Applied Computing,
UWTSD
Email:j.prince-devaraj@uwtsd.ac.uk
Module Name : Electronics I
Module Code : ACDB5002
Topic : Smart energy-saving device
Lecture : 15

## Slide 2: SENARIO
A smart energy-saving device is to be installed in rural homes where street lighting is minimal. The goal is to design a compact system that can automatically detect low light conditions and trigger an emergency light (LED), while also displaying status messages on an LCD.
Smart energy-saving device
UWTSD Lectures / ACDB5002 – Electronics 1

## Slide 3: Requirement
The system will use a PIC16F877A microcontroller and should operate using standard electronic components. It must be developed and tested using Proteus simulation software and programmed using CCS C.
Smart energy-saving device
UWTSD Lectures / ACDB5002 – Electronics 1

## Slide 4: System Specifications
1. A 12V DC source must be stepped down and regulated to 5V using a voltage regulator.
2. An LDR-based light sensor and an LM393 comparator circuit that must be used to detect ambient light:
      ─ Output LOW (0V) in darkness.
      ─ Output HIGH (5V) in brightness.
      ─ Output of the LDR Based circuit is connected to RB0 of PIC16F877A.
Smart energy-saving device
UWTSD Lectures / ACDB5002 – Electronics 1

## Slide 5: System Specifications
3. An LED connected to RC0 must:
      ─ Turn ON in dark conditions.
      ─ Turn OFF in bright conditions.
4. A 16x2 LCD connected to Port D must display:
      ─ "DARK CONDITION" when it is dark.
      ─ "BRIGHT CONDITION" when it is bright.
Smart energy-saving device
UWTSD Lectures / ACDB5002 – Electronics 1

## Slide 6: Questions
Design the schematic using Proetus.
Write the Program for the given scenario.
Simulate and verify the results.
Explain the working of Night light Sensor.
Explain the working of the Voltage Regulator.
Explain the functions of RS, RW, E, D0–D7, VSS, VDD and VEE in a 16x2 LCD module.
Smart energy-saving device
UWTSD Lectures / ACDB5002 – Electronics 1

## Slide 7
Thank you